DECODE VERSION 3.0 

Decode 3.0 is a modified version of DECODE 2.0.  The file is stored in
DECOD3.MAC and DECOD3.SAV.  The program provides additional features
over version 2.0.  Under version 3.0, the user is allowed to specify a
/S:nnnn and a /E:nnnn option.  These options override the default start
and end processing addresses for the decoding process.  Normally, the
addresses come from block 0 of the subject file.  Manual control allows
the user start instruction decoding before the program transfer address
and to end decoding after the end of the root segment.

The second enhancement allows the user to set up a command file which
will allow the decode program to switch from data mode to instruction
mode at specified octal addresses.  This file is of the form:


D 1000
I 1100
D 1200
I 1202
ect.

During execution of the decode program, it will read the file and
control the translation process.

To call the revised program type "RUN DECOD3" and answer the "*" prompt
in the form:

	LP:=prog,comm.DAT/S:nnnn/E:mmmm/P:2

This string will decode program "prog.SAV" with instructions starting at
nnnn and ending at mmmm.  The mode control will be defined in file
"comm.DAT".  Output will go to the line printer, and decoding will be
in accordance with the LSI-11 instruction set (/P:2 option).

These features are only available when decoding .SAV files!!!!!!


					Good Luck!

					Tom Rorro




		DECOD2.DOC V02
				BY YUKOH KOBAYASHI
				INSTRUCTION AND RESEARCH
				COMPUTER CENTER
				THE OHIO STATE UNIVERSITY
				MAY 10, 1980
	RT-11 SAV/LDA FILE  DISASSEMBLER

ABSTRACT

	DECOD2 IS A PROGRAM WRITTEN TO RUN UNDER RT-11
OPERATING SYSTEM TO DECODE (DISASSEMBLE).SAV AND .LDA FILES 
INTO THEIR EQIVALENT MACRO-11 ASSEMBLY CODE COMPLETE WITH
SELF GENERATED LABELS, ABSOLUTE LOCATION, SYMBOL TABLE,
CROSS REFERENCE TABLE, OCTAL, ASCII AND RADIX 50 EQUIVALENTS.
	DECOD2 IS A MODIFIED AND IMPROVED VERSION OF THE DECODE
V01J PROGRAM, WHICH WAS WRITTEN BY MICHAEL LEVINE AT NAVAL 
WEAPONS CENTER.
 	THE OUTPUT CAN BE ASSEMBLED BY THE MACRO-11 ASSEMBLER
AND LINKED TO RECREATE THE ORIGINAL FILE. BY THE USE OF SWITCHES
THE OUTPUT CODE CAN BE MADE TO REFLECT THE INSTRUCTION SET
OF ONE MACHINE CONFIGURATION ONLY INSTEAD OF ALL POSSIBLE
INSTRUCTIONS.


IMPROVED FEATURES OVER DECODE V01J

	DECOD2 IS AN IMPROVED VERSION OF ORIGINAL DECODE
	V01J PROGRAM. IMPROVED FEATURES ARE FOLLOWINGS:

	1. THE ORIGINAL DECODE PROGRAM DISASSEMBLED EVERY
	WORD INTO AN ASSEMBLY MNEMONIC CODE.IT CREATED 
	AN UNDESIRABLE PROBLEM THAT WHEN THE STARTING ADDRESS
	OF AN INPUT PROGRAM TO BE DECODED IS LOCATED AT THE MIDDLE 
	OF THE PROGRAM, THE FIRST INSTRUCTION AT THE
	STARTING ADDRESS MAY NOT BE DISASSEMBLED CORRECTLY 
	SINCE THE MEANING OF CURRENT WORD BEING DECODED DEPENDS ON
	THE PREVIOUS WORDS. THIS PROBLEM HAS BEEN CORRECTED
	IN DECOD2 WHICH DOES NOT DECODE THOSE WORDS LOCATED
	BETWEEN THE LOWEST LOCATION OF THE PROGRAM AND THE 
	STARTING ADDRESS OF THE PROGRAM. THESE WORDS WILL BE
	REGARDED AS DATA AND BE REPRESENTED BY .WORD MNEMONIC.

	2. DECOD2 HAS A NEW OPTION, /I, WHICH SPECIFIES
	THAT THE OUTPUT FROM DECOD2 WILL HAVE A FORMAT 
	SUITABLE TO AN INPUT TO MACRO-11 ASSEMBLER.
	IN THIS MODE, ALL COMMENT FIELDS ARE ELIMINATED.
	ALSO, THE SYMBOL TABLE AND CROSS REFERENCE TABLE
	ARE NOT OUTPUT.

	3. THE ORIGINAL DECODE PROGRAM NEGLECTED STARTING
	ADDRESS GIVEN IN A .LDA FILE. HOWEVER, DECOD2
	RECOGNIZES THE STARTING ADDRESS SPECIFIED IN
	A .LDA FILE. IF STARTING ADDRESS IS  0, DECOD2
	PRINTS A MESSAGE TO THE USER, AND PROCEEDS DECODING.
	FURTHER, DECOD2 CAN READ THE VALUE OF STARTING ADDRESS
	FOR A .LDA FILE AS AN OPTION.

	4. THE OUTPUT FROM THE ORIGINAL DECODE PROGRAM IS
	NOT EASY TO READ FOR THE REASON THAT LABELS PUT ON
	A DISASSEMBLED MNEMONIC LIST ARE NOT SORTED. IN DECOD2,
	LABELS APPEARING IN A MNEMONIC LIST ARE ALWAYS SORTED
 	AND FURTHER EVERY LABEL SHOWS THE LOCATION WHERE IT IS DEFINED.

	5. THE ORIGINAL DECODE HAS FEW COMMENTS, WHILE MORE
	COMMENTS ARE INCLUDED IN DECOD2.

	6. A SINGLE 0 VALUE WORD IS REPRESENTED AS A .WORD 0
	DIRECTIVE IN THE OUTPUT LIST IN DECOD2 INSTEAD OF HALT
	INSTRUCTION IN DECODE. TWO OR MORE CONTINUOUS 0 VALUE
	WORDS ARE REPRESENTED AS A .BLKW DIRECTIVE.
	FURTHER, LABELS APPEARING MIDDLE OF CONSECUTIVE 0'S 
	ARE OUTPUTED CORRECTLY.

	7. IN ORDER TO SAVE PRINTER PAPER, OUTPUT OF
	FF (FORM FEED) CODE IS MINIMIZED.

	8. THE PROBLEM THAT DEFINITION OF ALL LABELS IS
	OUTPUTED BEFORE OUTPUT OF TEXT WHEN THE BIGGINING
	(NOT STARTING) ADDRESS OF THE INPUT PROGRAM IS 0.


	9. OTHER SEVERAL SMALL POINTS HAVE BEEN MODIFIED.

INSTRUCTIONS

	THE COMMAND STRING TO DECOD2 IS;
*OUTFIL=INFIL/SW:VAL/SW:VAL

WHERE THE FILES HAVE THE STANDARD RT-11 FORMAT

DEV:FILNAM.EXT[SIZE]

DEFAULT EXTENTIONS ARE
INPUT FILE	.SAV
OUTPUT FILE	.DEC

SWITCHES

/A:VAL		USED TO LIMIT THE ARITHMETIC INSTRUCTIONS DECODED
		INTO MNEONICS. THE ARITHMETIC OPTION GIVEN BY VAL

		VAL=EIS
		    FIS
		    FPU

		GIVES THE SET OF ARITHMETIC INSTRUCTIONS
 		THAT ARE TO BE DECODED INTO NEMONICS. THE /A SWITCH IS
		RECOGNIZED ONLY IF THE /P SWITCH IS ALSO USED AND THE
		PROCESSOR SPECIFIED BY THE /P SWITCH  ALLOWS THE OPTIONS
		GIVEN BY VAL(FIS IS ILLEGAL FOR A 45 AS IS FPU FOR A 40).
		NOTE THAT A VAL OF FIS ALSO IMPILES EIS IS ON THE SYSTEM.	

/I		THE FORMAT OF OUTPUT WILL BE SUCH THAT THE OUTPUT 
		CAN BE AN INPUT TO MACRO-11 ASSEMBLER.

/L:VAL		FLAGS THAT THE INPUT FILE IS AN LDA FILE. IN THIS CASE
		THE INPUT FILE MUST HAVE .LDA FORMAT.
		VAL=STARTING ADDRESS (NOT LOADING ADDRESS) OF THE INPUT
		    PROGRAM IN OCTAL.
		SEE EXAMPLE 2

/M		USED TO LIMIT THE INSTRUCTION SET DECODED INTO NEMONICS.
		IN THIS CASE IT FLAGS THE EXISTENCE OF A MEMORY
		MANAGEMENT UNIT ON THE SYSTEM. THIS SWITCH IS IGNORED
		IF THE /P SWITCH IS NOT USED OR IF IT IS, THE
		PROCESSOR SPECIFIED DOES NOT HAVE THE CAPABILITY
		OF MEMORY MANAGEMENT(THAT MEANS 40'S AND ABOVE) AND
		THEN ONLY THE MEMORY MANAGEMENT INSTRUCTIONS
		THAT APPLY TO THAT PROCESSOR.

/P:VALUE.	SPECIFIES THE TYPE OF PROCESSOR TO DECODE FOR. IF
		VALUE IS NOT GIVEN-ONLY THE BASIC INSTRUCTION SET IS
		DECODED INTO NEMONICS. IF /P IS NOT USED,ALL POSSABLE
		PDP-11 INSTRUCTIONS ARE DECODED INTO THEIR NEMONICS.
		VALUE IS THE DECIMAL NUMBER OF THE TYPE OF PROCESSOR
		( 03,04,05,10,15,20,34,35,40,45,ETC)
		AND MUST BE FOLLOWED BY A '.' DECIMAL POINT TO TELL
		THE CSI THAT IT IS A DECIMAL NUMBER. THIS SWITCH MUST BE
		USED IF THE /A AND /M SWITCHES ARE TO BE RECOGNIZED AND
		THE OPTIONS SPECIFIED MUST BE COMPATABLE WITH THE
		PROCESSOR TYPE GIVEN BY THE /P:VAL. OR THEY WILL BE
		IGNORED. THE DISSASEMBLER BREAKS DOWN THE PDP-11
		INSTRUCTION SET INTO 9 CATEGORIES:



		1	BASIC INSTRUCTION SET AS FOR THE PDP 11/04
			THROUGH THE 11/20 SERIES.

		2	PDP 11/03 UNIQUE INSTRUCTIONS.

		3	PDP 11/40-11/45 UNIQUE BASIC INSTRUCTION SET.
			INCLUDES ALL THOSE NON OPTION INSTRUCTIONS
			UNIQUE TO THE 11/40 AND 45 COMPUTERS.

		4	PDP 11/45 UNIQUE BASIC INSTRUCTION SET.
			INCLUDES ALL THE NON OPTION INSTRUCTIONS
			UNIQUE TO THE 11/45 COMPUTER

		5	PDP 11/40-11/45 MEMORY MANAGEMENT INSTRUCTION
			SET. INCLUDES ALL THE MEMORY MANAGEMENT
			INSTRUCTIONS COMMON TO THE 11/40 AND 45
			COMPUTERS

		6	PDP 11/45 MEMORY MANAGEMENT INSTRUCTION SET.
			INCLUDES ALL THE MEMORY MANAGEMENT INSTRUCTIONS
			UNIQUE TO THE 11/45.

		7	EIS INSTRUCTION SET

		8	FIS INSTRUCTION SET

		9	FPU INSTRUCTION SET


VAL\INS. SET	1    2    3    4    5    6    7    8    9
NOVAL
0-2		X
4-20

3		X    X    X                   A    A

21-40		X         X         A         A    A

41-77		X         X    X    A    A    X         A


WHERE
	X=DEFAULT INSTRUCTION SET FOR VAL
	A=ACCEPTABLE ADDITONAL INSTRUCTION SET AVAILABLE FOR VAL
	 =INSTRUCTIONS NOT AVAILABLE FOR VAL


		THE DECODER USES THE OPTIONS SPECIFIED IN THE COMMAND
		STRING TO CHOOSE WHICH COMBINATION OF INSTRUCTION SETS
		TO DECODE INTO NEMONICS( DEFAULT FOR NO OPTION SWITCHES
		IN THE COMMAND STRING IS ALL OF THEM)



EXAMPLE 1	DISASSEMBLE A SAV FILE
.R DECOD2
*PIP=PIP
.

EXAMPLE 2	DISASEMBLE AN LDA FILE WHICH CONTAINS A STARTING
		ADDRESS
.R DECOD2
*ROLLIN=ROLLIN.LDA/L
.

OR
.R DECOD2
*AAAAAA=AAAAAA.LDA/L:600
.


EXAMPLE 3	DISASSEMBLE FOR A BASIC MACHINE (11/20)
.R DECOD2
*TEST=TEST/P
.
OR
.R DECOD2
*TEST=TEST/P:20.
.

EXAMPLE 4	FOR AN LSI-11 WITH ARITHMETIC CHIP
.R DECOD2
*TEST=TEST/P:3./A:FIS


EXAMPLE 5	AN 11/45 WITH MEMORY MANAGEMENT BUT NO FPU(EIS IS
		PART OF THE BASIC INSTRUCTION SET OF THE 45)
.R DECOD2
*TEST=TEST/P:45./M
.


DISASSEMBLER OPERATION

	THE DISASSEMBLER MAKES 2 OR 3 PASSES OVER THE INPUT
	DEPENDING ON THE TYPE OF FILE IT IS:

PASS 0	OPTIONAL LDA REFORMAT PASS
	CONVERTS AN LDA FILE INTO SAV FORMAT USEING A 128. BLOCK
	SCRATCH FILE ON THE SYSTEM DISK TO HOLD THE IMAGE FOR
	THE NEXT TWO PASSES. THE SCRATCH FILE NAME IS SY:WORK.DEC.

PASS 1	SEARCH FOR LABELS
	DECODE THE SAV FILE AND LOCATE ALL MEMORY REFERENCES
	(SRC/DEST MODES 2 THRU 7 AND ALL BRANCHES ETC) AND
	ASSIGN A LABEL TO THE VALUE FOUND

PASS 2	OUTPUT SOURCE
	DECODE AGAIN THE SOURCE NOW OUTPUTING IT SUBSTITUTEING
	LABELS FOR THE ABSOLUTE AND RELATIVE ADDRESSES FOUND
	IN PASS 1.


GENERATED CODE

	THE OUTPUT OF THE DISASSEMBLER IS BROKEN INTO 7 PARTS:

PART 1:	DEFINITIONS

	1	DEFINE ALL REGISTERS (AND ACCUMULATORS IF DECODEING FPU
		INSTRUCTIONS)
	2	DECLARE THE LOCATION OF THE STACK STARTING
		LOCATION(IF FOUND) AS THE GLOBAL NAME 'STACK'
		THIS IS SO WHEN LINKING,THE STACK CAN BE PROPERLY
		PLACED BY THE USE OF THE /M SWITCH OF THE LINKER.
		WHEN LINKING,SPECIFY THE /M SWITCH, THE LINKER
		WILL COME BACK ASKING FOR THE STACK SYMBOL, JUST TYPE
		'STACK' AND IT WILL BE PROPERLY PLACED.
	3	DECLARES AN .ASECT
	4	SETS THE POINT TO THE FIRST LOCATION DECODED (FOR SAVE
		FILES EITHER 1000 OR THE STARTING ADDRESS WHICH EVER
		IS LOWER AND FOR LDA FILES THE LOWEST ADDRESS FOUND)

PART 2:	LABEL DEFINITIONS

	THOSE LABELS GENERATED DURING PASS 1 AND WHOSE VALUE IS EITHER
	ODD OR WHOSE VALUE IS OUTSIDE THE BOUNDRIES OF THE PROGRAM ARE
	DEFINED HERE IN THE FORM:
	LXXX=VALUE WHERE XXX PRESENTS THE LOCATION IN OCTAL  WHERE
		THE LABEL IS DEFINED


PART 3:	GENERATED CODE

	THE GENERATED CODE LINE HAS SIX SEGMENTS

	1	LABEL	IF THE ADDRESS IS REFFERED TO BY A LABEL
		FOUND IN PASS 1, IT IS PRINTED OUT IN THE FORM
		LXXX:
		(IF THIS IS THE START ADDRESS THE LABEL
		START:
		PRECEEDS THIS LABEL ON THE LINE PREVIOUS ALL BY
		ITSELF)

	2	INSTRUCTION MNEMONIC OR .WORD OR .BLKW DIRECTIVE

	3	AS THE FIRST PART OF A COMMENT, THE LOCATION OF THE
		INSTRUCTION
		WHEN /I IS GIVEN, THESE COMMENT FIELDS ARE NOT PRODUCED.

	4	THE NEXT ITEM IN THE COMMENT ARE THE OCTAL CONTENTS
		OF THE WORDS MAKEING UP THE INSTRUCTION.

	5	THE THIRD ITEM IS A LIST OF THE EQUIVALENT ASCII
		CARACTERS OF THE WORDS THAT MAKE UP THE INSTRUCTION
		(ALL ASCII CHARACTERS WITH VALUES LESS THAN 40 ARE 
		REPACED BY BLANKS)

	6	THE LAST ITEM IN THE COMMENT IS THE RADIX 50 EQUIVALENT
		STRING OF THE WORDS OF THE INSTRUCTION


PART 4	LEFT OVER LABELS

	ANY LABELS FOUND DURING PASS 1 THAT HAVE NOT BEEN DEFINED IN
	EITHER PARTS 2 OR 3 ARE DEFINED HERE IN THE SAME MANNER AS IN 
	PART 2

PART 5	END STATEMENT
	THE END OF THE PROGRAM IS DECLARED FOR THE ASSEMBLER AS
	.END	START

PART 6	SYMBOL TABLE
	A COMPLETE SYMBOL TABLE IS PRINTED OUT GIVEING EACH ENTRY
	AND ITS VALUE(132 COLUMN FORMAT). AN OCTAL VALUE PROCEEDED
	BY E REPRESENTS ENTRY POSITION IN THE SYMBOL TABLE. THIS
	IS NOT OUTPUTED WHEN /I OPTION IS SPECIFIED.

PART 7	CROSS REFERENCE TABLE
	A LISTING OF ALL LABELS AND THE ABSOLUTE LOCATIONS THAT
	REFERENCE THEM. THIS IS NOT OUTPUTED WHEN /I OPTION
	IS SPECIFIED.


POSSIBLE MACRO ASSEMBLER ERRORS

	WHEN ASSEMBLING THE RESULTING CODE GENERATED WITH /I OPTION
	THROUGH THE MACRO-11 ASSEMBLER,THE FOLLOWING
	ERRORS CAN BE REPORTED:

M	MULTIPLE DEFINITION OF A LABEL. SINCE A LABEL GENERATED
	BY DECOD2 PROGRAM WILL HAVE UP TO 7 LETTERS, WHILE 
	THE ASSEMBLER RECOGNIZES ONLY FIRST 6 LETTERS, THIS
	ERROR MASSAGE MAY BE OBTAINED. TO CORRECT THIS ERROR,
	CHANGE THE LABEL NAMES AS YOU WANT USING UP TO 6 LETTERS.

Z	INSTRUCTION INCOMPATABLE ON VARIOUS PDP-11 MODELS.
	DATA, INTERPRETED AS INSTRUCTIONS, CAN COME UP AS
	THE MOST UNUSUAL INSTRUCTIONS-THIS ONE CAN BE IGNORED.

A	ADDRESS ERROR
	ONLY KNOW CASE IS FOR 
	SOB	RX,.+2
	WHERE DATA IS INTERPRETED AS AN SOB INSTRUCTION WITH
	AN OFFSET BRANCH DISTANCE OF 0 (.+2). THE ASSEMBLER
	TREATS THIS AS AN ERROR AND CHANGES IT TO 
	SOB	RX,.
	WHICH IS NOT THE SAME. DO NOT IGNORE THIS ERROR,CHECK
	ALL OCCOURANCES.

[END OF DECOD2.DOC]