ED is an easy to learn, easy to use scrolling video
text editor for use with a VT52 or VT55 terminal and
the RT-11 operating system. The terminal's screen is treated
as a "window" through which the user views a 24 line section
of a text file. Single keystroke commands, whose effects
are immediately visible, provide standard text editing
functions.



ED is loaded using the monitor command

    R ED

ED will clear the screen and then prompt for the name of the
text file to be edited. If a device name is not specified,
"DK:" is assumed. If the file name extension is omitted,
".PAS" is assumed. If the file name entered is not found
in the directory then ED will a new file is being created,
and the screen is cleared. For an existing file, the first
24 lines are displayed.


Editing can now be done using the following commands:

 Key                 Function

DELETE       Delete character at current cursor position
RETURN       Insert blank line following current line
UP-ARROW     Scroll forward one line
DOWN-ARROW   Scroll backward one line
LEFT-ARROW   Move cursor left one position
RIGHT-ARROW  Move cursor right one position
DLINE(red)   Delete current line
TOGGLE(blue) Toggle between character insert and delete modes
SEARCH(4)    Search forward for text string(Press twice to repeat)
TOP(5)       Position at beginning of file	
EXIT(6)      Terminate editing session and update file
TAG(7)       Tag current line for use by save command
SAVE(8)      Save text in file, beginning at tag and
             ending at current line
UNSAVE(9)    Retrieve text from a file and insert following
             current line


All of the command keys, with the exception of DELETE and
RETURN are located on the numeric keypad. Typing any other
key causes the corresponding character to be inserted immediately
preceeding the character pointed to by the blinking cursor.
The "current line" is always the last line displayed. Character
insertion and deletion are always done on this line. The
UP-ARROW and DOWN-ARROW commands allow any desired line to be
scrolled into the current line position. The repeat key
may be used to speed this scrolling  process. The screen is
at all times an accurate representation of a 24 line section
the file.


The TOGGLE command puts the editor in a mode where
a typed character replaces the character at the current
cursor position. Pressing the TOGGLE command key a second
time returns the editor to the normal mode where characters
are inserted rather than replaced.

The SEARCH command permits rapid positioning to any section
of a large file. The editor will prompt for the search
string and then scroll forward so that the line containing
the next occurance of the search string becomes the
current line. No scrolling is done if a match is not
found. Search strings are limited to 14 characters. An
automatic carriage return will be generated if a 15th
character is typed. It is not necessary to retype the 
search string when searching for the next instance of
the same string, simply press the SEARCH key a second
time in response to the prompt. In order to perform a
search of the entire file the TOP command should first
be used to position the current line pointer at the
beginning of the file.

The TAG, SAVE and UNSAVE commands can be used to save a
section of the file being edited on the disk, to insert
another file into the file being edited, or to perform
"cut and paste" operations. To save a section of text on
the disk first use some combination of the TOP, SEARCH,
UP-ARROW and DOWN-ARROW commands to position the window
so that the first line of the desired section has become
the current line. Next press the TAG key to mark this
line. Then use the UP-ARROW or SEARCH command to scroll
forward until the last line of the section becomes the
current line. Finally, press the SAVE key and enter a
file name in response to the prompt. The file name
"DK:TEMP.DAT" will  be assumed if a only carriage return
is  typed in respose to the prompt when using either
the SAVE or UNSAVE command. A section of text can
printed by responding with "LP:" to the prompt for a
a file name when using the SAVE command.

When the editing session has been completed, pressing
the EXIT key causes the updated file to be written to
the disk. The old file will automatically be renamed
using a ".BAK" extension. If ED is terminated using
Cntrl C the updated file is not written to disk and
the file remains unchanged. This creates a potential
problem, however, because the numeric keypad is left
in a special mode where it is no longer useable for
numeric input. It can be returned to the normal numeric
input mode by rerunning ED and exiting using the EXIT
command. Alternately, programs that require use of
the numeric keypad can output the code sequence(esc,'>')
that returns the keypad to the normal mode.


The editor does not page sections of the file being edited
to and from the disk. It is therefore limited to files
that can be entirely contained in main memory. On a 28K
computer using the Single Job Monitor, approxemately 40,000
characters are available in the text buffer. This is equivalent
to 800 lines, assumming 50 characters/line, and to 16
pages, assumming 50 lines/page.


Files supplied:

  ED.DOC    This document
  ED.SAV    A runnable version of ED
  ED.PAS    Source file
  ED.MAP    Current load map
  ED.CRS    Output of PASCAL cross reference generator
  ED.MAC    Assembler source output of ESI PASCAL compiler
  ED.LST    Listing generated by ESI PASCAL compiler




Any questions about ED should be refered to:

          Wayne Rasband
          National Institutes of Health
          Bldg. 36, Room 2A-03
          Bethesda, Md. 20014
          301-496-4957




Sources of information on the programming language PASCAL:

1) Jensen, Kathleen and Wirth, Niklaus, PASCAL User Manual and
   Report, New York, Springer-Verlag, 1974, $5.90.

2) ESI Supplement to the User Manual and Report
   Electro-Scientific Industries
   13900 NW Science Park Dr.
   Portland, OR
   Attn: Steven Hiebert

3) PASCAL User's Group, C/O Andy Mickel
   University Computer Center: 227 EX
   208 SE Union St.
   University of Minnesota
   Minneapolis, MN  55455
   Dues: $4/year

4) PASCAL Special Interest Group
   C/O DECUS
   146 Main St., PK-3/E55
   Maynard, MA  01754
   Attn: John Barr