Falcon Application RT-11
                                   (FART-11)

                                John M. Crowell
                                 Crow4ell,Ltd*
                                  145 Andanada
                              Los Alamos, NM 87544




     * but not very


           COPYRIGHT (C) NOT-AT-ALL

           This software is furnished under license  for  use  on  any
           computer system and may be copied with or without inclusion
           of  this  notice.  This  software,  or  any  other   copies
           thereof, may be provided or otherwise made available to any
           other person.  Title to and ownership of the software shall
           at all times remain in the public domain.

           The information in  this  software  is  subject  to  change
           without notice, and should not be construed as a commitment
           by  the  author  or  by Crow4ell, Ltd.   I  understand  the
           Digital Equipment Corporation can't be blamed either.
 
           The  author  assumes  no  responsibility  for  the  use  or
           reliability  of  this  software  on  equipment which is not
           supplied by someone.





     This  diskette  contains  TECO  command  files  which   will   perform
     sufficient  modification  of  RT-11 Version 4.0 source files to enable
     generation of an RT-11 system (SJ or FB) called FART-11 to run on  the
     SBC-11/21 FALCON microcomputer.  Why anyone would actually WANT to run
     RT-11 on a FALCON is quite beyond me.  If you choose to run FART-11 on
     your FALCON, it is up to you to see that the CPU is properly licensed.
     None of the files on this diskette represent  a breach  of contract or
     or contain proprietary code.  The author will assume neither responsi-
     bility  nor  liability  for  anyone  who attempts to use FART-11 on an
     unlicensed FALCON.



                                                                        Page 2


     Once the source  files  have been modified,  they may still be used to
     generate  "normal"  RT-11  systems.    All  FALCON  specific  code  is
     assembled  conditionally  depending  upon  values of flags in the file
     SYCND.MAC.

     I have tested the procedure for BL, SJ,  and  FB  monitors  in  memory
     mapping  MODE  0,  and, via a hardware kludge, MODE 3.  No attempt has
     been made to generate a MRRT system with this procedure.   No  attempt
     has been made to generate a multi-terminal system.

     New variables and conditionals show up in the file  SYCND.MAC.   These
     include:

          FART$$    A conditional assembly flag
          RAMSIZ    A variable to specify the size of memory of the  target
                    system
          BEVENT    A conditional assembly flag to denote that  the  FALCON
                    clock is to be the system clock
          AUTO$B    A  conditional  assembly  flag  to  signify  that   the
                    programmable  baud  rate  of the FALCON's SLU1 is to be
                    utilized.
          BAUD$$    A variable to specify the baud rate to be selected.

     If when booting RT-11, the programmable baud rate enable bit is set in
     the  CSR  of  SLU1,  the baud rate will not be changed.  (e.g.  if the
     baud rate was set by the primary bootstrap or by the  MACRO  ODT  ROMs
     available  for  the FALCON.) If the "autobaud" option is selected, and
     is not enabled at bootstrap time, the baud rate will  be  set  by  the
     secondary bootstrap program.

     The system configuration words are set to reflect the presence  of  an
     LSI-11  processor and, if appropriate, the presence of a system clock.
     The second configuration word is cleared.  (Who would run a VS60 on  a
     FALCON anyway?)

     There is also a patch for the file SYSGEN.CND which will  include  the
     FALCON  options  in the sysgen process.  It will cause the appropriate
     entries to be made in the SYCND.MAC and MONBLD.COM files.  If you must
     have FART-11, this is the recommended procedure.

     The TECO programs on this diskette assume that the source files to  be
     patched  reside  on  a volume named SRC:.  If all the source files and
     TECO files are  present  on  one  volume,  and  the  MUNG  command  is
     supported,  the  entire  patch  may  be  accompliched  by invoking the
     FART11.COM indirect command file.

     One final comment concerning the final operating system  generated  by
     this   procedure:   The  utility  program  RESORCE.SAV  tries  to  use
     nonexistent memory traps to identify some of the possible  devices  on
     the   Q-bus.    Since   the  FALCON  does  not  execute  these  traps,
     configuration of the system is likely to reflect some things that  may
     not be there, such as parity memory or a VT48 graphics device.