DECUS C LANGUAGE SYSTEM


                                 Cmath Library
                                Reference Manual


                                       by

                                  Hamish Ross
                            Department of Physiology
                                 Medical School
                             Birmingham University
                               BIRMINGHAM B15 2TJ








        This document describes  an  implementation  of  the  elementary
        maths functions for the DECUS C language.


                              Version of 15-Mar-85

         

         














                           Copyright (C) 1985, DECUS.

             General permission to copy  or  modify,  but  not  for
             profit,  is  hereby  granted,  provided that the above
             copyright notice is included and reference made to the
             fact  that  reproduction  privileges  were  granted by
             DECUS.

             The information in this document is subject to  change
             without  notice  and  should  not  be  construed  as a
             commitment by  Digital  Equipment  Corporation  or  by
             DECUS.

             Neither Digital Equipment Corporation, DECUS, nor  the
             author  assumes  any  responsibility  for  the  use or
             reliability  of  this  document   or   the   described
             software.

             This software is made available  without  any  support
             whatsoever.

















        UNIX is  a  trademark  of  Bell  Telephone  Laboratories.   RSX,
        RSTS/E,  RT11  and  VMS  are  trademarks  of  Digital  Equipment
        Corporation.


        Cmath Library Reference Manual                            Page 4



        1.0  Introduction and Scope             ____________ ___ _____

        This collection of programs provides a library of the elementary
        maths functions for the DECUS C system.  It differs from the PML
        library, supplied on the 11-SP-18  tape,  in  the  major  design
        objectives  which  it attempts to meet.  These are, to provide a
        set of functions which have the same names and functionality  as
        their counterparts in UNIX, and therefore in a number of other C
        compilers, and which have a high level  of  accuracy  throughout
        the entire range of their arguments.  A collection of algorithms
        which seems to satisfy the latter objective is published in  the
        book  "Software  Manual for the Elementary Functions" by William
        J.  Cody,  Jr.   and  William  Waite,  Prentice-Hall  Series  in
        Computational Mathematics (1980).  This kit is an implementation
        of all the algorithms in that book together  with  some  of  the
        closely  associated  functions  in  the  UNIX math library.  The
        functions provided are sqrt, log, log10,  exp,  pow,  sin,  cos,
        tan,  cotan, asin, acos, atan, atan2, sinh, cosh and tanh, based
        on the Cody and Waite algorithms, together with  the  additional
        functions fabs, floor, ceil, frexp, ldexp and modf.  Since there
        were some problems with the i/o functions atof and $$dtoa in the
        11-SP-18  set,  particularly  in  dealing  with double precision
        numbers, new versions of those, written in C, have been included
        also, as has an error handling package.
        There were found to be a number of bugs in the supplied 11-SP-18
        kit, in the handling of the /d switch by the compiler and in the
        handling of some i/o buffers in  the  run-time  library.   These
        bugs  have  been fixed and the patches are included in this kit.
        More details about that are included in section  4  and  in  the
        text files (.TXT) associated with each of the patches.
        Error handling is described more fully in the next  section  and
        portability  and maintainability in section 3.  Instructions for
        building  the  kit  are  provided  in  section  4,  and  further
        information  about  accuracy  and  testing in section 5.  A full
        description  of  each  of  the   functions,   including   useage
        instructions,  the meanings of all diagnostic messages and notes
        about any differences between the actual implementation and  the
        one  described  in  Cody  and  Waite,  appears in section 6.  An
        appendix contains a KWIK index.



        2.0  Error handling             _____ ________

        In dealing with errors, a number of somewhat  incompatible  aims
        had to be reconciled.  On the one hand the UNIX convention seems
        to be to do relatively little about errors  except  to  set  the
        EDOM  and  ERANGE  flags  for  domain and range values which lie
        outside the permissible  limits,  and  to  generate  a  floating
        exception  signal  for floating point exceptions.  Having become
        used to something rather more friendly in the Fortran system  on
        the  PDP-11,  it  seemed  desirable  to  do  more  than the UNIX
        minimum, but not in such a way as to cause  problems  in  moving


        Cmath Library Reference Manual                            Page 5



        programs between different systems.  Error handling is therefore
        done by calling a common function cmemsg(), with two  arguments;
        one  is  an error code number and the other is a pointer to some
        other piece of useful data, such as an argument value.   A  full
        list  of  the error codes and their associated messages is given
        in  the  documentation  for   the   function   cmathe(),   which
        initialises  and  reinitialises  the  error  handling mechanism.
        Cmathe() must be called at least once  to  start  up  the  error
        handling  system.  To avoid having to remember to do this at the
        beginning of each main program, and to eliminate the need for  a
        program  edit  when  moving  between operating systems a call to
        cmathe() has been included  in  an  initialiser  program  called
        cminit().   Thus, as long as cminit is loaded with each program,
        everything will be taken care of automatically.  Cminit plays  a
        role  similar  to  SUPORT  in  the LINK argument for RT11 and it
        could easily be included within it, but it seemed tidier to keep
        the  two  separate.   Cminit  also  contains  a call to the CLIB
        function fps(), which sets the floating point  exception  flags,
        and  code, which is conditionally compiled for RT11 only, to set
        up a vector to catch the floating  point  exception  interrupts.
        That  is done in $$traps for other operating systems but not for
        RT11, so these errors are caught and  handled  by  the  cmemsg()
        error  handling  function  also.   Further  details  about error
        handling, including instructions on how to add a  new  error  to
        the  system, are to be found in the documentation for cmathe and
        cminit in section 6.



        3.0  Portability and Maintainability             ___________ ___ _______________




        3.1  Portability of Application Programs             ___________ __ ___________ ________

        As mentioned in section 1, one of the main  objectives  of  this
        package  was  to facilitate the movement of application programs
        between other C math packages  and  this  one.   Therefore,  all
        functions  have  been given the same names and argument lists as
        their counterparts in UNIX.  In  all  cases  the  functions  use
        doubles  rather than floats to pass arguments and return values.
        Since DECUS C  does  not  always  use  the  UNIX  convention  of
        promoting  floats to doubles, for argument passing and return of
        results, there is an source of potential  problems  there.   The
        simple  solution  for  new  programs,  is  to  ensure  that  all
        functions which return  a  double  result  are  declared  double
        rather  than  float and likewise for any float/double arguments.
        This method must be used if the  DECUS  compiler  /f  switch  is
        used.   In  the  case  of  existing programs which declare their
        maths  functions  and  their  arguments  to  be  of  type  float
        everything  should  still  work properly if the /d switch of the
        DECUS compiler is used.  However,  in  practice,  it  does  not,


        Cmath Library Reference Manual                            Page 6



        unless the compiler is patched.  In the supplied version all the
        type conversions are not applied automatically.  A patch kit for
        the  CC103  module  of  the compiler which fixes that problem is
        included with this kit (see the Build instructions in section  4
        for  details).   One further consequence of the DECUS compiler's
        acceptance of arguments which are floats rather than doubles  is
        that printf and friends need to be able to distinguish those two
        types.  That is done by using  lower  case  format  symbols  for
        float  conversions, e.g., "%f" and upper case for doubles, e.g.,
        "%F".  The latter is not a normal usage for  other  C  compilers
        and  may  thus  cause  portability  problems.  Two solutions are
        offered.  One is to abandon the DECUS /f facility and  to  stick
        to  the more widely used convention.  In that case the /d switch
        must be made the default  (and  the  patched  version  of  CC103
        used),  then  a  patched version of the support library function
        doprnt which does not distinguish between upper and  lower  case
        format  must be used also.  A patch for that purpose is included
        in this kit (DOPRNT.TX2).  The other solution to the upper/lower
        case  format  problem  is  to  ensure  that  the correct case is
        provided for  whatever  maths/io  package  is  being  used.   To
        facilitate  conversion  between the two format conventions the 2
        utility programs FORMUC.C and FORMLC.C are supplied.  These  are
        C  programs built using LEX.  (The 11-SP-18 version of LEX seems
        to have the outermost layer of braces missing, this causes it to
        fail  while decoding the command line).  FORMUC will convert all
        formats to  upper  case,  FORMLC  to  lower  case.   Mixed  case
        programs will require hand editing.



        3.2  Portability of the cmath package             ___________ __ ___ _____ _______

        The portability of this package to other computers was  not  one
        of  the primary aims of this exercise.  The material in Cody and
        Waite shows that to obtain the best levels  of  accuracy  it  is
        necessary to know how the target machine does its arithmetic and
        thus portability and accuracy are to some  extent  incompatible.
        In  this  case  accuracy  has  been given precedence - this is a
        package designed to run  on  PDP-11s  with  FPU  floating  point
        hardware.   On  the other hand portability has not been ignored.
        The programs have been kept reasonably clean and tidy so  it  is
        easy  to  describe where the machine dependencies lie.  The main
        set of functions, that is to say the ones described as the  Cody
        and  Waite  set in section 1, together with ceil, floor and fabs
        do not contain any explicit assumptions about the  form  of  the
        floating  point  representation  of a number within the machine.
        Where they need to use such  information,  as,  for  example  in
        extracting  the mantissa and exponent of a number or the integer
        and fractional parts they use the  machine  dependent  functions
        ldexp(),  frexp()  or modf() which are written in MACRO.  In the
        functions sqrt, sin, cos, tan  and  cotan  it  is  necessary  to
        determine  whether or not an integer, n, was odd.  That has been
        done with a test on n & 1 which makes an  assumption  about  the


        Cmath Library Reference Manual                            Page 7



        representation  of  integers.  A package of this type inevitably
        contains a great many magic numbers, as the  constants  for  the
        polynomials  used  to calculate the functions in the basic range
        and as other factors such as pi, e or the square root of  three.
        Constants  such  as  the  latter,  which are used in a number of
        places, reside in the constants file  math.h.   That  file  also
        contains  machine  dependent  constants  such  the  largest  and
        smallest  numbers  representable  in  the  machine.   (see   the
        documentation  on  math.h  in  section  6  for further details).
        Other constants, which are specific to individual functions, are
        initialised  as static variables or in #define statements at the
        head of the function.



        3.3  Note to maintainers/improvers             ____ __ _____________________

        A casual examination of the code will  reveal  some  inefficient
        constructs  like  x = (y - 0.5) - 0.5.   Do  not  'improve' them
        unless you really understand the consequences  of  your  action.
        In  many cases the code is written in what might appear to be an
        odd way because Cody and Waite say that is the way it should  be
        done  to  get  the  best  accuracy  from  this type of hardware.
        Therefore, if you are attempting to use other  hardware  with  a
        different  type  of  arithmetic  processor  (decimal,  octal  or
        hexadecimal) you will need to make many changes to the  code  to
        retain  the  same level of accuracy in the algorithms.  It would
        be prudent not to make any changes without a careful reading  of
        Cody and Waite first.



        4.0  Building             ________

        Before compiling the functions and installing them in a  library
        it  is  advisable to apply some patches to the original 11-SP-18
        kit.  These patches are included in this package  in  the  files
        CC103.TXT,  DOPRNT.TXT,  DOSCAN.TXT,  FCLOSE.TXT  and IOABUF.TXT
        each of which includes an explanation  of  the  purpose  of  the
        patch  and  the  SLP  text  to  implement  it.  Very briefly the
        reasons for each of the patches is as follows:-
        CC103 - floats passed to and  from  functions  not  promoted  to
        doubles on /d.
        DOPRNT - increase buffer size  for  doubles  and  pass  size  to
        $$dtoa.
        DOPRNT - optionally treat e, f, g formats as E, F, G.
        DOSCAN - bad handling of EOF means malloc data overwritten.
        FCLOSE - incomplete  terminal  line  not  flushed  on  closedown
        (RT-11).
        IOABUF - tty buffer can overfill on lines > 80 chars (RT-11).
        All the C files of  the  math  package  contain  the  /*)LIBRARY
        command  for  BUILD.   In  addition,  the MACRO functions frexp,
        ldexp and modf (and in the case of RT11, fptrap  also)  must  be


        Cmath Library Reference Manual                            Page 8



        assembled.  The main decision which must be made is where to put
        the functions.  If almost  all  applications  need  to  use  the
        package  then  it is simplest to add them to CLIB, in which case
        modules ddtoa and atofd should be removed.  If it is desired  to
        leave  CLIB  unaltered  put  the  new  functions  in  a separate
        library, and ensure that it is called before CLIB.  In that case
        copies  of  atof.obj  and $$dtoa.obj should be left on device C:
        and should be protected.  In either case a copy of cminit should
        be left on that device also, remember it plays a role similar to
        SUPORT in RT11.  A command file which does all these things  for
        RT11 is included in the kit as cmath.com.  As it stands, it will
        build a system with CMATH  separate  from  CLIB.   Removing  the
        comment  marks  on the indicated sections will incorporate CMATH
        in CLIB.  The penalty for including CMATH in CLIB  is  not  only
        longer  search  times but inclusion of larger versions of $$dtoa
        and atof in programs which  do  not  use  floating  point.   The
        benefit  is  simpler  link  instructions  and fewer libraries to
        search for programs which use floating point.



        5.0  Accuracy and testing             ________ ___ _______

        All the test programs from the Cody and  Waite  book  have  been
        included  in  the kit.  They are in the archive file cwtest.arc.
        They were transcribed straight into C from the Fortran  listings
        in  the book, without any effort at making them portable.  There
        is a program, machar, which obtains values of machine  dependent
        constants  which  the other programs need.  It seems to work ok,
        but it is worth checking its output against the FPU manual.  The
        other  programs do a series of consistency checks on each of the
        functions  using  sets  of  random  arguments   which   exercise
        different  parts  of  the  algorithm  so  that  inaccuracies may
        tracked to a subcomponent of the algorithm.  The  test  programs
        in  the  kit  all  have  BUILD  instructions for a CMATH library
        incorporated into CLIB in which case commands of  the  type  RUN
        BUILD  TSQRT  will run the test.  If CMATH is separate the BUILD
        sequence should be modified to
        /*)BUILD
                $(LIBS) = {cmath cminit}
                $(DTOA) = 1
                $(ATOF) = 1
        */
        and again RUN BUILD TSQRT will run the test.  In  each  case  no
        args  are needed in the command line, but if argv[1] is supplied
        with a string 'xxxx' then the message 'Performance test on xxxx'
        will  appear  at  the  head of the output.  The root mean square
        relative error for all the random number tests was less than one
        binary  digit,  and  the  maximum relative error less than three
        bits, in most cases it was less than 2 bits.
        The package has been developed and tested  on  a  PDP11/34  with
        FP11-A FPU.  The operating system was RT-11 v4.  It has not been
        tested on any other  operating  system.   The  only  part  which


        Cmath Library Reference Manual                            Page 9



        should  be  operating  system dependent is the code for handling
        FPU interrupts.  It is conditionally included if  the  operating
        system  is  RT-11 (see documentation for cminit() in section 6).
        It is assumed that $$traps in CLIB will deal with floating point
        exceptions in other operating systems.



        6.0  Function descriptions             ________ ____________

        This section gives  useage,  description,  diagnostic  and  some
        internal  information  for  each  of the supplied functions.  It
        also gives some further background information about  the  error
        handling  package cmathe(), the initialisation function cminit()
        and the maths constants file math.h.  The fullest description of
        the  meanings  of  the  error messages is found here too, in the
        diagnostics section of the function concerned.
        For examples of the use of the functions see the listings of the
        test programs in the file cwtest.arc.


        Cmath Library Reference Manual                           Page 10
        $$dtoa  double to ascii conversion


        6.1  double to ascii conversion             ______ __ _____ __________



                                   **********
                                   * $$dtoa *
                                   **********



        File name:      dtoa.c



        NAME:   $$dtoa -- double to ascii conversion

        USAGE:

                char buff[];    /* space for result string */
                char conv;      /* conversion  type  'e',  'f',  or  'g'
                others default to e */
                int bsize;      /* size of buffer */
                int dplace;     /* places after the point */
                double value;   /* value to converted */
                $$dtoa(buff, conv, bsize, dplace, value);

        DESCRIPTION:

                $$dtoa is a (temporary?) replacement for the program  of
                the same name on the 11-SP-18 tape and described on page
                5-9  of  the  Wizard  document.   The   rest   of   this
                description is a copy of that.
                $$dtoa()  is  called  by  printf  to  convert  a  double
                precision  number  to  ascii.   The  text  is written to
                buff[].  Bsize is the maximum size of the result string;
                it  is  determined  by  the amount of space allocated to
                buff by the calling program (normally  doprnt).   Dplace
                is the number of decimal places after the decimal point.
                If the result  is  too  large  to  fit  into  the  space
                allocated  to  buff,  digits  are lost from the low end.
                With the buffer  size  of  30  bytes  allocated  by  the
                modified  version  of  doprnt()  (edit  b1) only rubbish
                digits can be lost in this way.  Conv is        'e', 'f'
                or 'g' to define the format.

        DAIGNOSTICS:

                None

        INTERNAL:

                The program uses the following algorithm:-
                set default value of dplace


        Cmath Library Reference Manual                           Page 11
        $$dtoa  double to ascii conversion


                strip off sign
                scale and compute no of leading digits
                decide if 'g' goes to 'e' or 'f'
                compute no of digits to print
                change 'f' to 'e' if insufficient space for result
                scale to range 1.0 - 10.0 and round up
                build digit string
                if not 'f' print exponent part
                print final null

        AUTHOR:

                Hamish Ross.

        DATE:

                9-Mar-85


        Cmath Library Reference Manual                           Page 12
        arsico  arc sin and arc cosine functions


        6.2  arc sin and arc cosine functions             ___ ___ ___ ___ ______ _________



                                   **********
                                   * arsico *
                                   **********



        File name:      arsico.c



        NAME:   arsico -- arc sin and arc cosine functions

        USAGE:

                double x, f, asin();
                double g, acos();
                f = asin(x);
                g = acos(x);

        DESCRIPTION:

                asin returns arcsin of x.
                acos returns arccosine of x.

        DIAGNOSTICS:

                If the absolute value of the argument is greater than  1
                the  error message 'asin, acos arg bad', followed by the
                value of  the  argument,  is  written  to  stderr.   The
                algorithm returns a result of HUGE.

        INTERNAL:

                Algorithm from Cody and Waite pp.  174-193.

        AUTHOR:

                Hamish Ross.

        DATE:

                8-Jan-85


        Cmath Library Reference Manual                           Page 13
        atan    arctan function


        6.3  arctan function             ______ ________



                                    ********
                                    * atan *
                                    ********



        File name:      atan.c



        NAME:   atan -- arctan function

        USAGE:

                double f, x, atan();
                f = atan(x);
                double g, u, v, atan2();
                g = atan2(v, u);

        DESCRIPTION:

                atan(x) returns the arctangent of x.

                atan2(v, u) returns the arctangent of v / u.

        DIAGNOSTICS:

                If both arguments  of  atan2  are  zero  the  result  is
                indeterminate.   The  message  'atan2  args  both  zero'
                followed by the value of the denominator, is written  to
                stderr and a value of zero is returned.

        INTERNAL:

                Algorithm based on Cody and  Waite  pp.   194-216.   The
                algorithm  here  has been modified slightly to avoid the
                test for overflow in v/u.  By checking which of u  or  v
                is  greater in magnitude all overflows become underflows
                which are set to zero without a message.  This has meant
                that  the  division  of the work between atan(), atan2()
                and the internal function _atan() is slightly  different
                from that suggested in Cody and Waite.

        AUTHOR:

                Hamish Ross.

        DATE:



        Cmath Library Reference Manual                           Page 14
        atan    arctan function


                1-Jan-85


        Cmath Library Reference Manual                           Page 15
        atof    ascii to double conversion


        6.4  ascii to double conversion             _____ __ ______ __________



                                    ********
                                    * atof *
                                    ********



        File name:      atof.c



        NAME:   atof -- ascii to double conversion

        USAGE:

                double d, atof();
                char *buffer;
                d = atof(buffer);

        DESCRIPTION:

                This program is a (temporary?) replacement for  the  one
                of  the  same  name described on page 5-52 of the Wizard
                document on the 11-SP-18 tape.  The type  of  conversion
                from  ascii string to double floating point number given
                there is reproduced here.  The BNF for numbers which can
                be decoded by that routine is :-
                <number> := <sign> <real number>
                <sign> := + | - | <empty>
                <real number> := <decimal  number>  |  <decimal  number>
                <exponent> | <exponent>
                <decimal  number>  :=  <integer>  |  <integer>  .   |  .
                <integer> | <integer> .  <integer>
                <integer> := <digit> | <integer> <digit>
                <exponent> := <explet> <sign> <integer>
                <explet> := E | e | D | d
                <digit> := 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
                This routine differs slightly from the above, in that  a
                number  may  not  start  at  the exponent part without a
                leading digit.  That means that  the  description  of  a
                real  nuber  is  now <real number> := <decimal number> |
                <decimal number> <exponent> The reason for doing it this
                way is that it stops scanf("%f", &x) eating its way into
                a following string if that string starts with a  'd'  or
                an  'e'.   It will still do that if the following string
                begins with a '.'.  K & R does not  define  what  atof's
                idea  of  a floating number is, but the above definition
                is closer than the DECUS C version to  their  definition
                of  a  floating  constant.   The conversion stops on the
                first  non-legal  character,  but  unlike  the  original


        Cmath Library Reference Manual                           Page 16
        atof    ascii to double conversion


                version  this  one  prints  an  error  message  and  the
                offending string  through  the  cmathe  error  reporting
                system.

        DIAGNOSTICS:

                If a non-legal  character  is  encountered  the  message
                'illegal  character  in floating input string', followed
                by the entire string in the buffer argument, is  written
                to  stderr.   The  value  of the number built up to that
                point is returned.

                If the input produces a number  which  would  result  in
                floating  overflow  the  message 'atof input too large',
                followed by the entire string in the buffer argument, is
                written to stderr.  The value HUGE is returned.

        INTERNAL:

                Algorithm is straightforward,  see  comments  in  source
                code for details.

        AUTHOR:

                Hamish Ross.

        DATE:

                22-Aug-84 original version

                25-Mar-85 insist numbers start with a digit not  'e'  or
                'd'.


        Cmath Library Reference Manual                           Page 17
        ceil    smallest integer not less than argument


        6.5  smallest integer not less than argument             ________ _______ ___ ____ ____ ________



                                    ********
                                    * ceil *
                                    ********



        File name:      ceil.c



        NAME:   ceil -- smallest integer not less than argument

        USAGE:

                double x, y, ceil();
                y = ceil(x);

        DESCRIPTION:

                Returns the smallest integer not less than the argument.

        DIAGNOSTICS:

                If the argument is greater than the integer part of HUGE
                a floating point overflow exception will occur.

        INTERNAL:

        AUTHOR:

                Hamish Ross.

        DATE:

                31-Jan-85


        Cmath Library Reference Manual                           Page 18
        cmathe  cmath error package


        6.6  cmath error package             _____ _____ _______



                                   **********
                                   * cmathe *
                                   **********



        File name:      cmathe.c



        NAME:   cmathe -- cmath error package

        USAGE:

                There are three  function  calls  associated  with  this
                package.

                int ercode;
                cmathe(ercode);

                int erno;
                char *datap;
                cmemsg(erno, datap);

                cmelog();

        DESCRIPTION:

                This  set  of  functions  provides  an  error  reporting
                package  for the floating point math package.  For RT-11
                it catches the FP error  interrupts  also.   It  may  be
                connected  to  any  other function which needs to report
                errors (such as square root  of  negative  number).   It
                provides  the option, present in Fortran, of reporting n
                errors and then either aborting or  ignoring  subsequent
                errors.   In  that case they are counted but no messages
                are printed.  Unless  there  is  an  abort,  control  is
                returned  to the calling function, which must be able to
                continue or else abort itself.

                The cmathe system is started or restarted by the call

                        cmathe(n);

                where is n is usually a literal constant.  If n is 0 all
                errors are reported and there is no aborting.  If n > 0,
                n errors  are  reported  then  there  is  an  abort,  so
                cmathe(1)  will  abort  after reporting the first error.
                If n < 0, n  errors  are  reported  then  the  reporting


        Cmath Library Reference Manual                           Page 19
        cmathe  cmath error package


                stops,  though the errors are still counted.  The errors
                are reported on stderr, and on an abort a  calltrace  is
                done to stderr.  This produces a trace of function calls
                leading to the error  if  profiling  has  been  enabled,
                otherwise  it  produces  a sequence of base addresses of
                the functions called.  The program then exits with  exit
                code  4.  Cmathe sets all the error counts to zero.  The
                cmath initialisation function cminit() calls cmathe with
                argument  zero,  so that if that argument is appropriate
                there is no need to call cmathe explicitly.  Cminit also
                calls  fps, and under RT-11 takes over the FPU interrupt
                vector  to  deal  with  the  FPU  exceptions.   See  the
                documentation on cminit for further details.

                The function which invokes the error reporting mechanism
                is

                        cmemsg(erno, datap);

                where erno is a symbol which defines the  error  number.
                These  definitions are in math.h.  Datap is a pointer to
                an object whose value might help to throw further  light
                on  the cause of the error.  Further information on both
                those items may be found in the internal section below.

                The cumulative error list may be printed on  stdout  via
                the call

                        cmelog();

                This call does not clear the error counts,  to  do  that
                use cmathe.

        DIAGNOSTICS:

                If cmemsg() is called with  an  error  number  which  is
                undefined or out of range the message 'error code out of
                range' is written to stderr.

        INTERNAL:

                The error table currently looks like :-

                Error Caller Sev Eno    Message                 Argument

                FP_OPER FPU     F E     floating op code error  PC

                FP_ZDIV FPU     F E     floating divide by zero PC

                FP_FTOI FPU     F E     floating integer        PC
                                        conversion error

                FP_OFLO FPU     F E     floating overflow       PC


        Cmath Library Reference Manual                           Page 20
        cmathe  cmath error package


                FP_UFLO FPU     W E     floating underflow      PC

                FP_UDEF FPU     W E     floating undefined      PC
                                        variable

                FP_BIGI atof    F R     atof input too large    string

                FP_BADC atof    F D     illegal character in    string
                                        floating input string

                FP_NESQ sqrt    F D     sqrt arg negative       value

                FP_LEXP exp     F R     exp overflow            value

                FP_SEXP exp     W R     exp underflow           value

                FP_NLOG log     F D     log arg negative or     value
                                        zero

                FP_TANE tancot  F D     tan, cot arg too large  value

                FP_TRIG sincos  F D     sin, cos arg too large  value

                FP_ATAN atan2   F D     atan2 args both zero    value

                FP_COTE cotan   F D     cotan arg too small     value

                FP_ARSC arsico  F D     asin, acos arg bad      value

                FP_SINH sinh    F D     sinh arg too large      value

                FP_COSH cosh    F D     cosh arg too large      value

                FP_POWN pow     F D     pow arg negative        value

                FP_POWO pow     F R     pow overflow            value

                FP_POWU pow     W R     pow underflow           value

                Error is the error number as defined in the math.h file.
                Caller  is  the  name of the function in which the error
                was  encountered,  or  it  is  FPU  for  floating  point
                exceptions.   Sev  is the severity of the error.  Errors
                of severity W(arning) do not print  their  messages  and
                their error counts do not count towards the abort limit.
                Their individual counts are updated and may  be  checked
                using  cmelog().   Eno  is  the  error  number  for  the
                perror() function.  Only three have been used E (SIGFPE)
                is  the  floating  point  exception error, D (EDOM) is a
                domain error (inadmissable argument) and R (ERANGE) is a
                range error (result out of range).  Message is the error
                message printed and  argument  is  an  argument  of  the
                function  which  encountered the error, or the PC in the


        Cmath Library Reference Manual                           Page 21
        cmathe  cmath error package


                case of FPU errors.

                To add a new error enter the error message in the  error
                message  table  in  the  cmathe.c file, define the error
                code  in  math.h,  then  place  a  cmemsg(erno,  datap);
                statement  in the function which needs to call the error
                system.  Erno is the index number of the  error  in  the
                error table (the first col in the table above) and datap
                is a pointer to the argument passed back (the  last  col
                in  the  table  above).  For FPU generated errors (error
                nos up to FP_NFPU) it points to an int  (value  of  PC),
                for  bad  string  errors  (error  nos  up  to  FP_NFPU +
                FP_NSTR) it points to a string and for all higher values
                it   points   to  a  double  precision  argument.   That
                organisation allows the addition of new  errors  passing
                any  of  those  argument  types  simply by adding to the
                error tables in this file and in math.h.

        AUTHOR:

                Hamish Ross.

        DATE:

                10-Feb-85


        Cmath Library Reference Manual                           Page 22
        cminit  cmath initialisation procedure


        6.7  cmath initialisation procedure             _____ ______________ _________



                                   **********
                                   * cminit *
                                   **********



        File name:      cminit.c



        NAME:   cminit -- cmath initialisation procedure

        USAGE:

                Do not call this procedure explicitly, but be sure  that
                it  is  loaded  by  including  its  name  in the linkers
                command string.  The program will then be called  during
                the  normal  initialisation  procedure  (via  SUPORT  in
                RT-11).

        DESCRIPTION:

                Used by the floating point math  package  to  initialise
                the  error  handling  system  and  to  set  the standard
                default parameters for the floating  point  status.   If
                the  operating  system is rt11, it arranges to catch the
                interrupts from the FPU since that is not done in  traps
                for   rt11  (c.f.   Wizard  and  source  code).   Though
                cmathe() and fps() are called  here  they  can  also  be
                called  at  any  stage  by  the  users program to invoke
                different  values  of  the  parameters  set   by   these
                functions.

        DIAGNOSTICS:

                None

        INTERNAL:

        AUTHOR:

                Hamish Ross

        DATE:

                31-Jan-85


        Cmath Library Reference Manual                           Page 23
        cosh    hyperbolic cosine function


        6.8  hyperbolic cosine function             __________ ______ ________



                                    ********
                                    * cosh *
                                    ********



        File name:      cosh.c



        NAME:   cosh -- hyperbolic cosine function

        USAGE:

                double x, f, cosh();
                f = cosh(x);

        DESCRIPTION:

                Returns hyperbolic cosine of argument.

        DIAGNOSTICS:

                If the argument is large enough to cause overflow in the
                result the message 'cosh arg too large', followed by the
                argument, is written to stderr.   A  value  of  HUGE  is
                returned.

        INTERNAL:

                Algorithm from pp.  217-238  of  Cody  and  Waite.   The
                constant  v  which  appears  in  2  define statements is
                chosen  so  that  log(v)  is  an  exact  octal  constant
                slightly  larger  than  log(2) (See C and W pp.  218 and
                227.

        AUTHOR:

                Hamish Ross.

        DATE:

                12-Jan-85


        Cmath Library Reference Manual                           Page 24
        exp     exponential function


        6.9  exponential function             ___________ ________



                                    *******
                                    * exp *
                                    *******



        File name:      exp.c



        NAME:   exp -- exponential function

        USAGE:

                double x, f, exp();
                f = exp(x);

        DESCRIPTION:

                Returns exponential of x.

        DIAGNOSTICS:

                If the argument is large enough to cause overflow in the
                result the message 'exp overflow', followed by the value
                of the argument, is written to stderr.  A value of  HUGE
                is returned.
                If the argument would  produce  a  result  exponent  too
                small  to  accomodate,  a  value of zero is returned.  A
                warning message 'exp underflow', followed by  the  value
                of  the  argument, is written to stderr, if warnings are
                enabled (normally not).

        INTERNAL:

                Algorithm from Cody and Waite pp.  60-83.
        AUTHOR:

                Hamish Ross.

        DATE:

                28-Dec-84


        Cmath Library Reference Manual                           Page 25
        fabs    floating absolute value of floating argument


        6.10  floating absolute value of floating argument              ________ ________ _____ __ ________ ________



                                    ********
                                    * fabs *
                                    ********



        File name:      fabs.c



        NAME:   fabs -- floating absolute value of floating argument

        USAGE:

                double x, y, fabs();
                y = fabs(x);

        DESCRIPTION:

                Returns the absolute value of its floating argument.

        DIAGNOSTICS:

                None

        INTERNAL:

        AUTHOR:

                Hamish Ross.

        DATE:

                31-Jan-85



        Cmath Library Reference Manual                           Page 26
        floor   largest integer not greater than argument


        6.11  largest integer not greater than argument              _______ _______ ___ _______ ____ ________



                                   *********
                                   * floor *
                                   *********



        File name:      floor.c



        NAME:   floor -- largest integer not greater than argument

        USAGE:

                double x, y, floor();
                y = floor(x);

        DESCRIPTION:

                Returns  the  largest  integer  not  greater  than   the
                argument.

        DIAGNOSTICS:

                If the argument is less than the integer part of -HUGE a
                floating point exception (overflow) will occur.

        INTERNAL:

        AUTHOR:

                Hamish Ross.

        DATE:

                31-Jan-85


        Cmath Library Reference Manual                           Page 27
        frexp   get mantissa and exponent of a number to base 2


        6.12  get mantissa and exponent of a number to base 2              ___ ________ ___ ________ __ _ ______ __ ____ _



                                   *********
                                   * frexp *
                                   *********



        File name:      frexp.c



        NAME:   frexp -- get mantissa and exponent of a number to base 2

        USAGE:

                double x, mant, frexp();
                int xi;
                mant = frexp(x, &xi);

        DESCRIPTION:

                This  is  the  UNIX  function  frexp.   It  returns  the
                mantissa  of  x as its value and the exponent of x as an
                integer via xi.

        DIAGNOSTICS:

                None

        INTERNAL:

                This does not exist as a  C  program.   The  program  is
                written  in  macro  since AS does not seem to handle the
                STEXP instruction properly.  This file is included  only
                for the documentation.

        AUTHOR:

                Hamish Ross.

        DATE:

                23-Aug-84


        Cmath Library Reference Manual                           Page 28
        ldexp   load mantissa and exponent of a number to base 2


        6.13  load mantissa and exponent of a number to base 2              ____ ________ ___ ________ __ _ ______ __ ____ _



                                   *********
                                   * ldexp *
                                   *********



        File name:      ldexp.c



        NAME:   ldexp -- load mantissa and exponent of a number to  base
                2

        USAGE:

                double x, mant, ldexp();
                int xi;
                x = ldexp(mant, xi);

        DESCRIPTION:

                This  is  the  UNIX  function  ldexp.   It  returns  the
                floating  point  number  built  from the exponent xi and
                mantissa mant.

        DIAGNOSTICS:

                None

        INTERNAL:

                This does not exist as a  C  program.   The  program  is
                written  in  macro, as ldexp.mac, since AS does not seem
                to handle the LDEXP instruction properly.  This file  is
                included only for the documentation.

        AUTHOR:

                Hamish Ross.

        DATE:

                23-Aug-84


        Cmath Library Reference Manual                           Page 29
        log     logarithm function


        6.14  logarithm function              _________ ________



                                    *******
                                    * log *
                                    *******



        File name:      log.c



        NAME:   log -- logarithm function

        USAGE:

                double x, f, log();
                f = log(x);

        DESCRIPTION:

                Returns logarithm of x.

        DIAGNOSTICS:

                If the argument is negative or zero the message 'log arg
                negative   or  zero',  followed  by  the  value  of  the
                argument, is written to stderr.   If  the  argument  was
                zero  a  value of -HUGE is returned, otherwise the value
                of log(fabs(x)) is returned.

        INTERNAL:

                Algorithm from pp.  35-59 of Cody and Waite.

        AUTHOR:

                Hamish Ross

        DATE:

                26-Dec-84


        Cmath Library Reference Manual                           Page 30
        log10   logarithm function base 10


        6.15  logarithm function base 10              _________ ________ ____ __



                                   *********
                                   * log10 *
                                   *********



        File name:      log10.c



        NAME:   log10 -- logarithm function base 10

        USAGE:

                double x, f, log10();
                f = log10(x);

        DESCRIPTION:

                Returns logarithm of x to base 10.

        DIAGNOSTICS:

                If the argument is negative or zero the message 'log arg
                negative   or  zero',  followed  by  the  value  of  the
                argument, is written to stderr.   If  the  argument  was
                zero  a  value of -HUGE is returned, otherwise the value
                of log(fabs(x)) is returned.

        INTERNAL:

                returns value of log(x) * log10(e)

        AUTHOR:

                Hamish Ross.

        DATE:

                26-Dec-84


        Cmath Library Reference Manual                           Page 31
        modf    modulus function


        6.16  modulus function              _______ ________



                                    ********
                                    * modf *
                                    ********



        File name:      modf.c



        NAME:   modf -- modulus function

        USAGE:

                double x, xi, fr, modf();
                fr = modf(x, &xi);

        DESCRIPTION:

                This  is  the  UNIX  function  modf.   It  returns   the
                fractional  part  of x as its value and the integer part
                of x as a double value in xi.  The result has  the  same
                sign as x.

        DIAGNOSTICS:

                None

        INTERNAL:

                The program is written in macro as  modf.mac.   It  uses
                the  FPU MODD instruction.  This C file is included only
                for the documentation.

        AUTHOR:

                Hamish Ross.

        DATE:

                22-Aug-84


        Cmath Library Reference Manual                           Page 32
        pow     x raised to power y


        6.17  x raised to power y              _ ______ __ _____ _



                                    *******
                                    * pow *
                                    *******



        File name:      pow.c



        NAME:   pow -- x raised to power y

        USAGE:

                double x, y, f, pow();
                f = pow(x, y);

        DESCRIPTION:

                Returns value of x raised to power y

        DIAGNOSTICS:

                There are three error possible error messages from  this
                function.

                If the x argument  is  negative  the  message  'pow  arg
                negative',  followed  by  the  value of x, is written to
                stderr.  The value of pow for |x| is returned.

                If x = 0.0 and y <=  0.0  or  if  result  overflows  the
                message  'pow  overflow', followed by the value of y, is
                written to stderr.  The value of HUGE is returned.

                If the result underflows and  if  warnings  are  enabled
                (normally not), the message 'pow underflow', followed by
                the value of y, is written to stderr.  The value of 0 is
                returned.

                The suggestion of Cody and Waite,  that  the  domain  be
                reduced to simplify the overflow test, has been adopted,
                consequently overflow is reported if  the  result  would
                exceed  HUGE  * 2**(-1/16).  2**(-1/16) is approximately
                0.9576.

        INTERNAL:

                Algorithm  from  Cody  and  Waite  pp.   84-124.    This
                algorithm  required  two  auxiliary  programs POWGA1 and


        Cmath Library Reference Manual                           Page 33
        pow     x raised to power y


                POWGA2 to calculate, respectively, the arrays  a1[]  and
                a2[]  used to represent the powers of 2**(-1/16) to more
                than machine  precision.   The  source  code  for  these
                programs  are  in  the  files POWGA1.AUX and POWGA2.AUX.
                The octal table on page 98 of Cody and Waite is  in  the
                file POWOCT.DAT which is required on stdin by POWGA2.

        AUTHOR:

                Hamish Ross.

        DATE:

                27-Jan-85


        Cmath Library Reference Manual                           Page 34
        powten  table of powers of 10


        6.18  table of powers of 10              _____ __ ______ __ __



                                   **********
                                   * powten *
                                   **********



        File name:      powten.c



        NAME:   powten -- table of powers of 10

        USAGE:

                extern double powten[];

        DESCRIPTION:

                This is an extern array of the powers of ten from  1e-38
                to 1e+38.  It is used by dtoa and atof.

        DIAGNOSTICS:

                None

        INTERNAL:

                powten[0] is 1e-38
                powten[38] is 1e0
                powten[76] is 1e38

        AUTHOR:

                Hamish Ross.

        DATE:

                25-Mar-85


        Cmath Library Reference Manual                           Page 35
        sincos  sin and cosine functions


        6.19  sin and cosine functions              ___ ___ ______ _________



                                   **********
                                   * sincos *
                                   **********



        File name:      sincos.c



        NAME:   sincos -- sin and cosine functions

        USAGE:

                double x, f, sin();
                double g, cos();
                f = sin(x);
                g = cos(x);

        DESCRIPTION:

                sin returns sin of x.
                cos returns cosine of x.

        DIAGNOSTICS:

                If the absolute value of the argument  is  greater  than
                TRIG_MAX  the  error  message  'sin, cos arg too large',
                followed by the value of the  argument,  is  written  to
                stderr.    The  algorithm  returns  a  result  of  lower
                accuracy.  The number of reliable decimal digits will be
                roughly 20 - log10(|x / pi|).

        INTERNAL:

                Algorithm from Cody and Waite  pp.   125-149.   A  small
                modification  to  the published algorithm has meant that
                the value of the argument is not  restricted  to  values
                whose integer part can be represented by a long integer.
                The accuracy of the result in those cases will, however,
                be very low (c.f.  above).

        AUTHOR:

                Hamish Ross.

        DATE:

                8-Jan-85


        Cmath Library Reference Manual                           Page 36
        sincos  sin and cosine functions


        6.20  hyperbolic sine function              __________ ____ ________



                                    ********
                                    * sinh *
                                    ********



        File name:      sinh.c



        NAME:   sinh -- hyperbolic sine function

        USAGE:

                double x, f, sinh();
                f = sinh(x);

        DESCRIPTION:

                Returns hyperbolic sine of argument.

        DIAGNOSTICS:

                If the argument is large enough to cause overflow in the
                result the message 'sinh arg too large', followed by the
                value of the argument, is written to stderr.  A value of
                HUGE, with the same sign as the argument, is returned.

        INTERNAL:

                Algorithm from pp.  217-238  of  Cody  and  Waite.   The
                constant  v  which  appears  in  2  define statements is
                chosen  so  that  log(v)  is  an  exact  octal  constant
                slightly  larger  than  log(2) (See C and W pp.  218 and
                227.

        AUTHOR:

                Hamish Ross.

        DATE:

                12-Jan-85


        Cmath Library Reference Manual                           Page 37
        sqrt    square root function


        6.21  square root function              ______ ____ ________



                                    ********
                                    * sqrt *
                                    ********



        File name:      sqrt.c



        NAME:   sqrt -- square root function

        USAGE:

                double x, f, sqrt();
                f = sqrt(x);

        DESCRIPTION:

                Returns square root of argument.

        DIAGNOSTICS:

                If the  argument  is  negative  the  message  'sqrt  arg
                negative',  followed  by  the  value of the argument, is
                written to stderr.  The  square  root  of  the  absolute
                value of the argument is returned.

        INTERNAL:

                Algorithm from pp.  17-34 of Cody  and  Waite.   Uses  3
                Newton iterations.
        AUTHOR:

                Hamish Ross.

        DATE:

                26-Dec-84


        Cmath Library Reference Manual                           Page 38
        tancot  tangent and cotangent functions


        6.22  tangent and cotangent functions              _______ ___ _________ _________



                                   **********
                                   * tancot *
                                   **********



        File name:      tancot.c



        NAME:   tancot -- tangent and cotangent functions

        USAGE:

                double x, f, tan();  double g, cotan();
                f = tan(x);  g = cotan(x);

        DESCRIPTION:

                tan returns tan of x.  cotan returns cotangent of x.

        DIAGNOSTICS:

                If the absolute value of the argument  is  greater  than
                TRIG_MAX  the  error message 'tan, cotan arg too large',
                followed by the value of the  argument,  is  written  to
                stderr.    The  algorithm  returns  a  result  of  lower
                accuracy.  The number of reliable decimal digits will be
                roughly 20 - log10(|x|).
                If the argument of cotan is less in magnitude than  1  /
                HUGE  the  error message 'cotan arg too small', followed
                by the value of the argument, is written to  stderr.   A
                value  of  HUGE  with  the  same sign as the argument is
                returned.

        INTERNAL:

                Algorithm from Cody and Waite  pp.   150-173.   A  small
                modification  to  the published algorithm has meant that
                the value of the argument is not  restricted  to  values
                whose integer part can be represented by a long integer.
                The accuracy of the result in those cases will, however,
                be very low (c.f.  above).

        AUTHOR:

                Hamish Ross.

        DATE:


        Cmath Library Reference Manual                           Page 39
        tancot  tangent and cotangent functions


                8-Jan-85


        Cmath Library Reference Manual                           Page 40
        tanh    hyperbolic tanh function


        6.23  hyperbolic tanh function              __________ ____ ________



                                    ********
                                    * tanh *
                                    ********



        File name:      tanh.c



        NAME:   tanh -- hyperbolic tanh function

        USAGE:

                double x, f, tanh();
                f = tanh(x);

        DESCRIPTION:

                Returns hyperbolic tanh of argument.

        DIAGNOSTICS:

                None

        INTERNAL:

                Algorithm from pp.  239-255 of Cody and Waite.
        AUTHOR:

                Hamish Ross.

        DATE:

                30-Jan-85


        Cmath Library Reference Manual                           Page 41
        math.h  cmath constants and definitions


        6.24  cmath constants and definitions              _____ _________ ___ ___________



                                   **********
                                   * math.h *
                                   **********



        File name:      math.h



        NAME:   math.h -- cmath constants and definitions

        USAGE:

                #include <math.h>

        DESCRIPTION:

                <math.h> is a file of constants and definitions used  by
                the  cmath  library  routines.   As  such it retains the
                commonly occurring magic numbers from  that  package  in
                one  convenient  location.   If any of those definitions
                have to be modified the cmath functions will need to  be
                recompiled  also.   In  some cases the accuracy of these
                constants is critical to the accuracy of some  component
                of  the  cmath package, so it would be wise not to touch
                them unless you understand  the  significance  for  that
                package of your actions.
                It will usually not be necessary to include this file in
                a  program  which  uses  the  cmath functions.  However,
                since it contains useful constants like PI, E,  PI_BY_2,
                ROOT_2  and  so  on it may be included to provide those.
                Full details of its contents appear  in  the  'internal'
                section of this documentation.

        DIAGNOSTICS:

                Not applicable

        INTERNAL:

                <math.h> contains 4 types of constants :-

                1) Absolute constants such as pi and e.

                2)  Checked  octal  constants;    these   are   absolute
                constants  for  which  it  has  been  verified  that the
                compiler converts the decimal representation given  here
                to  a  fully  accurate binary number inside the machine.


        Cmath Library Reference Manual                           Page 42
        math.h  cmath constants and definitions


                This level of accuracy is essential for at least one  of
                the algorithms in the package.

                3)  System  dependent  constants,  which  includes  such
                things  as  the  largest and smallest numbers, number of
                bits in the exponent and mantissa and so on.

                4) The symbolic values of the error codes for the cmathe
                error package.

                The symbolic names, values and descriptions of  each  of
                those groups of constants appears below.

                /*
                 * absolute constants
                 */

                PI 3.14159265358979324          pi
                HALF_PI 1.57079632679489662     pi/2
                REC_PI 0.318309886183790672     1/pi
                RPIBY2 0.636619772367581343     reciprocal of pi/2
                E 2.718281828459045235          e
                LOGBE2 0.69314718055994530942   log of 2 to base e
                LOGB2E 1.44269504088896341      log of e to base 2
                ROOT_2 1.4142135623730950488    square root of 2
                ROOT_3 1.732050807568877293     square root of 3

                /*
                 * checked octal constants
                 */

                PI_BY_2 1.57079632679489662     pi/2
                PI_BY_4 0.785398163397448310    pi/4
                LOGB10E 0.434294481903251828    log of e to base 10
                ROOT_05 0.70710678118654752440  square root of 0.5

                /*
                 * system dependent constants
                 */

                TINY 0.293873587705571877E-38   smallest no = 2**-128
                HUGE 0.170141183460469230E+39   largest no = 2**+127
                LOG_HUGE 0.880296919311130543E+02       log of HUGE
                LOG_TINY -0.887228391116729997E+02      log of TINY
                MIN_EXP -128                    minimum base 2 exponent
                MAX_EXP 127                     maximum base 2 exponent
                MAXLONG 017777777777L           largest long integer
                SIGFIGS 18                      max no useful digits for
                dtoa
                TRIG_MAX 3.1415926535897932385e12       trig fn limit
                ROOT_EPS 0.372529029846191406e-8        2**-28
                REC_HUGE 0.587747175411143754E-38       1 / HUGE



        Cmath Library Reference Manual                           Page 43
        math.h  cmath constants and definitions


                /*
                 * error codes to communicate with cmathe
                 */

                FP_OPER 1       /* FPU op code error             */
                FP_ZDIV 2       /* FPU divide by zero            */
                FP_FTOI 3       /* FPU float to integer conv error */
                FP_OFLO 4       /* FPU overflow                  */
                FP_UFLO 5       /* FPU underflow                 */
                FP_UDEF 6       /* FPU undefined variable (-0)   */
                FP_BIGI 7       /* Atof input too large          */
                FP_BADC 8       /* Bad character in atof input string */
                FP_NESQ 9       /* Square root of negative number */
                FP_LEXP 10      /* Exp argument too large        */
                FP_SEXP 11      /* Exp argument too small        */
                FP_NLOG 12      /* Log argument zero or negative */
                FP_TANE 13      /* Argument of tan too large     */
                FP_TRIG 14      /* Argument of sin/cos too large */
                FP_ATAN 15      /* Atan2 arguments both zero     */
                FP_COTE 16      /* Argument of cotan too small   */
                FP_ARSC 17      /* Bad argument for asin/acos    */
                FP_SINH 18      /* Argument of sinh too large    */
                FP_COSH 19      /* Argument of cosh too large    */
                FP_POWN 20      /* Negative argument in pow      */
                FP_POWO 21      /* Result of pow overflows       */
                FP_POWU 22      /* Result of pow underflows      */

                /* numbers of each type of error - to determine argument
                type    */

                FP_NFPU 6       /* No of FPU generated errors    */
                FP_NSTR 2       /* No of string argument errors  */
                FP_NMAR 14      /* No of math routine double arg  errors
                */

        AUTHOR:

                Hamish Ross

        DATE:

                24-Feb-85













                                   APPENDIX A

                              CMATH LIBRARY INDEX



        The following is  a  keyword  in  context  index  to  the  cmath
        library.   The entry in the left-hand column is the title of the
        routine in the cmath library documentation.


        fabs    argument          floating absolute value of floating   
        arsico                             arc cosine function          
        arsico                             arc sin function             
        atan                               arctan function atan         
        atan                               arctan function atan2        
        $$dtoa                   double to ascii conversion             
        atof                               ascii to double conversion   
        atan               arctan function atan                         
        atan               arctan function atan2                        
        log10           logarithm function base 10                      
        frexp      exponent of a number to base 2       get mantissa and
        ldexp      exponent of a number to base 2      load mantissa and
        math.h                       cmath constants and definitions    
        atof               ascii to double conversion                   
        $$dtoa             double to ascii conversion                   
        sincos                             cosine function              
        arsico                         arc cosine function              
        cosh                    hyperbolic cosine function              
        tancot                             cotangent function           
        math.h         cmath constants and definitions                  
        atof                      ascii to double conversion            
        $$dtoa                             double to ascii conversion   
        cmathe                       cmath error package                
        frexp   2         get mantissa and exponent of a number to base 
        ldexp   2        load mantissa and exponent of a number to base 
        exp                                exponential function         
        fabs    floating argument          floating absolute value of   
        fabs             absolute value of floating argument    floating
        floor          largest integer not greater than argument        
        cosh                               hyperbolic cosine function   
        sinh                               hyperbolic sine function     
        tanh                               hyperbolic tanh function     
        cminit                       cmath initialisation               
        floor   argument           largest integer not greater than     
        ceil    argument          smallest integer not less than        


        Cmath Library Reference Manual                          Page A-2
        Cmath Library Index


        floor   than argument              largest integer not greater  
        ceil          smallest integer not less than argument           
        log                                logarithm function           
        log10                              logarithm function base 10   
        frexp   number to base 2       get mantissa and exponent of a   
        ldexp   number to base 2      load mantissa and exponent of a   
        modf                               modulus function             
        pow                    x raised to power y                      
        powten                    table of powers of 10                 
        sqrt                        square root function                
        sincos                             sin function                 
        arsico                         arc sin function                 
        sinh                    hyperbolic sine function                
        ceil    than argument              smallest integer not less    
        sqrt                               square root function         
        powten                             table of powers of 10        
        tancot                             tangent function             
        tanh                    hyperbolic tanh function                
        floor          integer not greater than argument         largest
        ceil     smallest integer not less than argument