LAP:  SLAVE PRINT UTILITY


                                    ABSTRACT


     This  program simplifies process of printing a file on a LA50 compati-
     ble printer attached to a VT100 compatible terminal.  The printer  can
     be  configured  for  40, 80 or 132 columns and normal or enhanced den-
     sity.  If the file is unpaginated a four line skip  is  inserted  over
     page perforations.  For paginated documents, the formfeed is expanmded
     to the required number of linefeeds to circumvent the  TT:   handler's
     habit  of  gobbling up formfeeds.  The file name is printed at the top
     of the first page.  The program is set up for 70 lines per page with a
     4  line  skip, ie.  66 lines per page on A4 paper.These parameters can
     readily be altered.   The  default  options  are  normal  density,  80
     columns.   Other  combinations,  if  required, are presented as yes/no
     choices.  







































                                     - 1 -



                                        
                                        


                             LAP:SLAVE PRINT UTILITY


                                 OPERATING NOTES


             The  operation  of  this program is extremly simple.  Assuming
     the VT100, VT2xx etc.  and the LA50 are correctly connected,  run  the
     program  and  answer  the  questions.   Valid responses to the options
     queries are "Y" or "N".  The file  name  can  be  any  valid  RT11  or
     TSX-plus filename of the DEV:FILNAM.TYP form.  
             The  program  can be easily modified for other page lengths or
     skip values.  To alter page length, alter the value  of  the  variable
     PGELEN  and the LIN70 printer control code to suit.  To alter the skip
     value, alter the value of the variable PGSKIP .  
             Error messages are very basic:  
     There  are  warning messages for incorrect responses to option queries
     and invalid filename and three fatal error messages.  
     (i) LAP-F-READ  ERROR  indicates  a  hardware  error (unlikely) or the
     specified file not found 
     (ii) LAP-F-WRITE ERROR indicates a hardware error when the program at-
     tempted to write to the terminal 
     (iii) LAP-F-PRINTER  NOT  READY  means  what it says.  Most likely not
     powered on, not connected, out of paper etc.  





























                                     - 2 -