HEATH
                      Program to Set RT-11 Date and Time
                          From Heathkit GC1000 Clock

                              John M. Crowell
                                U.C. Davis


                               INTRODUCTION

The Heathkit Model GC1000 digital clock is a short-wave radio receiver tuned
to the National Bureau of Standards station WWV, which broadcasts the
date and time-of-day on frequencies of 5, 10, and 15 MHz.  The GC1000 decodes
the time and date signal and displays the time on a digital display.  An
optional RS-232 module on the clock puts the time and date out in an ASCII
string terminated by a carriage return.

This program sets the RT-11 date and time from the ASCII string produced
by the Heathkit GC1000 WWV clock connected to a DL11-type serial port.
An in-line interrupt service routine scans the input data for a carriage
return marking the end of a data "frame" and then stores characters in a
buffer until a second carriage return is encountered.  If a second carriage
return is not found before the end of the buffer (which is, of course, large
enough to accomodate the GC1000 data frame), an error will be generated, and
the program will exit without attempting to set the time or date. The GC1000
may be set to either 12hr or 24hr mode.

If no data appear on the serial port within a time-out period, the program
will exit with an "off-line" error message.  If the clock is running, but has
not set itself, the program will exit with a "not-set" error message.

If the clock is "set" but not locked, the tenths-of-seconds digit on the
clock will be dim indicating that the clock time is not necessarily
accurate.  In this case, the program will exit with a warning message, and 
a WARNING level error will be generated.



                             REQUIREMENTS

The following hardware and software are required:

Hardware:	Any PDP-11 or LSI-11 processor
		System clock at 50Hz or 60Hz
		Any DL-11 type serial port.
		Heathkit GC1000 clock with RS-232 option

Software:	RT-11 Version 5.0 or later.

			CUSTOMIZATION

The following locations can be patched to customize the program without
rebuilding it.

 1000	contains the base CSR for the serial port (defaults to 176500)

 1002	contains the interrupt vector for the serial port (defaults to 300)

 1004	contains the number of clock ticks to wait before assuming that there
	is nothing coming in the serial port, or that whatever is connected
	is not sending a "time frame" terminated by a carriage return.
	(defaults to 180. ticks, or 3 seconds with a 60Hz clock)

 1006	contains a fine-tuning value.  The ASCII output from the HEATH clock
	is delayed by about 1 second, which is taken into account by this
	program.  The computation time to convert the ASCII string into RT-11
	format date and time is processor dependent.  A fudge factor can be
	inserted at this location which will be added to the number of clock
	ticks since midnight, to adjust for processing time.

 1010	Error severity code for "fatal" errors.
	  e.g.	No input - "clock is off-line"
		Unable to protect interrupt vectors (another job has'em)
		Framing error - unable to sync to clock input (no <CR>)

 1012	Error severity code for "non-fatal" errors.
	  e.g.	Clock time is not set.
		Clock data frame is undecipherable

	If the program is run from a command file, patching these locations
	will affect the continuation of the command file, depending upon the
	current level of SET ERROR.

			SET ERROR LEVEL
	Value	 NONE	WARNING	ERROR	FATAL	SEVERE
	 0-1	cont	cont	cont	cont	cont	(success)
	  2	cont	abort	cont	cont	cont	(warning)
	  4	cont	abort	abort	cont	cont	(error)
	 10	cont	abort	abort	abort	abort	(fatal/severe)
	 20	abort	abort	abort	abort	abort	(unconditional)



                     WARNINGS and DISCLAIMERS

This program uses in in-line interrupt service routine.  When running under
the XM monitor, it should be run only as a background job, so that there is
no chance that the interrupt service routine will be in PAR1 or PAR2 and
possibly be mapped away.

The year in the GC1000 ASCII output is determined by switches inside the
clock. (WWV only sends month and day.)  The RT-11 date will be correctly
set through the year 1999.  Years 2000-2099 are to be supported in RT-11
beginning Version 5.5.  This program uses the "preannounced" protocol for
years 2000-2071.  From 2072-2099, this program will not set the year properly.
(If anyone is still using it by then, call me.)  There is, however, no
guarantee that the protocol used by this program will be the one finally
established in future versions of RT-11.  One can only hope.