* * * *  MAC6.DOC  * * * *

		MIKE FAVITTA - 5/16/79
		2 JANET LANE
		ALBANY, N.Y.  12203


	THIS PROGRAM IS AN EXTENSION OF MAC4.ASM THAT IS ALREADY AVAILIBLE
	FROM THE CP/M USERS GROUP. BOTH THESE PROGRAMS ADAPT THE TDL
	MACRO-ASSEMBLER TO WORK WITH DISK FILES UNDER THE CP/M OPERATING
	SYSTEM.


	* ENHANCEMENTS PRESENT IN MAC6.AZM THAT ARE NOT IN MAC4.ASM *


   1.	MULTI-EXTENSION SOURCE FILES (OVER 16K OF TEXT) MAY NOW BE
	ASSEMBLED WITHOUT ERROR.

   2.	THE HIGHEST MEMORY AVAILIBLE FOR USE BY THE ASSEMBLER CALCULATION
	HAS BEEN CORRECTED (IT IS POSSIBLE TO WRITE OVER THE FIRST JUMP
	VECTOR FOR CP/M IF YOU RUN OUT OF MEMORY USING MAC4.ASM).

   3.	DIAGNOSTIC ERROR MESSAGES HAVE BEEN ADDED ALONG WITH INCREASED
	ERROR DETECTION.

   4.	CONTROL OF THE ASSEMBLERS THREE PASSES HAS BEEN ADDED. IT IS
	POSSIBLE TO GENERATE JUST A LISTING OR A OBJECT FILE BY
	SPECIFYING OPTIONS ON THE ASSEMBLER CALL. NO OPTION CAUSES THE
	DEFAULT CASE OF BOTH A LISTING AND A OBJECT FILE TO BE CREATED.

   5.	FOR USERS WITH DUAL DRIVE SYSTEMS THE EFFICIENCY OF ASSEMBLY HAS
	BEEN INCREASED BY AUTOMATICALLY PLACING ANY OUTPUT FILES ON THE
	DRIVE THAT DOES NOT CONTAIN THE SOURCE FILE. THIS GREATLY
	REDUCES THE AMOUNT OF HEAD REPOSITIONING NECESSARY. IF YOU
	ONLY HAVE A SINGLE DRIVE SYSTEM OR WANT TO OVER RIDE THIS FILE
	PLACEMENT SCHEME, AN OPTION IS AVAILABLE TO FORCE ALL FILE I/O
	TO ONLY THE CURRANTLY LOGGED IN DRIVE.

   6.	MAC6.AZM IS WRITTEN FOR THE Z-80 AND WILL NOT RUN ON A 8080 BASED
	MICROCOMPUTER WITHOUT MODIFICATION.


	* GENERATION NOTES *


   1.	THE OBJECT CODE IS SUPPLIED IN A DIRECTLY EXECUTABLE FORM IN
	THE FILE MAC6.COM. THIS FILE CONTAINS THE CODE FROM ASSEMBLING
	MAC6.AZM AND IS SET TO RUN AT 100H. WHEN LOADED IT OCCUPIES
	MEMORY FROM 100H TO 820H. THIS ALLOWS PEOPLE THAT DON'T HAVE
	ANY Z-80 ASSEMBLER RUNNING UNDER CP/M TO STILL PUT THE TDL
	ASSEMBLER UP ON THEIR SYSTEM.

   2.	PROCEDURE:

	   A.	CREATE A FILE CALLED TDL.COM THAT CONTAINS THE TDL
		ASSEMBLER SET TO RUN AT 800H.

		- USE TDL'S RELOCATING LOADER TO LOAD THE ASSEMBLER
		  AT 800H (R,800).

		- ENTER OR BOOT CP/M AND TYPE
		  SAVE 48 TDL.COM (CR)

	   B.	USING DDT MERGE THE FILES TDL.COM AND MAC6.COM

		- ENTER DDT AND TYPE THE FOLLOWING COMMANDS

		  ITDL.COM (CR)
		  R (CR)
		  IMAC6.COM (CR)
		  R (CR)
		  ^C (^C = CONTROL C)
		  SAVE 48 MASM.COM

		- THE TDL.COM FILE MUST BE READ IN FIRST AS PART OF MAC6.COM
		  OVERLAYS IT.


	* NOTES ON OPERATION *


   1.	FORMAT OF ASSEMBLER CALL:	MASM FILENAME OPTIONS

	- FILENAME NEVER HAS THE EXTENSION. IT IS ALWAYS ASSUMED TO BE AZM.
	- OPTIONS AVAILIBLE ARE:
		S - USE THE CURRANTLY LOGGED IN DRIVE FOR ALL FILES
		    (SINGLE DRIVE MODE)
		L - PRODUCE A LISTING FILE ONLY (PASSES 1 AND 2)
		O - PRODUCE A OBJECT FILE ONLY (PASSES 1 AND 3)
	- ANY COMBINATION OF OPTIONS IS LEGAL EXCEPT OL AND LO
	- IF NO OPTIONS ARE SPECIFIED THEN DUAL DRIVE MODE AND A COMPLETE
	  ASSEMBLY (PASSES 1, 2 AND 3) IS ASSUMED

   2.	SAMPLE MASM CALLS:

	- MASM TEST
	- MASM TEST SL
	- MASM TEST O

   3.	WHEN A DISK ERROR OCCURS THE FOLLOWING INFORMATION IS PROVIDED:

	- THE ADDRESS IN THE PROGRAM AT WHICH THE ERROR OCCURED
	- THE STATUS RETURNED BY CP/M
	- THE TYPE OF DISK FUNCTION THAT WAS ATTEMPTED

   4.	THE ASSEMBLY LISTING AND OBJECT CODE WILL BE IN FILES WITH THE
	SAME FILE NAME AS THE SOURCE FILE AND WILL HAVE THE EXTENSIONS
	PRN AND HXR. THE TDL PSUEDO-OPS .PABS AND .LOC 100H CAN BE USED
	TO GENERATE CODE THAT CAN BE HANDLED BY CP/M'S LOAD PROGRAM (THE
	EXTENSION MUST BE CHANGED TO HEX). OTHERWISE THE OBJECT FILE
	CONTAINS FULLY RELOCATABLE CODE. A PROGRAM TO DIRECTLY
	LOAD (ANY WHERE IN MEMORY YOU WANT) THESE FILES UNDER CP/M
	IS BEING DEVELOPED AND WILL BE SUBMITTED TO THE CP/M USERS GROUP
	SHORTLY. IT WILL BE CALLED RELOC.AZM.

   5.	THIS PROGRAM HAS BEEN EXTENSIVELY TESTED, BUT IF ANY ERRORS ARE
	FOUND I WOULD APPRECIATE BEING NOTIFIED.