SPECTRUM ANALYSIS SOFTWARE

                 The programs in this package were written by:

                    Victor DePinto
                    2627-148th ave. S.E. Apt. 10
                    Bellevue, Washington  98007
                    (206) 641-7591

            The last revision date was January 27, 1982.

                 These programs provide the capability to perform  the  FFT
            and   inverse   FFT   and   to   perform  various  arithmetical
            manipulations on signals as well as to display the results.

                 The data processed by these programs is contained in  disk
            files. Data  is also output to disk files except when displayed
            on CRT or printer.  The data is in the form of  a  sequence  of
            1024  complex  numbers  representing 1024 data points in either
            the time or frequency domain.


                        INSTRUCTIONS FOR USE OF THE FFT PROGRAM

                 This program performs the FFT  or  inverse  FFT  on  files
            containing   a   sequence  of  1024  complex  values. The  user
            specifies the input and output filenames.  Filetypes  are .DAT.
            Enter  only  the  filename,  not the filetype.  It is necessary
            that the file FFT.COM be on the disk.

                 To operate this program, type "FFT". The program will  ask
            for  source  and  destination filenames and then will ask for a
            number specifying FFT or inverse FFT.  The  program  will  then
            perform  a  1024  point  FFT  on  the source file and write the
            result to the destination file.


                      INSTRUCTIONS FOR USE OF THE UTILITY PROGRAM

                 This is a general utility program which allows examination
            and  plotting  of  file  data  and  performs certain arithmetic
            operations on the data, such as  summing,  multiplication,  and
            windowing. In the event that other arithmetic manipulations are
            required, the user may write FORTRAN programs which operate  on
            1024  point complex arrays read and written to unformatted disk
            files.  It is necessary that the files UTIL.COM and ARIT.COM be
            on the disk.

                 To run the utility program, type "UTIL". The program  will
            respond with a menu. Following is a list of the menu items with
            a brief description of each:



                                          -1-Š               1  WRITE FILE TO CRT
                  Write real and imaginary parts of all values in  file  to
                  CRT.  The  user  first enters the filename then the first
                  point to be displayed,  and  types  "Q"  to  quit.  Three
                  points are displayed on each line. Each point consists of
                  a real and imaginary part. The first number is the  index
                  of the first point displayed.

               2  CREATE REAL PULSE FILE
                  Creates a file containing a  real  constant  in  a  user-
                  specified range of points. All other points are zero, and
                  all imaginary parts are zero.

               3  WINDOW FUNCTIONS
                  This will bring up another menu offering  to  multiply  a
                  range  of points by any one of a number of popular window
                  functions.

               4  ARITHMETIC FUNCTIONS
                  This  brings  up  a  menu  offering  to  add,   subtract,
                  multiply,  or  divide two files and place the result in a
                  third file. It will also multply a file by a constant and
                  find the conjugates or magnitude squared of a file.

               5  PRINT FILE ON PRINTER
                  Prints real and imaginary parts  of  of  a  file  on  the
                  system list device.

               6  RMS VALUE OF REAL PARTS OF A FILE
                  Computes the root mean square of he real parts of a  file
                  and writes this value to the CRT.

               7  MODIFY FILE
                  This allows the user to enter or modify the  data  points
                  on a point by point basis.

               8  TRANSLATE
                  This rotates (shifts) all data points in a file by  user-
                  specified  amount.  I  must apologize for the slowness of
                  this routine. No doubt a clever programmer could make  it
                  faster.

               9  PLOT FUNCTIONS
                  This brings up a menu offering to make graphic  plots  of
                  time  or  frequency domain files. The exact nature of the
                  functions depends on the type of plotting device used.  A
                  version is supplied which will make plots on any printer.
                  Another version will make high resolution  plots  on  the
                  Houston Instruments DMP2 plotter.

               10 RETURN TO OPERATING SYSTEM
                  Return to CPM.


                                          -2-Š                                 THE PLOTTER INTERFACE

                 The TTY version of UTIL.COM makes character plots  on  any
            standard  printer.  The  DMP2  version  plots  on  the  Houston
            Instruments DMP2 plotter. The plotter should be wired  for .005
            inch  per  step  and 9600 baud serial RS-232C interface.  Lower
            baud rates are permissible, but will slow the pen  motion.  The
            plotter  serial port must be interfaced to the CP/M BIOS as the
            PUNCH device.


                                 NOTES ON UTILIZATION

                 Certain types of data to be processed by this software may
            be generated by the utility program itself. (ie. pulses, double
            pulses, truncated spectra, etc.) Other data will  be  in  files
            written  by  user-generated  programs or possibly acquired from
            the real world. A lot of things  can  be  done  with  a  little
            imagination.

                 Here are  some  possibilities:  To  truncate  a  spectrum,
            multiply by a real pulse. To filter a signal, multiply it's FFT
            by the frequency domain filter function. This may be the FFT of
            the  impulse  response  of  the  filter. A  double pulse may be
            created by summing two single pulses. Signals may be added  and
            subtracted  in either the time or frequency domain. The program
            may be used to examine the spectra of waveforms in contemplated
            circuit  design,  to  determine  design suitability without lab
            measurements. The inverse FFT may be used  as  a  tool  in  the
            design of FIR filters.

                 One version of my software had  a  provision  for  uniform
            rate data acquisition from an analog to digital converter. This
            is not provided  in  the  package  because  of  it's  hardware-
            dependent  nature,  but  it  could easily be implemented by the
            user.  In order to get the ADC data into  a  format  compatible
            with  this  software,  write  a Microsoft FORTRAN program which
            defines both an integer array and a floating  point  array.  An
            assembly   language  subroutine  is  linked  with  the  FORTRAN
            program. By means of data area declared  COMMON,  the  assembly
            language  routine  routine  fills  the  integer array with 1024
            samples from the ADC.  The FORTRAN program will  then  transfer
            the  data  from  the  integer  array  to  the real parts of the
            floating point array and write it to disk. The integer  numbers
            will  automatically  be  converted to floating point.  The data
            would then be  processed  by  this  software.  Thus,  with  the
            addition  of  an  analog  to  digital  converter,  the computer
            becomes a Fourier Transform spectrum analyzer.






                                          -3-Š                                    FILE STRUCTURE

                 This software processes data in arrays consisting of  1024
            complex  data  points. Each  complex data point consists of two
            floating point numbers, the real part and the  imaginary  part.
            When  in  memory,  these  numbers  are  stored in the following
            sequence: real part of point 0, imaginary part of point 0, real
            part  of  point  1, imaginary part of point 1, and so on. Since
            each floating point number occupies four bytes, a complex  data
            point occupies 8 bytes.

                 These arrays, or signal vectors, are stored in disk  files
            in  internal  machine  format  (not  ASCII). This  permits much
            faster access and more compact storage. In  general  a  program
            will  get  a 1024 point signal vector to be processed from such
            an unformatted disk file, and then write the processed data  to
            a  similar  file. Each  disk  file  occupies  8 kilobytes. Disk
            filenames are specified by the user. The filetypes  are  always
            DAT.

                 If  the  user  writes  programs  generating  data  to   be
            processed  by this software, it should be stored in memory in a
            2 by 1024 array.  Element  (1,N)  is  real;  element  (2,N)  is
            imaginary. The  data  should  then be written to disk using the
            FORTRAN unformatted write statement.

                                  DISK I/O WITH BASIC

                 Compatible data files can be also be read and  written  to
            disk  using  Microsoft  BASIC. Since the data must be stored in
            internal binary form, you must use only random access files.  A
            file   must   contain   1024  complex  values.  A  file  called
            DISKIO.BAS is included in this package, as an example.

                                 COMPILING AND LINKING

                 In order to produce executable  object  programs,  compile
            the  FOR  files  with  the  Microsoft  FORTRAN-80  compiler and
            assemble  the  MAC  files  with  the  MACRO-80  assembler.  The
            resulting  REL  files must then be linked using the L80 linking
            loader. The final developement work on this  package  was  done
            with FORTRAN-80 version 3.4.

                 The objective is to produce three COM files:

                        UTIL.COM
                        ARIT.COM
                        FFT.COM

            FFT.COM performs the 1024 point FFT and inverse FFT by means of
            a  radix-2  Cooley-Tukey algorithm. UTIL.COM is a program which
            performs various computation and display functions. ARIT.COM is


                                          -4-Š            not intended to be run by itself, but is chained by UTIL.COM.

                 A note of  explaination  is  needed  with  regard  to  the
            plotting  capabilities  of this package. It is possible to make
            two different versions of UTIL.COM.  They are identical  except
            for  their  plotting functions. The TTY version will make plots
            on any printer. The DMP2 version produces high resolution plots
            on  the  Houston  Instruments DMP2 plotter. You will be able to
            modify the plotting modules  of  this  software  to  accomodate
            other  types  of  plotting devices. The chart below shows which
            source files are needed to produce each COM file.


            TASK            SOURCE FILE     MODULE NAMES IN FILE
            -------------------------------------------------------------
            (DMP2 version)
            UTIL.COM        UTIL.FOR        UTIL
                            NAME.FOR        READ, NAME
                            WIND.FOR        WIND, RECTAN, COSBEL, HAFSIN
                                            TRIANG, HANNIN, HFSIN3
                                            HAMMIN, COSSQR, PARZEN
                            QCHEK.MAC       QCHEK
                            PLOT.FOR        PLOT
                            HI.FOR          DRAW, HOME, VECTOR
                                            GRID, BORDER, SPEED
                            HIA.MAC         PRINT, STTIM, PENUP
                                            PENDN


            (TTY version)
            UTIL.COM        UTIL.FOR        UTIL
                            NAME.FOR        READ, NAME
                            WIND.FOR        WIND
                            QCHEK.MAC       QCHEK
                            TTYPLOT.FOR     PLOT, TTDRAW


            ARIT.COM        ARIT.FOR        ARIT
                            NAME.FOR        READ, NAME


            FFT.COM         FFT.FOR         FFT1K
                            NAME.FOR        NAME











                                          -5-Š                 To facilitate linking of the runtime  tasks,  four  submit
            files are provided. Before these submit files are used, the FOR
            and MAC files must be compiled and assembled.

                    To link                 Type

                    UTIL.COM (TTY vers.)    SUBMIT UTIL#T
                    UTIL.COM (DMP2 vers.)   SUBMIT UTIL#H
                    ARIT.COM                SUBMIT ARIT#
                    FFT.COM                 SUBMIT FFT#


                                  THE TWIDDLE PROGRAM

                 For speed, the FFT program has the needed sine and  cosine
            values  initialized in data memory. These values were generated
            by a FORTRAN program which wrote them to disk  in  ASCII  form.
            The  sines and cosines were then edited into the DATA statement
            in the FFT.FOR program.  The twiddle factor  generator  program
            is  provided  in a file named TWIDDLE.FOR for those who wish to
            use it to make other FFT programs.

































                                          -6-Š                                    FILES SUPPLIED

                 Following is a list of files supplied in this package. Two
            versions  of the executable utility program are supplied. UTIL-
            TTY.COM plots on any standard printer. UTIL-HI.COM plots on the
            Houston  Instruments  DMP2  plotter. Rename the one you want to
            use as UTIL.COM.

            FILENAME        COMMENTS

            ARIT.FOR        Arithmetic functions.
            ARIT.COM        Executable arithmetic functions.
            ARIT#.SUB       Submit file.
            DISKIO.BAS      Disk file I/O in BASIC.
            FFT.FOR         1024 point FFT.
            FFT.COM         Executable FFT program.
            FFT#.SUB        Submit file.
            HI.FOR          DMP2 driver.
            HIA.MAC         DMP2 driver.
            NAME.FOR        Filename getter.
            PLOT.FOR        Plotter plot routine.
            QCHEK.MAC       Checks for abort command.
            SPECTRUM.DOC    This documentation.
            TTYPLOT.FOR     Printer plot routine.
            TWIDDLE.FOR     Generates twiddle factor table.
            UTIL.FOR        Utility program.
            UTIL#H.SUB      Submit file.
            UTIL#T.SUB      Submit file.
            UTIL-HI.COM     DMP2 version of UTIL.COM.
            UTIL-TTY.COM    TTY version of UTIL.COM.
            WIND.FOR        Window functions.























                                          -7-Š