Notes on SMOKE.BAS.
The programme emulates the programme run by Warren Springs Laboratory to 
analyse the results from a network of monitoring stations throughout the 
UK.  The stations sample a quantity of air which is filtered and leaves a 
stain on a filter paper. The air is then passed through a hydrogen peroxide
solution to absorb sulphur dioxide. The resultant darkening of the filter 
paper is measured as a percentage of its original reflectivity. The peroxide
solution is titrated against a solution of sodium tetraborate.
The results are entered weekly on a sheet along with the readings from a meter
which measures the volume of air drawn through the apparatus.  These readings 
are used to calculate the amount of smoke and sulphur dioxide in the air in 
microgrammes/cu metre. (Note meter readingin cu ft)
 
The Programme :- The programme contains machine specific control codes for an 
OSBORNE 1 at its start. The subroutine at 130 contains an instruction to 
position the cursor which will be machine specific.  A form feed CHR$(12) is 
in the printout section towards the end. Otherwise everything standard.

Instructions :- Type CRUN2 SMOKE to load and run the programme.
The initial enquiry screen loaded from disk (SMOKE.MSK)
Questions are answered which set the parameters required for calculations.
The next meter reading and date are then entered to determine daily volume of 
air passing through sampler between readings.
Smoke stains and volume of titre entered and concentrations displayed.
After weeks records have been entered next meter reading & date requested.
After records have been entered for period the averages for smoke & SO2 
displayed.
The results can be sent to printer if required and records are automatically 
recorded on disk in a File.REC.
Dates with volumes of air outside the 55 to 85 cu.ft. range are marked with *
Limited correction is possible by entering '^' in reply to request for smoke 
reading. The previous entry is deleted and can be re-entered. This can be 
repeated, however going beyond the current week will upset results.
Entering '^' in reply to request for SO2 deleted that days smoke readings and 
allows re-entry.
'ALK' or 'N' readings are entered with <RET> only and assigned the value 999.
Zero titre should be entered as 0, not null string.
Where meter not read on Mondays then enter <RET> only until date of first or 
last entry reached. These days are not taken into account in averages.
The programme can be repeated for subsequent months at the same station or for 
other stations. Provided the station name and year remain the same, rerunning 
the programme will append the results to the same file.
The data entered cannot be checked for clerical errors, if disaster strikes 
then CONTROL C, break or reset in reply to entry inputs before the print starts
will avoid the records being recorded on disk.
THE RESULTS ARE SUBJECT TO SLIGHT DIFFERENCE TO THOSE PRODUCED BY WSL BUT 
SHOULD BE WITHIN 1 FOR THE AVERAGE SMOKE AND ACCURATE FOR THE AVERAGE SO2.