NULU MODIFICATION

This  is an update to Martins original documentation.  It details
which locations to patch to install NULU. These have been updated
as part of the modification process to create NULU 1.52.

Patches are listed in the order in which they appear in NULU.COM.  
Each  patch  is  explained  and the  default  values  are  listed 
immediately  next  to  the  patch  address.   All  addresses  are 
absolute hexadecimal.

Patch     Default             Explanation
00194h      50h               Number  of  characters  each   full 
                              video   line  can   contain.    Not 
                              necessarily  the same as the number 
                              you can see.
00195h      50h               Number  of characters visible on  a 
                              line at any one time.
00198h      07h               This  byte indicates the number  of 
                              files  that NULU can have  open  at 
                              any  one time.   The base number is 
                              4 and should never fall below that.  
                              The value of 3 has been added to it 
                              to  allow  3 level nesting  of  NCF 
                              files.    If   the  NCF  value   is 
                              increased or  decreased,  identical 
                              changes  should  be  made  to  this 
                              byte.  (See Patch at 00251h.)
00199h   0010h                This   obscure  word  controls  the 
                              number  of relocatable  tasks  that 
                              can   be  controlled  by  the  NULU 
                              memory     management     routines.  
                              Because each file is a  relocatable 
                              task,  the  same modifications  for 
                              the previous byte apply here.   The 
                              base  value  of this word is  000dh 
                              and  should never fall  below  that 
                              point.  (See Patch at 00251h.)
0019bh     10h                Number  of  contiguously   numbered 
                              disk drives in your system.  If you 
                              have drives A and B, set this value 
                              to  2.   It  will prevent you  from 
                              accessing an invalid drive.
0019ch     10h                Number  of  contiguous  user  areas 
                              that   NULU  will  be  allowed   to 
                              access.   Under  normal  CP/M  2.2, 
                              Turbo-Dos  or  a  ZCPR  system,   I 
                              understand that this number can  be 
                              as high as 20h.   For CP/M Plus  or 
                              most  systems  that  use  time/date 
                              stamping  this  number  should  not 
                              exceed 10h.
001cdh    0005h               This  is  the address of  the  BDOS 
                              vector.  All operating system calls 
                              go  through this address.   If  you 
                              have some weird,  non-standard CP/M 
                              implementation  you can patch  this 
                              to try to make NULU work with it.

0024dh      00h               Set  to  a non-zero value  to  make 
                              NULU READ/ONLY.   No operators will 
                              be  executed that could change  the 
                              library or disk directories in  any 
                              way.
0024eh      00h               LU.COM   was   set   up   to   exit 
                              automatically if a command tail was 
                              used when LU was invoked.  With the 
                              release  version of NULU,  it takes 
                              the -X command to exit.   Set  this 
                              byte to a 01h to get it to act like 
                              LU  in this respect.   That is,  it 
                              will   automatically   exit   after 
                              executing the passed command  tail, 
                              if one was present.
0024fh      01h               Set  to  a 00h to start  NULU  with 
                              BRIEF  mode  ON (long messages  not 
                              printed).
00250h      01h               Set  to zero to prevent users  from 
                              being  able  to  ESC,RET  from  the 
                              PROMPT  AND CHAIN TO PREVIOUS  MODE 
                              prompts in NCF files.  (Be sure  to 
                              also  change  the values at  00198h 
                              and 00199h.)
00251h      03h               This  byte  indicates  the  nesting 
                              level  allowed  for NCF  files.   I 
                              have  no idea what the upper  limit 
                              is,  but  watch  that  Data  Buffer 
                              Size!
00252h      '-Y *LBR -O',0    Starting here are 39 bytes in which 
                              any  valid  NULU operators  may  be 
                              stored.     This   line   will   be 
                              automatically executed when NULU is 
                              loaded,   even  before  any   other 
                              parameters  passed  on the  command 
                              line.  This might be used to create 
                              a  version  of  NULU  that,   after 
                              loading,    sets   the   drive/user 
                              defaults to B0:,  prints the  menu, 
                              scans  the drive for library files, 
                              then  switches to the open  library 
                              mode.  That command line would look 
                              like this:

                              -U B: -H -Y *LBR -O

                              Notice that all characters in  this 
                              line  MUST  be  UPPER  CASE.    The 
                              entire line MUST be terminated by a 
                              null  byte.    Only  39  bytes  are 
                              available  for  text...not  a  byte 
                              more.   The  40th  byte is for  the 
                              null terminator.


002a0h      3ch               This  is  the number of lines  that 
                              NULU will print on each page during 
                              member file printing.   Change this 
                              value  in accordance with the  line 
                              printer  patch  below.   Set it  to 
                              zero  to  have  NULU  ignore   line 
                              counts altogether.

Starting at 0027dh are 5 data areas used to define strings needed 
to control the console attributes.  Each string is preceded by an 
identification  byte  and a byte indicating  its  active  length.  
Then 5 bytes are available for the actual definition.   Therefore 
a  total  of 7 bytes is consumed for  each  video  control.   The 
attributes are, in order:
     DIM or REVERSE VIDEO ON   (DIM is preferred)
     DIM or REVERSE VIDEO OFF
     UNDERLINING ON
     UNDERLINING OFF
     CLEAR SCREEN

Each control becomes active as soon as it is patched in.

Likewise,  there  is one string defined for the LST:  device that 
will be issued immediately before printing a file.   It begins at 
002a2h and has the same format as the strings above.


will be issued immediately before printing a file.   It begins at 
002a2h and has the same format as the strings above.