OPT: A Three Pass Optimiser for Small C

 NOTE - Xopt is a version of opt to work with xc80. Only one of the
 optimisations does not apply, and this has been commented out in the .c file,
 and mentioned below. Some other changes were also necessary, and I've also
 converted two more functions into assembler.  Any bugs that have
 crept in are mine. 

 I have also altered the file protocol to allow the program to follow directly
 from xc80, and if so desired, proceed to assembly with no user intervention.
 Paragraphs describing the new bits are marked (*). For 'opt' below, read 
 'xopt'.  

 The program could be further improved by recompiling with a version of iolib
 allowing larger file buffers (currently 1024 bytes). To do so would require
 LGH to be changed in iolib.h, recompiling iolib.c and linking it to 
 xopt.obj and string.obj . Since only 2 files are open at any time, and since
 buffers are now allocated only as required, a 64k system would allow LGH to
 be as high as 8k.  

 R I M Sadek.


  Opt is a simple optimiser which improves the execution speed of the 
  assembler output of the Z80 Small C compiler.  It normally gives a net 
  reduction in the size of the assembled program.

  To call the optimiser use a command of the form:

     xopt filename [-a]  [> or >>filename]			(*)

  Opt assumes that the file has the extension .ASM and produces its output 
  in FILENAME.ASM.  On exit the original assembly code will be contained in
  a backup file FILENAME.BAK . NOTE THAT ANY FILE ALREADY EXISTING WITH THAT
  NAME WHEN XOPT IS CALLED WILL BE DELETED. (*)

  The optional -a causes the program to load and run the zmac assembler 
  once it has finished optimising. The source for the assembler will be
  the optimised .asm file produced by xopt. (*)

  Any number of files may be specified, but only the last will be processed. 
  The -a can be placed before or after the filename. (*)

  Redirection of screen output is allowed, using > and >>. Thus >FNAME.XXX
  will create a new file FNAME.XXX (deleting any existing file of that name)
  and send all screen output to that file. Similarly >>FNAME.XXX will redirect
  screen output, but in this case will add it to the end of any existing file
  of that name. In both cases there must be no spaces between the > or >> and 
  the filename; ie '>filename' and not '> filename'. (*) 

  The optimiser can also be invoked directly from xc80 with the -o option. (*)

  Using the optimiser on a variety of programs such as itself, the Z80 
  Small C compiler and a number of utilities has been found to give an 
  improvement in run time of 15-20%.  The resulting programs are also 
  slightly smaller.

  The following optimisations are applied.  The left-hand column gives the 
  original code, the optimised code is on the right.


  1.1) Negative constant


          LD HL,<number>                  LD HL,0-<number>
          CALL ccneg


      This avoids a particular stupidity of the Small C compiler, which 
      loads the absolute value of a negative constant and then negates it 
      rather than using the assembler to do the negating.  Saves 3 bytes.



  1.2) Double constant


          LD HL,<number>                  LD HL,2*<number>
          ADD HL,HL


      A further stupidity of the assembler is that it calculates constant 
      array offsets at run-time rather than at compile time.  Here we use 
      the assembler to do the sum for us.  Saves 1 byte.

  1.3) Push and pop around LD HL


          PUSH HL                         EX DE,HL
          LD HL,<anything>                LD HL,<anything>
          POP DE


      The compiler tends to load everything through the HL register pair 
      and get things into DE as an afterthought.  The above example is 
      better accomplished by exchanging the DE and HL registers.  The 
      previous contents of DE are lost in both the above fragments.  Saves 
      1 byte.



  1.4) Zero subscript


          EX DE,HL                        LD D,H
          LD HL,<0 or 2*0>                LD E,L
          ADD HL,DE


      The above construct is frequently used to find the address of the 
      first element of an array.  There is no reason to suppose that the 
      new contents of DE (the base address of the array) will ever be 
      used, but I put them there anyway, just in case.  Saves 3 bytes.



  1.5) One subscript


          EX DE,HL                        LD D,H
          LD HL,1                         LD E,L
          ADD HL,DE                       INC HL


      This construct is used to find the address of the second element of 
      a character array (with a constant index 1).  It's quicker just to 
      increment the base address.  Saves 2 bytes.



  1.6) Two subscript


          EX DE,HL                        LD D,H
          LD HL,<2 or 2*1>                LD E,L
          ADD HL,DE                       INC HL
                                          INC HL


      Constant subscripts of 2 are improved by the above substitution.  
      Saves 1 byte.


  1.7) Fetch integer from top of stack


          LD HL,0                         POP HL
          ADD HL,SP                       PUSH HL
          CALL ccgint


      Local variables in Small C are kept on the stack and fetched by 
      adding an offset to the stack pointer to get an address from which 
      the value is fetched.  If the required variable is at the top of the 
      stack it is quicker to pop it off.  Note that this is the fastest 
      way of fetching an integer, so the most frequently used variable in 
      a routine should be the last one to be defined.  Saves 5 bytes.



  1.8) Fetch second top integer from stack


          LD HL,2                         POP BC
          ADD HL,SP                       POP HL
          CALL ccgint                     PUSH HL
                                          PUSH BC


      This is similar to 1.7).  The BC register does not seem to be used 
      for much in the Small C compiler, so it's safe to trample all over 
      it.  Saves 3 bytes.



  2.1) Double EX DE,HL


          EX DE,HL                        <nothing>
          EX DE,HL


      Obvious, isn't it?  Save 2 bytes



  2.2) DE <- HL followed by EX DE,HL


          LD D,H                          LD D,H
          LD E,L                          LD E,L
          EX DE,HL


      If DE and HL contain the same thing there's no point in swapping 
      them.  Saves 1 byte.



  2.3) DE <- HL followed by LD HL


          LD D,H                          EX DE,HL
          LD E,L                          LD HL,<anything>
          LD HL,<anything>


      Loading DE from HL and then overwriting HL is the same as swapping 
      DE and HL and overwriting HL.  You still lose what used to be in DE.  
      Saves 1 byte.



  2.4) Expand ccpchar


          CALL ccpchar                    LD A,L
                                          LD (DE),A


      The run-time routine to store a character from HL to the address 
      pointed to by DE is only two bytes long - shorter than a CALL to it.  
      Saves 1 byte. This optimisation is already performed by the xc80 
      compiler and is therefore commented out in xopt. (*)



  2.5) Expand ccgint to DE


          CALL ccgint                     LD E,(HL)
          EX DE,HL                        INC HL
          LD HL,<anything>                LD D,(HL)
                                          LD HL,<anything>


      The run-time routine ccgint fetches the integer pointed to by HL and 
      puts it in HL.  If a call to ccgint if followed by a swap and load 
      to HL it is equivalent to loading the integer pointed to by HL 
      straight into DE.  Saves 1 byte.



  2.6) Expand ccgint


          CALL ccgint                     LD A,(HL)
                                          INC HL
                                          LD H,(HL)
                                          LD L,A


      The run-time routine ccgint on its own can be expanded to the above 
      in-line code.  Uses 1 extra byte.



  2.7) Expand ccpint

          CALL ccpint			POP DE	(*)
					LD A,L
					LD (DE),A
					INC DE
					LD A,H
					LD (DE),A


      The run-time routine ccpint stores the integer in HL at the address 
      in DE.  This can be expanded to in-line code. Uses 3 extra bytes.
      Xc80 requires the integer to be on the stack. This is now catered 
      for. (*)


  2.8) Expand ccgchar to DE


          CALL ccgchar                    LD A,(HL)
          EX DE,HL                        LD E,A
          LD HL,<anything>                RLCA
                                          SBC A,A
                                          LD D,A
                                          LD HL,<anything>


      The run-time routine ccgchar fetches and sign extends into HL a 
      character from the address pointed to by HL.  If a call to ccgchar 
      is follwed by a swap and load to HL it is equivalent to a load 
      directly to DE.  Uses 1 extra byte.



  2.9) Expand ccgchar


          CALL ccgchar                    LD A,(HL)
                                          LD L,A
                                          RLCA
                                          SBC A,A
                                          LD H,A


      The run-time routine ccgchar on its own can be expanded to in-line 
      code.  Uses 2 extra bytes.



  3.1) LD HL; EX: LD HL  ->  LD DE; LD HL


          LD HL,<thing>                   LD DE,<thing>
          EX DE,HL                        LD HL,<thing2>
          LD HL,<thing2>


      This another case where the compiler loads things into DE through 
      HL.  It's quicker to load directly into DE, unless <thing> is an 
      explicit memory address.  Saves 1 byte.



  3.2) JZ around unconditional jump


          JP Z,<where>                    JP NZ,<else>
          JP <else>                where:
   where:


      A conditional jump around an unconditional jump is the same as a 
      jump to the destination of the unconditional jump, but with the 
      condition reversed.  (The corresponding case for JNZ does not seem 
      to occur in Small C output and is not tested for.)  Saves 3 bytes.



  3.3) Store followed by load


          LD <x>,<y>                      LD <x>,<y>
          LD <y>,<x>


      After storing <y> in <x> there is no need to load <y> from <x>.  The 
      number of bytes saved depends on the particular LD instructions.  It 
      is either one or three.  For accounting purposes the optimiser 
      program assumes a saving of 2 bytes.

 case where the compil