--ZDIS  Z-80/8080  DISASSEMBLER--

ORIGINAL AUTHORS: B.W. Lee, and Timothy Mark Burke.
DATE:   May, 1979 and October, 1979.
EDITED ENLARGED AND AMENDED:
Chris Maxfield. GW3HAI.
DATE:   Sept, 1982.


The program  will  disassemble  any  Z-80  or  8080  object
program and reconstruct a ZILOG/MOSTEK or TDL/8080 assembly
 source file on  the  console  or  disk.  The  object  file
resides  in  memory  at  any  location  up  to the starting
address of the disassembler. COM files may be loaded at any
time  and  utilities are provided to manipulate and examine
loaded files. Disassembly may be effected in  multi-segment
passes,  with  each  segment  starting  at any location and
ending at any location within the program. The  latter  may
or  may  not  be  the  execution  locations  of  the object
program. ZDIS needs a Z80 to run.

The  source  file  for ZDIS can be assembled by Z80ASMUK or
almost any other ZILOG/MOSTEK assembler.

The following commands are available when the  disassembler
is in the command mode:-

 	   ---ALL PARAMETERS ARE IN HEX ---
C	
	Close source file.  Use  this  command  when  write
	errors  occur,  or  end  of  medium,  or instead of
	option j.
	
Daaaa,bbbb	
	Disassemble memory  from start address aaaa to  end
	address bbbb
	
E	
	Exit to DDT. Before this command is used it is VERY
	IMPORTANT that DDT or ZSID is co-resident in memory
	with ZDIS. See Note 1.
	
Haaaa,bbbb	
	Hex math.  The sum and difference will be displayed.

Maaaa,bbbb,cccc
	Move memory starting at aaaa and ending  at  bbbb
	to address cccc.
	
Oa,b,c,...	
	Set runtime options as described below. All options 
	are reset with this command and selectively set.
	
Pnn	
	Sets the number (in Hex) of lines per Page.  Paging
	may be switched off with P0, or even just P, and is
	automatically suspended  while  option  c  is  set.
	Press  any  key  except  'full stop' to display the
	next page. (The space bar is convenient). Use 'full
	stop'  to  abort  the  listing  and  return  to the
	command mode. The paging does  not  appear  in  any
	Source file generated.
	
Q	
	Quit session and  return  to  CPM.  The  number  of
	current symbol table entries is displayed.
	
Rdrive:file	
	Read a binary file into memory. All files must have
	a  'COM'  extension.  Files  are  loaded  at  start
	address 100H and the length of  the  file  will  be
	displayed at the console.
	
Saaaa,bbbb	
	Show memory in HEX (Similar to DDT Dump).
	
Taaaa,bbbb	
	Type memory in ASCII.
	
Xaaaa,bbbb[,E or C]	
	Generate Equates and/or Cross  Reference  table  of
	all  labels.  The  X command will not work unless a
	symbol table has already been  built.  Without  the
	optional  parameter [E or C] both Equates and Cross
	Reference table will be generated. E will  generate
	Equates only. C will generate Cross Reference only.
	X without any parameters will generate  a  list  of
	Equates  of all symbols in the table and is a handy
	way of getting a sorted symbol list. See Note 2 for
	further details.
	
 All line   editing   features   of   CPM are available  in
the command  mode except Control-C. DO NOT USE CONTROL-C TO
RETURN TO CPM.

	
RUBOUT	delete and echo the last character typed
	
ctl-U	delete entire line
	
ctl-X	(same as ctl-U)
	
ctl-R	retype current line
	
ctl-E	physical end of line
	
ctl-S	stop the console output temporarily


		     RUN TIME OPTIONS

 For each segment/pass, run-time options may  be  specified 
as follows:-

 ALL OPTIONS ARE SELECTED WITH THE 'O' COMMAND. ALL DESIRED
OPTIONS  MUST BE SELECTED EACH TIME THE 'O' COMMAND IS USED
AS THE COMMAND FIRST RESETS ALL OPTIONS PREVIOUSLY SET.

	[a] Use the symbol table for the  label  field  and
	address  field  (see option g) This option must not
	be set when building the symbol table  because  the
	table  cannot be simultaneously built and used. 

	 [b] Do not initialize the  symbol  table  nor  the
	disk  source file. Use this option without option a
	to append entries to the  symbol  table  and,  with
	options a and h, to add new lines to the disk file.

	[c] Build symbol table using the Lxxxx  format  for
	extended Reference instructions. Unless option b is
	set,  this  option  initializes  the  symbol  table
	first.  Paging  is temporarily suspended while this
	option is selected.

	[d] Generate labels Lxxxx instead  of  the  default
	HEX values xxxxH.

	[e] Generate ASCII characters in  quotes  depending
	on  option  f.  If  option f is true, all printable
	ASCII characters will be placed in quotes following
	the DEFB or DB pseudo opcode. If option f is false,
	all two operand  instructions  with  data  will  be
	followed as a comment by the quoted ASCII character
	corresponding to the data.

	[f] Generate DEFB or DB pseudo opcodes  instead  of
	default  assembly  code. Use this option for proper
	disassembly of segments consisting  of  tables  and
	ASCII strings.

	[g] Normally the operands of LD Rpair,nnnn  or  LXI
	instructions  are  treated as addresses and used to
	generate labels, use this option to  override  this
	default and treat the operands as two byte data.

	[h] Write/Build a reconstructed SOURCE FILE on disk
	and  in  a format ready for re-assembly by Z80ASMUK
	or ASM, or (with minor editing), by the  TDL  MACRO
	RELOCATING  ASSEMBLER.  If  the source file is new,
	you will be prompted  for  the  filename.  However,
	ZDIS  will  supply  the  ZSM or ASM extension auto-
	matically. If it is intended to append  entries  to
	the  source  file  but the b option has been erron-
	eously omitted then reply to  the  filename  prompt
	with  a  'new-line'  to return to the command mode.
	Option h also provides an ORG  0100H  psuedo-op  at
	the start of the source file.

	[i] Generate  TDL/8080  mnemonics  instead  of  the
	default ZILOG/MOSTEK ones.

	[j] Close the source file at the normal termination
	of this segment/pass.

	[k] Suppress console output. Use this option during
	symbol  table building passes to expedite disassem-
	bly. 


Note 1

Providing the memory size is more than 20K, DDT may be made
to  co-reside with ZDIS. This has the advantage that all of
DDT's commands are available, as well as those belonging to
ZDIS,  by Exiting from ZDIS with the E command. However, it
is not essential that this arrangement is  used,  and  ZDIS
will  work  on  its own. DO NOT USE THE E COMMAND IF DDT IS
NOT CO-RESIDENT as this will have unpredictable results and
almost certainly cause a system 'crash'.

DDT may be made to co-reside  with  ZDIS  at  start  up  by
typeing  DDT  ZDIS.COM and then G100, or alternatively, DDT
ZDIS.HEX and Gxxxx where xxxx is the address chosen for the
start  of ZDIS at assembly. (See the implementation notes).
On  exit  from  ZDIS  with the E command, DDT responds with
the  address xxxx minus 1, and this should be noted (if not
already known) for future use.

Note 2

The X command is used to generate  Equates  and/or  a Cross
Reference  table. The  operands should be the start and end
of the program including data areas, but  it  is  sometimes
useful  to  give  addresses  of just a section to find what
labels are used therein with the Cross Reference generator.
The X command sorts the symbol table first before using it,
but this does not affect its  subsequent  use  with  the  D
command.  However, this may take up to half a minute, so be
patient !   If  an  illegal  op-code  is  found  the  Cross
Reference  generator  gives  a  *DATA AREA WARNING at xxxx*
message, and because the disassembler will now  be  out  of
step  it  aborts at the end of the pass to permit the range
of the pass to be changed. Usually  it  will  be  a  faulty
ED,FD or DD prefix opcode and so a very rare occourrence.

The Cross Reference list has semicolons  at  the  start  of
each  line,  so that it may be appended to a source file on
disk, using the appropriate disassembler options.


Note 3

A blank comment (;) line is  inserted  automatically  after
all  unconditional  changes of address. This is intended to
show  that  what  follows  is  a  new  routine  and  not  a
continuation  of  the  old.  A  comment  would  normally be
appropriate at this point  anyway,  and  the  automatically
generated  one  can  serve  as  a reminder when editing the
source file afterwards. If a  comment  is  not  immediately
followed  by  a  label,  there is a strong possibility that
what follows is either data or is not  used.  However  this
should  be  treated  with  caution  as  some  jumps  do not
generate labels i.e. JP   (HL)     JP   (IX) etc.

A comment is not generated after a conditional jump or CALL
or  RET,  so (for instance), RET NZ followed later by RET Z
will not cause the break it logically should. The complica-
tion  necessary to overcome this limitation would be out of
all proportion to the benefit it would give.

If, after all, you find this feature irritating, it may  be
removed  at assembly by inserting a RET at the start of the
REM: subroutine.	

EXAMPLE OF USING ZDIS :-

1.
Invoke ZDIS. Either by typing ZDIS or DDT ZDIS.COM  or  DDT
ZDIS.HEX.  If using the second method type G100 when DDT is
ready. If using the third method type Gxxxx where  xxxx  is
the address chosen for PRLOC: when ZDIS was assembled.

Whatever way ZDIS is loaded and  run,  it  will  enter  the
command mode and prompt you for a command.

2.
Load the file to be disassembled.  Use  the  R  command  by
typing RA:FILENAME newline. (A .COM extension is not needed
as this is supplied by ZDIS). ZDIS will reply with:-

SECTORS READ = xxxx

NEXT ADDRESS = xxxx

3.
Find the data  areas.  Inspect  the  program  to  find  the
location  of  data  areas  and ASCII strings by using the T
command.

i.e. T100,700

Note the start and end addresses of  any  strings  seen  so
that  they can be disassembled as data areas. The S command
or a  crude  labelless  disassembly  using  the  D  command
without  any  options set may be helpful in finding the non
ASCII data.


4.
Build a symbol table. Select option C by typing OC

ZDIS will reply with:-

OPTIONS SELECTED = C

Disassemble using the D command.

Type Daaaa,bbbb

where aaaa and bbbb are start and end of the program.

If a very rough disassembly is all  that  is  needed,  then
data  areas can be included when building the symbol table,
but it is  then  important  to  bear  in  mind  the  strong
possibility  that 'mystery labels' will be generated. ASCII
space (20 Hex),is particularly troublesome as it is  inter-
preted as JR NZ,DISP. If a 'proper' disassembly is required
and data areas are present, then the symbol table will have
to  be  built  in  sections  using the D command (with only
option C set for the first section, but with options B  and
C set for all subsequent sections) thus:-

Daaaa,bbbb  (Option C set)

Dcccc,dddd  (Options C and B set)

Deeee,ffff  (Options C and B set)

etc

(Note: Option B prevents the symbol table being initialised
each time the D command is used)

Where bbbb to cccc and dddd to eeee are data areas.

5.
Disassemble. Having established where the data  areas  are,
and  built  a  symbol  table,  a  full  disassembly  can be
attempted. Use option A for this.

Type OA

ZDIS will reply with:-

OPTIONS SELECTED = A

If a TDL/8080 disassembly is required, the options selected
should include I so type OA,I

Having set the options,  you  may  disassemble  the  opcode
areas of the program by typing:-

Daaaa,bbbb

Data areas can be disassembled using option F and  possibly
E.

Type OA,F,E,I (the I for  TDL/8080)  and  then  use  the  D
command.

Type Ddddd,eeee

6.
Build a source file on disk:-

Having decided where the data areas are, and built a symbol
table,  a  source file may be constucted. There is room for
'self expression' in this work, and the order  given  below
is only a guide.

Start with a block of Equates (it would be quite  in  order
to end with these !).

Select the disk file opening options thus:-

OA,H    (possibly also I)

OPTIONS SELECTED = AH

Type Xaaaa,bbbb,E

Where aaaa is the beginning of the program, and bbbb is the
end,  including  data areas. Normaly aaaa is 0100H and bbbb
the NEXT ADDRESS value given when the file is loaded. The E
is for Equates only.

ZDIS will ask for an output  file  name.  Give  it  one  by
typing  FILENAME  without  any  extension (The .ZSM or .ASM
extension is supplied by ZDIS).

There will then be a short pause while the symbol table  is
sorted,  followed  by a stream of Equates preceeded (as the
file has just been opened) by the ORG 0100H pseudo-op.

It will usually be desired to disassemble the data and  non
data  areas sequentially, as found in the original program,
in ascending order. Use options A,B,H (and possibly I)  for
non  data areas and  options  A,B,F (and possibly E),H (and
possibly I) for data areas.

Type OA,B,F,H

OPTIONS SELECTED =ABFH

Then Daaaa,bbbb

Where aaaa and bbbb are the starting and  ending  addresses
of the first section.

If at this point you are prompted for a file title, it is a
sure  sign  you  have forgotten to set option B. To proceed
will erase the contents of the file you have  just  created
and open a fresh one. To abort back to the command mode, do
not give a file name but just press  'new  line'.  You  may
then  issue  the  correct  set  of  options  and start that
section again.

Having successfully disassembled the first section,  change
the  options  and  disassemble the next as described above.
Continue in this way until the last section is reached when
option J should be included to close the file at the end of
this pass.

Let us assume it is decided to  make  the  last  section  a
cross Reference listing.

Set the options first.

Type OA,B,H,J

Then Xaaaa,bbbb,C

The procedure  will be as described for the Equates, except
that  the  table takes longer to construct and the letter C
means build a Cross Reference table only. As  option  J  is
set  the  section will terminate by adding an END psuedo-op
and closing the disk file. If option J has  been  forgotten
the  C  command  will have the same effect. Nothing further
can be added to the disk file now.

7.
Exit from ZDIS by typing Q for Quit.

It will reply with:-

NUMBER OF ENTRIES IN SYMBOL TABLE = xxxx

and return you to CPM.

You may then edit your source file, putting more meaningful
labels and comments into it before re-assembly. Dont forget
to edit the ORG pseudo-op if the built-in value of 0100H is
not what is required. Furthermore, if you intend to use the
TDL RELOCATING MACRO ASSEMBLER to reassemble the file, then
you will need to change the following pseudo-ops:-
	ORG becomes .LOC
	EQU    "      =
	DB     "    .BYTE
	END    "    .END

	       ----IMPLEMENTATION NOTES----   
The most difficult decision to make, is where  ZDIS  should
reside in memory. If it is set too low, there won't be room
for your COM files, and if too high, you will  run  out  of
symbol  table.  The  length  of the symbol table is related
loosely to the length of the COM file, and experience shows
that,  if  the  COM  file takes 70% of the free memory, the
symbol  table  will  take  the  remaining  30%.  The  exact
proportions depend  upon  many factors, such as programming
style, and the purpose the program serves,  and  the  70/30
ratio  is  therefore  only  a  rule of thumb. Anyway, 70/30
seems about right in practice, and I suggest it is  adopted
where memory is tight.

Calculating in decimal, a simple formula can be worked out.

Mem size    = Memory * 1024

Free Memory =(( Mem size - CPM)- Page 1)-ZDIS

	    = Mem size - 14592 for CPM 1.4

	    = Mem size - 15872 for CPM 2.2

Where  CPM = 5888 for CPM 1.4 
or     CPM = 7168 for CPM 2.2
and Page 1 = 256 
      ZDIS = 8448

If Free memory is very much greater  than  2048  then, ZDIS
can co-reside with DDT, and 2048 should be deducted.

From the above we have:-

PRLOC:   = INT(Free mem * 0.7 / 256) * 256 + Page 1 
Rounded to the nearest Hex page boundary.

SYMNUM:  = INT( Free mem * 0.3)

As each symbol is 7 Bytes long 
SYCOUN: = INT (SYMNUM / 7)


                            CPM 1.4 
    ___________________________________________________
    ! Memory   !  20K  !  24K  !  32K  !  48K  !  64K !
    ---------------------------------------------------
    PRLOC:       4352    5632    11520   22784   34304
    SYMNUM:      1766    2380     4838    9753   14668
    SYCOUN:       252     340      691    1393    2095

                            CPM 2.2
    ___________________________________________________
    ! Memory   !  20K  !  24K  !  32K  !  48K  !  64K !
    ---------------------------------------------------
    PRLOC:       3328    4864    10496   22016   33536
    SYMNUM:      1382    1996     4454    9369   14284
    SYCOUN:       197     285      636    1338    2040

  Even though more memory than 32K  is  present,  there  is
probably little point in departing from the 32K figures, as
these will handle COM files up to 10.5K long. A COM file of
this length will generate 63K of source, and it is arguable
that it would be so difficult to find one's  way  around  a
file  of  this  length, without meaningful labels and comm_
ents, that it is probably not  worth  having.  Furthermore,
the  Editor  would  generate  a  back  up  file of the same
length, and it is possible  that  disk  space  might  be  a
problem in some systems.

OTHER EQUATES TO ADJUST:-

LNNUM
Sets the default number of lines  of listing  displayed  by
the P command.

NUMDBS
Sets the number of DEFB's in each  row  when  in  the  DEFB
mode.  Four seems a good value even if the VDU will display
more. Remember that a PRN file generated by  the  assembler
will  take  up  at  least 24 characters at the start of the
line before the DEFB pseudo op and the row of DEFB's.

REFSLN
Sets the number of Cross reference addresses (not  counting
the label), in each row, when the X command is in use.

Line 276
The number of Bytes per line displayed  by  the  S  command
can  be  either  8  or  16. Change the AND   07H in routine
DDD1: (Line 276) for AND    0FH if 16 are required.

LOADING ZDIS:-

Having  assembled ZDIS,  possibly using Z80ASMUK,  the  Hex
file  can be used to make a COM file by means of DDT.(Don't
use LOAD for this operation).

Type DDT ZDIS.HEX

and make a note of the NEXT value supplied by DDT.

You will need to know the starting address of the  program.
There  are  several  ways  of  finding  this out. One is to
convert PRLOC: into Hex, another to subtract the length  of
the program from the NEXT value, but perhaps the easiest is
to use DDT's L command to inspect the loader. A jump to the
start address will be found at 010BH.

Now move the program down to where the loader wants it.

Mxxxx,NEXT,01FF

Where xxxx is the starting address minus 1.

If you have 20K or less memory,  immobilize  the  'Exit  to
DDT' command, by changing the byte at 01FF from FF to 00.

Now exit to CPM with G0, and then

SAVE 34 ZDIS.COM

FURTHER READING AND HISTORY:-

1.
The original was published in Dr. Dobb's journal,  February
1977.'An 8080 Disassembler with exquisite documentation' by
Ward Christensen.

2.
An extended version  generating  TDL  mnemonics,  was  also
puplished  in  Dr.  Dobb's  journal,  May 1979. 'A Z-80/ZAP
DISASM' by B.W. Lee.

3.
The Z-80/ZAP DISASM, was adapted for CPM by Tim Burke. This
appeared in Vol 42 of the US User Group's library September
1979. Under the titles DIS.ASM and DIS.DOC.

4.
Transcribed for ZILOG/MOSTEK mnemonics, enlarged, and  sev-
eral  bugs  removed,  by  Chris  Maxfield. September, 1982.
London.



	 for ZILOG/MOSTEK mne