*** UKSTOIC2.DOC   BY K.C.GOLDIE-MORRISON  6 MAR 1983 *************************


STOIC  (STACK ORIENTED INTERACTIVE COMPILER)

        THIS DISK IS SUPPLIED TO THE CP/M USERS GROUP (UK)  BY COURTESY OF THE
U.S. PUBLIC-DOMAIN RELEASE OF THE STOIC LANGUAGE BY :-

         MASSACHUSETTS INSTITUTE OF TECHNOLOGY AND HARVARD UNIVERSITY,
         BIOMEDICAL ENGINEERING CENTER 1977.  ALL RIGHTS RESERVED. 

THE ORIGINAL STOIC.DOC FROM THE US USERS GROUP VOL.23 HAS BEEN CORRECTED AND
UPDATED TO COVER ALL THE CP/M AMENDMENTS AND ADDITIONS.

	STOIC IS A GENERAL PURPOSE INTERACTIVE PROGRAM
WHICH INCORPORATES THE CAPABILITIES OF A COMPILER, EDITOR
ASSEMBLER, DEBUGGER, LOADER, AND OPERATING SYSTEM WITHIN
A SINGLE CONSISTENT ARCHITECTURE.  IT IS MEMORY-EFFICIENT
WHILE RETAINING HIGH RUNNING SPEEDS.  IN ADDITION, THE
LANGUAGE IS EXTREMELY FLEXIBLE, PERMITTING THE USER TO
DEVELOP A WORKING VOCABULARY OF SUBROUTINES TAILORED TO
HIS SPECIFIC APPLICATION.

	THE SINGLE MOST PROMINENT FEATURE OF STOIC IS ITS
PRINCIPAL DATA STRUCTURE, CALLED THE DICTIONARY.  THE
DICTIONARY IS AN ORDERED LIST OF ENTRIES CALLED WORDS.
ASSOSCIATED WITH THE DICTIONARY ENTRY FOR EACH WORD IS A
NAME; A LEGAL NAME FOR A WORD IS ANY STRING OF UP TO 127
ASCII CHARACTERS.  PUNCTUATION, NUMERICS, AND MOST OTHER
SPECIAL CHARACTERS MAY BE FREELY USED WITHIN A NAME.  TWO
NAMES ARE EQUIVALENT IF AND ONLY IF THEIR FIRST FIVE CHARACTERS
ARE THE SAME AND THEY HAVE EXACTLY THE SAME LENGTH.  ILLEGAL
CHARACTERS WITHIN A NAME ARE:

	SPACE
	TAB
	CARRIAGE RETURN
	FORM FEED
	LINE FEED
	RUBOUT
	NULL

EXAMPLES:

ABCDE   IS NOT EQUIVALENT TO  ABCDEF
(HEAD1) IS EQUIVALENT TO      (HEAD2)

	A LITERAL IS A SEQUENCE OF CHARACTERS WHICH DESCRIBES
A CONSTANT.  THE BASIC STOIC SUPPORTS TWO TYPES OF LITERAL;
16-BIT INTEGER AND STRING.  THE LANGUAGE MAY BE EXTENDED TO
INCLUDE OTHER DATA TYPES SUCH AS FLOATING POINT OR DOUBLE
PRECISION INTEGER.

	AN INTEGER LITERAL IS A SEQUENCE OF DIGITS
OPTIONALLY PRECEDED BY A PLUS OR MINUS SIGN.  ALL DIGITS
MUST BE LESS THAN THE CURRENT RADIX.  NO SPACES MAY BE
EMBEDDED WITHIN THE LITERAL.  INTEGER LITERAL MUST BE IN
THE RANGE OF -32768 TO 32767 IF SIGNED OR 0 TO 65535 IF
UNSIGNED.

EXAMPLES:

-1234	IS A LEGAL LITERAL
+-100	IS NOT A LEGAL LITERAL
-AFC0	IS A LEGAL LITERAL IF RADIX IS HEXADECIMAL


	STRING LITERALS MAY TAKE ONE OF THREE FORMS:
1) A STRING ENCLOSED IN DOUBLE QUOTES:

 "STRING"

2) A STRING ENCLOSED IN BACKSLASHES:

 \STRING\

3) A STRING PRECEDED BY SINGLE QUOTE AND TERMINATED BY SPACE OR TAB:

 'STRING

IN ANY OF THE ABOVE TYPES OF STRING LITERAL, THE END OF THE
LINE (RETURN OR FORM FEED) MAY SERVE AS A TERMINATOR.  SPECIAL
CHARACTERS SUCH AS RETURN, RUBOUT, ETC. MAY BE INCLUDED IN A
STRING LITERAL BY ENCLOSING THE CORRESPONDING OCTAL ASCII CODE
BETWEEN TWO AMPERSANDS (&).

EXAMPLES:

"THIS IS A STRING LITERAL"
\THIS LITERAL CONTAINS A RETURN &15&\
'&177&&15&


	STOIC SYNTAX IS QUITE SIMPLE.  A LEGAL COMMAND
LINE CONSISTS OF A SEQUENCE OF LITERALS AND/OR NAMES OF WORDS
SEPARATED BY SPACES OR TABS, AND TERMINATED BY CARRIAGE
RETURN OR FORM FEED.

	PROGRAMMING IN STOIC CONSISTS PRIMARILY OF
DEFINING A SET OF NEW WORDS BASED ON WORDS WHICH HAVE
ALREADY BEEN DEFINED.  AN INITIAL VOCABULARY OF ABOUT ONE
HUNDRED WORDS CALLED THE KERNEL ENABLES THE USER TO GET
STARTED.

	THE PRINCIPAL VEHICLE FOR COMMUNICATION BETWEEN
WORDS IS THE PARAMETER STACK, FREQUENTLY CALLED "THE
STACK".   TYPICALLY, THE PARAMETERS UPON WHICH A WORD WILL
OPERATE ARE PUSHED ON THE STACK, THE WORD POPS ITS
PARAMETERS FROM THE STACK AND PUSHES ITS RESULTS ON THE
STACK.  COMMUNICATION THROUGH VARIABLES IN FIXED
LOCATIONS IS ALSO USED.

	STOIC USES REVERSE POLISH NOTATION FOR ALL
OPERATIONS.  THIS MEANS THAT ALL OPERANDS PRECEDE THEIR
OPERATORS;  PARENTHESES ARE NEVER NECESSARY.

EXAMPLES:

1 1 + 2 *   IN ALGEBRAIC NOTATION IS   (1+1)*2
1 2 3 * -   IN ALGEBRAIC NOTATION IS   1-(2*3)

	UNLIKE MOST OTHER HIGER LEVEL LANGUAGES, STOIC
ENABLES THE USER TO MANIPULATE ADDRESSES AS WELL AS DATA.
IT IS VERY IMPORTANT HOWEVER FOR THE USER TO REMAIN AWARE
OF THE DISTINCTION BETWEEN AN ADDRESS AND ITS CONTENTS.
	THERE ARE THREE COMMON TYPES OF WORDS WHICH PUSH
NUMBERS ON THE STACK; LITERALS, CONSTANTS, AND VARIABLES.
A REFERENCE TO A LITERAL OR A CONSTANT CAUSES ITS VALUE
TO BE PUSHED ON THE STACK.  A REFERENCE TO A VARIABLE
CAUSES ITS ADDRESS TO BE PUSHED ON THE STACK.  THE TWO
OPERATORS "@" AND "!" ARE USED TO OBTAIN AND MODIFY THE
VALUE OF A VARIABLE.  THEY ARE DEFINED AS FOLLOWS:

	@	REPLACE THE ADDRESS ON THE TOP OF THE
		STACK BY THE CONTENTS OF THAT ADDRESS.
		THIS WORD IS USED TO LOAD THE CONTENTS
		OF A MEMORY LOCATION ONTO THE STACK.

	!	STORE AT THE ADDRESS ON THE TOP OF THE
		STACK THE NUMBER NEXT TO TOP OF THE
		STACK.  BOTH NUMBERS ARE REMOVED FROM
		THE STACK.

EXAMPLES:

IN THE FOLLOWING EXAMPLES, X, Y, AND Z ARE VARIABLES,
WHILE A, B, AND C ARE CONSTANTS.

100 X !		SET VALUE OF X TO 100.

X 100 !		STORE THE ADDRESS OF X IN LOCATION 100
		(UNDER NORMAL CIRCUMSTANCES, THIS WOULD
		BE A VERY SERIOUS ERROR).

X @ Y !		SET THE VALUE OF Y TO THE VALUE OF X

X Y !		SET THE VALUE OF Y TO THE ADDRESS OF X

X @ Y @ + Z !	ADD THE VALUES OF X AND Y AND STORE THE
		RESULT IN Z.

X A + Y !	STORE (ADDRESS OF X)+A IN Y.

X A B + + @ Y !	SET VALUE OF Y TO THE CONTENTS OF
		LOCATION X+A+B.


	STOIC PROVIDES THE USER WITH AN UNUSUALLY LARGE
NUMBER OF FIXED POINT OPERATORS FROM WHICH THE FOLLOWING
MORE COMMON EXAMLES HAVE BEEN EXTRACTED.  UNLESS OTHERWISE
SPECIFIED, ALL NUMBERS ARE 16-BIT INTEGERS.

UNARY OPERATORS

THE FOLLOWING OPERATORS REPLACE THE TOP OF THE STACK
WITH THEIR RESULT.  THE NUMBER ON THE TOP OF THE
STACK IS CALLED "A".

	MINUS	-A

	ABS	ABSOLUTE VALUE OF A

	NOT	LOGICAL COMPLEMENT OF A

	2*	A*2

	2/	A/2 (SIGNED)

	U2/	A/2 (UNSIGNED)

	1+	A+1

	1-	A-1

	EQZ	-1 IF A EQUAL TO 0
		 0 OTHERWISE

	NEZ	-1 IF A NOT EQUAL TO 0
		 0 OTHERWISE

	LTZ	-1 IF A LESS THAN 0
		 0 OTHERWISE

	LEZ	-1 IF A LESS OR EQUAL TO 0
		 0 OTHERWISE

	GEZ	-1 IF A GREATER OR EQUAL TO 0
		 0 OTHERWISE

	GTZ	-1 IF A GREATER THAN 0
		 0 OTHERWISE

BINARY OPERATORS

THE FOLLOWING OPERATORS REPLACE THE TOP TWO NUMBERS ON
THE STACK WITH THEIR RESULT.  THE NUMBER ON THE TOP OF
THE STACK IS CALLED "A", THE NEXT TO TOP IS CALLED "B".

	+	B+A

	-	B-A

	*	B*A

	/	B/A

	MAX	MAXIMUM (B,A) (SIGNED)

	MIN	MINIMUM (B,A) (SIGNED)

	AND	LOGICAL AND OF B,A

	OR	LOGICAL OR OF B,A

	XOR	LOGICAL EXCLUSIVE OR OF B,A

	EQ	-1 IF B EQUAL TO A
		 0 OTHERWISE

	NE	-1 IF B NOT EQUAL TO A
		 0 OTHERWISE

	LT	-1 IF B LESS THAN A
		 0 OTHERWISE

	LE	-1 IF B LESS OR EQUAL TO A
		 0 OTHERWISE

	GE	-1 IF B GREATER OR EQUAL TO A
		 0 OTHERWISE

	GT	-1 IF B GREATER THAN A
		 0 OTHERWISE


	A NUMBER OF OPERATORS ARE ALSO PROVIDED WHOSE
SOLE FUNCTION IS TO REORGANIZE THE ELEMENTS OF THE STACK:

		STACK	STACK
	NAME	BEFORE	AFTER	DESCRIPTION

	DUP	A	A	DUPLICATES TOP OF STACK
			A

	OVER	A	B	DUPLICATES TOP - 1
		B	A
			B

	2OVER	A	C	DUPLICATES TOP - 2
		B	A
		C	B
			C

	3OVER	A	D	DUPLICATES TOP - 3
		B	A
		C	B
		D	C
			D

	UNDER	A	A	STORES TOP AT TOP - 1
		B

	2UNDER	A	B	STORES TOP AT TOP - 2
		B	A
		C

	3UNDER	A	B	STORES TOP AT TOP - 3
		B	C
		C	A
		D

	DROP	A	B	DISCARDS TOP
		B

	2DROP	A	C	DISCARDS TOP 2 STACK ENTRIES
		B
		C

	3DROP	A	D	DISCARDS TOP 3 STACK ENTRIES
		B
		C
		D

	SWAP	A	B	EXCHANGES TOP AND TOP - 1
		B	A

	2SWAP	A	A	EXCHANGES TOP - 1 AND TOP - 2
		B	C
		C	B

	FLIP	A	C	EXCHANGES TOP AND TOP - 2
		B	B
		C	A

	+ROT	A	B	ROLL TOP 3 STACK ENTRIES UP
		B	C
		C	A

	-ROT	A	C	ROLL TOP 3 STACK ENTRIES DOWN
		B	A
		C	B

	DDUP	A	A	DUPLICATE THE TOP 2 STACK ENTRIES
		B	B
			A
			B

I/O WORDS
"N" IS THE NUMBER ON THE TOP OF THE STACK.

	COLUMN	VARIABLE CONTAINING THE CURRENT COLUMN NUMBER

	TYO	OUTPUT THE ASCII CHARACTER IN THE RIGHTMOST
		8 BITS OF N.  COLUMN IS INCREMENTED UNLESS THE
		CHARACTER OUTPUT IS A RETURN IN WHICH CASE IT
		IS ZEROED.

	CR	OUTPUT A RETURN FOLLOWED BY A LINE FEED.
		COLUMN IS ZEROED.

	IFCR	OUTPUTS A RETURN, LINE FEED IF COLUMN IS NON-ZERO.

	SPACE	OUTPUT A SPACE.

	SPACES	OUTPUT N SPACES.

	TAB	TAB TO COLUMN N.  IF ALREADY AT OR BEYOND COLUMN
		N, NOTHING IS OUTPUT.

	TYI	INPUT A CHARACTER.AND PLACE IT'S ASCII NUMBER ON STACK.

	=	OUTPUT N IN THE CURRENT RADIX FOLLOWED BY SPACE.

	?	OUTPUT THE CONTENTS OF THE LOCATION
		ADDRESSED BY N FOLLOWED BY SPACE.

	TYPE	OUTPUT N CHARACTERS STARTING AT BYTE
		POINTER AT TOP - 1.

        MSG     TYPE OUT THE STRING WHOSE POINTER IS AT TOP.


WORDS WHICH CHANGE THE CURRENT RADIX

	OCTAL	SET CURRENT RADIX TO OCTAL

	DECIMAL	SET CURRENT RADIX TO DECIMAL

	HEX	SET CURRENT RADIX TO HEXADECIMAL


WORDS USED TO REFERENCE MEMORY LOCATIONS

A REPRESENTS THE TOP OF THE STACK, B REPRESENTS
THE NEXT TO TOP.

	<-	STORE A AT LOCATION B (SAME AS "!" EXCEPT
		ARGUMENTS ARE REVERSED).

	0<-	STORE 0 AT LOCATION A

	-1<-	STORE -1 AT LOCATION A

	+!	ADD B TO THE CONTENTS OF LOCATION A

	1+!	INCREMENT LOCATION A

	1-!	DECREMENT LOCATION A

	MOVE	COPY THE CONTENTS OF THE LOCATION ADDRESSED
		BY B TO THE LOCATION ADDRESSED BY A.

	XCHG	EXCHANGE THE CONTENTS OF LOCATIONS A AND B.

	MVBYTES	COPIES BYTES SEQUENTIALLY FROM ONE AREA TO ANOTHER
		BYTE COUNT AT TOP, SOURCE BYTE ADDRESS AT TOP - 2,
		DESTINATION BYTE ADDRESS AT TOP - 1.

EXAMPLES:

0> 1 MINUS =
-1

0> -1 ABS =
1

0> -1 EQZ =
0

0> 0 EQZ =
-1

0> 1 1 + =
2

0> 1 1 1 + + =
3

0> 1 2 3 = = =
3 2 1

0> 1 2 SWAP = =
1 2

0> 1 2 DUP = = =
2 2 1

0> 1 2 1 - EQ =
-1

0> 100 X ! X ?
100

0> -1 5 MAX =
5

0> -1 5 MIN =
-1


COLON DEFINITIONS

	STOIC PROVIDES THE CAPABILITY OF DEFINING A NEW
WORD IN TERMS OF PREVIOUSLY DEFINED WORDS BY MEANS OF
THE COLON DEFINITION.  ITS SYNTAX IS AS FOLLOWS:

'NEWWORD : WORD1 WORD2 ... WORDN ;

	THIS CREATES A NEW DICTIONARY ENTRY CALLED NEWWORD
WHICH, WHEN EXECUTED, WILL IN TURN EXECUTE WORD1, WORD2,
... IN SEQUENCE.  AFTER EXECUTING WORDN, IT WILL RETURN.
EACH OF THE WORDS WORD1, WORD2, ... MUST ALREADY EXIST
AS ENTRIES IN THE DICTIONARY.  IF NOT, A FATAL ERROR
MESSAGE OF THE FOLLOWING FORM WILL BE GENERATED:

UNDEFINED
(NAME OF UNDEFINED WORD)

	A WORD MAY BE REDEFINED AT ANY TIME.  IN THIS
CASE, ALL PRIOR DEFINITIONS WHICH REFERENCED THAT WORD
WILL STILL EXECUTE THE OLD VERSION.  ALL SUBSEQUENT
DEFINITIONS HOWEVER WILL EXECUTE THE MOST RECENTLY
DEFINED VERSION. REDEFINING A WORD WILL GENERATE THE
FOLLOWING WARNING MESSAGE:

REDEFINING (NAME OF WORD)

EXAMPLES:

'AVERAGE : + 2/ ;

	THIS DEFINES THE WORD AVERAGE WHICH COMPUTES
	THE AVERAGE OF THE TOP 2 NUMBERS ON THE STACK.

	0> 2 4 AVERAGE =
	3

'SPACE : 40 TYO ;

	THIS DEFINES THE WORD "SPACE" WHICH TYPES A SPACE.
	(THE ASCII CODE FOR SPACE IS 40 OCTAL).

	IF THE NAME OF A WORD BEING REDEFINED APPEARS
WITHIN THE NEW DEFINITION, ITS OLD MEANING WILL BE USED.
THE PROCEDURE FOR MAKING RECURSIVE CALLS IS DESCRIBED
BELOW UNDER "RECURSION".


ITERATION

	STOIC PROVIDES FIVE MEANS FOR ITERATIVE
EXECUTION OF A SEQUENCE OF WORDS, NAMELY:

N ( ... )

	EXECUTE THE WORDS INCLUDED IN PARENTHESES N TIMES.

BEGIN ... END

	EXECUTE WORDS BETWEEN "BEGIN" AND "END" UNTIL A CONDITION
	IS SATISFIED.

BEGIN ... IF ... REPEAT

	SIMILAR TO BEGIN ... END EXCEPT THE CONDITION
	IS TESTED AT THE BEGINNING OF THE LOOP.

DO ... LOOP

	EXECUTE THE WORDS BETWEEN "DO" AND "LOOP", RUNNING
	AN INDEX FROM A LOWER TO AN UPPER LIMIT, INCREMENTING
	BY 1 EACH TIME.

DO ... N +LOOP

	EXECUTE THE WORDS BETWEEN "DO" AND "+LOOP", RUNNING
	AN INDEX FROM A LOWER TO AN UPPER LIMIT, INCREMENTING
	BY N EACH TIME.

	ITERATIONS MAY BE NESTED SUBJECT TO THE NORMAL
RESTRICTIONS ON OVERLAPPING RANGES, I.E. ANY ITERATION
WHICH IS INITIATED WITHIN THE RANGE OF ANOTHER ITERATION
MUST BE TERMINATED WITHIN THAT SAME RANGE.


( ... )

	A SEQUENCE OF WORDS MAY BE EXECUTED REPETITIVELY
USING THE FOLLOWING SYNTAX:

N ( WORD1 WORD2 ... WORDN )

	THIS CAUSES THE SEQUENCE WORD1, WORD2, ... TO BE
EXECUTED N TIMES WHERE N IS THE NUMBER ON THE TOP OF THE
STACK.  IF N IS ZERO OR NEGATIVE, THE SEQUENCE OF WORDS
IS NOT EXECUTED AT ALL AND CONTROL PASSES TO THE WORD
FOLLOWING THE ")".

EXAMPLE:

'DINGDING : 2 ( DING ) ;

	THIS DEFINITION IS FUNCTIONALLY EQUIVALENT TO:

	'DINGDING : DING DING ;

	IN EITHER CASE, EXECUTING "DINGDING" CAUSES THE
	WORD "DING" TO BE EXECUTED TWICE.

'SPACES : ( SPACE ) ;

	THIS IS A DEFINITION OF THE WORD "SPACES".
	THUS "20 SPACES" CAUSES "SPACE" TO BE EXECUTED
	20 TIMES.

	AN UNSIGNED VERSION OF PARENTHESIS ITERATION IS USED
WHERE THE ITERATION COUNT IS BETWEEN 32767 AND 65535:

	N U( ... )


BEGIN ... END

	THE BEGIN ... END SYNTAX PERMITS THE USER TO EXECUTE
A SEQUENCE OF WORDS AND THEN, DEPENDING ON A COMPUTED
LOGICAL VARIABLE, EITHER LOOP BACK OR CONTINUE ON:

BEGIN WORD1 WORD2 ... WORDN END

	THE SEQUENCE WORD1, WORD2, ... IS EXECUTED ONCE.
WHEN THE "END" IS REACHED, THE TOP OF THE STACK IS
POPPED AND  TESTED.  IF IT IS TRUE (NON-ZERO) THEN
CONTROL PASSES TO THE WORD FOLLOWING "END".  IF IT IS
FALSE (ZERO) CONTROL PASSES BACK TO THE WORD FOLLOWING
"BEGIN".

EXAMPLE:

	'EXAMPLE : BEGIN 1- DUP DUP = EQZ END DROP ;

	THIS DEFINES THE WORD "EXAMPLE" WHICH MIGHT BE
	CALLED AS FOLLOWS:

	0> 5 EXAMPLE
	4 3 2 1 0

	EACH TIME THROUGH THE LOOP, THE TOP OF THE STACK
	(INITIALLY THE NUMBER 5) IS DECREMENTED, PRINTED,
	AND COMPARED TO ZERO.  IF IT IS NOT ZERO, THE
	LOOP IS REPEATED,  WHEN IT BECOMES ZERO, THE LOOP
	TERMINATES.


BEGIN ... IF ... REPEAT

	BEGIN ... IF ... REPEAT IS SIMILAR TO BEGIN ...
END EXCEPT THAT THE TEST IS MADE AT THE BEGINNING OF THE
LOOP RATHER THAN AT THE END.  THE WORDS FROM "BEGIN" TO
"IF" ARE EXECUTED.  IF THE TOP OF THE STACK IS TRUE
(NON-ZERO) THE WORDS BETWEEN "IF" AND "REPEAT" ARE
EXECUTED AND CONTROL THEN PASSES BACK TO THE WORD
FOLLOWING "BEGIN".  IF THE TOP OF THE STACK IS FALSE
(ZERO), CONTROL PASSES TO THE WORD FOLLOWING "REPEAT".

EXAMPLE:

	BEGIN EOF NOT IF READ-RECORD REPEAT

	THIS EXAMPLE MIGHT BE USED TO READ THE CONTENTS
	OF A FILE.  "EOF" RETURNS A -1 IF END OF FILE
	HAS BEEN ENCOUNTERED; A 0 OTHERWISE.  "READ-RECORD"
	READS THE NEXT ENTRY IN THE FILE.  BY TESTING
	FOR EOF AT THE BEGINNING OF THE LOOP, THE
	CASE OF A ZERO-LENGTH FILE IS PROPERLY
	HANDLED.


DO LOOPS

	A DO LOOP FACILITY IS PROVIDED BY STOIC FOR
INDEXING THROUGH A SEQUENCE OF WORDS.  THERE ARE TWO
FORMS OF DO LOOP:

HIGH LOW DO WORD1 WORD2 ... WORDN LOOP

HIGH LOW DO WORD1 WORD2 ... WORDN INCR +LOOP

	THE LIMITS "HIGH" AND "LOW" (THE TOP TWO STACK
ENTRIES) ARE COMPARED.  IF "HIGH" IS LESS THAN OR EQUAL TO
"LOW", CONTROL PASSES TO THE WORD FOLLOWING "LOOP" OR
"+LOOP".  OTHERWISE, THE SEQUENCE WORD1, WORD2, ... IS
EXECUTED.  "LOOP" CAUSES THE LOWER LIMIT ("LOW") TO BE
INCREMENTED BY 1 AND COMPARED TO THE UPPER LIMIT ("HIGH").
IF "LOW" IS EQUAL TO OR GREATER THAN "HIGH", THE LOOP IS
TERMINATED.  OTHERWISE ANOTHER ITERATION IS PERFORMED.
"+LOOP" IS IDENTICAL TO "LOOP" WITH THE EXCEPTION THAT
"LOW" IS INCREMENTED BY THE WORD ON THE TOP OF THE STACK
("INCR").  "INCR" IS NORMALLY A POSITIVE NUMBER.

	WITHIN THE RANGE OF THE LOOP, THE CURRENT VALUE
OF THE LOOP INDEX IS AVAILABLE BY USING THE WORD "I".
IF DO LOOPS ARE NESTED, "I" ALWAYS CONTAINS THE VALUE
OF THE INNERMOST INDEX.  THE NEXT OUTER INDICES ARE
AVAILABLE USING THE WORDS "J" AND "K".  THE WORD "I'"
IS USED TO OBTAIN THE VALUE OF "HIGH"+"LOW"-I-1.  THIS IS
USED TO RUN AN INDEX BACKWARDS FROM "HIGH"-1 TO "LOW".
THE WORDS "J'" AND "K'" ARE SIMILARLY DEFINED.  WHEN
PARENTHESES ARE NESTED WITH "DO" LOOPS, THEY COUNT AS
ONE LEVEL OF INDEXING.  "I" USED WITHIN THE RANGE
OF A PARENTHESIS ITERATION WILL RETURN THE CURRENT VALUE
OF THE ITERATION COUNT (WHICH RUNS FROM ITS INITIAL VALUE
DOWNWARDS TO ONE).

	THE WORD "EXIT", CAUSES THE INNERMOST LOOP IN
WHICH IT IS EMBEDDED TO UNCONDITIONALLY TERMINATE ON THE
NEXT CYCLE, WHETHER A DO LOOP OR A PARENTHESIS LOOP.

EXAMPLES:

	5 0 DO I = LOOP

	THIS CUASES THE NUMBERS FROM 0 TO 4 INCLUSIVE
	TO BE TYPED OUT.

	5 0 DO 5 0 DO J 5 * I + = LOOP CR LOOP

	THIS TYPES OUT THE NUMBERS FROM 0 TO 24
	INCLUSIVE AS 5 LINES OF 5 NUMBERS EACH.

	5 0 DO I' = LOOP

	THIS TYPES OUT THE NUMBERS FROM 4 TO 0
	INCLUSIVE.

	0 21 1 DO I + DUP = 2 +LOOP DROP

	THIS TYPES OUT THE FIRST 10 PERFECT SQUARES
	STARTING WITH 1.

	WHEN USING "I'" (OR "J'" OR "K'") IN CONJUNCTION WITH
"+LOOP", "HIGH" SHOULD BE REPLACED BY "HIGH"-"INCR"+1, IF IT
IS DESIRED TO PRODUCE THE SAME SET OF INDICES AS WITH "I".
FOR EXAMPLE:

	0> 24 0 DO I = 4 +LOOP
	0 4 8 12 16 20

	0> 24 0 DO I' = 4 +LOOP
	23 19 15 11 7 3 1

	0> 24 4 - 1 + 0 DO I' = 4 +LOOP
	20 16 12 8 4 0

	AN UNSIGNED DO LOOP IS USED WHERE THE LIMITS MUST BE
CONSIDERED AS UNSIGNED NUMBERS; E.G. WHERE THE LIMITS ARE BYTE
ADDRESSES IN THE UPPER 32K BYTES OF MEMORY:

	HIGH LOW UDO ... ULOOP
	HIGH LOW UDO ... INCR U+LOOP


CONDITIONALS

	STOIC HAS A POWERFUL IF ... ELSE ... THEN CONSTRUCTION
WHICH ALLOWS COMPLICATED LOGICAL TESTS TO BE PERFORMED.
CONDITIONALS MAY BE NESTED, WITH THE SAME RESTRICTIONS
THAT APPLY TO ITERATIONS.

FOR THE PURPOSES OF THE CONDITIONAL, "TRUE" IS CONSIDERED
TO BE ANY NON-ZERO VALUE; "FALSE" IS ANY ZERO VALUE.

N IF T1 T2 ... TN THEN

	THE TOP OF THE STACK, "N" IS TESTED.

	IF TRUE (NON-ZERO) THE WORDS T1, T2, ... TN ARE
	EXECUTED.

	IF FALSE (ZERO) CONTROL PASSES TO THE WORD
	FOLLOWING "THEN".

N IF T1 T2 ... TN ELSE F1 F2 ... FN THEN

	THE TOP OF THE STACK, "N" IS TESTED.

	IF TRUE (NON-ZERO) THE WORDS T1, T2, ... TN
	ARE EXECUTED; CONTROL THEN PASSES TO THE WORD
	FOLLOWING "THEN".

	IF FALSE (ZERO) CONTROL PASSES TO THE WORD
	FOLLOWING "ELSE".  THE WORDS F1, F2, ... FN ARE
	EXECUTED.

EXAMPLES:

	'ABS : DUP LTZ IF MINUS THEN ;

	THIS DEFINES THE WORD "ABS" WHICH REPLACES THE
	TOP OF THE STACK WITH ITS ABSOLUTE VALUE.

	'MAX : DDUP GT IF DROP ELSE UNDER THEN ;

	THIS DEFINES THE WORD "MAX" WHICH COMPARES THE
	TOP TWO STACK ENTRIES AND LEAVES THE LARGER OF
	THE TWO.


COMMENTS

	THE WORD "%" APPEARING ON A LINE CAUSES THE
REMAINDER OF THAT LINE TO BE IGNORED.  NOTE THAT THE "%",
TO BE RECOGNIZED AS A WORD, MUST BE PRECEDED AND FOLLOWED
BY SPACE OR TAB.

EXAMPLES:

	X @ Y !		% THIS IS A COMMENT
	%THIS IS NOT A COMMENT


USING STOIC FROM THE KEYBOARD

	WHEN TYPING IN A COMMAND FROM THE KEYBOARD,
THE RUBOUT KEY MAY BE USED TO DELETE THE LAST CHARACTER;
TYPING A NULL DELETES THE ENTIRE COMMAND LINE.

	WHEN ACTIVATED, STOIC TYPES A PROMPT MESSAGE
CONSISTING OF THE CURRENT NESTING DEPTH (SEE BELOW)
FOLLOWED BY "> " TO INDICATE THAT IT IS AWAITING KEYBOARD
INPUT.  AT THIS POINT THE OPERATOR TYPES IN A COMMAND LINE.
AS SOON AS RETURN OR FORM FEED IS TYPED, STOIC COMPILES
THE COMMAND LINE AND, IN THE ABSENCE OF COMPILATION ERRORS,
EXECUTES IT.  UPON COMPLETION OF COMMAND EXECUTION, THE
COMPILED CODE FROM THE LAST COMMAND IS DISCARDED AND STOIC
AGAIN TYPES ITS PROMPT MESSAGE AND WAITS FOR THE NEXT COMMAND
LINE.


NESTING DEPTH AND CONTINUATION LINES

	STOIC MAINTAINS A NESTING DEPTH WHICH IS USED
FOR SYNTAX CHECKING AND TO DETERMINE WHEN A MULTI-LINE
COMMAND HAS BEEN COMPLETED AND IS READY TO EXECUTE.
INITIALLY, THE NESTING DEPTH IS SET TO ZERO; IT IS INCREMENTED
WHENEVER ANY OF THE FOLLOWING WORDS ARE ENCOUNTERED DURING
COMPILATION:

IF	ELSE	(	U(	BEGIN	DO	:
UDO

THE NESTING DEPTH IS DECREMENTED BY THE FOLLOWING WORDS:

THEN	ELSE	)	END	LOOP	+LOOP	;
ULOOP	U+LOOP
REPEAT (DECREMENTS NESTING DEPTH BY 2)

IF THE NESTING DEPTH EVER BECOMES NEGATIVE, THE FATAL
ERROR "SYNTAX ERROR" IS GIVEN.  A "SYNTAX ERROR" IS ALSO
GENERATED IF THE NESTING DEPTH IS NON-ZERO EITHER AT THE
BEGINNING OR AT THE END OF A COLON DEFINITION.

	AFTER COMPILING A LINE, STOIC CHECKS THE NESTING
DEPTH; IF IT IS ZERO, THE LINE IS EXECUTED, IF NON-ZERO,
IT CONTINUES COMPILATION ON THE NEXT LINE.  FOR EXAMPLE:

	0> 3 0 DO
	1> 2 0 DO
	2> I =
	2> LOOP
	1> CR
	1> LOOP
	0 1
	0 1
	0 1
	0>

THUS, THE EXECUTION OF THE DO LOOP IS AUTOMATICALLY
POSTPONED UNTIL THE NESTING DEPTH RETURNS TO ZERO,
I.E. WHEN THE "LOOP" MATCHING THE FIRST "DO" IS ENCOUNTERED.
SIMILARLY, A MULTI-LINE COLON DEFINITION IS EXTENDED TO
INCLUDE ALL WORDS UP TO THE MATCHING ";".

	EXECUTION OF COMPILED CODE MAY BE POSTPONED
EVEN IF THE NESTING DEPTH IS ZERO BY USING THE WORD
"^".  IF "^" IS USED ANYWHERE ON A LINE, COMPILATION
WILL UNCONDITIONALLY CONTINUE ON TO THE NEXT LINE.
THIS FEATURE MAY BE USED AS FOLLOWS.NOTE "^" IS
ASCII CHARACTER 5E HEX, NOT THE CONTROL KEY "^".

	0> 5 0 DO I = LOOP ^
	0> 5 0 DO I = LOOP
	0 1 2 3 4 0 1 2 3 4
	0>

	A MORE REASONABLE APPLICATION OF "^" INVOLVES
THE USE OF STRING LITERALS.  SINCE COMPILED CODE OUTSIDE
OF A COLON DEFINITION IS DISCARDED AFTER EXECUTION,
STRING LITERALS TYPED IN ON ONE LINE ARE NOT ACCESIBLE TO
SUBSEQUENT LINES UNLESS "^" IS USED TO FORCE THE
COMPILED STRING LITERAL TO BE SAVED.  FOR EXAMPLE:

0> \THIS IS A LONG MESSAGE WHICH USES THE ENTIRE LINE\ ^
0> MSG
THIS IS A LONG MESSAGE WHICH USES THE ENTIRE LINE
0>

REPEATING THE LAST COMMAND LINE

	TYPING A LINE FEED CAUSES STOIC TO RECOMPILE AND RE-EXECUTE
THE LAST COMMAND LINE EXECUTED. FOR EXAMPLE:

0> 2 2 + =
4
0>		(LINE FEED TYPED)
4
0>		(LINE FEED TYPED)
4


ERROR HANDLING

	THE FOLLOWING TWO WORDS ARE USED TO HANDLE FATAL
ERRORS IN STOIC:

	ABORT	CLEARS THE PARAMETER, RETURN, AND LOOP
		STACKS, RESETS THE NESTING DEPTH TO ZERO,
		AND FORCES CONTROL TO RETURN TO THE
		KEYBOARD.  "ABORT" IS INVOKED BY CONTROL A.

	ERR	TYPES THE STRING AT THE TOP OF THE STACK
		FOLLOWED BY THE NAME OF THE WORD LAST
		SCANNED FROM THE INPUT STREAM, AND, IF
		INPUT IS NOT COMING FROM THE KEYBOARD,
		THE LINE LAST COMPILED FROM THE INPUT FILE.
		"ABORT" IS THEN INVOKED TO RESET STOIC.


DEFINING CONSTANTS, VARIABLES, AND ARRAYS

CONSTANTS

	A CONSTANT IS A DICTIONARY ENTRY WHICH CAUSES A
16-BIT INTEGER TO BE PUSHED ON THE PARAMETER STACK.  TO
DEFINE A CONSTANT, THE WORD "CONSTANT" IS USED:

VALUE 'NAME CONSTANT

	HERE, "VALUE" IS THE NUMBER ON THE TOP OF THE
STACK AND "NAME" IS THE NAME TO BE ASSIGNED TO THE
CONSTANT.

EXAMPLE:

	5 'NPTS CONSTANT

	THIS SETS UP A DICTIONARY ENTRY WITH NAME
	"NPTS".  EXECUTING THE WORD "NPTS" WILL CAUSE
	A 5 TO BE PUSHED ON THE STACK.

VARIABLES

	A VARIABLE IS A DICTIONARY ENTRY WHICH CONTAINS
A 16-BIT INTEGER AS ITS VALUE.  WHEN EXECUTED, IT CAUSES
THE ADDRESS OF ITS VALUE TO BE PUSHED ON THE PARAMETER
STACK.  VARIABLES ARE DEFINED AS FOLLOWS:

VALUE 'NAME VARIABLE

	"VALUE" IS THE NUMBER ON THE TOP OF THE STACK
AND "NAME" IS THE NAME TO BE ASSIGNED TO THE VARIABLE.
"VALUE" IS USED TO SET THE INITIAL VALUE OF THE VARIABLE.

EXAMPLE:

	100 'X VARIABLE

	THIS DEFINES A VARIABLE "X" WITH AN INITIAL
	VALUE OF 100.


ARRAYS

	WHILE STOIC DOES NOT HAVE A BUILT-IN ARRAY
HANDLING FACILITY, ITS ABILITY TO PERFORM ADDRESS
ARITHMETIC MAKES SUBSCRIPTING POSSIBLE.  THERE
ARE SEVERAL METHODS FOR SETTING ASIDE STORAGE FOR
AN ARRAY.  THE SIMPLEST IS TO USE THE WORD "ARRAY":

	LENGTH 'NAME ARRAY

	THIS DEFINES AND ZEROS AN ARRAY WHOSE LENGTH (IN
	16-BIT WORDS) AND NAME ARE SPECIFIED.  THE ARRAY IS
	JUST A VARIABLE WITH EXTRA STORAGE LOCATIONS
	RESERVED.  REFERENCING AN ARRAY THUS CAUSES
	THE ADDRESS OF THE ZEROTH ELEMENT TO BE PUSHED.

	EXAMPLE:

	100 'BUFFER ARRAY

	THIS DEFINES AND ZEROES A 100-WORD ARRAY NAMED
	"BUFFER".

	AN EXAMPLE OF A CONVENIENT TECHNIQUE FOR
	DEFINING SMALL ARRAYS IS :

	0 '3VEC VARIABLE 1 , 2 ,

	THIS DEFINITION SETS UP A 3-VECTOR CALLED "3VEC"
	WHOSE INITIAL VALUE IS (0,1,2).  THE WORD ","
	TAKES A NUMBER FROM THE TOP OF THE STACK AND
	APPENDS IT TO THE END OF THE DICTIONARY,
	AUTOMATICALLY EXTENDING THE LENGTH OF THE
	MOST RECENT DEFINITION.  THIS SERVES THE
	DUAL FUNCTIONS OF RESERVING SPACE IN THE
	DICTIONARY AND INITIALIZING THE ARRAY.


THE CONTENTS OF AN ARRAY MAY BE INITIALIZED TO ZERO OR
ANY CONSTANT VALUE USING THE FOLLOWING WORDS:

	FILL	FILLS AN ARRAY WHOSE ADDRESS IS AT TOP-2
		AND HAS LENGTH (IN WORDS) AT TOP-1 WITH THE
		CONSTANT VALUE AT TOP.

	0FILL	ZERO FILLS AN ARRAY WHOSE ADDRESS IS AT
		TOP-1 AND HAS LENGTH (IN WORDS) AT TOP.

	EXAMPLE:

	100 'X ARRAY
	X 100 -1 FILL

	THIS DEFINES A 100-WORD ARRAY "X" WHICH IS THEN
	FILLED WITH -1'S.  EQUIVALENTLY, THE SAME ACTION
	IS PERFORMED BY:

	-1 'X VARIABLE 99 ( -1 , )


REFERENCING ARRAY ELEMENTS

	TO REFERENCE AN ELEMENT OF AN ARRAY, ALL THAT IS
NECESSARY IS TO ADD AN APPROPRIATE OFFSET TO THE ADDRESS
OF THE ZEROTH ELEMENT.  NOTE THAT SINCE THE FIRST ELEMENT
HAS OFFSET ZERO, THE NTH ELEMENT HAS OFFSET N-1.

EXAMPLE:

	10 'X ARRAY
	10 0 DO I X I 2* + ! LOOP

	THE ABOVE CODE DEFINES A 10 ELEMENT ARRAY "X"
	AND FILLS IT WITH THE NUMBERS 0 TO 9.

	NOTE THAT SINCE ADDRESSES ARE IN BYTES, THE
	INDEX MUST BE MULTIPLIED BY 2.

	MULTIDIMENSIONAL SUBSCRIPTING IS HANDLED IN A
SIMILAR FASHION.

EXAMPLE:

	100 'X ARRAY
	10 0 DO 10 0 DO I J + J 10 * I + 2* X + ! LOOP LOOP

	THIS EXAMPLE SETS UP A 100 ELEMENT ARRAY "X"
	WHICH IS TREATED AS A 10 BY 10 MATRIX AND
	THEN STORES I+J IN THE ELEMENT (I,J).


THE DICTIONARY

	THE DICTIONARY STARTS IN LOW CORE AND GROWS
UPWARD TOWARD THE TOP OF MEMORY.  EACH DEFINITION, AS
IT IS MADE, IS APPENDED TO THE END OF THE DICTIONARY.
THE VARIABLE ".D" IS A POINTER TO THE FIRST FREE WORD
FOLLOWING THE END OF THE DICTIONARY.

THE WORD "." PUSHES THE VALUE OF THE DICTIONARY
POINTER (".D") AND IS EQUIVALENT TO TYPING ".D @".

	THE ADDRESS OF A DICTIONARY ENTRY MAY BE
OBTAINED BY INVOKING THE FOLLOWING WORD:

	() NAME

		PUSHES ON THE STACK THE ADDRESS OF
		THE PARAMETER FIELD OF THE NAMED
		WORD.

	THIS WORD MAKES IT POSSIBLE TO MODIFY THE
	VALUE OF A CONSTANT.  FOR EXAMPLE:

	100 'N CONSTANT
	200 () N !

	THE FIRST LINE DEFINES A CONSTANT "N" WHOSE
	VALUE IS 100.  THE NEXT LINE RESETS THE VALUE
	TO 200.

	THIS FEATURE SHOULD NOT BE USED IN ANY PROGRAM
	WHICH WILL SUBSEQUENTLY BE COMMITTED TO READ-
	ONLY MEMORY.

	THE FOLLOWING WORD IS USED TO OBTAIN THE
	ADDRESS OF A WORD IN THE DICTIONARY GIVEN
	ITS NAME:

	ADDRESS		TAKES A STRING ARGUMENT ON
			THE STACK WHICH IS LOOKED
			UP IN THE DICTIONARY.  IF
			NOT FOUND, AN ERROR MESSSAGE
			IS TYPED.  IF FOUND, THE ADDRESS
			OF THE PARAMETER FIELD OF THE
			WORD IS RETURNED ON THE STACK.

	EXAMPLE:

	'NEWVAL : ADDRESS 200 SWAP ! ;

	THIS DEFINES A WORD "NEWVAL" WHICH SETS THE
	PARAMETER FIELD OF ITS ARGUMENT TO 200.
	THUS,

	'N NEWVAL

	IS EQUIVALENT TO THE PREVIOUS EXAMPLE.

        NOTE.  () N  IS EQUIVALENT TO 'N ADDRESS


***EOF***



	'N NEWVAL

	IS EQUIVALENT TO THE PREV