---- CZMON ----
                   A simple Z80 monitor written in Small C
 
                                by John Hill

CZMON is a simple Z80 monitor which was primarily written as a test for a
CP/M version of Ron Cain's Small C compiler.  Many of the command letters, 
symbols and formats are similar to those of the NAS-SYS monitor in my Nascom.
I chose them because I was used to them, but they can quite easily be changed 
in the C listing to others.

The version of the monitor supplied copies itself up to start at $8000 after
loading. Other programs can then be loaded and/or saved below it. Programs to
run at other locations can be created by modifying and compiling the Small C
listing of the program to get Z80 mnemonics and then assembling them. It is
probably worth making up an edited version of CRUN.LIB which omits the setting
up of the SP and the jump to "main" at the beginning, as the monitor needs a
slightly special start because of the code for copying it up to its working
position and the presence of the jump table. A small saving of memory can 
also be achieved if the DMA input and output buffer space is shared. This 
requires that the DEFS pseudo-ops near the end of FILE.LIB are changed 
to:    ccINBUF EQU 80H    and   ccFCBI EQU 5CH.
Z80ASM works satisfactorily, but it is best to use the offset loading 
facility of DDT to convert the HEX file rather than to create a big file
full of null bytes with LOAD.COM. 

For example the instructions used to convert a version of the HEX file
for the $8000 monitor could be:

        DDT                             (Run DDT)
        ICZMON.HEX                      (Load FCB with file name)
        R810E                           (Read file with offset)
        S100   .....Enter 11 bytes to move the program from $10E to $8000
                ( This version involves moving $1700 bytes )
                21 0E 01 11 00 80 01 00 17 ED B0 C3 00 80 ..        
        G0                               (Back to CP/M)
        SAVE 23 CZMON.COM

The first line of the HEX file which contains the block move code can be noted
and then stripped off beforehand using an editor.




Commands: (All argument values are in hex.)
========

B nn            Set a breakpoint at nn. The address given must be the first
                byte of an instruction or chaos will result. When the break-
                point is encountered, the contents of the main registers are
                displayed as well as the state of the C,Z,P and S flags and 
                the next few bytes of code. There is no single step facility
                in this monitor, but it is possible to go from breakpoint to
                breakpoint with modifications to the registers and other 
                operations in between.

C n1 n2 n3      Copy a block of n3 bytes starting at n1 to a location starting
                at n2. This is an 'intelligent' copy which avoids corrupting 
                overlapping blocks.

D               Display directory of current disk. The monitor uses the DIR
                routines in the CCP and indicates which version of CP/M it is
                assuming in its cold start header. If you have a version of 
                CP/M other than 1.4 or 2.2, the D command will probably not 
                work unless the start and finish of the DIR routines in your
                version are put into the program.

E nn            Execute program at nn. After a breakpoint the argument should
                be omitted to continue with the stack etc. as they were. It is
                permissible to use other commands before continuing and to
                change registers with the S command, but changes to the SP will
                only come into effect after an E command with an argument. If
                the E command is given to continue from a breakpoint, and the
                breakpoint address has not been altered to a new value, program
                execution will proceed without the break being implemented.

I n             Input a byte from port n. This is a simple input without any
                handshaking etc.

L n             Log in drive. n can be 0,1 or A,B etc. Current drive is assumed
                if there is no argument given. The maximum number of drives is
                defined by the value of DRIVES at the beginning of the C 
                program. The code will need modification for users with higher
                drive letters than F though hexadecimal argument values equal
                to drive number + $0A should give the result required if
                the value of DRIVES is set appropriately. DRIVES is set at 2 
                in the version supplied.
               
M nn            Modify memory from address nn. ':' to step back. '/nn' to jump
                to a new address nn. '.' to terminate. Several values can be
                entered on one line.

N               Normal execution - remove breakpoint

O n1 n2         Output the byte n2 to port n1

R nn            Read file to start at nn. [Drive:]Name.type  prompted for.
                Input ends when an attempt is made to read past the end of
                the file. A certain amount of stuff at the end of the last
                buffer of the file will therefore also be moved to memory.

S               Set initial register values before execution. '.' to terminate.
                The SP,AF,HL,DE,BC,IX and IY registers are all loaded with pre-
                set values when a program is executed. These stored values will
                generally be those in the registers at the time of a break-
                point. The values can be altered before continuing. As 
                mentioned above, a change to the SP will not come into effect
                until a program is restarted with a complete E nn command.
                The default value for SP is $7800 in the $8000 monitor version.

T n1 n2 n3      Tabulate from n1 to n2 scrolling n3 lines at a time. If n3 is
                omitted, the whole lot tabulates at once. If only n1 is given
                8 lines of 16 bytes are tabulated. '.' to terminate.

W n1 n2         Write address n1 to n2 to file. [Drive:]Name.type will be
                prompted for. CON: and LST: are acceptable file names and can
                be used if desired to list ASCII files in memory whose start
                and finish are known.

^C              Exit to BDOS.



Jumps to useful subroutines.

$8000   Cold start. All breakpoints etc. cleared.
$8005   Warm start. The normal return to the monitor for command input.
$800B   Get a character to A from the keyboard. Registers preserved except AF.
$800E   Output A to VDU. All registers preserved.
$8011   Output cr/lf to VDU. Registers preserved.
$8014   Get a null-terminated line of input to a buffer pointed to by DE.
        Return with DE still pointing to the start of the buffer.

N.B. The breakpoint is achieved by inserting the code for RST 8 ($CF) at the
breakpoint address when the E command is implemented. A jump to the breakpoint
routines is set up at address 8 during a cold start. This location is not used
officially by CP/M but it is possible that some implementations may use it as
a scratch-pad.  If a program is run with the breakpoint set, but without the
breakpoint being encountered, the code for the break is liable to be left in 
place instead of the correct byte. When a break does occur, the original code
is replaced before the breakpoint display is put on the screen.
the correct byte. When a break does occur, the original cod