GFCOM.COM
	GFCOM.COM is an ASCII file comparison utility supplied with CP/MUGUK
Vol 8. As supplied it requires the use of a VDU terminal with specific control
codes. Unfortunately my Gemini Galaxy did not use exactly the same codes
although they were similar enough to tempt me to modify the programme.
	The programme was therefore dissassembled and the control codes
changed to those for the Gemini. On testing the modified programme, surprise,
surprise it did not work!!. On looking again at the dissassembly, it was seen
that the control codes were sent to the VDU using the BDOS routine 9.
Unfortunately this can not be done on the Gemini Galaxy as it uses a buffered
keyboard attached to the VDU card using control codes to the VDU to access the
keyboard. BDOS routine 9 automatically tests the keyboard for CTL C etc
during its operation. If a control code sequence to the keyboard occurrs
during a control code sequence to the VDU the system can lock up. The cure
is to use BDOS routine 6 which does not test the keyboard.
	A subroutine was then written to handle the characters using BDOS
routine 6 resulting in a useful programme for my files. FCOM only uses a 
few control characters as shown below:-
	FCOM		GFCOM		ACTIOM
	^E		ESC,"*"		Clear from cursor to end of line
	^J		^J		Line Feed
	^L		^]		Cursor Right
	^M		^M		Carriage Return
	^N		 -		Inverse Video Off
	^O		 -		Inverse Video On
	ESC=LineChar	ESC=LineChar	Cursor Positioning

	The Gemini handles inverse video in a different way so this was
ignored.
					T. GIBSON 16/05/84
					Tel (0642) 452775