The following is a commented version of CONFIGUR.SUB
This runs the NewBrain CONFIGUR program and inserts the following parameters.
The last - "which drive to be configured?" - is left blank so that control C
may be used instead !  Entering 0 will configure drive A.

This configuration shuld then be saved with (e.g.) SAVECON CSCOMMS8.040
XSUB
If the disk is then left with this configuration it can be autobooted into
UKM.COM by using SETINIT. (assuming drive A is used). The printer will not
work of course, and it will be necessary to EXIT and logon to a new system
disk if you want to use the printer ( putting comms disk in B).

This submit file assumes the (unlikely!) use of one 80-track drive and one
40-track drive. This is just to show the possibilities. For a 40-40 or an
80-80 simply copy the appropriate drive characteristics.

The sequence is: SUBMIT CONFIGUR - (enter drive number) - SAVECON filename
- EXIT ( and then return ) - (test UKM and when happy ) - SETINIT ukm - EXIT.
If you need to reconfigure - be certain to have the standard configuration
in a file ( or you will have to use sysgen !) then the COMMS setup can be 
restored at any time with RESTCON CSCOMMS8.040


XSUB
CONFIGUR
2 			/* The number of drives
0			/* The first drive
42			/* Gap length
40			/* Gap length after formatting
0                       /* Special Parameter Byte 
4			/* 
512			/* Bytes per Sector
10			/* Sectors per Track
0			/* Software Skew
2			/* Number of sides
2			/* (if 2) How does it read them? (Alternately)
80			/* Tracks per side
2			/* Reserved Tracks
4			/* Block size (K bytes)
128			/* Directory entries
1			/* Removeable disk?
1			/* Now the same rigmarole for drive B.......
42
40
0
20
512
10
0
1			/* single sided, next question omitted....
40			/* Tracks per side ....
2
2			/*  .... half the block-size...
64
1
19			/* Stream one. Buffered Keyboard -device (19)
0			/* Port.
 			/* Parameter string. None - make sure the CR is in file
18			/* Stream two. Emasculated Screen-editor for CP/M
0			/* Port.
 			/* No Parameters ( sigh!)
16			/* Serial Printer on E.I.M.
0			/* Port
L0T300*0		/* Dummy, but transmit rate must match comms.
17			/* THE SERIAL COMMS device !
0			/* Port
T300R300S1D8PZN*0	/* Transmit/Receive/Stop/Data/Parity/Network/Buffer(0).
3			/* Keyboard status - LCD display
0			/* Port
16			/* Line length
			/* Blank - to add drive to configure or abandon with ^C
**** EOF ****