KERMIT Commands                                                         Page 49


9.3. Terminal Emulation Commands

CONNECT This  verb,  valid  only  for a local Kermit, means to go into terminal
        emulation mode; present the illusion of being directly connected  as  a
        terminal  to the remote system.  Provide an "escape character" to allow
        the user to "get back" to the local system.  The escape character, when
        typed, should take a single-character argument; the following are  sug-
        gested:

            0   (zero) Transmit a NUL
            B   Transmit a BREAK
            C   Close the connection, return to local KERMIT command level
            P   Push to system command processor
            Q   Quit logging (if logging is being done)
            R   Resume logging
            S   Show status of connection
            ?   Show the available arguments to the escape character
            (a  second  copy  of  the  escape  character):  Transmit the escape
                character itself

        Lower case equivalents should be accepted.  If any invalid argument  is
        typed, issue a beep.

Also see the SET command.


9.4. Special User-Mode Commands

These commands are used only by Users of Servers.

BYE     This  command  sends  a message to the remote server to log itself out,
        and upon successful completion, terminate the local Kermit program.

FINISH  This command causes the remote server to shut  itself  down  gracefully
        without logging out its job, leaving the local KERMIT at KERMIT command
        level, allowing the user to re-CONNECT to the remote job.


9.5. Commands Whose Object Should Be Specified

Some  Kermit implementations include various local file management services and
commands to invoke them.  For instance, an implementation might  have  commands
to  let  you  get  directory  listings, delete files, switch disks, and inquire
about free disk space without having to exit and restart the program.   In  ad-
dition,  remote  servers may also provide such services.  A user Kermit must be
able to distinguish between commands aimed at its own system and those aimed at
the remote one.  When any confusion is possible, such a command may be prefixed
by one of the following "object prefixes":

REMOTE  Ask the remote Kermit server to provide this service.

LOCAL   Perform the service locally.

If the "object prefix" is omitted, the command should be executed locally.  The
services include:

KERMIT Commands                                                         Page 50


LOGIN   This  should  be  used  in its timesharing sense, to create an identity
        ("job", "session", "access", "account") on the system.

LOGOUT  To terminate a session that was initiated by LOGIN.

COPY    Make a new copy of the specified file with the specified name.

CWD     Change Working Directory.  This is ugly, but more  natural  verbs  like
        CONNECT and ATTACH are too imprecise.  CWD is the ARPAnet file transfer
        standard command to invoke this function.

DIRECTORY
        Provide  a  list  of  the  names, and possibly other attributes, of the
        files in the current working directory (or the specified directory).

DELETE  Delete the specified files.

ERASE   This could be a synomym for DELETE, since its meaning is clear.

            (It doesn't seem wise to include UNDELETE  or  UNERASE  in  the
            standard  list; most systems don't support such a function, and
            users' expectations should not be toyed with...)

KERMIT  Send a command to the remote KERMIT server in its own interactive  com-
        mand syntax.

RENAME  Change the name of the specified file.

TYPE    Display the contents of the specified file(s) at the terminal.

SPACE   Tell how much space is used and available for storing files in the cur-
        rent working directory (or the specified directory).

SUBMIT  Submit the specified file(s) for background (batch) processing.

PRINT   Print the specified file(s) on a printer.

MOUNT   Request a mount of the specified tape, disk, or other removable storage
        medium.

WHO     Show  who  is  logged in (e.g. to a timesharing system), or give infor-
        mation about a specified user or network host.

MAIL    Send electronic mail to the specified user(s).

MESSAGE Send a terminal message (on a network or timesharing system).

HELP    Give brief information about how to use KERMIT.

SET     Set various parameters relating to debugging, transmission, file  mode,
        and so forth.

SHOW    Display settings of SET parameters, capabilities in force, etc.

STATISTICS
        Give information about the performance of the most recent file transfer

KERMIT Commands                                                         Page 51


        -- elapsed time, effective baud rate, various counts, etc.

HOST    Pass  the  given command string to the specified (i.e. remote or local)
        host for execution in its own command language.

LOGGING Open or close a remote transaction or debugging log.


9.6. The SET Command

A SET command should be provided to allow the user to tailor  a  connection  to
the  peculiarities  of the communication path, the local or remote file system,
etc.  Here are some parameters that should be SET-able:

BLOCK-CHECK
        Specify the type of block check to be used: single character  checksum,
        two-character checksum, 3-character CRC.

DEBUGGING
        Display  or  log  the  packet  traffic,  packet numbers, and/or program
        states.  Useful for debugging new versions of  KERMIT,  novel  combina-
        tions of KERMIT programs, etc.

DELAY   How  many seconds a remote (non-server) KERMIT should wait before send-
        ing the Send-Init packet, to give the user time to escape back  to  the
        local KERMIT and type a RECEIVE command.

DUPLEX  For terminal emulation, specify FULL or HALF duplex echoing.

EIGHT-BIT-PREFIXING
        Specify  that "8th bit" prefixing must be done; normally it will not be
        done.

END-OF-LINE
        Specify any line terminator that must be used after a packet.

ESCAPE  Specify the escape character for terminal emulation.

FILE attributes
        Almost any of the attributes listed above  in  the  Attributes  section
        (8.5).    The most common need is to tell the KERMIT program whether an
        incoming or outbound file is text or binary.

FLOW-CONTROL
        Specify the flow control mechanism for  the  line,  such  as  XON/XOFF,
        DTR/CTS, etc.  Allow flow control to be turned off as well as on.  Flow
        control is done only on full-duplex connections.

HANDSHAKE
        Specify  any  line-access  negotiation  that  must be used or simulated
        during file transfer.  For instance, a half duplex  system  will  often
        need to "turn the line around" after sending a packet, in order to give
        you  permission  to reply.  A common handshake is XON (^Q); the current
        user of the line transmits an XON when done transmitting data.

LINE    Specify the line or device designator for the connection.  This is  for

KERMIT Commands                                                         Page 52


        use  in  a  KERMIT program that can run in either remote or local mode;
        the default line is the controlling terminal  (for  remote  operation).
        If an external device is used, local operation is presumed.

LOG     Specify  a local file in which to keep a log of the transaction.  There
        may be logs for debugging purposes (packet traffic, state  transitions,
        etc)  and  for auditing purposes (to record the name and disposition of
        each file transferred).

MARKER  Change the start-of-packet marker from the default of SOH  (CTRL-A)  to
        some  other control character, in case one or both systems has problems
        using CTRL-A for this purpose.

PACKET-LENGTH
        The maximum length for a packet.  This should normally be no less  than
        30  or  40,  and can never be greater than 96.  Short packets can be an
        advantage on noisy lines; they reduce the  probabily  of  a  particular
        packet  being  corrupted,  as  well as the retransmission overhead when
        corruption does occur.

PADDING The number of padding  characters  that  should  be  sent  before  each
        packet, and what the padding character should be.  Rarely necessary.

PARITY  Specify  the parity (ODD, EVEN, MARK, SPACE, NONE) of the physical con-
        nection.  If other than none, the "8th bit" cannot be used to  transmit
        data and must not be used by either side in block check computation.

PAUSE   How  many  seconds to pause after receiving a packet before sending the
        next packet.  Normally 0, but when a system communication processor  or
        front  end  has  trouble keeping up with the traffic, a short pause be-
        tween packets may allow it to recover its  wits;  hopefully,  something
        under a second will suffice.

PREFIX  Change  the default prefix for control characters, 8-bit characters, or
        repeated quantities.

PROMPT  Change the program's prompt.  This is useful when  running  KERMIT  be-
        tween  two  systems  whose  prompt  is the same, to eliminate confusion
        about which KERMIT you are talking to.

REPEAT-COUNT-PROCESSING
        Change the default for repeat count processing.  Normally, it  will  be
        done if both KERMIT programs agree to do it.

RETRY   The  maximum number of times to attempt to send or receive a packet be-
        fore giving up.  The normal number is about 5, but the user  should  be
        able  to  adjust it according to the condition of the line, the load on
        the systems, etc.

TIMEOUT Specify the length of the timer to set when waiting for a packet to ar-
        rive.

KERMIT Commands                                                         Page 53


9.7. Macros, the DEFINE Command

In  addition  to the individual set commands, a "macro" facility is recommended
to allow users to combine the characteristics of specific systems into a single
SET option.  For example:

  DEFINE IBM = PARITY ODD, DUPLEX HALF, HANDSHAKE XON
  DEFINE UNIX = PARITY NONE, DUPLEX FULL
  DEFINE TELENET = PARITY MARK

This could be done by providing a fancy runtime parser for commands  like  this
(which  could be automatically TAKEn from the user's KERMIT initialization file
upon program startup), or simply hardwired into the SET command table.

With these definitions in place, the user would simply  type  "SET  IBM",  "SET
UNIX",  and so forth, to set up the program to communication to the remote sys-
tem.

Terminal Emulation                                                      Page 54


10. Terminal Emulation

The local system must be able to act as a terminal so that the user can connect
to the remote system, log in, and start up the remote KERMIT.

Terminal  emulation should be provided by any KERMIT program that runs locally,
so that the user need not exit and restart the local KERMIT program in order to
switch between terminal and protocol operation.  On smaller  systems,  this  is
particularly important for various reasons -- restarting the program and typing
in  all  the  necessary SET commands is too inconvenient and time-consuming; in
some micros, switching in and out of terminal emulation may  cause  carrier  to
drop, etc.

Only bare-bones terminal emulation need be supplied by KERMIT; there is no need
to  emulate  any  particular  kind of "smart" terminal.  Simple "dumb" terminal
emulation is sufficient to do the job.  Emulation of fancier terminals is  nice
to  have, however, to take advantage of the remote system's editing and display
capabilities.  In some cases, microcomputer firmware will take  care  of  this.
To build emulation for a particular type of terminal into the program, you must
interpret and act upon escape sequences as they arrive at the port.

No  error  checking  is  done  during  terminal  emulation.  It is "outside the
protocol"; characters go back and forth "bare".  In this sense, terminal emula-
tion through KERMIT is no better than actually using a real terminal.

Some KERMIT implementations may allow logging of the terminal emulation session
to a local file.  Such a facility allows "capture" of  remote  typescripts  and
files,  again  with  no  error  checking  or correction.  When this facility is
provided, it is also desirable to have a convenient way of "toggling" the  log-
ging on and off.

If  the  local  system does not provide system- or firmware-level flow control,
like XON/XOFF, the terminal emulation program should attempt  to  simulate  it,
especially if logging is being done.

The terminal emulation facility should be able to handle either remote or local
echoing (full or half duplex), any required handshake, and it should be able to
transmit any parity required by the remote side or the communication medium.

A  terminal emulator works by continuously sampling both console input from the
local terminal and input from the communication line.  Simple input and  output
functions  will not suffice, however, since if you ask for input from a certain
device and there is none available, you will generally block until  input  does
become  available,  during  which time you will be missing input from the other
device.  Thus you must have a way  to  bounce  back  and  forth  regardless  of
whether input is available.  Several mechanisms are commonly used:

   - Continuously jump back and forth between the port status register and
     the  console  status  register,  checking  the  status bits for input
     available.  This is only  practical  on  single-user,  single-process
     systems, where the CPU has nothing else to do.

   - Issue an ordinary blocking input request for the port, but enable in-
     terrupts on console input, or vice versa.

   - Handle port input in one process and console input in another, paral-

Terminal Emulation                                                      Page 55


     lel process.  The UNIX KERMIT program listed in this manual uses this
     method.

Any input at the port should be displayed immediately on the screen.  Any input
from the console should be output immediately to the port.  In addition, if the
connection is half duplex, console input should also be sent immediately to the
screen.

The  terminal  emulation  code must examine each console character to determine
whether it is the "escape character".  If so, it should take the next character
as a special command, which it executes.  These commands are  described  above,
in section 9.3.

The terminal emulator should be able to send every ASCII character, NUL through
DEL,  and  it  should  also  be able to transmit a BREAK signal (BREAK is not a
character, but an "escape" from ASCII transmission in which a 0 is put  on  the
line  for  about  a  quarter  of a second, regardless of the baud rate, with no
framing bits).  BREAK is important when  communicating  with  various  systems,
such as IBM mainframes.

Finally, it is sometimes necessary to perform certain transformations on the CR
character  that is normally typed to end a line of input.  Some systems use LF,
EOT, or other characters for this function.  To complicate matters, intervening
communications equipment (particularly the public packet-switched networks) may
have their own independent requirements.  Thus if using KERMIT  to  communicate
over,  say,  TRANSPAC  with  a  system  that uses LF for end-of-line, it may be
necessary to transform CR into LFCR (linefeed first -- the CR tells the network
to send the packet, which will contain the LF, and the host  uses  the  LF  for
termination).  The user should be provided with a mechanism for specifying this
transformation, a command like "SET CR sequence".

Writing a KERMIT Program                                                Page 56


11. Writing a KERMIT Program

Before writing a new implementation of KERMIT or modifying an old one, first be
sure  to  contact the KERMIT Distribution center at Columbia University to make
sure that you're not duplicating someone else's effort, and that you  have  all
the  latest material to work from.  If you do write or significantly modify (or
document) a KERMIT program, please send it back to Columbia so that it  can  be
included  in  the  standard KERMIT distribution and others can benifit from it.
It is only through this kind of sharing that KERMIT has grown from  its  modest
beginnings to its present scale.

The following sections provide some hints on KERMIT programming.


11.1. Program Organization

A  basic  KERMIT  implementation  can  usually be written as a relatively small
program, self-contained in a single source file.  However, it is often the case
that a program written to run on one system will be adapted  to  run  on  other
systems  as  well.   In that case, it is best to avoid having totally divergent
sources, because when new features are added to (or bugs fixed in) the  system-
independent parts of the program -- i.e. to the protocol itself -- only one im-
plementation will reap the benefits initially, and the other will require pain-
ful, error-prone "retrofitting" to bring it up to the same level.

Thus,  if  there  is any chance that a KERMIT program will run on more than one
machine, or under more than one operating system, or support more than one kind
of port or modem, etc, it is desirable to isolate the system-dependent parts in
a way that makes the common parts usable by the various implementations.  There
are several approaches:

   1. Runtime support.  If possible, the program can inspect the  hardware
      or  inquire  of  the system about relevant parameters, and configure
      itself dynamically at startup time.  This is hardly ever possible.

   2. Conditional compilation (or assembly).  If the number of systems  or
      options  to  be supported is small, the system dependent code can be
      enclosed in conditional compilation brackets  (like  IF  IBMPC  ....
      ENDIF).  An example is provided in UNIX KERMIT listing included with
      this  manual.    However, as the number of system dependencies to be
      supported  grows,  this  method  becomes  unwieldy  and  error-prone
      --  installing  support for system X tends to break the pre-existing
      support for system Y. 

   3. Modular composition.  When there is a potentially  large  number  of
      options  a  program  should  support,  it  should  be broken up into
      separate modules (source  files),  with  clearly  specified,  simple
      calling conventions.  This allows people with new options to provide
      their  own  support for them in an easy way, without endangering any
      existing support.  Suggested modules for a KERMIT program are:

         - System-Indendent protocol  handling:  state  switching,  packet
           formation, encoding (prefixing) and decoding, etc.

         - User Interface: the command parser.  Putting this in a separate
           module  allows  plug-in  of  command parsers to suit the user's

Writing a KERMIT Program                                                Page 57


           taste,  to mimic the style of the host system command parser or
           some popular application, etc.

         - Screen i/o: This module would contain the screen control codes,
           cursor positioning routines, etc.

         - Port i/o: Allows support of various port hardware.  This module
           can define the port status register location, the status  bits,
           and so forth, and can implement the functions to read and write
           characters at the port.

         - Modem   control:   This   module  would  support  any  kind  of
           "intelligent" modem, which is not simply a  transparent  exten-
           sion  of  the communications port.  Such modems may accept spe-
           cial commands to perform functions like dialing out,  redialing
           a  recent  number,  hanging  up, etc., and may need special in-
           itialization (for instance, setting modem signals like DTR).

         - Console input: This module would supply  the  function  to  get
           characters  from  the  console;  it would know about the status
           register  locations  and  bits,  interrupt  structure,  key-to-
           character   mappings,   etc.,  and  could  also  implement  key
           redefinitions, keystroke macros,  programmable  function  keys,
           expanded control and meta functions, etc.

         - Terminal  Emulation:  This  module  would  interpret escape se-
           quences in the incoming character  stream  (obtained  from  the
           port i/o module) for the particular type of terminal being emu-
           lated  and  interpret  them by making appropriate calls the the
           screen i/o module, and it would send user typein (obtained from
           the console input module) out the serial port (again using  the
           port  i/o module).  Ideally, this module could be replacable by
           other modules to emulate different  kinds  of  terminals  (e.g.
           ANSI, VT52, ADM3A, etc).

         - File i/o: This module contains all the knowledge about the host
           system's  file  structure; how to open and close files, perform
           "get next file" operations, read and write files, determine and
           set their attributes, detect the end of a file, and  so  forth,
           and  provides  the  functions,  including  buffering,  to get a
           character from a file and put a character  to  a  file.    This
           module  may  also  provide  file  management services for local
           files -- directory listings, deleting, renaming,  copying,  and
           so forth.

         - Definitions  and  Data: Separate modules might also be kept for
           compile-time parameter definitions and for global runtime data.

Writing a KERMIT Program                                                Page 58


11.2. Programming Language

The  language  to  be used in writing a KERMIT program is more than a matter of
taste.  The primary consideration is that the language  provide  the  necessary
functionality and speed.  For instance, a microcomputer implementation of BASIC
may  not  allow  the  kind of low-level access to device registers needed to do
terminal emulation, or to detect console input during file transfer, or even if
it can do these things, it might not be able to run fast enough  do  drive  the
communication line at the desired baud rate.

The  second  consideration in choosing a language is portability.  This is used
in two senses: (1) whether the language is in the  public  domain  (or,  equiv-
alently,  provided  "free"  as part of the basic system), and (2) whether it is
well standardized and in wide use on a variety of systems.  A language that  is
portable in both senses is to be preferred.

Whatever  programming  language  is selected, it is important that all lines in
the program source be kept to 80 characters or less (after expansion of  tabs).
This  is because KERMIT material must often be shipped over RJE and other card-
format communication links.

In addition, it is important that the names of all files used in  creating  and
supporting  a  particular  KERMIT  implementation be (possibly a subset) of the
form NAME.TYPE, where NAME is limited to six characters, and TYPE is limited to
three, and where the NAME of each file begin with a common  2  or  3  character
prefix.    This is so that all related files will be grouped together in an al-
phabetic directory listing, and so when all of the hundreds of  KERMIT  related
files  are  placed together on a tape, all names will be both legal and unique,
especially on systems (like PDP-11 operating  systems)  with  restrictive  file
naming conventions.


11.3. Documentation

A  new  KERMIT program should be thoroughly documented; one of the hallmarks of
KERMIT is its documentation.  The documentation should  be  at  both  the  user
level  (how  to  use  the  program,  what the commands are, etc, similar to the
documentation presently found in the Kermit Users  Guide),  and  the  implemen-
tation  level  (describe system dependencies, give pointers for adapting to new
systems, and so forth).    In  addition,  programs  themselves  should  contain
copious  commentary.   Like program source, documentation should be kept within
80-character lines.

If possible, a section for the implementation should be written for the  KERMIT
User  Guide using the UNILOGIC Scribe formatting language (subsets of which are
also to be found in some microcomputer text processing software such as Perfect
Writer or Final Word), using  the  same  general  conventions  as  the  existic
Scribe-format implementation sections.

KERMIT programs should also contain a revision history, in which each change is
briefly  explained,  assigned an "edit number", and the programmer and site are
identified.  The lines or sections comprising the edit should  be  marked  with
the corresponding edit number, and the KERMIT program, upon startup, should an-
nounce its version and edit numbers, so that when users complain of problems we
will know what version of the program is in question.

Writing a KERMIT Program                                                Page 59


The version number changes when the functionality has been changed sufficiently
to  require  major revisions of user documentation.  The edit number should in-
crease (monotonically, irrespective of version number)  whenever  a  change  is
made  to  the program.  The edit numbers are very important for program manage-
ment; after shipping out a version of, say, CP/M KERMIT-80,  we  often  receive
many copies of it, each containing its own set of changes, which we must recon-
cile in some manner.  Edit numbers help a great deal here.


11.4. Bootstrapping

Finally,  a  bootstrap  procedure should be provided.  KERMIT is generally dis-
tributed on magnetic tape to large central sites; the users at those sites need
ways of "downloading" the various implementations to  their  micros  and  other
local  systems.  A simple bootstrap procedure would consist of precise instruc-
tions on how to accomplish an "unguarded" capture of the program.    Perhaps  a
simple,  short  program  can be written for each each end that will do the job;
listings and instructions can be provided for the user to type in and run these
programs.

Packet Format and Types                                                 Page 60


I. Packet Format and Types

KERMIT Packet Layout:

  +------+-----+-----+------+------------+-------+
  | MARK | LEN | SEQ | TYPE |    DATA    | CHECK |
  +------+-----+-----+------+------------+-------+

Send-Init Data Field Layout:

   1      2      3      4      5      6      7      8      9      10...
  +------+------+------+------+------+------+------+------+------+-------
  | MAXL | TIME | NPAD | PADC | EOL  | QCTL | QBIN | CHKT | REPT | CAPAS
  +------+------+------+------+------+------+------+------+------+-------

KERMIT  packet  types  and subtypes; required types are marked with an asterisk
(*):

Y*  Acknowledge (ACK)
N*  Negative acknowledge (NAK)
S*  Send initiate (exchange parameters)
I   Initialize (exchange parameters)
F*  File header
A   File attributes
D*  Data packet
Z*  End of file (EOF)
B*  Break transmission (EOT)
E*  Error
R   Receive Initiate (ask the server to send the specified files)
C   Host Command
K   KERMIT Command
T   Reserved for internal use
G   Generic Kermit Command; Subcommands:

    I   Login (or logout)
    C   CWD, Change Working Directory
    L   Bye
    F   Finish
    D   Directory
    U   Disk Usage Query
    E   Erase, Delete
    T   Type
    R   Rename
    K   Copy
    W   Who's logged in?
    M   Short Message
    H   Help
    Q   Server Status Query
    P   Program Invocation
    J   Journal Control
    V   Variable Set/Query

List of Features                                                        Page 61


II. List of Features

There's  no  true  linear  scale along which to rate Kermit implementations.  A
basic, minimal implementation provides file transfer in both  directions,  and,
for  microcomputers  (PC's,  workstations, other single user systems), terminal
emulation.  Even within this framework, there can be variations.  For instance,
can the program send a file group in a single command, or  must  a  command  be
issued for each file?  Can it time out?  Here is a list of features that may be
present;  for  any KERMIT implementation, the documentation should show whether
these features exist, and how to invoke them.

   - File groups.  Can it send a group of files  with  a  single  command,
     using  "wildcard",  pattern,  or  list notation?  Can it successfully
     send or receive a group of files of mixed types?  Can it recover from
     an error on a particular file and go on to the next one?  Can it keep
     a log of the files involved showing the disposition of each?

   - Filenames.  Can it take action to avoid overwriting a local file when
     a new file of the same name arrives?  Can it convert filenames to and
     from legal or "normal form"?

   - File types.  Can binary as well as text files be transmitted?

   - 8th-Bit prefixing.  Can it send and  receive  8-bit  data  through  a
     7-bit channel using the prefixing mechanism?

   - Repeat-Count  processing.  Can it send and receive data with repeated
     characters replaced by a prefix sequence?

   - Terminal Emulation.  Does it  have  a  terminal  emulation  facility?
     Does  it  provide  various  communication  options,  such  as duplex,
     parity, and handshake selection?  Can it transmit all  ASCII  charac-
     ters?  Can it transmit BREAK?  Can it log the remote session locally,
     to provide unguarded file capture?

   - Communications Options.  Can duplex, parity, handshake, and line ter-
     minator be specified for file transfer?

   - Block  Check  Options.    In  addition  to the basic single-character
     checksum, can the two-character checksum and the three-character  CRC
     be selected?

   - Basic  Server.  Can it run in server mode, accepting commands to send
     or receive files, and to shut itself down?

   - Advanced Server.  Can it accept  server  commands  to  delete  files,
     provide directory listings, send messages, and forth?

   - Issue  Commands  to  Server.    Can it send commands to a server, and
     handle all possible responses?

   - Host Commands.  Can it parse and send remote "host commands"?  If  it
     is  a  server,  can it pass these commands to the host system command
     processor and return the results to the local user Kermit?

   - Interrupt File Transfers.  Can it interrupt sending  or  receiving  a

List of Features                                                        Page 62


     file?  Can it respond to interrupt requests from the other side?

   - Local  File  Management  Services.    Are there commands to get local
     directory directory listings, delete local files, and so forth?

   - File Attributes.  Can it send file attribute information about  local
     files,  and  can  deal with incoming file attribute information?  Can
     alternate dispositions be specified.  Can files be archived?

   - Debugging Capability.    Can  packet  traffic  be  logged,  examined,
     single-stepped?

Unresolved Issues                                                       Page 63


III. Unresolved Issues

KERMIT doesn't do everything.  Here is a short list of things it doesn't do, or
could do better.

   - KERMIT cannot be used through IBM 3270 protocol emulators.  These are
     devices that allow asynchronous ASCII terminals or PCs to communicate
     with  IBM mainframes as though they were synchronous full-screen dis-
     plays.  The problems include: (a) the protocol  converter  translates
     from  EBCDIC  to  ASCII -- that is, it assumes it is receiving EBCDIC
     when KERMIT is supposed to be sending ASCII -- according to  its  own
     translate  table,  which  may  vary  from  site to site, and is not a
     1-to-1 mapping in any case; (b) non-printing control characters (like
     SOH) cannot be sent at all; (c) the protocol converter looks for 3270
     formatting commands and translates them to escape sequences  for  the
     ASCII  terminal,  possibly  modifying packet data; (d) the IBM system
     automatically pauses at the end of each screenful; (e)  the  protocol
     converter  thinks it knows what is "on the screen" and may attempt to
     optimize.  In general, one  never  knows  exactly  how  a  particular
     protocol  converter will work, or how it may differ from another one.
     Still, it may be possible to work around these problems if  the  Ker-
     mits  on  either  end  are put into a special "3270 mode", "clear the
     screen" between each packet, and agree on some special convention for
     packet delimitation and data translation.

   - Control character prefixing.  This can get pretty expensive  for  bi-
     nary  files  or  other files that contain lots of control characters.
     Since most hosts won't choke on every single  control  character,  it
     might  be  a good idea for each host to inform the other of what con-
     trol characters it can receive "bare".  On the other hand, this could
     backfire when the two hosts are connected by a network or device that
     chokes on control characters that neither of the hosts choke on.  For
     hardwired connections with no unknown factors, however, many  control
     characters could be sent "bare".

   - When  long  sequences  of  characters  in the control range are being
     sent, individually prefixing each character  is  costly.    Shift-in/
     shift-out  codes  might be used more effectively here.  Same for long
     strings of characters with the parity bit on, when 8th-bit  prefixing
     is  being  done.  The cost would be yet another set of prefix charac-
     ters, and the associated complexity of packet formation and decoding.

   - In some situations, certain printable characters can't get through  a
     communication  link.    For instance, a network terminal server might
     reserve "@" as its attention character.  Should  the  protocol  allow
     some  way  to encode such characters for translation?  A set of user-
     definable escape sequences could be useful here.

   - Ironically, some systems do not fare well with KERMIT's small  packet
     sizes.  These are typically big mainframes that expect to communicate
     with  block  mode  terminals,  receiving thousands of characters at a
     time.  Such systems find that KERMIT is simply too expensive to  run.
     Meanwhile,  other systems that can run KERMIT with no difficulty find
     the performance disappointing (the  efficiency  generally  works  out
     somewhere  between 50 and 80 percent, i.e. data characters divided by
     the speed of the the transmission line, in  characters  per  second).

Unresolved Issues                                                       Page 64


     These  two  problems  could  be  solved  in either of two ways: allow
     longer packets, or allow multiple data packets to be sent end to end.

        * Without changing the format or encoding of  the  packet  control
          fields, it might be possible to have longer packets by reserving
          packet lengths of 0, 1, 2, 3 to be codes for bigger numbers like
          200,  500,  1000,  2000.    However,  the longer the packet, the
          greater  the  probability  of  corruption,  and  the  longer  to
          retransmit  once  corrupted.    In addition, the adequacy of the
          single-character block check would  be  much  reduced  for  long
          packets;  long packets should therefore be sent with type 2 or 3
          block checks.

        * It would be possible to extend the protocol to  allow  transmis-
          sion  of data packets while ACKs were still outstanding, and any
          ACK would be taken as an ACK for the specified  packet  and  all
          previous  ones.  A limit on the number of outstanding ACKs could
          be agreed upon; the maximum size of this "floating window" would
          have to be less than 64, which is where  KERMIT  packet  numbers
          wrap  around,  and the window could not extend over a wraparound
          or else KERMIT would have no way of knowing whether n  times  64
          packets  had  been skipped.  A floating window of 8 and a packet
          size of 95 would give about the  same  effect  as  700-character
          packets.   A NAK would require the sender to back up all the way
          to the NAK'd packet.  A future edition of  the  Protocol  Manual
          might include a specification for floating windows.

A KERMIT Program                                                        Page 65


IV. A KERMIT Program

What  follows  is  a listing of a real production version of KERMIT, written in
              4
the C language .  It is designed to run under  various  versions  of  the  UNIX
operating  system.   The basic KERMIT functionality is present, but very little
in the way of optional features.  Only the most rudimentary  (UNIX-style)  com-
mand  parser  is  provided.  The program illustrates many of the considerations
described in this manual, with respect to the protocol, the program design, and
so forth.

It must be emphasized that this is a bare  minimum  implementation  of  Kermit.
Anyone  writing  a  new Kermit from scratch is encouraged to look at the source
for one of the more advanced implementations as a model (check the Kermit Users
Guide for a list of KERMIT implementations and their features).   Although  you
may  not  understand the language it's written in, there should be profuse com-
ments that can be useful.

The following program uses decimal notation for numbers,  and  tochar()  rather
than char() for integer-to-character conversion.

/*
 *  K e r m i t  File Transfer Utility
 *
 *  UNIX Kermit, Columbia University, 1981, 1982, 1983
 *      Bill Catchings, Bob Cattani, Chris Maio, Frank da Cruz, Alan Crosswell
 *
 *  Also:   Jim Guyton, Rand Corporation
 *          Walter Underwood, Ford Aerospace
 *
 *  usage:  kermit c [lbe line baud escapechar]         to connect
 *          kermit s [d..iflb line baud] file ...       to send files
 *          kermit r [d..iflb line baud]                to receive files
 *
 *  where   c=connect, s=send, r=receive,
 *          d=debug, i=image mode, f=no filename conversion, l=tty line,
 *          b=baud rate, e=escape char.
 *
 *  For remote Kermit, format is either:
 *          kermit r                                    to receive files
 *  or      kermit s file ...                           to send files
 *
 */









_______________

  4
   Kernighan & Ritchie, The C Programming Language:  Prentice-Hall (1978)

A KERMIT Program                                                        Page 66



/*
 *  Modification History:
 *
 *  Oct. 17 Included fixes from Alan Crosswell (CUCCA) for IBM_UTS:
 *          - Changed MYEOL character from \n to \r.
 *          - Change char to int in bufill so getc would return -1 on
 *            EOF instead of 255 (-1 truncated to 8 bits)
 *          - Added read() in rpack to eat the EOL character
 *          - Added fflush() call in printmsg to force the output
 *          NOTE: The last three changes are not conditionally compiled
 *                since they should work equally well on any system.
 *
 *          Changed Berkeley 4.x conditional compilation flag from
 *              UNIX4X to UCB4X.
 *          Added support for error packets and cleaned up the printing
 *              routines.
 */

#include <stdio.h>          /* Standard UNIX definitions */

/* Conditional compilation for different machines/operating systems */
/* One and only one of the following lines should be 1 */

#define UCB4X       1       /* Berkeley 4.x UNIX */
#define TOPS_20     0       /* TOPS-20 */
#define IBM_UTS     0       /* Amdahl UTS on IBM systems */
#define VAX_VMS     0       /* VAX/VMS (not yet implemented) */

/* Conditional compilation for the different Unix variants */
/* 0 means don't compile it, nonzero means do */

#if UCB4X
#define V6_LIBS     0       /* Dont't use retrofit libraries */
#define NO_FIONREAD 0       /* We have ioctl(FIONREAD,...) for flushinput() */
#define NO_TANDEM   0       /* We have TANDEM line discipline (xon/xoff) */
#endif

#if IBM_UTS
#define V6_LIBS     0       /* Don't use retrofit libraries */
#define NO_FIONREAD 1       /* No ioctl(FIONREAD,...) for flushinput() */
#define NO_TANDEM   1       /* No TANDEM line discipline (xon/xoff) */
#endif

#if V6_LIBS
#include <retrofit/sgtty.h>
#include <retrofit/signal.h>
#include <retrofit/setjmp.h>
#else
#include <sgtty.h>
#include <signal.h>
#include <setjmp.h>
#endif

A KERMIT Program                                                        Page 67



#if NO_TANDEM
#define TANDEM      0       /* define it to be nothing if it's unsupported */
#endif


/* Symbol Definitions */

#define MAXPACKSIZ  94      /* Maximum packet size */
#define SOH         1       /* Start of header */
#define CR          13      /* ASCII Carriage Return */
#define SP          32      /* ASCII space */
#define DEL         127     /* Delete (rubout) */
#define ESCCHR      '^'     /* Default escape character for CONNECT */

#define MAXTRY      10      /* Times to retry a packet */
#define MYQUOTE     '#'     /* Quote character I will use */
#define MYPAD       0       /* Number of padding characters I will need */
#define MYPCHAR     0       /* Padding character I need (NULL) */

#if IBM_UTS
#define MYEOL       '\r'    /* End-Of-Line character for UTS systems */
#else
#define MYEOL       '\n'    /* End-Of-Line character I need */
#endif

#define MYTIME      10      /* Seconds after which I should be timed out */
#define MAXTIM      60      /* Maximum timeout interval */
#define MINTIM      2       /* Minumum timeout interval */

#define TRUE        -1      /* Boolean constants */
#define FALSE       0


/* Macro Definitions */

/*
 * tochar: converts a control character to a printable one by adding a space.
 *
 * unchar: undoes tochar.
 *
 * ctl:    converts between control characters and printable characters by
 *         toggling the control bit (ie. ^A becomes A and A becomes ^A).
 */
#define tochar(ch)  ((ch) + ' ')
#define unchar(ch)  ((ch) - ' ')
#define ctl(ch)     ((ch) ^ 64 )


/* Global Variables */

A KERMIT Program                                                        Page 68



int     size,               /* Size of present data */
        rpsiz,              /* Maximum receive packet size */
        spsiz,              /* Maximum send packet size */
        pad,                /* How much padding to send */
        timint,             /* Timeout for foreign host on sends */
        n,                  /* Packet number */
        numtry,             /* Times this packet retried */
        oldtry,             /* Times previous packet retried */
        ttyfd,              /* File descriptor of tty for I/O, 0 if remote */
        remote,             /* -1 means we're a remote kermit */
        image,              /* -1 means 8-bit mode */
        debug,              /* indicates level of debugging output (0=none) */
        filnamcnv,          /* -1 means do file name case conversions */
        filecount;          /* Number of files left to send */

char    state,              /* Present state of the automaton */
        padchar,            /* Padding character to send */
        eol,                /* End-Of-Line character to send */
        escchr,             /* Connect command escape character */
        quote,              /* Quote character in incoming data */
        **filelist,         /* List of files to be sent */
        *filnam,            /* Current file name */
        recpkt[MAXPACKSIZ], /* Receive packet buffer */
        packet[MAXPACKSIZ]; /* Packet buffer */

FILE    *fp,                /* File pointer for current disk file */
        *log;               /* File pointer for Logfile */

jmp_buf env;                /* Environment ptr for timeout longjump */


/*
 *  m a i n
 *
 *  Main routine - parse command and options, set up the
 *  tty lines, and dispatch to the appropriate routine.
 */

main(argc,argv)
int argc;                           /* Character pointers to and count of */
char **argv;                            /* command line arguments */
{
    char *ttyname,                      /* tty name for LINE argument */
        *cp;                            /* char pointer */
    int speed,                          /* speed of assigned tty, */
        cflg, rflg, sflg;               /* flags for CONNECT, RECEIVE, SEND */

    struct sgttyb
        rawmode,                        /* Controlling tty raw mode */
        cookedmode,                     /* Controlling tty cooked mode */
        ttymode;                        /* mode of tty line in LINE option */

    if (argc < 2) usage();              /* Make sure there's a command line */

    cp = *++argv; argv++; argc -= 2;    /* Set up pointers to args */

A KERMIT Program                                                        Page 69



/*  Initialize these values and hope the first packet will get across OK */

    eol = CR;                           /* EOL for outgoing packets */
    quote = '#';                        /* Standard control-quote char "#" */
    pad = 0;                            /* No padding */
    padchar = NULL;                     /* Use null if any padding wanted */

    speed = cflg = sflg = rflg = 0;     /* Turn off all parse flags */
    ttyname = 0;                        /* Default is remote mode */

#if UCB4X                               /* Default to 7-bit masking, CRLF */
    image = FALSE;                      /* translation and filename case */
    filnamcnv = TRUE;                   /* conversion for UNIX systems */
#else
    image = TRUE;                       /* Default to no processing for */
    filnamcnv = FALSE;                  /* non-UNIX systems */
#endif

    escchr = ESCCHR;                    /* Default escape character */

    while ((*cp) != NULL)               /* Parse characters in first arg. */
        switch (*cp++)
        {
            case 'c': cflg++; break;    /* C = Connect command */
            case 's': sflg++; break;    /* S = Send command */
            case 'r': rflg++; break;    /* R = Receive command */

            case 'd':                   /* D = Increment debug mode count */
                debug++; break;

            case 'f':
                filnamcnv = FALSE;      /* F = don't do case conversion */
                break;                  /*     on filenames */

            case 'i':                   /* I = Image (8-bit) mode */
                image = TRUE; break;    /* (this is default for non-UNIX) */

            case 'l':                   /* L = specify tty line to use */
                if (argc--) ttyname = *argv++;
                else usage();
                if (debug) printf("Line to remote host is %s\n",ttyname);
                break;

            case 'e':                   /* E = specify escape char */
                if (argc--) escchr = **argv++;
                else usage();
                if (debug) printf("Escape char is \"%c\"\n",escchr);
                break;

A KERMIT Program                                                        Page 70



            case 'b':                   /* B = specify baud rate */
#if UCB4X
                if (argc--) speed = atoi(*argv++);
                else usage();
                if (debug) printf("Line speed to remote host is %d\n",speed);
                break;
#else
                printmsg("Speed setting implemented for Unix only.");
                exit(1);
#endif
        }

/* Done parsing */

    if ((cflg+sflg+rflg) != 1)          /* Only one command allowed */
        usage();


    if (ttyname)                        /* If LINE was specified, we */
    {                                   /* operate in local mode */
        ttyfd = open(ttyname,2);        /* Open the tty line */
        if (ttyfd < 0)
        {
            printmsg("Cannot open %s",ttyname);
            exit(1);
        }
        remote = FALSE;                 /* Indicate we're in local mode */
    }
    else                                /* No LINE specified so we operate */
    {                                   /* in remote mode (ie. controlling */
        ttyfd = 0;                      /* tty is the communications line) */
        remote = TRUE;
    }


/* Put the proper tty into the correct mode */

    if (remote)                         /* If remote, use controlling tty */
    {
        gtty(0,&cookedmode);            /* Save current mode so we can */
        gtty(0,&rawmode);               /* restore it later */
        rawmode.sg_flags |= (RAW|TANDEM);
        rawmode.sg_flags &= ~(ECHO|CRMOD);
        stty(0,&rawmode);               /* Put tty in raw mode */
    }
    else                                /* Local, use assigned line */
    {
        gtty(ttyfd,&ttymode);
        ttymode.sg_flags |= (RAW|TANDEM);
        ttymode.sg_flags &= ~(ECHO|CRMOD);

A KERMIT Program                                                        Page 71



#if UCB4X                               /* Speed changing for UNIX only */
        if (speed)                      /* User specified a speed? */
        {
            switch(speed)               /* Get internal system code */
            {
                case 110: speed = B110; break;
                case 150: speed = B150; break;
                case 300: speed = B300; break;
                case 1200: speed = B1200; break;
                case 2400: speed = B2400; break;
                case 4800: speed = B4800; break;
                case 9600: speed = B9600; break;

                default:
                    printmsg("Bad line speed.");
                    exit(1);
            }
            ttymode.sg_ispeed = speed;
            ttymode.sg_ospeed = speed;
        }
#endif /* UCB4X */

        stty(ttyfd,&ttymode);           /* Put asg'd tty in raw mode */
    }


/* All set up, now execute the command that was given. */

    if (debug)
    {
        printf("Debugging level = %d\n\n",debug);

        if (cflg) printf("Connect command\n\n");
        if (sflg) printf("Send command\n\n");
        if (rflg) printf("Receive command\n\n");
    }

    if (cflg) connect();                /* Connect command */

    if (sflg)                           /* Send command */
    {
        if (argc--) filnam = *argv++;   /* Get file to send */
        else
        {   if (remote)
                stty(0,&cookedmode);    /* Restore controlling tty's modes */
            usage();                    /* and give error */
        }
        fp = NULL;                      /* Indicate no file open yet */
        filelist = argv;                /* Set up the rest of the file list */
        filecount = argc;               /* Number of files left to send */
        if (sendsw() == FALSE)          /* Send the file(s) */
            printmsg("Send failed.");   /* Report failure */
        else                            /*  or */
            printmsg("done.");          /* success */
    }

A KERMIT Program                                                        Page 72



    if (rflg)                           /* Receive command */
    {
        if (recsw() == FALSE)           /* Receive the file(s) */
            printmsg("Receive failed.");
        else                            /* Report failure */
            printmsg("done.");          /* or success */
    }

    if (remote) stty(0,&cookedmode);    /* Restore controlling tty's modes */
}


/*
 *  s e n d s w
 *
 *  Sendsw is the state table switcher for sending files.  It loops until
 *  either it finishes, or an error is encountered.  The routines called
 *  by sendsw are responsible for changing the state.
 *
 */

sendsw()
{
    char sinit(), sfile(), sdata(), seof(), sbreak();

    state = 'S';                        /* Send initiate is the start state */
    n = 0;                              /* Initialize message number */
    numtry = 0;                         /* Say no tries yet */
    while(TRUE)                         /* Do this as long as necessary */
    {
        if (debug) printf("sendsw state: %c\n",state);
        switch(state)
        {
            case 'S':   state = sinit();  break; /* Send-Init */
            case 'F':   state = sfile();  break; /* Send-File */
            case 'D':   state = sdata();  break; /* Send-Data */
            case 'Z':   state = seof();   break; /* Send-End-of-File */
            case 'B':   state = sbreak(); break; /* Send-Break */
            case 'C':   return (TRUE);           /* Complete */
            case 'A':   return (FALSE);          /* "Abort" */
            default:    return (FALSE);          /* Unknown, fail */
        }
    }
}


/*
 *  s i n i t
 *
 *  Send Initiate: send this host's parameters and get other side's back.
 */

char sinit()
{
    int num, len;                       /* Packet number, length */

A KERMIT Program                                                        Page 73



    if (numtry++ > MAXTRY) return('A'); /* If too many tries, give up */
    spar(packet);                       /* Fill up init info packet */

    flushinput();                       /* Flush pending input */

    spack('S',n,6,packet);              /* Send an S packet */
    switch(rpack(&len,&num,recpkt))     /* What was the reply? */
    {
        case 'N':  return(state);       /* NAK, try it again */

        case 'Y':                       /* ACK */
            if (n != num)               /* If wrong ACK, stay in S state */
                return(state);          /* and try again */
            rpar(recpkt);               /* Get other side's init info */

            if (eol == 0) eol = '\n';   /* Check and set defaults */
            if (quote == 0) quote = '#';

            numtry = 0;                 /* Reset try counter */
            n = (n+1)%64;               /* Bump packet count */
            return('F');                /* OK, switch state to F */

        case 'E':                       /* Error packet received */
            prerrpkt(recpkt);           /* Print it out and */
            return('A');                /* abort */

        case FALSE: return(state);      /* Receive failure, try again */

        default: return('A');           /* Anything else, just "abort" */
   }
 }


/*
 *  s f i l e
 *
 *  Send File Header.
 */

char sfile()
{
    int num, len;                       /* Packet number, length */
    char filnam1[50],                   /* Converted file name */
        *newfilnam,                     /* Pointer to file name to send */
        *cp;                            /* char pointer */

    if (numtry++ > MAXTRY) return('A'); /* If too many tries, give up */

A KERMIT Program                                                        Page 74



    if (fp == NULL)                     /* If not already open, */
    {   if (debug) printf("   Opening %s for sending.\n",filnam);
        fp = fopen(filnam,"r");         /* open the file to be sent */
        if (fp == NULL)                 /* If bad file pointer, give up */
        {
            error("Cannot open file %s",filnam);
            return('A');
        }
    }

    strcpy(filnam1, filnam);            /* Copy file name */
    newfilnam = cp = filnam1;
    while (*cp != '\0')                 /* Strip off all leading directory */
        if (*cp++ == '/')               /* names (ie. up to the last /). */
            newfilnam = cp;

    if (filnamcnv)                      /* Convert lower case to upper  */
        for (cp = newfilnam; *cp != '\0'; cp++)
            if (*cp >= 'a' && *cp <= 'z')
                *cp ^= 040;

    len = cp - newfilnam;               /* Compute length of new filename */

    printmsg("Sending %s as %s",filnam,newfilnam);

    spack('F',n,len,newfilnam);         /* Send an F packet */
    switch(rpack(&len,&num,recpkt))     /* What was the reply? */
    {
        case 'N':                       /* NAK, just stay in this state, */
            num = (--num<0 ? 63:num);   /* unless it's NAK for next packet */
            if (n != num)               /* which is just like an ACK for */
                return(state);          /* this packet so fall thru to... */

        case 'Y':                       /* ACK */
            if (n != num) return(state); /* If wrong ACK, stay in F state */
            numtry = 0;                 /* Reset try counter */
            n = (n+1)%64;               /* Bump packet count */
            size = bufill(packet);      /* Get first data from file */
            return('D');                /* Switch state to D */

        case 'E':                       /* Error packet received */
            prerrpkt(recpkt);           /* Print it out and */
            return('A');                /* abort */

        case FALSE: return(state);      /* Receive failure, stay in F state */

        default:    return('A');        /* Something else, just "abort" */
    }
}

A KERMIT Program                                                        Page 75



/*
 *  s d a t a
 *
 *  Send File Data
 */

char sdata()
{
    int num, len;                       /* Packet number, length */

    if (numtry++ > MAXTRY) return('A'); /* If too many tries, give up */

    spack('D',n,size,packet);           /* Send a D packet */
    switch(rpack(&len,&num,recpkt))     /* What was the reply? */
    {
        case 'N':                       /* NAK, just stay in this state, */
            num = (--num<0 ? 63:num);   /* unless it's NAK for next packet */
            if (n != num)               /* which is just like an ACK for */
                return(state);          /* this packet so fall thru to... */

        case 'Y':                       /* ACK */
            if (n != num) return(state); /* If wrong ACK, fail */
            numtry = 0;                 /* Reset try counter */
            n = (n+1)%64;               /* Bump packet count */
            if ((size = bufill(packet)) == EOF) /* Get data from file */
                return('Z');            /* If EOF set state to that */
            return('D');                /* Got data, stay in state D */

        case 'E':                       /* Error packet received */
            prerrpkt(recpkt);           /* Print it out and */
            return('A');                /* abort */

        case FALSE: return(state);      /* Receive failure, stay in D */

        default:    return('A');        /* Anything else, "abort" */
    }
}


/*
 *  s e o f
 *
 *  Send End-Of-File.
 */

char seof()
{
    int num, len;                       /* Packet number, length */
    if (numtry++ > MAXTRY) return('A'); /* If too many tries, "abort" */

A KERMIT Program                                                        Page 76



    spack('Z',n,0,packet);              /* Send a 'Z' packet */
    switch(rpack(&len,&num,recpkt))     /* What was the reply? */
    {
        case 'N':                       /* NAK, just stay in this state, */
            num = (--num<0 ? 63:num);   /* unless it's NAK for next packet, */
            if (n != num)               /* which is just like an ACK for */
                return(state);          /* this packet so fall thru to... */

        case 'Y':                       /* ACK */
            if (n != num) return(state); /* If wrong ACK, hold out */
            numtry = 0;                 /* Reset try counter */
            n = (n+1)%64;               /* and bump packet count */
            if (debug) printf("   Closing input file %s, ",filnam);
            fclose(fp);                 /* Close the input file */
            fp = NULL;                  /* Set flag indicating no file open */

            if (debug) printf("looking for next file...\n");
            if (gnxtfl() == FALSE)      /* No more files go? */
                return('B');            /* if not, break, EOT, all done */
            if (debug) printf("   New file is %s\n",filnam);
            return('F');                /* More files, switch state to F */

        case 'E':                       /* Error packet received */
            prerrpkt(recpkt);           /* Print it out and */
            return('A');                /* abort */

        case FALSE: return(state);      /* Receive failure, stay in Z */

        default:    return('A');        /* Something else, "abort" */
    }
}


/*
 *  s b r e a k
 *
 *  Send Break (EOT)
 */

char sbreak()
{
    int num, len;                       /* Packet number, length */
    if (numtry++ > MAXTRY) return('A'); /* If too many tries "abort" */

    spack('B',n,0,packet);              /* Send a B packet */
    switch (rpack(&len,&num,recpkt))    /* What was the reply? */
    {
        case 'N':                       /* NAK, just stay in this state, */
            num = (--num<0 ? 63:num);   /* unless NAK for previous packet, */
            if (n != num)               /* which is just like an ACK for */
                return(state);          /* this packet so fall thru to... */

A KERMIT Program                                                        Page 77



        case 'Y':                       /* ACK */
            if (n != num) return(state); /* If wrong ACK, fail */
            numtry = 0;                 /* Reset try counter */
            n = (n+1)%64;               /* and bump packet count */
            return('C');                /* Switch state to Complete */

        case 'E':                       /* Error packet received */
            prerrpkt(recpkt);           /* Print it out and */
            return('A');                /* abort */

        case FALSE: return(state);      /* Receive failure, stay in B */

        default:    return ('A');       /* Other, "abort" */
   }
}


/*
 *  r e c s w
 *
 *  This is the state table switcher for receiving files.
 */

recsw()
{
    char rinit(), rfile(), rdata();     /* Use these procedures */

    state = 'R';                        /* Receive-Init is the start state */
    n = 0;                              /* Initialize message number */
    numtry = 0;                         /* Say no tries yet */

    while(TRUE)
    {
        if (debug) printf(" recsw state: %c\n",state);
        switch(state)                   /* Do until done */
        {
            case 'R':   state = rinit(); break; /* Receive-Init */
            case 'F':   state = rfile(); break; /* Receive-File */
            case 'D':   state = rdata(); break; /* Receive-Data */
            case 'C':   return(TRUE);           /* Complete state */
            case 'A':   return(FALSE);          /* "Abort" state */
        }
    }
}


/*
 *  r i n i t
 *
 *  Receive Initialization
 */

char rinit()
{
    int len, num;                       /* Packet length, number */

A KERMIT Program                                                        Page 78



    if (numtry++ > MAXTRY) return('A'); /* If too many tries, "abort" */

    switch(rpack(&len,&num,packet))     /* Get a packet */
    {
        case 'S':                       /* Send-Init */
            rpar(packet);               /* Get the other side's init data */
            spar(packet);               /* Fill up packet with my init info */
            spack('Y',n,6,packet);      /* ACK with my parameters */
            oldtry = numtry;            /* Save old try count */
            numtry = 0;                 /* Start a new counter */
            n = (n+1)%64;               /* Bump packet number, mod 64 */
            return('F');                /* Enter File-Receive state */

        case 'E':                       /* Error packet received */
            prerrpkt(recpkt);           /* Print it out and */
            return('A');                /* abort */

        case FALSE:                     /* Didn't get packet */
            spack('N',n,0,0);           /* Return a NAK */
            return(state);              /* Keep trying */

        default:     return('A');       /* Some other packet type, "abort" */
    }
}


/*
 *  r f i l e
 *
 *  Receive File Header
 */

char rfile()
{
    int num, len;                       /* Packet number, length */
    char filnam1[50];                   /* Holds the converted file name */

    if (numtry++ > MAXTRY) return('A'); /* "abort" if too many tries */

    switch(rpack(&len,&num,packet))     /* Get a packet */
    {
        case 'S':                       /* Send-Init, maybe our ACK lost */
            if (oldtry++ > MAXTRY) return('A'); /* If too many tries "abort" */
            if (num == ((n==0) ? 63:n-1)) /* Previous packet, mod 64? */
            {                           /* Yes, ACK it again with  */
                spar(packet);           /* our Send-Init parameters */
                spack('Y',num,6,packet);
                numtry = 0;             /* Reset try counter */
                return(state);          /* Stay in this state */
            }
            else return('A');           /* Not previous packet, "abort" */

A KERMIT Program                                                        Page 79



        case 'Z':                       /* End-Of-File */
            if (oldtry++ > MAXTRY) return('A');
            if (num == ((n==0) ? 63:n-1)) /* Previous packet, mod 64? */
            {                           /* Yes, ACK it again. */
                spack('Y',num,0,0);
                numtry = 0;
                return(state);          /* Stay in this state */
            }
            else return('A');           /* Not previous packet, "abort" */

        case 'F':                       /* File Header (just what we want) */
            if (num != n) return('A');  /* The packet number must be right */
            strcpy(filnam1, packet);    /* Copy the file name */

            if (filnamcnv)              /* Convert upper case to lower */
                for (filnam=filnam1; *filnam != '\0'; filnam++)
                    if (*filnam >= 'A' && *filnam <= 'Z')
                        *filnam |= 040;

            if ((fp=fopen(filnam1,"w"))==NULL) /* Try to open a new file */
            {
                error("Cannot create %s",filnam1); /* Give up if can't */
                return('A');
            }
            else                        /* OK, give message */
                printmsg("Receiving %s as %s",packet,filnam1);

            spack('Y',n,0,0);           /* Acknowledge the file header */
            oldtry = numtry;            /* Reset try counters */
            numtry = 0;                 /* ... */
            n = (n+1)%64;               /* Bump packet number, mod 64 */
            return('D');                /* Switch to Data state */

        case 'B':                       /* Break transmission (EOT) */
            if (num != n) return ('A'); /* Need right packet number here */
            spack('Y',n,0,0);           /* Say OK */
            return('C');                /* Go to complete state */

        case 'E':                       /* Error packet received */
            prerrpkt(recpkt);           /* Print it out and */
            return('A');                /* abort */

        case FALSE:                     /* Didn't get packet */
            spack('N',n,0,0);           /* Return a NAK */
            return(state);              /* Keep trying */

        default:    return ('A');       /* Some other packet, "abort" */
    }
}

A KERMIT Program                                                        Page 80



/*
 *  r d a t a
 *
 *  Receive Data
 */

char rdata()
{
    int num, len;                       /* Packet number, length */
    if (numtry++ > MAXTRY) return('A'); /* "abort" if too many tries */

    switch(rpack(&len,&num,packet))     /* Get packet */
    {
        case 'D':                       /* Got Data packet */
            if (num != n)               /* Right packet? */
            {                           /* No */
                if (oldtry++ > MAXTRY)
                    return('A');        /* If too many tries, abort */
                if (num == ((n==0) ? 63:n-1)) /* Else check packet number */
                {                       /* Previous packet again? */
                    spack('Y',num,6,packet); /* Yes, re-ACK it */
                    numtry = 0;         /* Reset try counter */
                    return(state);      /* Don't write out data! */
                }
                else return('A');       /* sorry, wrong number */
            }
            /* Got data with right packet number */
            bufemp(packet,len);         /* Write the data to the file */
            spack('Y',n,0,0);           /* Acknowledge the packet */
            oldtry = numtry;            /* Reset the try counters */
            numtry = 0;                 /* ... */
            n = (n+1)%64;               /* Bump packet number, mod 64 */
            return('D');                /* Remain in data state */

        case 'F':                       /* Got a File Header */
            if (oldtry++ > MAXTRY)
                return('A');            /* If too many tries, "abort" */
            if (num == ((n==0) ? 63:n-1)) /* Else check packet number */
            {                           /* It was the previous one */
                spack('Y',num,0,0);     /* ACK it again */
                numtry = 0;             /* Reset try counter */
                return(state);          /* Stay in Data state */
            }
            else return('A');           /* Not previous packet, "abort" */

        case 'Z':                       /* End-Of-File */
            if (num != n) return('A');  /* Must have right packet number */
            spack('Y',n,0,0);           /* OK, ACK it. */
            fclose(fp);                 /* Close the file */
            n = (n+1)%64;               /* Bump packet number */
            return('F');                /* Go back to Receive File state */

        case 'E':                       /* Error packet received */
            prerrpkt(recpkt);           /* Print it out and */
            return('A');                /* abort */

A KERMIT Program                                                        Page 81



        case FALSE:                     /* Didn't get packet */
            spack('N',n,0,0);           /* Return a NAK */
            return(state);              /* Keep trying */

        default:     return('A');       /* Some other packet, "abort" */
    }
}

/*
 *  c o n n e c t
 *
 *  Establish a virtual terminal connection with the remote host, over an
 *  assigned tty line.
 */

connect()
{
    int pid,                            /* Holds process id of child */
        connected;                      /* Boolean connect flag */
    char bel = '\07',
        c;

    struct sgttyb
        rawmode,                        /* Controlling tty raw mode */
        cookedmode;                     /* Controlling tty cooked mode */

    if (remote)                         /* Nothing to connect to in remote */
    {                                   /* mode, so just return */
        printmsg("No line specified for connection.");
        return;
    }

    gtty(0,&cookedmode);                /* Save current mode so we can */
    gtty(0,&rawmode);                   /* restore it later */
    rawmode.sg_flags |= (RAW|TANDEM);
    rawmode.sg_flags &= ~(ECHO|CRMOD);
    stty(0,&rawmode);                   /* Put tty in raw mode */

    pid = fork();           /* Start fork to get typeout from remote host */

A KERMIT Program                                                        Page 82



    if (pid)                        /* Parent: send type-in to remote host */
    {
        printmsg("connected...\r");
        connected = TRUE;               /* Put us in "connect mode" */
        while (connected)
        {
            read(0,&c,1);               /* Get a character */
            if ((c&0177) == escchr)     /* Check for escape character */
            {
                read(0,&c,1);
                if ((c&0177) == escchr)
                    write(ttyfd,&c,1);
                else
                switch (c&0177)
                {
                    case 'c':
                    case 'C':
                        connected = FALSE;
                        write(0,"\r\n",2);
                        break;

                    case 'h':
                    case 'H':
                        write(0,"\r\nYes, I'm still here...\r\n",26);
                        break;

                    default:
                        write(0,&bel,1);
                        break;
                }
            }
            else
            {                           /* If not escape charater, */
                write(ttyfd,&c,1);      /* write it out */
                c = NULL;               /* Nullify it (why?) */
            }
        }
        kill(pid,9);                    /* Done, kill the child */
        wait(0);                        /* and bury him */
        stty(0,&cookedmode);            /* Restore tty mode */
        printmsg("disconnected.");
        return;                         /* Done */
    }
    else                  /* Child does the reading from the remote host */
    {
        while(1)                        /* Do this forever */
        {
            read(ttyfd,&c,1);
            write(1,&c,1);
        }
    }
}

A KERMIT Program                                                        Page 83



/*
 *      KERMIT utilities.
 */

clkint()                                /* Timer interrupt handler */
{
    longjmp(env,TRUE);                  /* Tell rpack to give up */
}


/*
 *  s p a c k
 *
 *  Send a Packet
 */

spack(type,num,len,data)
char type, *data;
int num, len;
{
    int i;                              /* Character loop counter */
    char chksum, buffer[100];           /* Checksum, packet buffer */
    register char *bufp;                /* Buffer pointer */

    if (debug>1)                        /* Display outgoing packet */
    {
        if (data != NULL)
            data[len] = '\0';           /* Null-terminate data to print it */
        printf("  spack type: %c\n",type);
        printf("         num:  %d\n",num);
        printf("         len:  %d\n",len);
        if (data != NULL)
            printf("        data: \"%s\"\n",data);
    }

    bufp = buffer;                      /* Set up buffer pointer */
    for (i=1; i<=pad; i++) write(ttyfd,&padchar,1); /* Issue any padding */

    *bufp++ = SOH;                      /* Packet marker, ASCII 1 (SOH) */
    *bufp++ = tochar(len+3);            /* Send the character count */
    chksum  = tochar(len+3);            /* Initialize the checksum */
    *bufp++ = tochar(num);              /* Packet number */
    chksum += tochar(num);              /* Update checksum */
    *bufp++ = type;                     /* Packet type */
    chksum += type;                     /* Update checksum */

A KERMIT Program                                                        Page 84



    for (i=0; i<len; i++)               /* Loop for all data characters */
    {
        *bufp++ = data[i];              /* Get a character */
        chksum += data[i];              /* Update checksum */
    }
    chksum = (((chksum&0300) >> 6)+chksum)&077; /* Compute final checksum */
    *bufp++ = tochar(chksum);           /* Put it in the packet */
    *bufp = eol;                        /* Extra-packet line terminator */
    write(ttyfd, buffer,bufp-buffer+1); /* Send the packet */
}

/*
 *  r p a c k
 *
 *  Read a Packet
 */

rpack(len,num,data)
int *len, *num;                         /* Packet length, number */
char *data;                             /* Packet data */
{
    int i, done;                        /* Data character number, loop exit */
    char t,                             /* Current input character */
        type,                           /* Packet type */
        cchksum,                        /* Our (computed) checksum */
        rchksum;                        /* Checksum received from other host */

#if UCB4X                               /* TOPS-20 can't handle timeouts... */
    if (setjmp(env)) return FALSE;      /* Timed out, fail */
    signal(SIGALRM,clkint);             /* Setup the timeout */
    if ((timint > MAXTIM) || (timint < MINTIM)) timint = MYTIME;
    alarm(timint);
#endif /* UCB4X */

    while (t != SOH)                    /* Wait for packet header */
    {
        read(ttyfd,&t,1);
        t &= 0177;                      /* Handle parity */
    }

    done = FALSE;                       /* Got SOH, init loop */
    while (!done)                       /* Loop to get a packet */
    {
        read(ttyfd,&t,1);               /* Get character */
        if (!image) t &= 0177;          /* Handle parity */
        if (t == SOH) continue;         /* Resynchronize if SOH */
        cchksum = t;                    /* Start the checksum */
        *len = unchar(t)-3;             /* Character count */

        read(ttyfd,&t,1);               /* Get character */
        if (!image) t &= 0177;          /* Handle parity */
        if (t == SOH) continue;         /* Resynchronize if SOH */
        cchksum = cchksum + t;          /* Update checksum */
        *num = unchar(t);               /* Packet number */

A KERMIT Program                                                        Page 85



        read(ttyfd,&t,1);               /* Get character */
        if (!image) t &= 0177;          /* Handle parity */
        if (t == SOH) continue;         /* Resynchronize if SOH */
        cchksum = cchksum + t;          /* Update checksum */
        type = t;                       /* Packet type */

        for (i=0; i<*len; i++)          /* The data itself, if any */
        {                               /* Loop for character count */
            read(ttyfd,&t,1);           /* Get character */
            if (!image) t &= 0177;      /* Handle parity */
            if (t == SOH) continue;     /* Resynch if SOH */
            cchksum = cchksum + t;      /* Update checksum */
            data[i] = t;                /* Put it in the data buffer */
        }
        data[*len] = 0;                 /* Mark the end of the data */

        read(ttyfd,&t,1);               /* Get last character (checksum) */
        rchksum = unchar(t);            /* Convert to numeric */
        read(ttyfd,&t,1);               /* get EOL character and toss it */
        if (!image) t &= 0177;          /* Handle parity */
        if (t == SOH) continue;         /* Resynchronize if SOH */
        done = TRUE;                    /* Got checksum, done */
    }

#if UCB4X
    alarm(0);                           /* Disable the timer interrupt */
#endif

    if (debug>1)                        /* Display incoming packet */
    {
        if (data != NULL)
            data[*len] = '\0';          /* Null-terminate data to print it */
        printf("  rpack type: %c\n",type);
        printf("         num:  %d\n",*num);
        printf("         len:  %d\n",*len);
        if (data != NULL)
            printf("        data: \"%s\"\n",data);
    }
                                        /* Fold in bits 7,8 to compute */
    cchksum = (((cchksum&0300) >> 6)+cchksum)&077; /* final checksum */

    if (cchksum != rchksum) return(FALSE);

    return(type);                       /* All OK, return packet type */
}


/*
 *  b u f i l l
 *
 *  Get a bufferful of data from the file that's being sent.
 *  Only control-quoting is done; 8-bit & repeat count prefixes are
 *  not handled.
 */

A KERMIT Program                                                        Page 86



bufill(buffer)
char buffer[];                          /* Buffer */
{
    int i,                              /* Loop index */
        t;                              /* Char read from file */
    char t7;                            /* 7-bit version of above */

    i = 0;                              /* Init data buffer pointer */
    while((t = getc(fp)) != EOF)        /* Get the next character */
    {
        t7 = t & 0177;                  /* Get low order 7 bits */

        if (t7 < SP || t7==DEL || t7==quote) /* Does this char require */
        {                                   /* special handling? */
            if (t=='\n' && !image)
            {                           /* Do LF->CRLF mapping if !image */
                buffer[i++] = quote;
                buffer[i++] = ctl('\r');
            }
            buffer[i++] = quote;        /* Quote the character */
            if (t7 != quote)
            {
                t = ctl(t);             /* and uncontrolify */
                t7 = ctl(t7);
            }
        }
        if (image)
            buffer[i++] = t;            /* Deposit the character itself */
        else
            buffer[i++] = t7;

        if (i >= spsiz-8) return(i);    /* Check length */
    }
    if (i==0) return(EOF);              /* Wind up here only on EOF */
    return(i);                          /* Handle partial buffer */
}


/*
 *      b u f e m p
 *
 *  Put data from an incoming packet into a file.
 */

bufemp(buffer,len)
char  buffer[];                         /* Buffer */
int   len;                              /* Length */
{
    int i;                              /* Counter */
    char t;                             /* Character holder */

A KERMIT Program                                                        Page 87



    for (i=0; i<len; i++)               /* Loop thru the data field */
    {
        t = buffer[i];                  /* Get character */
        if (t == MYQUOTE)               /* Control quote? */
        {                               /* Yes */
            t = buffer[++i];            /* Get the quoted character */
            if ((t & 0177) != MYQUOTE)  /* Low order bits match quote char? */
                t = ctl(t);             /* No, uncontrollify it */
        }
        if (t==CR && !image)            /* Don't pass CR if in image mode */
            continue;

        putc(t,fp);
    }
}


/*
 *  g n x t f l
 *
 *  Get next file in a file group
 */

gnxtfl()
{
    if (debug) printf("   gnxtfl: filelist = \"%s\"\n",*filelist);
    filnam = *(filelist++);
    if (filecount-- == 0) return FALSE; /* If no more, fail */
    else return TRUE;                   /* else succeed */
}


/*
 *  s p a r
 *
 *  Fill the data array with my send-init parameters
 *
 */

spar(data)
char data[];
{
    data[0] = tochar(MAXPACKSIZ);          /* Biggest packet I can receive */
    data[1] = tochar(MYTIME);           /* When I want to be timed out */
    data[2] = tochar(MYPAD);            /* How much padding I need */
    data[3] = ctl(MYPCHAR);             /* Padding character I want */
    data[4] = tochar(MYEOL);            /* End-Of-Line character I want */
    data[5] = MYQUOTE;                  /* Control-Quote character I send */
}

A KERMIT Program                                                        Page 88



/*  r p a r
 *
 *  Get the other host's send-init parameters
 *
 */

rpar(data)
char data[];
{
    spsiz = unchar(data[0]);            /* Maximum send packet size */
    timint = unchar(data[1]);           /* When I should time out */
    pad = unchar(data[2]);              /* Number of pads to send */
    padchar = ctl(data[3]);             /* Padding character to send */
    eol = unchar(data[4]);              /* EOL character I must send */
    quote = data[5];                    /* Incoming data quote character */
}


/*
 *  f l u s h i n p u t
 *
 *  Dump all pending input to clear stacked up NACK's.
 *  (Implemented only for Berkeley Unix at this time).
 */

#if UCB4X&(~NO_FIONREAD)
flushinput()
{
    long int count;                     /* Number of bytes ready to read */
    long int i;                         /* Number of bytes to read in loop */

    ioctl(ttyfd, FIONREAD, &count);     /* See how many bytes pending read */
    if (!count) return;                 /* If zero, then no input to flush */

    while (count)                       /* Loop till all are flushed */
    {
        i = (count<sizeof(recpkt)) ?    /* Read min of count and size of */
            count : sizeof(recpkt);     /*  the read buffer */
        read(ttyfd, recpkt, i);         /* Read a bunch */
        count -= i;                     /* Subtract from amount to read */
    }
}
#else
flushinput()            /* Null version for non-Berkeley Unix */
{}
#endif /* UCB4X&(~FIONREAD) */

A KERMIT Program                                                        Page 89



/*
 *  Kermit printing routines:
 *
 *  usage - print command line options showing proper syntax
 *  printmsg -  like printf with "Kermit: " prepended
 *  error - like printmsg if local kermit; sends a error packet if remote
 *  prerrpkt - print contents of error packet received from remote host
 */

/*
 *  u s a g e
 *
 *  Print summary of usage info and quit
 */

usage()
{
#if UCB4X
    printf("Usage: kermit c[lbe line baud esc.char]      (connect mode)\n");
    printf("or:    kermit s[diflb line baud] file ...    (send mode)\n");
    printf("or:    kermit r[diflb line baud]             (receive mode)\n");
#else
    printf("Usage: kermit c[le line esc.char]            (connect mode)\n");
    printf("or:    kermit s[difl line] file ...          (send mode)\n");
    printf("or:    kermit r[difl line]                   (receive mode)\n");
#endif
    exit(1);
}

/*
 *  p r i n t m s g
 *
 *  Print message on standard output if not remote.
 */

/*VARARGS1*/
printmsg(fmt, a1, a2, a3, a4, a5)
char *fmt;
{
    if (!remote)
    {
        printf("Kermit: ");
        printf(fmt,a1,a2,a3,a4,a5);
        printf("\n");
        fflush(stdout);                 /* force output (UTS needs it) */
    }
}

A KERMIT Program                                                        Page 90



/*
 *  e r r o r
 *
 *  Print error message.
 *
 *  If local, print error message with printmsg.
 *  If remote, send an error packet with the message.
 */

/*VARARGS1*/
error(fmt, a1, a2, a3, a4, a5)
char *fmt;
{
    char msg[80];
    int len;

    if (remote)
    {
        sprintf(msg,fmt,a1,a2,a3,a4,a5); /* Make it a string */
        len = strlen(msg);
        spack('E',n,len,msg);           /* Send the error packet */
    }
    else
        printmsg(fmt, a1, a2, a3, a4, a5);

    return;
}

/*
 *  p r e r r p k t
 *
 *  Print contents of error packet received from remote host.
 */
prerrpkt(msg)
char *msg;
{
    printf("Kermit aborting with following error from remote host:\n%s\n",msg);
    return;
}

The ASCII Character Set                                                 Page 91


V. The ASCII Character Set

ASCII Code (ANSI X3.4-1968)

There  are 128 characters in the ASCII (American national Standard Code for In-
formation Interchange) "alphabet".  The characters are listed in order of ASCII
value; the columns are labeled as follows:

Bit             Even parity bit for ASCII character.
ASCII Dec       Decimal (base 10) representation.
ASCII Oct       Octal (base 8) representation.
ASCII Hex       Hexadecimal (base 16) representation.
EBCDIC Hex      EBCDIC hexadecimal equivalent for Kermit translate tables.
Char            Name or graphical representation of character.
Remark          Description of character.

The first group consists of nonprintable 'control' characters:


     .....ASCII.... EBCDIC
Bit  Dec   Oct  Hex  Hex    Char  Remarks
 0   000   000   00   00    NUL   ^@, Null, Idle
 1   001   001   01   01    SOH   ^A, Start of heading
 1   002   002   02   02    STX   ^B, Start of text
 0   003   003   03   03    ETX   ^C, End of text
 1   004   004   04   37    EOT   ^D, End of transmission
 0   005   005   05   2D    ENQ   ^E, Enquiry
 0   006   006   06   2E    ACK   ^F, Acknowledge
 1   007   007   07   2F    BEL   ^G, Bell, beep, or fleep
 1   008   010   08   16    BS    ^H, Backspace
 0   009   011   09   05    HT    ^I, Horizontal tab
 0   010   012   0A   25    LF    ^J, Line feed
 1   011   013   0B   0B    VT    ^K, Vertical tab
 0   012   014   0C   0C    FF    ^L, Form feed (top of page)
 1   013   015   0D   0D    CR    ^M, Carriage return
 1   014   016   0E   0E    SO    ^N, Shift out
 0   015   017   0F   0F    SI    ^O, Shift in
 1   016   020   10   10    DLE   ^P, Data link escape
 0   017   021   11   11    DC1   ^Q, Device control 1, XON
 0   018   022   12   12    DC2   ^R, Device control 2
 1   019   023   13   13    DC3   ^S, Device control 3, XOFF
 0   020   024   14   3C    DC4   ^T, Device control 4
 1   021   025   15   3D    NAK   ^U, Negative acknowledge
 1   022   026   16   32    SYN   ^V, Synchronous idle
 0   023   027   17   26    ETB   ^W, End of transmission block
 0   024   030   18   18    CAN   ^X, Cancel
 1   025   031   19   19    EM    ^Y, End of medium
 1   026   032   1A   3F    SUB   ^Z, Substitute
 0   027   033   1B   27    ESC   ^[, Escape, prefix, altmode
 1   028   034   1C   1C    FS    ^\, File separator
 0   029   035   1D   1D    GS    ^], Group separator
 0   030   036   1E   1E    RS    ^^, Record separator
 1   031   037   1F   1F    US    ^_, Unit separator

The last four are usually associated with the  control  version  of  backslash,
right  square  bracket,  uparrow (or circumflex), and underscore, respectively,

The ASCII Character Set                                                 Page 92


but some terminals do not transmit these control characters.
The following characters are printable:

First, some punctuation characters.

     .....ASCII.... EBCDIC
Bit  Dec   Oct  Hex  Hex    Char  Remarks
 1   032   040   20   40    SP    Space, blank
 0   033   041   21   5A    !     Exclamation mark
 0   034   042   22   7F    "     Doublequote
 1   035   043   23   7B    #     Number sign, pound sign
 0   036   044   24   5B    $     Dollar sign
 1   037   045   25   6C    %     Percent sign
 1   038   046   26   50    &     Ampersand
 0   039   047   27   7D    '     Apostrophe, accent acute
 0   040   050   28   4D    (     Left parenthesis
 1   041   051   29   5D    )     Right parenthesis
 1   042   052   2A   5C    *     Asterisk, star
 0   043   053   2B   4E    +     Plus sign
 1   044   054   2C   6B    ,     Comma
 0   045   055   2D   60    -     Dash, hyphen, minus sign
 0   046   056   2E   4B    .     Period, dot
 1   047   057   2F   61    /     Slash

Numeric characters:

     .....ASCII.... EBCDIC
Bit  Dec   Oct  Hex  Hex    Char  Remarks
 0   048   060   30   F0    0     Zero
 1   049   061   31   F1    1     One
 1   050   062   32   F2    2     Two
 0   051   063   33   F3    3     Three
 1   052   064   34   F4    4     Four
 0   053   065   35   F5    5     Five
 0   054   066   36   F6    6     Six
 1   055   067   37   F7    7     Seven
 1   056   070   38   F8    8     Eight
 0   057   071   39   F9    9     Nine

More punctuation characters:

     .....ASCII.... EBCDIC
Bit  Dec   Oct  Hex  Hex    Char  Remarks
 0   058   072   3A   7A    :     Colon
 1   059   073   3B   5E    ;     Semicolon
 0   060   074   3C   4C    <     Left angle bracket
 1   061   075   3D   7E    =     Equal sign
 1   062   076   3E   6E    >     Right angle bracket
 0   063   077   3F   6F    ?     Question mark
 1   064   100   40   7C    @     "At" sign

The ASCII Character Set                                                 Page 93


Upper-case alphabetic characters (letters):

     .....ASCII.... EBCDIC
Bit  Dec   Oct  Hex  Hex    Char  Remarks
 0   065   101   41   C1    A
 0   066   102   42   C2    B
 1   067   103   43   C3    C
 0   068   104   44   C4    D
 1   069   105   45   C5    E
 1   070   106   46   C6    F
 0   071   107   47   C7    G
 0   072   110   48   C8    H
 1   073   111   49   C9    I
 1   074   112   4A   D1    J
 0   075   113   4B   D2    K
 1   076   114   4C   D3    L
 0   077   115   4D   D4    M
 0   078   116   4E   D5    N
 1   079   117   4F   D6    O
 0   080   120   50   D7    P
 1   081   121   51   D8    Q
 1   082   122   52   D9    R
 0   083   123   53   E2    S
 1   084   124   54   E3    T
 0   085   125   55   E4    U
 0   086   126   56   E5    V
 1   087   127   57   E6    W
 1   088   130   58   E7    X
 0   089   131   59   E8    Y
 0   090   132   5A   E9    Z

More punctuation characters:

     .....ASCII.... EBCDIC
Bit  Dec   Oct  Hex  Hex    Char  Remarks
 1   091   133   5B   AD    [     Left square bracket
 0   092   134   5C   E0    \     Backslash
 1   093   135   5D   BD    ]     Right square bracket
 1   094   136   5E   5F    ^     Circumflex, up arrow
 0   095   137   5F   6D    _     Underscore, left arrow
 0   096   140   60   79    `     Accent grave

The ASCII Character Set                                                 Page 94


Lower-case alphabetic characters (letters):

     .....ASCII.... EBCDIC
Bit  Dec   Oct  Hex  Hex    Char  Remarks
 1   097   141   61   81    a
 1   098   142   62   82    b
 0   099   143   63   83    c
 1   100   144   64   84    d
 0   101   145   65   85    e
 0   102   146   66   86    f
 1   103   147   67   87    g
 1   104   150   68   88    h
 0   105   151   69   89    i
 0   106   152   6A   91    j
 1   107   153   6B   92    k
 0   108   154   6C   93    l
 1   109   155   6D   94    m
 1   110   156   6E   95    n
 0   111   157   6F   96    o
 1   112   160   70   97    p
 0   113   161   71   98    q
 0   114   162   72   99    r
 1   115   163   73   A2    s
 0   116   164   74   A3    t
 1   117   165   75   A4    u
 1   118   166   76   A5    v
 0   119   167   77   A6    w
 0   120   170   78   A7    x
 1   121   171   79   A8    y
 1   122   172   7A   A9    z

More punctuation characters:

     .....ASCII.... EBCDIC
Bit  Dec   Oct  Hex  Hex    Char  Remarks
 0   123   173   7B   C0     {    Left brace (curly bracket)
 1   124   174   7C   4F     |    Vertical bar
 0   125   175   7D   D0     }    Right brace (curly bracket)
 0   126   176   7E   7E     ~    Tilde


Finally, one more nonprintable character:

 0    127   177  7F   07    DEL   Delete, rubout

Index                                                                   Page 95


Index


          8th Bit   5, 27                           NAK   7, 36
                                                    Normal Form for File Names   15
          ACK   7
          ASCII   6, 10, 91                         Packet   7, 20
                                                    Parity   22, 26, 91
          Baud   8                                  Prefix   27, 30
          Binary Files   9, 10                      Prefixed Sequence   28
          Binary Mode   8                           Printable Files   10
          Bit Positions   5                         Program, Kermit   56, 65
          Block Check   21, 22                      Protocol   3
          Bootstrap   59
          BREAK   55                                Raw Mode   8
                                                    Records   10
          Capabilies   25                           Remote   5, 8
          CAPAS   25                                Repeat Prefix   27
          Char(x)   6                               Reserved Fields   25
          Checksum   21
          Control Character   6                     Send-Init   23
          Control Characters   20, 91               Sequence Number   12
          Control Fields   22                       Sequential Files   3
          Ctl(x)   6                                Server   5
                                                    Server Command Wait   28
          Data Encoding   22                        Server Commands   32
          DEFINE   53                               Server Operation   28
          Duplex   8                                Short Reply   31
                                                    SOH   8
          EBCDIC   8, 10, 91
          Edit Number   58                          Tab Expansion   10
          Encoding   27, 30                         Text Files   10
          End-Of-Line (EOL)   8, 21                 Timeout   7
          Errors   14                               Transaction   12
                                                    Transaction Log   16
          Fatal Errors   14                         TTY   5
          File Names   15
          Flow Control   8, 16                      Unchar(x)   6
          Full Duplex   8                           User   5

          GET Command   31                          XON/XOFF   8, 16, 91

          Half Duplex   8
          Host   5

          Initial Connection   23

          KERMIT   3

          Language, Programming   58
          Line Terminator   21
          Line Terminator (see End-Of-Line)
          Local   5
          Logical Record   10
          Logical Records   10
          Long Reply   31

Table of Contents                                                        Page i


                               Table of Contents

1. Introduction                                                               3

1.1. Background                                                               3
1.2. Overview                                                                 3

2. Definitions                                                                5

2.1. General Terminology                                                      5
2.2. Numbers                                                                  5
2.3. Character Set                                                            6
2.4. Conversion Functions                                                     6
2.5. Protocol Jargon                                                          7

3. System Requirements                                                        8

4. Printable Text versus Binary Data                                         10

4.1. Printable Text Files                                                    10
4.2. Binary Files                                                            10

5. File Transfer                                                             12

5.1. Conditioning the Terminal                                               13
5.2. Timeouts, NAKs, and Retries                                             13
5.3. Errors                                                                  14
5.4. Heuristics                                                              14
5.5. File Names                                                              15
5.6. Robustness                                                              16
5.7. Flow Control                                                            16
5.8. Basic KERMIT Protocol State Table                                       17

6. Packet Format                                                             20

6.1. Fields                                                                  20
6.2. Terminator                                                              21
6.3. Other Interpacket Data                                                  21
6.4. Encoding, Prefixing, Block Check                                        22

7. Initial Connection                                                        23

8. Optional Features                                                         27

8.1. 8th-Bit and Repeat Count Prefixing                                      27
8.2. Server Operation                                                        28
     8.2.1. Server Commands                                                  29
     8.2.2. Timing                                                           30
     8.2.3. The R Command                                                    31
     8.2.4. The K Command                                                    31
     8.2.5. Short and Long Replies                                           31
     8.2.6. Additional Server Commands                                       32
     8.2.7. Host Commands                                                    34
     8.2.8. Exchanging Parameters Before Server Commands                     34

Table of Contents                                                       Page ii


8.3. Alternate Block Check Types                                             34
8.4. Interrupting a File Transfer                                            36
8.5. Transmitting File Attributes                                            37
8.6. Advanced KERMIT Protocol State Table                                    43

9. KERMIT Commands                                                           48

9.1. Basic Commands                                                          48
9.2. Program Management Commands                                             48
9.3. Terminal Emulation Commands                                             49
9.4. Special User-Mode Commands                                              49
9.5. Commands Whose Object Should Be Specified                               49
9.6. The SET Command                                                         51
9.7. Macros, the DEFINE Command                                              53

10. Terminal Emulation                                                       54

11. Writing a KERMIT Program                                                 56

11.1. Program Organization                                                   56
11.2. Programming Language                                                   58
11.3. Documentation                                                          58
11.4. Bootstrapping                                                          59

I. Packet Format and Types                                                   60

II. List of Features                                                         61

III. Unresolved Issues                                                       63

IV. A KERMIT Program                                                         65

V. The ASCII Character Set                                                   91

Index                                                                        95