EINDISK Experimental Direct Disk Editor  850924 pb.

 This program allows discs to be read, edited and rewritten using 
direct access. It also shows use of some of the MCAL system calls 
on the Einstein. The sector i/o deliberately uses routines built 
in to EINDISK to allow parameters such as bytes/sector and sector
skew to be adjusted. Hopefully it will be extended to cope with 
variable formats.

  Each 512 - byte sector is displayed in two parts to fit on the
screen properly. Starting drive, track and sector may be selected. 

  The editing is dealt with using calls to MOS Tabulate and Modify
commands. This results in the display showing a "fake" address base
of 0FE00H which corresponds to the physical sector buffer address.

  The Modify command also needs a little care: ensure that the 
cursor sits at the start of a byte before entering a full stop to 
terminate "modify". The program then redisplays the modified part 
of the sector for checking before it is rewritten.

   
term