UKM7 for the Tatung PC2000
                    By Richard Limebear G3RWL

This UKM7 is a bare-bones one because of the nature of the PC2000, the serial
port being somewhat constrained in it's flexibility.

Normally use the SETUP program supplied with your machine to set the baud-
rate of the serial port as the program, as supplied, does no initialisation of
the Z80-DART; assuming it to be already set up. Should you wish to use the
facilities of the DART chip, the registers are as set out below together with
the assembly listing. This will work but, if you haven't had a close look at
the circuit diagram of the PC2000, handshaking with the outside world is
non-existant with the DART channel B's CTS & RTS pins hard wired together and
DCD tied to ground.

Should you wish to make speed alterations in any other way, the speed is set
from Z80-CTC channel 2 (port 0EH).


Z80-DART Read & Write registers:

Read Register 0
D7  D6  D5  D4  D3  D2  D1  D0
l   l   l   l   l   l   l   > Rx character available
l   l   l   l   l   l   > INT pending (ch a only)
l   l   l   l   l   > Tx buffer empty
l   l   l   l   > DCD  ]
l   l   l   > RI       ]
l   l   > CTS          ]-- used with "External/status interrupt" mode
l   > not used         ]
> Break                ]


Read Register 1                                     Read Register 2
D7  D6  D5  D4  D3  D2  D1  D0                      D0 to D7 = V0 to V7
l   l   l   l   l   l   l   > All sent              interrupt vector
l   l   l   l   not  used
l   l   l   > Parity error
l   l   > Rx over-run error
l   > Framing error
> not used


Write Register 0
D7  D6  D5  D4  D3  D2  D1  D0
\   /   \       /   >--->--->--- 0 0 0 = Register 0     0 1 1 = Register 3
 \ /     \     /                 0 0 1 = Register 1     1 0 0 = Register 4
  l       \   /                  0 1 0 = Register 2     1 0 1 = Register 5
  l        \ /
  l         l-> 0 0 0 = Null code           1 0 0 = Enable INT on next Rx char
  l             0 0 1 = not used            1 0 1 = Reset TxINT pending
  l             0 1 0 = RST Ext/status INTs 1 1 0 = Error reset
  l             0 1 1 = Channel reset       1 1 1 = Return from INT (ch a only)
  l-> not used


Write Register 1
D7  D6  D5  D4  D3  D2  D1  D0
l   l   l   \   /   l   l   > Ext INT enable
l   l   l    \ /    l   > Tx INT enable
l   l   l     l     > Status affects vector (ch b only)
l   l   l     >0 0 = Rx INT disable        1 0 = INT on all Rx chars (see book)
               0 1 = Rx INT on first char  1 1 = - - - - " - - - - - " - - - -
l   l   > Wait/Ready on R/T
l   > Wait/Ready function
> Wait/Ready enable


Write Register 2 Channel B only D0-D7 = V0-V7 interrupt vector


Write Register 3
D7  D6  D5  D4  D3  D2  D1  D0
\   /   l   \\\\\\\///////  > Rx enable
 \ /    l          > Not used. PROGRAM TO 0.
  l     > Auto enables
  > 0 0 = 5 bit    1 0 = 6 bit    Rx word length
    0 1 = 7 bit    1 1 = 8 bit


Write Register 4
D7  D6  D5  D4  D3  D2  D1  D0
\   /   \   /   \   /   l   > Parity enable
 \ /     \ /     \ /    > Parity Even/odd (0 for odd)
  l       l       > 0 0 = not used      1 0 = 1.5 stop bits
  l       l         0 1 = 1 stop bit    1 1 = 2 stop bits
  l       > not used
  > 0 0 = x1 clock     1 0 = x32 clock
    0 1 = x16 clock    1 1 = x64 clock


Write Register 5
D7  D6  D5  D4  D3  D2  D1  D0
l   \   /   l   l   l   l   > not used
l    \ /    l   l   l   > RTS
l     l     l   l   > not used
l     l     l   > Tx enable
l     l     > Send break
l     > 0 0 = 5 bits (or less)   1 0 = 6 bits    Tx word length
l       0 1 = 7 bits             1 1 = 8 bits
> DTR



;Z80-DART setter-up for Z80, can be assembled with ASM.
;patch this into UKM7TPC2.ASM with your word processor at the point indicated
;in the early part of that program.
;
INITMOD:LDA	INITFLG
	ORA	A
	RNZ
	LXI	H,DATA
	MVI	C,MODCTLP
	MVI	B,9
	DB	0EDH,0B3H		;Z80 OTIR INSTRUCTION
	JMP	CLBUF 
DATA:	DB	18H,1H,0H,3H,0C1H	;reset chan, disable INTs, Rx/Tx enable
	DB	4H,44H,5H,68H		;8 bits, 1 stop, no parity, x16 clock.
CLBUF:	CALL	INMODDATP
	CALL	INMODDATP 		;clear buffers
	RET
;
;