SUMFIX.COM

SUMFIX  reads an Intel format (.HEX) file and computes the  value 
which  must  be  programmed into a PROM to make the  (8-bit)  sum 
zero.   It  automatically  creates  a  new  .HEX  file  with  the 
appropriate  change  made so that the check byte needn't be  hand 
programmed into the PROM.

SUMFIX has a number of other features:

     The PROM "Redcode" (standard CRC used by the BBC for  PROMs) 
     is computed and displayed;  it is also written into the end-
     of-file  record of the output file (it replaces the "execute 
     address").

     The  PROM size is automatically determined by  the  program. 
     This may be overridden in cases when the actual PROM used is 
     of  a different size (for example when the PROM is less than 
     half full).

     The PROM's erased state defaults to 0FFH, but can optionally 
     be specified to be any 8-bit value.  This allows PROMs which 
     erase to zero to be catered for.

     The checkbyte location defaults to address 5 in the PROM, in 
     accordance  with  the BBC's "standard" PROM  header  format. 
     This  can  be  overridden in cases when the  check  byte  is 
     elsewhere.

     The  program will tolerate input files with  an  end-of-file 
     record having the non-standard record type of zero.  However 
     the  output  file always has an end-of-file record with  the 
     correct type (one).


The command line syntax for SUMFIX.COM is as follows:

     SUMFIX hexfile {/switch}

where braces ({}) signify "repeat zero or more times".

hexfile is  the filename of the input and output  files.  A  disk 
        drive other than the default drive may be specified,  but 
        the extension (if any) is ignored:  the files always have 
        the extension .HEX and are in Intel format.   If an error 
        occurs the input file is left unchanged,  otherwise it is 
        replaced by the output file.

switch  is one of the following:

        a:nnnn  specify the PROM start address as nnnnH.

        z:nnnn  specify the PROM end address as nnnnH.

        c:nnnn  specify the address of the check byte in the PROM 
                as nnnnH.

        f:nn    specify  the PROM's erased state (fill value)  as 
                nnH.

When the /a, /z or /c options are used, the address given must be 
the  actual address as in the input file (e.g.  if the data for a 
2K  byte PROM starts at 0C000H,  with checkbyte at  0C005H,  then 
specify /a:c000/z:c7ff/c:c005).

If  the  input file contains data other than Intel  records  (for 
example a section of descriptive text;  this is permitted so long 
as  it  does  not contain a colon character) this  data  will  be 
passed  to the output file unchanged.   The only exception is  if 
the data follows the end-of-file record, in which case it will be 
lost.


Possible error messages from SUMFIX are as follows:

Bad address sequence            The input file contained  records 
                                not   in  an  ascending   address 
                                sequence.

Hex file is empty               The input file contained no data!

Bad PROM address range          The  specified  end  address  was 
                                less  than or equal to the  start 
                                address.

Bad checkbyte address           The checkbyte address was outside 
                                the PROM.

Bad switch format               The   switch   option   was   not 
                                recognised.

Checksum error                  An  Intel  format record  had  an 
                                incorrect checksum.

Bad Intel record type           An  Intel record had an incorrect 
                                record  type (should be zero  for 
                                all data records and zero or  one 
                                for the end-of-file record).

End of file before end of data  No  end-of-file record was found. 
                                Probably a corrupted .HEX file.

File not found                  The  input  file  could  not   be 
                                found.

Directory full                  There  was  insufficient room  in 
                                the   directory  to  create   the 
                                output file.

Disk full                       There  was insufficient  room  on 
                                the disk for the output file.

Close error                     The   output  file  couldn't   be 
                                closed;  possibly  the  disk  had 
                                been changed.

In addition to these "fatal" errors there is one warning message: 
"checkbyte  location occupied".  This indicates that the location 
to  be  changed already contained a value other than  the  PROM's 
erased  state.  An appropriate change to correct the PROM sum  is 
still  carried  out  (if  the  PROMs  sum  was  already  correct, 
necessitating no change, this message may safely be ignored).

 
                                      Richard Russell, 08-09-1986
   COM Ì²0%€
SUMFIX  Z80 m²'(€DDISK    COM ´²':CMPARE  COM Ã²'<€