The following material was obtained from the XEROX Laurel Network.
It is about as close to a 820-II MOUSE as we will ever see.  This
listing is a condensation of several files, combined and edited by Duane
Baugher.


Introduction

     The following information will allow you to add a "trackball" or
joystick to your Xerox 820-II.  You may use any Atari compatible
trackball or joystick.  I personally prefer the Wico trackball.  I have
seen it locally for around $30.

     There are two parts to this project.  First, you must construct a
special cable.  This will require some soldering.  The cost of the cable
is about $10.00.  Secondly, you must assemble the code that is listed in
the second message with the ASM program of CP/M and install it with DDT.
If you do not know how to do either of these tasks, you will need to
find some one to assist you.

     Once both tasks are completed, you will be able to use the
trackball instead of the arrow keys (you may also use the arrow keys).
This will work with any CP/M program.  In many programs, the speed with
which you may move from place to place with the arrow keys is actually
limited by the repeat speed built into the keyboard.  For these
programs, you will be able to move much faster with the trackball.  In
Supercalc and Multiplan the trackball will allow you to move from cell
to cell.  In Spellbinder Word Processor, you may move the cursor
anywhere in the text as well as scroll the text at a speed much faster
than allowed by the cursor keys.  You can even move diagonally across the
screen.  (Spellbinder is considered by most users to be far superior to
Wordstar, with fully adjustable proportional spacing, macro programming,
function keys on the keypad and many other features.  If you are
interested in Spellbinder, message Quenell.wbst.)  While Wordstar will
work with the trackball, the cursor tends to jump because of Wordstars
restriction that the cursor can only be on text.

     The trackball will also work with some of the games written for the
820-II.

The Interface Cable

     You will need the following to construct the interface cable:
            20 pin female dual line ribbon connector
            DB9 male solder tail connector
            6" of 20 wire ribbon
            6" of 22 gauge solid copper wire

     To see what the 20 pin connector looks like, refer to page 48 of
"system components" in the CP/M reference manual.  This will be plugged
into the 40 pin male J8 connector, but we only need the lower 20 lines.

   1.  Mate the ribbon cable into the 20 pin connector.

   2.  On the opposite end of the ribbon cable locate wires 1, 6, 8,
   10, 12, 14, and 20.  Wire 1 is located by the triangle on the side of
   the connector.

   3.  Cut back all other wires by 1".  We will not use them.

   4.  Remove 1/16" of insulation and solder each wire in the solder tail
   of the DB9 as follows: Number on 20 pin DB9 Number Connector

                 1------------------------------8
                 6------------------------------2
                 8------------------------------1
                 10-----------------------------4
                 12-----------------------------3
                 14-----------------------------6
                 20-----------------------------7

   5.  Cut wire 20 at the 20 pin connector and remove 1/4" insulation
   from the side leading to the DB9 connector.

   6.  Remove 1/4" insulation from copper wire on one end and 1/2" from
   the other.

   7.  Form the 1/2" of bare copper wire into a corkscrew shape by
   wrapping in around something like a bar piece of the same wire.

   8.  Solder the bare 1/4" end of the copper wire to 1/4" bare piece of
   ribbon cable, wire 20 and cover the connection with electrical tape.

   9.  With the power off, remove the cover on your 820-II by removing
   the top 2 screws.

   10.  Locate male connector J8 at the back of the CPU board.  Facing
   the front of the computer, the left side of the connector is 1, 2, 3,
   etc.  Gently press the connector onto the pins with pin 1 matching
   the markings on the computer board.

   11.  Take the loose copper wire with the corkscrew end and gently
   press it over pin 20 of male connector J11 which is located to the
   right of J8 and at right angles to it.  Make sure it does not touch
   any other pins on that connector.

   12.  With the DB9 connector sticking out the back, replace the cover.
   Installation of the Software

     In the second part of this message, you will find the code to run
the trackball.  To install it, you will need the ASM and DDT programs.

   1.  Download the program in the second message into a file called
   TB.ASM.

   2.  Assemble the file: A>asm tb

   3.  When that is done load the file into memory: A>ddt tb.hex
   MFDDA,FE5B,126    (this is the part that was missing)

   4.  After it has been loaded in DDT, type <crtl-C> then:
       A>save 4 TB.COM

   To load the trackball code simply type:

            A>tb

     The code will remain in memory until the power is turned off or the
machine is reset.

     I am leaving Xerox January 8, 1985, but until then I will be happy
to answer any questions you have.  I have a number of computers in my
department using trackballs.

Brad Perkins
8*223-4564


     The trackball interface does work with the updated instruction set.
I tried it with an Atari joystick last nite and found it totally useless
with Wordstar.... the cursor moves too fast and the input buffer
overflows easily.  Also, as pointed out, Wordstar allows the cursor to
be only on text.  Now, on to Spellbinder and track ball.

     I had difficulty locating a DB9 connector for the joystick/track
ball to  plug into, so I used a male transision connector.  (yes, a
hack)  Below is the pin numbering for the plug on the joystick/track
ball.

    [----------------]
   [      6 7 8 9     ]
  [    1  2  3  4  5   ]
 [----------------------]

     (I know the drawing is a bit bizzare, but it indicates the wider
side at the bottom and pin one on the left as you look into the plug.)