|File:	LUDEF1.DOC		Date:	82-11-04
|Replaces:
|	LUDEF.DOC	       Dated:	82-10-31

 From:	Gary P. Novosielski
 To:	All LU users

 Subj:	.LBR format definition

|	This file is a revision of and obsoletes the previous
|	version.  Revised material is indicated by a vertical
|	bar (|) to the left of the text.

 0. Introduction
    There have been several requests for a formal definition of
 the format of library (.LBR) files as used by the LU Library
 Utility program and the LRUN command-file load-and-go utility.

    Well, better late than never.  I hope that this definition
 will allow other programmers to make effective use of .LBR
 files in their programming without the need for detective
 work or guesswork about the library format.  Enjoy.

 
 1. Library Overview
    A library is a disk file which is assumed to be logically
 divided into one or more subparts called members.  The library
 have any filename and filetype, except that ".LBR" is
 considered to be the default filetype.  Programs must assume
 and may optionally require the .LBR extension on any file which
 is to be treated as a library.

 2. Access Method
    Libraries are normally treated as Random Record files by
 programs, but must never contain unallocated "holes" which
 are normally allowed in Random Record files.  A library can
 therefore be safely treated as a sequential file if desired.
    This allows copy programs, compacting programs, and remote
 transfer programs to process the library sequentially, and to
 safely make the assumption that the first occurrence of a
 no-record-found condition truly indicates the physical end of
 the library.

 3. Internal Organization
    A library must contain at least one member, the directory,
 and may contain an arbitrary number of other members, up to
|the limits of file size imposed by the operating system.  The
|library may also contain unused sectors which are not assigned
|to any member.  These sectors may occur as a result of the
|deletion of members, or of an unsuccessful add operation.
|   There are no constraints on the contents of members, except
 for the directory, which is always the first member in the
 library, and has a specific format defined later.  However,
 each member must comprise a whole number of 128 byte sectors;
|i.e. each sector of the file belongs to at most one library
 member, and no member has a fractional number of sectors.  A
 member may have 0 sectors.
|   Members may be referred to by a name of up to 8 characters,
|and an extension of up to 3 characters.  The naming rules
|are identical to those for the naming of disk files.
    The start and end points of each member are defined by the
 pointers in the directory entry for the member.  There are no
 embedded start or end marks separating the members.  All
 sectors between the start and end sectors of a member belong
 to that member.

 4. Directory Format
    The directory is the first member of a library, and must
 begin in sector 0 of the file.  It must contain at least one
 sector, and may contain an arbitrary number of sectors.
    The directory is composed of entries.  Each entry is 32
 bytes in length, so that the number of entries is equal to four
 times the number of sectors in the directory.  The number of
 entries determines the maximum number of members in the
 library, one entry per member.
    All entries are initialized to one of three possible states:
 Active, Deleted, or Unused.  The first entry is always active,
 and is the entry corresponding to the directory itself.
    Unused entries always occur after all active and deleted
 entries.  If the directory is scanned beginning with the
 first entry, and an unused entry is found, then all remaining
 entries from there through the end of the directory must also
 be tagged as unused.
    However, active and deleted entries may be mixed in any
 order.  Finding a deleted entry does not guarantee that all
 active entries have been scanned.

 5. Directory Entry Format
    The 32 bytes of each entry have the following significance:
 		
 	Byte			Meaning
 	----	------------------------------------------
 	0	Status  Possible values (in hexadecimal) are:
 		00	Active Entry
| 		FE	Deleted Entry
 		FF	Unused Entry
			Any other value should be treated as
|			a deleted entry.

 	1-8	Name	Rules are identical with those which
 			govern the naming of disk files.  Names
 			shorter than the maximum are padded
 			with spaces.  No two members may have
 			the same name.  The name of the
 			directory member (first entry) is all
 			spaces.

 	9-11	Extension	(same rules as Name)

 	12-13	Index	Pointer to the first sector of this
 			member within the library.  Stored as
 			a two-byte binary value, least signifi-
 			cant byte first.  To begin reading at
 			the start of a member, this value
 			is loaded into the Random Record field
 			of the File Control Block.

 	14-15	Length	The length of the member in sectors.
 			Stored as a two-byte binary value,
 			least significant byte first.  If this
 			value is zero, then the member is null,
 			and the Index field (above) is meaning-
 			less.

 	16-31	Filler 	Reserved for future use.  In unused
| 			and deleted entries, and in the first
|			(directory) entry, these bytes are
|			garbage.  In all other active entries,
 			they are explicitly set to binary zero.
 			Any future enhancements to the .LBR
 			format which use these bytes must
 			recognize this zero value as a
 			non-error condition to allow a library
 			created with an old version of LU to
 			be processed by future versions.

|Notes: In unused and deleted entries all bytes except the
|	Status byte are undefined.
|	   The contents of any data sectors which are not
|	assigned to an active member are not defined.
|	They remain allocated to the .LBR file, to provide
|	for sequential processing, as noted above, but no
|	assumptions should be made as to their contents.
|	These sectors are eliminated from the library when
|	it is reorganized.

 6. Conclusion
    If there are any further questions, comments, requests, etc.
 regarding library format, or if you note any ambiguities or
 contradictions in these specifications, please feel free to
 contact me.

 	Gary P. Novosielski

 	Voice phone: (201) 935-4087  Evenings and weekends
 	CompuServe:  [70160,120]     EMAIL or CP-MIG

 

 End of file.