[GASP.DOC of JUGPDS Vol.7]

  -----------------------------------------------------------------
  !								  !
  !   Simulation with GASP (General Activity Simulation Program)  !
  !								  !
  !                               by				  !
  !								  !
  !           Makoto Yamagiwa (JUG-CP/M No.61)	June 16, 1984  	  !
  !		   Phone: 0424-61-5440 (evenings)		  !
  -----------------------------------------------------------------

		            Abstract

     GASP is a Fortran program package for general purpose simulation.  A
user defined main program in Microsoft FORTRAN-80 or SSS FORTRAN-86 serves
as a chassis into which subroutines are the building blocks.  All simula-
tion models are virtually machine independent.  Thus, you can also use this 
package under MS-Fortran.
     The user must provide the main and key routines.  However, all other 
low-level subroutines have been included in the package as the GASP library
so that you can link them with the main program.



                              Contents

1.  Introduction					page 1
2.  The GASP II Programming language			page 1
3.  Statement of the sample models			page 4
4.  GASP Data Format					page 5
5.  Data Format for Example 1				page 8
6.  How to Use GASP					page 9



  

1.  Introduction

     The GASP (General Activity Simulation Program) is a simulator for 
Discrete Event Simulation models.  GASP II [1] was developed at Arizona State
University from the original GASP developed at U. S. Steel and RAND Corpora-
tion [2].  GASP II was written in FORTRAN-IV for IBM 1130 Computer with the
limitation of 8K words of storage (16-bit per word).  Further updated version
of GASP is available [3].

     The present version of GASP is based on GASP II and has been written for
Microsoft FORTRAN-80 (CP/M-80), SSS FORTRAN-86 and ai-Fortran86 (CP/M-86). 


2. The GASP II Programming Language

2.1 Functional Breakdown of GASP II

     A functional breakdown of the GASP II subprograms is shown in Table 1.
A brief description is given here.  The GASP executive controls a simula-
tion by updating simulation time (TNOW) from event to event and calling 
programmer-written events through subroutine EVNTS.  Subroutine DATAN
initializes all GASP II variables and reads from disk all initial events 
and entities into filing array NSET.

     The storage of information is accomplished by subroutine FILEM.  This
routine inserts the values contained in the buffer storage vector ATRIB into
the first available column of the filing array NSET and calls subroutine SET,
which updates the pointing system to insert the entry into subroutine RMOVE.
This routine removes an entry from NSET,  and stores its row values in the
buffer storage array ATRIB, then calls subroutine SET to update the file by
altering the pointing system.  To find specific entries in a file to locate
an entry whose attributes satisfy stated conditions. The various conditions
for which search can be performed in subroutine FIND.

     Monitoring and error reporting are performed through the use of sub-
routines MONTR and ERROR.  These subroutines have been designed to assist the
programmer in debugging a simulation program.  Subroutine MONTR can also be
used to obtain intermediate results during the course of a simulation run.

     The routines involved in data collection, statistical computations and
reporting, random variable generation, and other support functions are 
listed in Table 1.


        Table 1  Functional Breakdown of the GASP Subprograms
----------------------------------------------------------------------
  Function              !        Subprogram
----------------------------------------------------------------------
GASP Executive          !       Subroutine GASP(NSET)
Initialization          !       Subroutine DATAN(NSET)
Information Storage	!	Subroutine SET(JQ,NSET)
and Retrieval           !	Subroutine FILEM(JQ,NSET)
                        !       Subroutine RMOVE(KCOL,JQ,NSET)
                        !       Subroutine FIND(XVAL,MCODE,JQ,
                        !                	JATT,KCOL,NSET)
Data Collection         !       Subroutine COLCT(X,N,NSET)
                        !       Subroutine TMST(X,T,N,NSET)
                        !       Subroutine HISTO(X1,A,W,N)
Statistic Computations  !	Subroutine PRNTQ(JQ,NSET)
and Reporting 		!       Subroutine ERROR (J,NSET)
Random Deviate		!	Subroutine DRAND(ISEED,RNUM)
Generators              !       Subroutine RANDU(IY,YFL)
                        !       Function UNFRM(A,B)
                        !       Function RNORM(J)
                        !       Function RLOGN(J)
                        !       Function ERLNG(J)
---------------------------------------------------------------------

2.2 A Typical GASP Program in Fortran

     Table 2 and Fig.1 are the basic idea of Single Server Queueing System.
While Listing 1 shows a prototype (skeleton) program for the main and sub-
routine EVNTS of the service system.  Note that the main and EVNTS programs
are user defined and normally follow the format given here.  In subroutine 
EVNTS, "I" is an event code.  Subroutine EVNTS selects one of the events 
ARRVL, ENDSV, or ENDSM.  The programmer (user) needs to write only the 
event subroutines in order to have a complete simulation program.

      Table 2  General conditions of Single Server Queueing System
------------------------------------------------------------------------
ENTITIES    ATTRIBUTES   EVENTS      ATTRIBUTES       RELATIONSHIP
------------------------------------------------------------------------
Customers  Arrival rate  Arrival of  Time of arrival  Customers who wait-
           Arrival type  a customer  Customer  type   ing area of server
           Job type                  Service prior-
                                     ity

Server     Server rate   End of      Time of comple- 
                         service     tion
------------------------------------------------------------------------



Arriving Customers ----> Waiting area ---> Server ---> Departing

Customers -----> Satisfied Customers
          -----> Dissatisfied customers
                 Customers Who have been served.

Fig 1.  General transition of Single Server Queueing System


Listing 1.  Layout of the main and Subroutine EVNTS.

C       MAIN PROGRAM
        DIMENSION NSET(6,ID)
C       ID; to be specified by user
        COMMON  (GASP variables)
        COMMON  (non-GASP variables)
C
C       Initialization of non-GASP variables
        CALL    GASP(NSET)
C       If more runs are desired, insert GO TO statement
C       to either reinitialize non-GASP variables or
C       to call GASP again
        CALL    EXIT
        END
C
        SUBROUTINE      EVNTS(I,NSET)
        DIMENSION NSET(6,ID)
C       ID; to be specified
        COMMON  (GASP variables)
        COMMON  (non-GASP variables)
C
        GO TO (1,2,3), I
    1   CALL    ARRIV(NSET)
        RETURN
    2   CALL    ESERV(NSET)
        RETURN
    3   CALL    ENDSM(NSET)
        RETURN
        END

2.3 GASP Library
     The GASP subprograms given in Table 1 have been provided as the
GASP library (GASPLIB.FOR, GASLIBX.FOR, etc.).  Here is an outline 
hierarchy  for EXA1 (USER1, see 3.2 below).

*EXA1 (Main)
	GASP
		DATAN
		MONTR
		RMOVE
			SET
		*EVNTS
			*ARRVL
				DRAND
				TMST
				COLCT
				FILEM
					SET
			*ENDSV
				COLCT
				HISTO
				TMST
				RMOVE
				FILEM
			*ENDSM
				TMST
				RMOVE
				ENDSV
		SUMRY
	       *OTPUT
		ERROR

Note that the programs with asterisk are user defined.
		
3. Statement of A Sample Modeling

     In the following I am going to describe a model case in detail.
You can interpret the other examples in the similar manner.

	 Example 1: A Single-Channel Queueing Situation

 Program-id.    	USER1.FOR	USER1.F86
 GASP library  		GASPLIB.FOR	GASPLIB.F86
 Load module   		USER1.COM	EXA1.COM
 GASP data file     	GASP1.DAT	GASP1.DAT

 3.1 Statement of the problem
     The system to be simulated consists of a single server who processes 
arriving items sequentially.  When the server is processing an item, other
items arriving must wait for service.  Only a single queue can form, and 
there is no limitation on its length.  The time between arrivals of items
and the processing time for the server are assumed to be exponentially
distributed.  The mean time between the arrival of items is 10 time units
and the mean processing time is 6 time units.  The system is to be simulated
for 3000 time units.  Estimates of the expected value and standard deviation
of the server's idle time , the total time spent by items in system, and the
waiting time of the items are to be calculated.

     All items arriving before time 3000 should be processed, and the sta-
tistics concerning these items should be included in the overall statis-
tics of the simulation. 

        The intial conditions are:

        1) The server is busy and will complete service at time 3.5.
        2) The first new arrival to the system will occur at time 0.0.
        3) No items are waiting in the queue.

3.2 Procedure
	The following programs are necessary:

	1) The main program of the simulation ..... EXA1
	2) Arrival of an item to the system....... Subroutine ARRVL
	3) A completion of the processing of an item by the server
	                                   ....... Subroutine ENDSV
	4) The completion of the simulation at a time specified by 
	   the programmer                  ....... Subroutine ENDSM
	5) Control routine for subroutines ARRVL, ENDSV, and ENDSM
                                           ....... Subroutine EVNTS
	6) To provide information in addition to that normally printed 
   	   in the GASP summary report      ....... Subroutine OTPUT
	
Note that all of the above programs must be written by the programmer
(user).  They have been designated as USER*.*.

4. GASP Data Format
      There are eight types of "Data Card" to be input to GASP.  They are 
listed in Tables 3 through 10, and are stored as GASP*.DAT files in the
card image.

Table 3  Type 1 Data Card for GASP
-----------------------------------------------------------------
GASP variables      Column (FORMAT)	   Definition
Initialized 
-----------------------------------------------------------------
NAME        	    1 to 12 (6A2)       Title of simulation
NPROJ               13 to 16 (I4)       Project number
MON                 17 to 18 (I2)       Month number (MM)
NDAY                19 to 20 (I2)       Day number (DD)
NYR                 21 to 24 (I4)       Year number (19YY)
NRUNS               25 to 28 (I4)   	Number of simulation runs
					to be made
------------------------------------------------------------------

 Table 4  Type 2 Data Card for GASP
----------------------------------------------------------------------
GASP variables      Column (FORMAT)         Definition
Initialized 
----------------------------------------------------------------------
NPRMS               1 to 5 (I5)         Number of sets of parameters
                        		to be used insimulation
NHIST               6 to 10 (I5)        Number of histograms required
                                	for the simulation
NCLCT               11 to 15 (I5)       Number of variables for which
                        		statistics are collected in
                                        subroutine COLCT
NSTAT               16 to 20 (I5)       Number of variables for which
                        		statistics are collected in
                                        subroutine TMST
ID                  21 to 25 (I5)       Number of columns in the filing
                        		array NSET
IM                  26 to 30 (I5)       Maximum number of attributes
                        		associated with any entry of
                                        the filling array
NOQ                 31 to 35 (I5)       Number of files contained in
                        		the filling array
MXC                 36 to 40 (I5)       Largest number of cells to be
                        		used in any histogram
SCALE               41 to 50 (F10.2)    Parameter used to scale attri-
                        		bute value to avoid truncation
                                        errors due to the use of fixed
					point array for the filling 
----------------------------------------------------------------------

Table 5  Type 3 Data Card for GASP. If NHIST > 0, the number of cells
 	 for each histogram used is initialized from Type 3 Data Card.
	 The GASP variable NCELS(K) is the number of cells in histogram
	 K ,not including the end cells.
-----------------------------------------------------------------------
GASP variables      Column (FORMAT)          Definition
Initialized 
--------------------------------------------------------------------
NCELS(1)              1 to 5  (I5)
NCELS(2)              6 to 10  (I5)
NCELS(3)              11 to 15 (I5)
NCELS(4)              16 to 20 (I5)
--------------------------------------------------------------------

Table 6  Type 4 Data Card for GASP.  The values of the vector KRANK
	 are initialized with Type 4 Data Card.
--------------------------------------------------------------------
GASP variables      Column (FORMAT)        Definition
Initialized 
--------------------------------------------------------------------
KRANK(1)              1 to 5   (I5)
KRANK(2)              6 to 10  (I5)
KRANK(3)              11 to 15 (I5)
KRANK(4)              16 to 20 (I5)
--------------------------------------------------------------------

Table 7  Type 5 Data Card for GASP.  This card reads value for the
	 vector INN.  INN(J) is the variable that specifies
	 whether File J is a low-value-first (LVF) or high-value-
	 first (HVF) file. The code for LVF and HVF are 1 and 2,
	 respectively.
-------------------------------------------------------------------
GASP variable
initialized 	    Column (FORMAT)           Definition
-------------------------------------------------------------------
INN(1)              1 to 5   (I5)
INN(2)              6 to 10  (I5)
INN(3)              11 to 15 (I5)
INN(4)              16 to 20 (I5)
-------------------------------------------------------------------

Table 8  Type 6 Data Card for GASP.  This card is used only when
	 parameters are used in the simulation (NPRMS >= 1).
-----------------------------------------------------------------
GASP variables
Initialized 	    Column (FORMAT)            Definition
-----------------------------------------------------------------
PARAM(J,1)          1 to 10  (F10.4)
PARAM(J,2)          11 to 20 (F10.4)
PARAM(J,3)          21 to 30 (F10.4) 
PARAM(J,4)          31 to 40 (F10.4)
-----------------------------------------------------------------

Table 9  Type 7 Data Card for GASP
----------------------------------------------------------------------
GASP variable
initialized 	Column (FORMAT)      	Definition
-----------------------------------------------------------------------
MSTOP		1 to 5 (I5)	       0: End of simulation, event has
                        	       been furnished by the programmer.
                                       MSTOP > 0: The simulation is to
				       end when TNOW >= TFIN.
                                       MSTOP < 0: Programmer indicated 
				       the simulation run is completed
				       and ask the final reports. 
JCLR            6 to 10 (I5)           0: Do not clear statistical
                        	       storage areas.
                                       1: Clear statistical storage
NOPRT           11 to 15 (I5)          0: Final GASP summary report
                                       1: No final summary report
NEP             16 to 20 (I5)          A control variable which
                    		       determine the data card
                                       type at which DATAN will 
                                       begin to process foe the
                                       next simulation run
TBEG            21 to 30 (F10.3)       Beginning time of the simula-
                        	       tion run.
TFIN            31 to 40 (F10.3)       Final or ending time of the
                        	       simulation if MSTOP > 0. 
JSEED           41 to 44 (I4)          Random number seed,
                        	       ISEED = JSEED
----------------------------------------------------------------------

Table 10  Type 8 Data Card for GASP.  Actually there are two kinds of
	  Type 8 Cards. They are used to initialize the filing array and
	  to insert initial entries into it.  Each set of Type 8 Cards 
	  contains the file number (JQ) and the attributes (ATRIB) for
	  one entry that is to be inserted in file JQ. If JQ is negative,
	  the entire filing array is initialized.  If JQ is positive,
	  the values in ATRIB are inserted into an entry in File JQ.
-----------------------------------------------------------------------
GASP variable       Column (FORMAT)         Definition
Initialized 
-----------------------------------------------------------------------
JQ	            1 to 10 (I10)       File number, if JQ < 0 
					the array is initialized.
-----------------------------------------------------------------------
ATRIB(1)            1 to 10 (F10.4)
ATRIB(2)            11 to 20 (F10.4)
ATRIB(3)            21 to 30 (F10.4)
  .                         .
  .                         .
ATRIB(7)            61 to 70 (F10.4)
----------------------------------------------------------------------

  
5.  Data Format for Example 1 (GASP1.DAT)

Column Layout:
              1         2         3         4         5         6
     123456789012345678901234567890123456789012345678901234567890

     TEST-PROG-1    1 2281984   1                          Type 1 Card
         0    1    2    2   25    4    2   22      10.00   Type 2 Card
        20                                                 Type 3 Card
         1    3                                            Type 4 Card
         1    1                                            Type 5 Card
         0    1    0    7     0.0    3000.0  0567          Type 7 Card
             -1                                            Type 8 Card
	    0.0    1.0       0.0       0.0                 Type 8 Card
              1                                            Type 8 Card
         3000.0    3.0       0.0       0.0                 Type 8 Card
              1						   Type 8 Card	
            3.5    2.0       0.0       0.0                 Type 8 Card
              0                                            End of data
       
 Remarks
        File 1 is the event file, and File 2 is the queue of items
        waiting for processing. The attributes associated with each
        of these files are shown below:

	  File 1
        Attribute 1:    Scheduled time of event.
        Attribute 2:    Event Code.
        Attribute 3:    Time customer enters system, if event code
                        is 2.
        Attribute 4:    Not used.

	  File 2
        Attributes 1, 2 and 4: Not used.
        Attribute 3:    Time item entered system.

6. How to Use GASP
6.1 Organization of GASP Disks
    The GASP program package submitted to the Public Domain consists
of the following four volumes.

	Vol.1 of 4: Documentation and CP/M-80 (FORTRAN-80) Version
	Vol.2 of 4: CP/M-86 (SSS FORTRAN/ai-FORTRAN) Version and
		    Source Programs of GASP Subprograms
	Vol.3 of 4: Executable GASP Code for CP/M-86
	Vol.4 of 4: Extended Version of GASP II for F80 and F86

    Those who have only FORTRAN-80 should get Vols. 1, 2 and 4.

6.2 Using Microsoft FORTRAN-80 on CP/M-80
1) Compile user programs in FORTRAN-80
   f80 USER1,tty:=USER1/n  (c/r)

2) Compile GASP Library programs
   f80 GASLIB,tty:=GASLIB/n  (c/r)

3) Link USER1.REL, and GASLIB.REL to make object module
   l80 USER1,GASLIB,forlib/s,EXA1/n/e

4) Execute Object module EXA1.COM
   EXA1  (c/r)

5) Input GASP Data file
   Output GASP data file to Display(3) or Printer(2)
   Enter Output Device number 2 or 3: 2 (c/r)

   Input GASP data file name (max 8 characters): GASP1   (c/r)
   Input GASP data file name: GASP1   DAT

6.3  Using Super Soft FORTRAN-86

 1) Compile user programs in FORTRAN-86
    for USER1.F86  USER1.REL  (c/r)
    cnv USER1.REL  USER1.R86  (c/r)

 2) Compile GASP Library programs
    for  GASLIB.F86  GASLIB.REL
    for  GASLIB.REL  GASLIB.R86

 3) Link USER1.R86, and GASLIB.R86 to make object module
    link86 -o EXEC1 semu USER1 GASLIB sflib.lib mlib.lib

 4) Execute Object module EXEC1.CMD
    EXEC1  (c/r)

 5) Input GASP Data file
    Output GASP data file to Display(1) or Printer(4): 
    Output Device number 1 or 4: 4 (c/r)

    Input GASP data file name (max 12 characters) : GASP1.DAT (c/r)
    Input GASP data file name : GASP1.DAT



                             REFERENCES

[1] A. Alan, B. Pritsker and P. J. Kiviat: "Simulation with GASP II -
    A FORTRAN based Simulation Language," 1969
[2] P. J. Kiviat: "GASP- A General Activity Simulation Program,"
    Applied Research Lab., United States Steel Corporation, 
    Monroeville, Pa., 1963
[3] A. Alan  and B. Pritsker: "The GASP IV Simulation Language," 
     Wiley, New York, 1975


****************************************************************
Editor's comments to Japanese users:

	Japanese documentation on this program package has been
published by the contributor in the following journal.

ÔÏ·ÞÜ ÏºÄ: ¢16bit Ö³ FORTRAN Compiler É Test£, Information,
	  Vol.4 (1985), No.3, p.21