DIAL is an extension to any terminal program allowing
     4 dialing options and then the automatic load
     and execution of the terminal program itself.

Features and functions:

1.  Continual dialing of a number or list of
    numbers from a file until one answers.

2.  Searching of a range of numbers for a carrier.

6.  Z80 code.

7.  Typing of files.

8.  Directory with disk system reset.


This program will only run on z80 based machines.

As distributed DIAL will run as-is on an Osborne-1
double-density machine with a Hayes Smartmodem 1200
or 300 connected to the rs232 port.

The file DIAL11.MAC is the source code for this program.
As originally written Microsoft's M80 and L80 will be
needed to assemble it. Further, Richard Conn's SYSLIB.REL
will be required (version 2.3 or later).  If these are not
available to you there is another way to go about customizing
DIAL for your machine.  I hope someday to have enough time to
do this myself but meanwhile perhaps some enterprising soul
will undertake the task!!  I refer to taking the .com (or .obj)
file and disassemble it using dasm or rezilog etc.  The comments
in DIAL11.MAC and the labels could be transfered to the dis-
assemble listing and even then be translated to an 8080 .asm
file. Failing an 8080 translation, one would at least have a
zasm compatible file that would not require syslib to assemble, or
M80.

As I say, I hope to do this myself some day!!

Another use for the .mac file even if you don't have M80 etc. &
don't want to go to the bother of disassembly etc. is to use the
file to ascertain the locations to patch for your machine. All of
the principal storage is in the first 256 bytes or so of the
program. Simply count the bytes with ddt or zsid and compare them
to the source code.

*************************************************************
******  NOTE: the patch area for this version (1.1) *********
******        is NOT the same as for version 1.0.   *********
*************************************************************

NOTE 2:    Near the start of the program (after the storage area) you
		will find a jump to a routine that sets the baud rate
		on a Osborne 1.  This routine probably cannot be patched
		but rather will definitely require assembly. If you can't
		assemble the .mac file, locate this jump by using the source
		code and zsid and patch the jp opcode (C3) and the next two
		bytes to 00 00 00. This will bypass the initial call and
		run the program at whatever baud you have preset before
		running DIAL.  This will, however mean that the baud rate
		shown in the menu may be inaccurate. It will also mean that
		using the "B" option to change the baud rate will crash the
		program. As long as the "B" option is avoided the program
		should run fine.

Best of luck and feel free to get in touch with me if you run into
problems with installing DIAL on your machine.

=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=-=

Version 1.1 as of 10/20/83
""""""""""""""""""""""""""
The program is pretty well self prompting but a brief
explanation of the functions follows:

1: The repeat option prompts for the number to
   dial. The number is dialed until a carrier is
   detected or the user aborts with ^C. ^X will also
   abandon the dial routine but will not work after
   a connection has been made. ^X is a little faster at
   getting back to the menu.

2: The file dial option will dial numbers
   sequentially from a file. At the end of the file
   the program loops back to the start again.
   This continues until a carrier is detected.
   The file must be structured as follows:
        #231-9538;comments etc.
   ie a # sign followed by the number,
      followed by a ; (semicolon)
      followed by any comments.
      Comments may continue for as many lines as
      you like as the program ignores all up to
      the next # sign. Example:

        #232-0442;.......RCP/M 1 Toronto
	#232-0269;.......RCP/M 2 Toronto
        #231-1262;.......RCP/M 3 Toronto
	#484-9663;.......Another RCP/M Toronto
        #232-2644;.......Heath Toronto
        #423-3265;.......ETI Toronto
        #223-2625;.......Pet UG Toronto
        #624-5431;.......PSI Word-Pro Toronto
        #499-7023;.......PC Canada Toronto
        #222-3626;.......Nightowl Toronto
        #226-9260;.......Willowdale RCP/M, Toronto


       I keep two files on my modem disk,


      1: phn.lst
       Which is a list of all phone numbers I have for
       Bulletin Boards &/or RCP/M Systems.

       If I want a number from a file I just use the
       Type option and get it.


      2: phn.dil
       Which has those more commonly called numbers in it.

       If I want to just dial until I get a carrier
       I run the File dial option with the phn.dil
       file as the specified file.


3: The search function prompts for area code and
   whether or not it is long distance and then
   searches that area for carriers. If one is found
   it is stored to a disk file structured as shown
   for number 2: above.

	Two other methods of dialing are available:
		1: O for one number dial which dials the
		   entered number once only and then
		   returns to the menu.

		2: If the first character struck at the
		   Select? prompt is a digit 1-9 then the
		   O option is assumed and the digit is
		   treated as the first of string of numbers
		   that will constitute a phone number to
		   be dialed.

4: Type will type a file one 'page' at a time.

5: Directory displays the directory for the
   selected drive and resets the disk system.
   (Any disk action also relogs the drives)

6: "M" will allow you to temporarily change the name
   of the program to be loaded when a carrier is found.

7: "I" will allow the temporary change of the modem
   initialization string.

8: "X" will jump to the named program without
   waiting for a carrier.

9: "K" will delete a file from the specified drive.


When a carrier is found for all but the search option
a bell is sounded until a key is struck at which time
the named program is loaded.


Simon Ewins,         08/13/83   (update 10/20/83)
676 Oriole Parkway,
Toronto, Ontario.

Phone: 416-484-9427


-------- end --------