Originated - 7/8/82 by Tom Vyse, San Diego, Calif.

The FAST program is specific to the Osborne 1.

It also will only work on those Osbornes which have 
MPI disk drives. Those can be identified by a plastic
lever hanging down in the right hand side of the 
disk drive slot. This is part of the door interlock
mechanism. Osbornes are also shipped with other, and
frequently slower, drives from different manufac-
turers.

FAST is designed to increase the disk drive step
rate from 20 ms./step (the default) to 6ms./step.
It does this by altering the value in the operating
system parameter table which controls this rate.
The address of this parameter (in both versions
1.2 and 1.3) is EF13H.  The effect of various
parameters in this location are:

            Value   Step Rate
            -----   ---------

              0      6 ms. (MPI only)
              1     12 ms.
              2     20 ms. (Seimens)
              3     30 ms. 

The code to drive this is simply:

      MVI    A,0
      STA    0EF13H
      JMP    0
      END

Not much of a program, but it sure makes programs
with a lot of disk access run nicer. Also, the MPI
drive will operate more quietly at the higher step
rate.

Fini.