MENU.DOC

MENU.COM is a menu-driven turnkey type program.  To compile it you will need
SYSLIB21.REL and MENU.MAC and M80.COM.

In addition you will need DU to modify the system tracks of your turnkeyed disk.

This program is specific to the Osborne-1 Double-Density machine.


Modify MENU.MAC as needed for:

1. The use of a password before running the selected program.
2. The names of the files that are on the disk.
3. The command line parameters passed with the selected file.


After running the selected program the system will return to the MENU with
the following considerations:

1. If the program exits by way of a jump to 0h then the system will return to MENU.
2. If the program ends by way of a RET then the system will return to the A> prompt.

If one of the programs to be included in the menu ends with a ret it should be
modified to end with a jump to 0h in order to return to the MENU.

If you do not wish to run MENU but still want an auto-load of a program on both
a cold and warm boot then just follow the following, substituting your program
name (and parameters if needed) (up to 128 characters total) for MENU.

THIS PROGRAM REQUIRES MODIFICATION TO THE SYSTEM TRACKS OF YOUR DISKS,
BE SURE YOU INITIALLY USE A SPARE DISK TO WORK WITH.

USING DU2 (IF RUNNING ZCPR) OR DU-V77 OTHERWISE:

ENTER:		T0
		S1
		CH7 6 <-----------(this (6) is the length of the file/command line)
		CA8 A:MENU<0> <---(change this to your program name)
		W

TO SET THE NAME OF THIS PROGRAM INTO THE CCP.
   (WAS ALL SPACES)


THEN ENTER:	T1
		S13
		CH57 C3 B6 E5
		W

TO BYPASS THE OVERWRITE TO THE CCP THAT CBIOS 1.4 DOES.
   (WAS:   21 9D E1)

AND THEN:	S1
		T14
		CH38 0
		W
		X

TO REWRITE THE BIOS FOR CCP RE-ENTRY AT BASE OF CCP ON BOTH COLD &
WARM BOOTS SCANNING FOR LENGTH OF COMMAND AND EXECUTING.
   (WAS:  03)



THE SYSTEM TRACKS WILL NOW CONTAIN AN AUTOLOAD OF THE MENU
PROGRAM UPON COLD OR WARM (CONTROL-C) BOOT.



	THE ORIGINAL SYSTEM TRACKS CAN BE RESTORED BY EXECUTING
	CP/M's SYSGEN.COM WITH A 'NON-TURNKEYED' SYSTEM AS THE
	SOURCE DISKETTE.




---------- end -------------