The purpose of tasmio.mac is to interface the TDL ver 1.2 paper
tape macòo cssembler to any CP/M operating system having a Z80 CPU and
at least 20k of memory (will run in 16k system, but is cramped).
The operation of the assembler is in most respects identical to the
operation of the standard CP/M assembler.  The differences are listed
below:

	a. The assumed extension of the source file is 'MAC'.
	b. The extension of the object file (if any) is 'REL'.
	c. The source file must have as its last statement an ".END".
	d. A "Y" in the list field in the command line will output the
	   listing file to the currently assigned system list device.
	e. The assembler converts horizontal tabs to blanks when writing
	   the list file producing large print files (gobbles up disk
	   space).
	f. The assembler will produce Intel hex format object files only
	   if the ".PABS" pseudo operator is used in the source file.
	g. A control C from the console will cause the assembler to
	   return control to CP/M.
	h. The list file is formatted into pages with form-feed charac-
	   ters (the standard TDL assembler uses CRLFs to paginate the
	   listing).
	i. A control S character typed at the console will cause output
	   to the console to freeze (like the CP/M assembler); a con-
	   trol Q must then be typed to reenable console output.


	To create a CP/M version of your TDL assembler, do the fol-
lowing:

	a. Load the assembler in memory beginning at ABASE (070BH in the
	   hex file on this diskette).
	b. Type "save 45 tasm.com" under CP/M.
	c. Type "ddt tasmio.hex"
	d. Type a control C to exit ddt.
	f. Type "save 45 tasm.com"
	g. The assembler is now ready to use - if it doesn't work,
	   check to make sure that you have version 1.2 of the assembler.