This note is from Ward Christensen.

Here is some documentation which will be useful to VDM,
VTI, Flashwriter, or other memory-mapped or 16 line 
video displays:  It modifies the "P" command to scroll
15 lines instead of 23:

	for 1.3 ED:

	AC95   MVI M,F    F=15, SETS NEW LINE COUNT

	FOR 1.4 ED:

	A161B	LXI H,F

in either case, do as follows:  Either SID or DDT ED.COM,
noting how high in memory it went (NEXT value) so you will
know how much to save later.  Then do an L command at the
appropriate address (C95 or 161B), verifying that the
instruction there is either an MVI M or LXI H, with the
previous value (I believe it was 17H).  Then patch in the
new instruction.  Control-C to re-boot, then save nn EDVDM.COM.
Use this several times to be certain it is ok, then 
ERA ED.COM and REN ED.COM=EDVDM.COM.