KERMIT-80(1C)    UCB Microcomputer Users Manual     KERMIT-80(1C)



NAME
     _K_e_r_m_i_t-_8_0 - CP/M 80 file transfer program

SYNOPSIS
     _K_e_r_m_i_t-_8_0 is interactive and understands the following com-
     mands:

     Connect
     Receive
     SENd afn

     ERa afn
     EXit
     Help
     Dir [ afn ]
     LOG ufn
     SET BAud rate
     SET BLock-check-type   1 | 2 | 3
     SET Default-disk   d:
     SET Escape
     SET File-mode   Ascii | Binary | Default
     SET Ibm   ON | OFf
     SET Local-echo   ON | OFf
     SET PArity  Even | Mark | None | Odd | Space
     SET POrt
     SET Vt52   ON | OFf
     SET Warning   ON | OFf
     SHow
     STatus

     The commands and keywords can be abbreviated, CAPITAL
     letters must be entered, small letters are optional.  Typing
     a `?' in place of a command or keyword will display the
     options.  Control-H (^H) is backspace and control-U (^U) is
     delete line.

DESCRIPTION
     _K_e_r_m_i_t is a file transfer and terminal emulation utility
     distributed by Columbia University.  It has been implemented
     for many different computers, including microcomputers.  Any
     two machines running _K_e_r_m_i_t can reliably exchange files over
     normal character terminal lines.  For file transfers, a _K_e_r_-
     _m_i_t program must be running in the microcomputer to exchange
     data packets with the _K_e_r_m_i_t program on UNIX, _C_M_S or another
     micro.  Micro versions differ slightly from one to another
     and only a few are currently supported by UCB, however, in
     principle, any _K_e_r_m_i_t should be able to communicate with the
     UCB UNIX version and any other microcomputer or mainframe
     _K_e_r_m_i_t.  At this time, only UCB micro _K_e_r_m_i_t versions can
     communicate with the UCB _C_M_S _K_e_r_m_i_t ( see IMPLEMENTATION).

     ufn  is a unique cp/m file name of the form



Printed 2/13/84         13 February 1984                        1






KERMIT-80(1C)    UCB Microcomputer Users Manual     KERMIT-80(1C)



          `d:NAME5678.TYP'.  _K_e_r_m_i_t-_8_0 commands allow only
          letters, digits and `@[\]^' in the name and type
          fields.  Other characters cause an error or the command
          acts as if no file name was given.  When an afn can be
          specified, these characters can be overlooked by using
          `?' instead.

     afn  is a ufn or an ambiguous file name of the form
          `d:NAME5678.TYP' with cp/m wild-card characters `?' or
          `*' in the name or type field.  The afn matches all
          files on disk d: with the specified character name and
          type.  `?' matches any single character; `*` matches
          any number of characters from none to the end of the
          name or type field in which it occurs.

     Connect
          The connect command initiates or continues a terminal
          emulation session.  Characters typed on the micro con-
          sole are sent out on the communications line and char-
          acters received by the micro are displayed on the micro
          console.  The transmission speed may have to be set
          before calling up _K_e_r_m_i_t-_8_0, although some _K_e_r_m_i_t-_8_0
          versions can set the rate with the `set baud' command.
          For connection to CMS, the parity should be even (use
          `set ibm on').

          One character is reserved to allow escape from the con-
          nection.  The micro shows the connect-escape character
          each time you connect, but it is usually control-
          backslash (`^\').  The connect-escape character can be
          changed with `set escape'.

          The connect-escape followed by `c' closes the connec-
          tion and returns to _K_e_r_m_i_t-_8_0 command mode.  Close is
          used to switch back to _K_e_r_m_i_t-_8_0 to start a file send
          or receive, to change parameters, etc..  The connect
          command can be used to resume connect mode.  Closing
          connect mode does not drop the terminal connection,
          UNIX or _C_M_S will wait if they are idle or continue to
          output if they are sending to your terminal.  Be sure
          to logout from UNIX or _C_M_S, when that is your inten-
          tion, before closing the connection.

          There are other command characters that follow the
          connect-escape character.  `s' shows the _K_e_r_m_i_t-_8_0
          parameters.  `0' sends a NULL character (ascii 00 hex).
          `b' sends a `break' character (actually a 300 mil-
          lisecond broken line signal).  Two connect-escape char-
          acters send the connect-escape character itself.  The
          connection is not closed, but if output is arriving,
          some characters may be lost between the time the
          connect-escape is typed and the command character is



Printed 2/13/84         13 February 1984                        2






KERMIT-80(1C)    UCB Microcomputer Users Manual     KERMIT-80(1C)



          typed.  `?' displays all the connect-escape commands
          and waits for you to type one.

     Receive
          In receive mode, also called downloading, _K_e_r_m_i_t-_8_0
          attempts to store the file with the name supplied by
          the sending computer.  The first eight valid characters
          before the first period are used as the name part, and
          the first three valid characters after the first period
          are used as the type part.  Some _K_e_r_m_i_t versions will
          not send or receive files with names containing control
          characters or certain special characters.  If a file is
          received with the same name as an existing file on the
          micro, _K_e_r_m_i_t-_8_0 changes the incoming name by appending
          ampersands (`&') to the name part and issuing a warning
          message.  If warning is off, _K_e_r_m_i_t-_8_0 will overwrite
          the existing file on the micro.  BUG: if the file is
          $r/o, cp/m will abort _K_e_r_m_i_t-_8_0 `BDOS err on d: $r/o'.

          All characters are written to the file, both printable
          and control.  All eight bits of each received byte are
          stored if _K_e_r_m_i_t-_8_0 is in parity none mode, otherwise
          the eigth parity bit is trimmed off leaving a seven bit
          character.  Do not forget that the sender may trim off
          the eighth bit itself, or the communication path may
          not pass it (_C_M_S).  Files that are not an exact multi-
          ple of 128 bytes are padded to the next 128 byte boun-
          dry with the cp/m end-of-file character (^Z = 1Ah).

     SENd ufn
          In send mode, also called uploading, files are sent
          from _K_e_r_m_i_t-_8_0 to UNIX _K_e_r_m_i_t, _C_M_S _K_e_r_m_i_t or another
          micro.  Each file is sent with its cp/m name
          (`NAME5678.TYP').  _K_e_r_m_i_t-_8_0 will not send control
          characters or spaces (00-20 hex) in a name but will
          send the rest of the name without them.  Files are sent
          in cp/m directory order.

          All characters are sent exactly as they occur in the
          file, both printable and control.  All eight bits of
          each file character are sent if _K_e_r_m_i_t-_8_0 is in parity
          none mode, otherwise the eigth bit is set to the speci-
          fied parity.  Remember that the receiver may trim the
          eighth bit and may add or delete characters to suit its
          own file system (UNIX may map CR-LF to newline; _C_M_S
          cannot receive eight bits, removes CR-LF for recfm V
          and pads to lrecl for recfm F).

          If the _K_e_r_m_i_t-_8_0 file-mode parameter is default or
          binary, the entire cp/m file will be sent including the
          cp/m end-of-file characters (control-Z is ^Z is 1A
          hex).  Cp/m files are allways a multiple of 128 bytes



Printed 2/13/84         13 February 1984                        3






KERMIT-80(1C)    UCB Microcomputer Users Manual     KERMIT-80(1C)



          long with ^Z is used to pad to the next 128 byte multi-
          ple, if necessary.  BUG: the default file-mode is sup-
          posed to trim off the trailing ^Z's.

          If the file-mode is ascii, the file is truncated at the
          first cp/m end-of-file character (^Z).  BUG: this works
          properly only if the ^Z occurs in the last block, oth-
          erwise, all blocks with ^Z's are truncated and file
          transfer continues.  However, such files are not proper
          cp/m files.

Send / Receive Display
     The packet display shows the progress of a send or receive:

     Number of packets:  12
     Number of retries:   3
     File Name: EXAMPLE.TXT
     ?File renamed to EXAMPLE&.TXT
     RECEIVE  [CR retry, ^X skip file, ^Z quit, ^A abort]
     Noise or Messages Received:

     The number of packets is the count of packets sucessfully
     sent or received.  The count should increment about once
     each second at 1200 baud.  The count includes the send-
     initiate packet (once), the file-name packet (once per
     file), the data packets (once per 91 data bytes), the end-
     of-file packet (once per file) and the end-of-transmission
     packet (once).

     The number of retries is the count of times _K_e_r_m_i_t-_8_0 had to
     restart a packet send or receive.  If the communication line
     is noisy, you may also see junk characters appear below the
     noise line.  If a message is lost or doesn't arrive within
     14 seconds, _K_e_r_m_i_t-_8_0 will retry.  A carriage-return will
     cause one retry, if doing that makes you feel better.
     _K_e_r_m_i_t-_8_0 never gives up, but the remote _K_e_r_m_i_t may quit for
     various reasons.  If the remote sends an error packet,
     _K_e_r_m_i_t-_8_0 will display the message and abort the transfer.
     If the remote quits without sending an error packet, mes-
     sages or a prompt from the remote system may appear under
     the noise and messages line.  You should probably abort with
     control-A.

     The file name is the name of the cp/m file being sent or the
     name given by the sender of a file being received.  The
     error message line is normally blank, but may give warning
     of transmission problems.  _K_e_r_m_i_t-_8_0 will continue trying.
     The next line gives the name of the operation being per-
     formed and a list of control characters.  Control-X discon-
     tinues the current file and starts the next file.  Control-Z
     cancels the whole send or receive, but tries to close the
     packet exchange by notifying the remote _K_e_r_m_i_t.



Printed 2/13/84         13 February 1984                        4






KERMIT-80(1C)    UCB Microcomputer Users Manual     KERMIT-80(1C)



Utility Commands
     Dir [ ufn ]
          Displays the file names, file sizes and space remaining
          on the default drive.  If a ufn is specified, the
          display covers the names matched on the drive specified
          (or default); the space remaining takes all files into
          account.  Typing any key stops the file display and
          displays the space remaining.  If ufn contains any
          characters not allowed by _K_e_r_m_i_t, all files are
          displayed.

     Era ufn
          The erase command is the same as for CP/M.

     EXit The exit command is used to go back to cp/m.  Exit does
          not drop the terminal connection, so be sure to logout
          from UNIX or _C_M_S when that is your intention.  If exit
          is used without logging out of UNIX or _C_M_S, to use
          cp/m, etc., then _K_e_r_m_i_t-_8_0 can be restarted and the
          connect command used to resume the terminal connection.
          CAUTION: inadvertently using the micro exit command
          while still connected to UNIX will logout (actually
          exit from csh).  Use the micro abreviation `ex'
          instead.

     HELP Lists the commands available.  Typing a `?' in place of
          a command gives the same list.  Typing a `?' in place
          of keyword will display the options.  During terminal
          connect mode, a connect-escape character followed by
          `?' lists the connect-escape commands and wait for you
          to type one.

     SET Baud rate
          Set the transmission speed of the communications line.
          Implemented in the Kaypro version, but not in the TRS-
          80 P+T or Morrow MicroDecision versions.

     SET BLock-check-type   1 | 2 | 3
          This sets the type of error checking used during file
          transfer.  Each data or control packet has a block
          check to validate its contents.  1 is a single byte
          checksum and is the default packet checksum.  2 is a
          two byte checksum that is more reliable but is not yet
          supported on UNIX or _C_M_S _K_e_r_m_i_t.  3 is a two character
          cyclic redundancy check (CCITT) and is probably the
          most reliable of the three, but is not yet supported on
          UNIX or _C_M_S _K_e_r_m_i_t.  3 is probably the best checkusm to
          use for micro to micro transfers, but is more compli-
          cated to calculate and may reduce the maximum transfer
          rate.

     SET Default-disk   d:



Printed 2/13/84         13 February 1984                        5






KERMIT-80(1C)    UCB Microcomputer Users Manual     KERMIT-80(1C)



          Changes the default disk drive to disk `d:'.  This is
          necessary for receiving because the sender cannot and
          should not be able to specify the disk drive to write
          on.  For sending, the disk can alternatively be speci-
          fied in the file name to be sent.  CAUTION: the colon
          (:) is necessary; check that the next _K_e_r_m_i_t-_8_0 promt
          shows the proper disk letter.  BUG: if the disk
          selected does not exist on your cp/m, cp/m will abort
          _K_e_r_m_i_t-_8_0 `BDOS err on d: Select'.

     SET Escape
          This allows the connect-escape character to be changed
          (see Connect).  _K_e_r_m_i_t-_8_0 will prompt for the charac-
          ter.

     SET File-mode   Ascii | Binary | Default
          Sets the send file mode (see SENd).

     SET Ibm ON | OFf
          Ibm off is the normal mode for file transfers UNIX and
          other micros.  Ibm ON is used for transfers with _C_M_S
          _K_e_r_m_i_t, it sets even parity and enables IBM xon half-
          duplex line turn around processing.  Set ibm off
          restores the default values for local-echo and parity.

     SET Local-echo ON | OFf
          Normally, local echo is off for communication with both
          UNIX and UCB _C_M_S because both services provide full
          duplex communication with UCB Port Selectors.  To use
          UCB _K_e_r_m_i_t-_8_0 with a non-UCB _C_M_S _K_e_r_m_i_t or other half-
          duplex connection, use `set local on' after `set ibm
          on`.

      SET PArity   Even | Mark | None | Odd | Space
          The normal parity for UNIX is none.  The normal parity
          for CMS is even, however even parity is set by the `set
          ibm on' command.  The parity applies both to terminal
          connection and file transfer, so none is required for
          eight-bit transfers.

     SET POrt
          Some microcomputers have more than one serial port.
          This command allows changing the port to be used.

     SET Vt52 ON | OFf
          The _K_e_r_m_i_t-_8_0 terminal emulation is primitive and is
          based on a DEC VT52 terminal screen without reverse
          scrolling or hard tabs, no keyboard emulation is done.
          If you know that your microcomputer terminal type is
          available from UNIX or _C_M_S, use that terminal type and
          tell _K_e_r_m_i_t-_8_0 to `set vt52 off'.  Otherwise, use a
          terminal type of `kermit' (or `pckermit' if you have a



Printed 2/13/84         13 February 1984                        6






KERMIT-80(1C)    UCB Microcomputer Users Manual     KERMIT-80(1C)



          25-line display).

     SET Warning ON | OFf
          Sets file-warning on or off (see Receive).

     SHow Shows the current setting of all _K_e_r_m_i_t-_8_0 parameters.
          Can be displayed while terminal connected by typing
          connect-escape `?'.  The same as STatus.

     STatus
          Shows the current setting of all _K_e_r_m_i_t-_8_0 parameters.
          Can be displayed while terminal connected by typing
          connect-escape `?'.  The same as SHow.

     Bye, Finish, LOGOut
          Not used at UCB, see Columbia manuals.

EXAMPLES
     For the examples below, the micro is turned on, the disk
     containing _K_e_r_m_i_t-_8_0 is put in the A drive, and your own
     formatted data disk is put in the B drive.  What you type is
     in boldface; annotations appear in italics.

     For UNIX _K_e_r_m_i_t:

     A>                            # _C_p/_m _8_0 _p_r_o_m_p_t, _d_e_f_a_u_l_t _d_i_s_k _A.
     A>mkermit                     # _R_u_n _K_e_r_m_i_t-_8_0.
     Kermit-80 V3.6 (UCB36.16) [TRS-80 II P+T CP/M]# _V_e_r_s_i_o_n _b_a_n_n_e_r
     Kermit-80 A:>                 # _K_e_r_m_i_t-_8_0 prompt, default disk A:.
     Kermit-80 A:>set default b:   # _S_e_t _d_e_f_a_u_l_t _d_i_s_k _t_o _B:.
     Kermit-80 B:>connect          # _C_o_n_n_e_c_t _t_o _t_h_e _c_o_m_m. _l_i_n_e.
                                   # _N_o_w _t_h_e _m_i_c_r_o _a_c_t_s _a_s _a
                                   # _n_o_r_m_a_l _t_e_r_m_i_n_a_l.
                                   # _D_i_a_l-_i_n _o_r _p_r_e_s_s _p_o_r_t-_s_e_l_e_c_t_o_r
                                   # _b_u_t_t_o_n _a_n_d _s_e_l_e_c_t _a _s_y_s_t_e_m.
                                   # _L_o_g_i_n _t_o _y_o_u_r _U_n_i_x _a_c_c_o_u_n_t.
     ...                           # _U_n_i_x _m_e_s_s_a_g_e_s, _e_t_c.
     TERM = (tvi920c): kermit      # _o_r `_p_c_k_e_r_m_i_t', _e_t_c.
     %                             # _N_o_w _y_o_u _a_r_e _t_a_l_k_i_n_g _t_o _U_n_i_x,

     % kermit r                    # _S_e_t _u_p _U_N_I_X _t_o _r_e_c_e_i_v_e _f_i_l_e_s.
     % ^\c                         # _U_N_I_X _w_a_i_t_s, _r_e_t_u_r_n _t_o _m_i_c_r_o.
     Kermit-80 B:>send  *.for      # _S_e_n_d _a_l_l _f_o_r_t_r_a_n _f_i_l_e_s _t_o _U_N_I_X.
     ...                           # _M_i_c_r_o _d_i_s_p_l_a_y_s _s_e_n_d _p_r_o_g_r_e_s_s.
     Kermit-80 B:>                 # _S_e_n_d _i_s _f_i_n_i_s_h_e_d.

     Kermit-80 B:>connect          # _C_o_n_n_e_c_t _b_a_c_k _t_o _U_N_I_X.
     % kermit s frog               # _S_e_t _u_p _U_N_I_X _t_o _s_e_n_d `_f_r_o_g'.
     % ^\c                         # _U_N_I_X _w_a_i_t_s, _r_e_t_u_r_n _t_o _m_i_c_r_o.
     Kermit-80 B:>receive          # _R_e_c_e_i_v_e _t_h_e _f_i_l_e `_f_r_o_g' _o_n _m_i_c_r_o.
     ...                           # _M_i_c_r_o _d_i_s_p_l_a_y_s _r_e_c_e_i_v_e _p_r_o_g_r_e_s_s.
     Kermit-80 B:>                 # _R_e_c_e_i_v_e _i_s _f_i_n_i_s_h_e_d.



Printed 2/13/84         13 February 1984                        7






KERMIT-80(1C)    UCB Microcomputer Users Manual     KERMIT-80(1C)



     Kermit-80 B:>connect          # _C_o_n_n_e_c_t _b_a_c_k _t_o _U_N_I_X.
     % logout                      # _L_o_g_o_u_t _f_r_o_m _U_N_I_X.
     ^\c                           # _R_e_t_u_r_n _t_o _m_i_c_r_o.
     Kermit-80 B:>exit             # _R_e_t_u_r_n _t_o _c_p/_m.
     A>                            # _C_p/_m _8_0 _p_r_o_m_p_t, _d_e_f_a_u_l_t _d_i_s_k _A.

     Similarly, for _C_M_S _K_e_r_m_i_t:

     A>                            # _C_p/_m _8_0 _p_r_o_m_p_t, _d_e_f_a_u_l_t _d_i_s_k _A.
     A>mkermit                     # _R_u_n _K_e_r_m_i_t-_8_0.
     Kermit-80 V3.6 (UCB36.16) [TRS-80 II P+T CP/M]# _V_e_r_s_i_o_n _b_a_n_n_e_r
     Kermit-80 A:>                 # _K_e_r_m_i_t-_8_0 prompt, default disk A:.
     Kermit-80 A:>set drive b:     # _S_e_t _d_e_f_a_u_l_t _d_i_s_k _t_o _B:.
     Kermit-80 B:>set ibm on       # _S_e_t _f_o_r _I_B_M _c_a_l _m_o_d_e.
     Kermit-80 B:>connect          # _C_o_n_n_e_c_t _t_o _t_h_e _c_o_m_m. _l_i_n_e.
                                   # _N_o_w _t_h_e _m_i_c_r_o _a_c_t_s _a_s _a
                                   # _n_o_r_m_a_l _t_e_r_m_i_n_a_l.
                                   # _D_i_a_l-_i_n _o_r _p_r_e_s_s _p_o_r_t-_s_e_l_e_c_t_o_r
                                   # _b_u_t_t_o_n _a_n_d _s_e_l_e_c_t _C_A_L _m_o_d_e.
                                   # _L_o_g_i_n _t_o _y_o_u_r _C_M_S _a_c_c_o_u_n_t.
     ...                           # _C_M_S _m_e_s_s_a_g_e_s, _e_t_c.
     .                             # _N_o_w _y_o_u _a_r_e _t_a_l_k_i_n_g _t_o _C_M_S,
     .                             # _a_s _a _l_i_n_e _m_o_d_e _t_e_r_m_i_n_a_l.

     Kermit-CMS> receive           # _S_e_t _u_p _C_M_S _t_o _r_e_c_e_i_v_e _f_i_l_e_s.
     . ^\c                         # _C_M_S waits, return to micro.
     Kermit-80 B:>send  *.for      # _S_e_n_d _a_l_l _f_o_r_t_r_a_n _f_i_l_e_s _t_o _C_M_S.
     ...                           # _M_i_c_r_o _d_i_s_p_l_a_y_s _s_e_n_d _p_r_o_g_r_e_s_s.
     Kermit-80 B:>                 # _S_e_n_d _i_s _f_i_n_i_s_h_e_d.

     Kermit-80 B:>connect          # _C_o_n_n_e_c_t _b_a_c_k _t_o _U_N_I_X.
     Kermit-CMS> send frog file    # _S_e_t _u_p _C_M_S to send `frog file'.
     ^\c                           # _C_M_S waits, return to micro.
     Kermit-80 B:>receive          # _R_e_c_e_i_v_e `_f_r_o_g._f_i_l' _o_n _m_i_c_r_o.
     ...                           # _M_i_c_r_o _d_i_s_p_l_a_y_s _r_e_c_e_i_v_e _p_r_o_g_r_e_s_s.
     Kermit-80 B:>                 # _R_e_c_e_i_v_e _i_s _f_i_n_i_s_h_e_d.

     Kermit-80 B:>connect          # _C_o_n_n_e_c_t _b_a_c_k _t_o _C_M_S.
     % logoff                      # _L_o_g_o_f_f _f_r_o_m _C_M_S.
     ^\c                           # _R_e_t_u_r_n _t_o _m_i_c_r_o.
     Kermit-80 B:>exit             # _R_e_t_u_r_n _t_o _c_p/_m.
     A>                            # _C_p/_m _8_0 _p_r_o_m_p_t, _d_e_f_a_u_l_t _d_i_s_k _A.

FEATURES
     The Kermit file transfer protocol uses 96 character check-
     summed packets, with ACK/NACK packet responses and timeouts.
     Only printing ASCII characters, control-A, carriage-return,
     line-feed are used for transmission, hence, packets should
     pass through most modems and networks unharmed.  Control
     characters are mapped into two characters, an escape charac-
     ter (usually `#') and a printing character corresponding to
     the control character (control-character exclusive or'ed



Printed 2/13/84         13 February 1984                        8






KERMIT-80(1C)    UCB Microcomputer Users Manual     KERMIT-80(1C)



     with 40 hex).  Some connections may not preserve the eighth
     bit of each byte and are limited to text data.

     _K_e_r_m_i_t-_8_0 uses a fourteen second timeout designed to be much
     longer than UNIX or _C_M_S _K_e_r_m_i_t.  The time out is necessary
     to keep the packet exchange going when lost packets occur.
     _K_e_r_m_i_t-_8_0 never gives up, the operator must manually abort
     the send or receive (see Send / Receive Display).

IMPLEMENTATIONS
     Various microcomputer kermit versions are available from the
     CS Microcomputer Consultant (262 Evans Hall, 642-4072).
     Currently, IBM-PC, TRS-80 II (Pickles and Trout CP/M),
     KAYPRO II and Morrow MICRO DECISION versions are available.
     Versions for the Apple II, Apple II  with cp/m card and the
     Compupro are under developement.  Source for many other
     machines with UCB changes is available, but versions built
     from them cannot be supported by UCB, since machines and
     staff time for testing are not available.

     Micro kermits to be used for file transfer with UCB CMS must
     have local modifications.  The UCB port selector echos
     received characters.  This requires that the micro kermit
     not echo locally.  More important, the echoed start-of-
     header from a packet sent is received and retained by the
     serial port circuitry and confuses the packet driver into
     thinking its own tail is the next packet to be received.
     These UCB modifications should not interfere with use on
     other CMS systems except that `set local on' should be used
     after `set ibm on' since UCB ibm does not set local echo.

SEE ALSO
     kermit(1c), kermit-86(1c), kermit-CMS(1c), upload(1).

     _K_e_r_m_i_t _U_s_e_r_s _G_u_i_d_e, Fourth Edition (19 July 83), Frank da
     Cruz, Daphne Tzoar, Bill Catchings

     _K_e_r_m_i_t _P_r_o_t_o_c_o_l _M_a_n_u_a_l, Fourth Edition (4 November 83),
     Frank da Cruz, Bill Catchings

BUGS for _K_e_r_m_i_t-_8_0 Version UCB36.16
     Send with file-mode default is supposed to truncate the
     trailing ^Z's (cp/m end-of-file padding).  Send with file-
     mode ascii is supposed to truncate the file at the first ^Z,
     but works properly only if the ^Z occurs in the last block,
     otherwise, blocks with ^Z's are truncated but file transfer
     continues.  However, such files are not proper cp/m files.

     When ^Z or ^X are used to terminate a receive, _K_e_r_m_i_t-_8_0
     does not stop immediately or may even abort or hang.  This
     is due to protocol differences between our older UNIX _K_e_r_m_i_t
     and _C_M_S _K_e_r_m_i_t and the newer _K_e_r_m_i_t-_8_0.



Printed 2/13/84         13 February 1984                        9






KERMIT-80(1C)    UCB Microcomputer Users Manual     KERMIT-80(1C)



     Certain cp/m BDOS errors abort _K_e_r_m_i_t-_8_0.  Simply type CR or
     ^C, wait for cp/m to warm boot, and reload _K_e_r_m_i_t-_8_0.  Any
     operation on an invalid disk gives `BDOS err on D: Select'.
     ERA of a $r/o file will give `BDOS err on A: R/O'.

     _K_e_r_m_i_t-_8_0 commands allow only letters, digits and `@[\]^' in
     the name and type fields.  Other characters cause an error
     or the command acts as if no file name was given.

     When connected to UCB CAL mode, a BREAK must be used to
     interrupt output since CAL mode is half-duplex.  _K_e_r_m_i_t-_8_0
     cannot generate a BREAK.

     The Kaypro displays RUBOUTS (7F hex).  CMS uses rubouts as
     idle characters to hold the line while it prepares to send
     the next packet, hence for very long delays, enough RUBOUTS
     may be displayed below the noise line to to scroll the
     display which messes up the full screen presentation.

     If the file does not exist for a send command, the error
     message is displayed on line 5 assuming the packet display
     is up, which it is not, hence the message and the prompt may
     appear in a field of previous lines.

     PDP-11 UNIX _K_e_r_m_i_t (A-F) fails to respond at the end of a
     send or receive command.  It appears that UNIX does not
     respond to an "EOT" message.  The file has been transfered
     correctly.

     The _K_e_r_m_i_t-_8_0 retry counter increments on each new file when
     receiving from UNIX.  The fact that the retry counter incre-
     ments at the end of each new file, suggests a timing or pro-
     tocol problem.  File transfer is not affected.

     Please report other problems to micros@opal or the CS Micro-
     computer Consultant (262 Evans Hall, 642-4072).

BUGS for _K_e_r_m_i_t-_8_0 Version UCB 3.1
     These old bugs are listed for convienence.  All _K_e_r_m_i_t-_8_0
     users should upgrade to the latest version UCB36.16.

     Line noise or system messages can cause a received packet to
     be longer than 96 characters, hence exceeding the receive
     packet buffer.  Depending on the length of the packet and
     the junk, this could cause the file buffer, subroutine argu-
     ments, and other later data to be clobbered.  Probably mani-
     fested as occasional junk in files and mystery probelms that
     go away.

     When sending in image mode, sometimes an additional 32k of
     data appears in the file.




Printed 2/13/84         13 February 1984                       10






KERMIT-80(1C)    UCB Microcomputer Users Manual     KERMIT-80(1C)



     VT52 emulation does not work properly in most versions.
     Caused by absence of cursor addressing and errors in the
     vt52 to terminal table.

     CP/M files with $r/o or $sys attributes set loose one or
     more characters of the file type when that file is sent out
     because the attribute bit (bit 8) on the type characters
     causes them to be rejected.

     If a duplicate file name is received kermit crashes with
     "file r/o" if the existing file is $r/o.  This is because
     the attribute bits are not cleared in the file control block
     (fcb) after the initial open and, hence, the modified
     filename is created $r/o and kermit cannot write it!









































Printed 2/13/84         13 February 1984                       11