OKIC
OKIC/CPM.COM (CP/M version)
OKIC/EX.COM  (Osborne Executive version)
copyright (c) 1985 by Randall B. Sparks

OKIC  creates alternate character sets for the Okidata  Microline 
92  dot-matrix printer.   From within the OKIC program,  you  can 
create  new character sets,  save a character set to a disk file, 
load a previously created set and edit it,  download a set to the 
printer,  and produce sample strings from the character set being 
edited to assist you in designing and editing new characters.  An 
alternate  character  set  may  then  be  used  at  any  time  by 
downloading  it to the printer,  either with OKIC or with PIP.

All  commercial  rights to the OKIC program are reserved  by  the 
author.  However, the program is released into the public  domain
and  permission is given to make unlimited copies of the  program 
for non-commercial purposes.

When OKIC is run, the following menu appears:

     OKIC MENU

     (C)reate a new character set
     (L)oad (from disk) a character set to edit
     (E)dit the current character set
     (S)ave the current character set to a disk file
     (D)ownload the current character set to the printer
     (P)rint a sample of the alternate character set
     e(X)it program

     Which?

Select what you want to do by typing one of the highlighted  keys 
(c,l,e,s,d,p, or x).

(C)reate:

The  first thing you will want to do is to create a new character 
set.  When you select Create from the menu, the current character 
set  is cleared and the Edit mode is entered.   You will then  be 
asked which character you want to edit.   At this point, type the 
key  for the character you want to edit and press  RETURN.   (See 
below  for a description of the Edit mode.)  If you don't want to 
edit, just press RETURN to get back to the menu.

(L)oad:

If you have previously created and  saved  an alternate character 
set,  you may load it for further editing or downloading with the 
Load  command.   You  will  be  asked for  the  filename  of  the 
character set file. 

(E)dit:

In  the Edit mode,  you will be shown a list of which  keys  have 
already  been  defined in the current character set and  will  be 
asked  which  key  you now want to edit.   After  you  enter  the 
character to edit,  the screen will look like this (assuming  the 
keys shown have already been defined and you select 'c' to edit:

Keys assigned so far in current character set (descenders dim):

! # $ % & 1 3 5 7 9 A B C [ ] a b

Key being edited: c

Use arrows to move. Enter "X" for pixel, SPACE to erase an "X".

                   11
          12345678901
         -------------
        1|           |
        2|           |
        3|           |
        4|           |
        5|           |
        6|           |
        7|           |
         -------------

The  cursor will appear in the upper left-hand corner of the box.  
Each  character  printed by the printer consists of a  matrix  of 
pixels (dots) 11 columns wide by 7 rows tall. By using the cursor 
keys, you can move around within the box, turning a pixel on with 
and 'X' (or 'x'),  and turning any pixels off with the space bar.  
When you are finished editing the character,  press RETURN.   You 
will then be asked whether the character is a Descender, that is, 
whether  it should be printed with the last two  rows  descending 
below the base line as in the case of the letters 'p',  'y,  'g', 
etc.   You  will also be given an opportunity to abandon the edit 
of   this  character.    If  the  character  has   been   defined 
previously,  abandoning  the current edit will restore it to  its 
former   definition.    After  you  have  created  one  or   more 
characters,  the  keys you have edited will appear at the top  of 
the edit screen.  If a character has been defined as a descender, 
it  will  appear in the dim video mode (in the Osborne  Executive 
version) or with an underscore ('_') following the character  (in 
the CP/M version).

(S)ave:

After  you have created a character set,  save it on a disk  with 
the  Save option on the menu.   You will be asked for a  filename 
for the  character set file.   The filename must follow the  CP/M 
standard  of  [d:]filename[.ext],  that  is,  an  optional  drive 
specification, a filename of up to 8 characters in length, and an 
optional  extension.   You  will  likely want to  give  the  same 
extension (eg. .oki) to all your alternate character set files.

(D)ownload:

Downloading  sends the alternate character set to the printer  so 
that  it  will  be  available for use.   You  will  be  given  an 
opportunity  to  cancel  the download if  you  have  accidentally 
selected this command.

(P)rint sample:

While  you are editing a character,  you may want to see what  it 
will look like when printed.  You can do this by returning to the 
menu,  downloading the character set to the printer, and printing 
a  sample  string containing the characters you have included  in 
your alternate character set.   You can then continue editing the 
current character set.  You will be asked which pitch to use (10, 
12,  or 17 characters per inch) and for a sample  string.   Enter 
any string of characters which you have defined in your alternate 
character set.

An  alternate character set may be used by any program which uses 
the printer (such as WordStar).   First,  the alternate character 
set  must  be downloaded to the printer.   This can  be  done  by 
Loading the character set and the Downloading it with OKIC, or by 
simply  sending  the character set file to the printer with  PIP.  
When  an alternate character set file is PIPed,  the  "o"  option 
(Object file) should be used. To download a character file called 
"charfile.oki"  with  PIP,   for  example,  you  would  type  the 
following from the CP/M command prompt:

pip lst:=charfile.oki[o] <RETURN>

The alternate set will then be available, along with the standard 
set,  as  long  as  the printer  remains  on.   To  activate  the 
alternate set, the printer must be sent the sequence of the ASCII 
'Escape'  character (decimal 27) followed by the ASCII  character 
'2' (decimal 50).   To return to the standard character set, send 
the sequence ASCII character 'Escape' followed by ASCII character 
'0'  (decimal 48).   You can install WordStar to send these codes 
from two of the user-definable print functions  (^PQ,  ^PW,  ^PE, 
^PR).   It  is also possible to send these control codes directly 
from the CP/M command prompt.   Simply activate the printer  with 
CONTROL-P  and press the 'ESCAPE' key,  the '2' or '0'  key,  and 
RETURN.

When an alternate character set is downloaded with OKIC, only the 
characters  in  the current set will be  available.   However,  a 
character  set PIPed to the printer will overlay  any  previously 
downloaded  character set.   That is,  any characters defined for 
the first set PIPed to the printer which are not also defined  in 
the  second set PIPed will still be available along with the  new 
set of characters.

A sample alternate character set, 'SPRSCRPT.OKI' is included with 
the OKIC.COM program.  This character set was intended to be used 
for printing superscript characters,  but could also be used just 
to print smaller characters.

Notes:

OKIC  was  written in Turbo Pascal for a system consisting of  an 
Osborne Executive and an Okidata m92 printer.   I suspect that it 
will  also  work  with  the  Okidata m93  printer  and  that  the 
Executive version will work fine with an Osborne I as well, but I 
have no way to test this.  The general CP/M version is  identical 
except that several graphics characters and functions relating to 
manipulation  of  the  screen  display have  been  replaced  with 
characters and functions which should work on any CP/M system.  I 
have  not  been  able to test  this,  however.   There  are  also 
undoubtedly hidden bugs.   Any comments,  suggestions, etc. would 
be appreciated.  Just remember the overseas postage:

     Randall Sparks
     Kunigundendamm 150
     D-8600 Bamberg
     West Germany