PRNTDF  Version 1.0
                             Copyright May, 1986
                             All rights reserved

Steve T. Jones
East Central College
P.O. Box 529
Union, MO 63084


PRNTDF (PRiNT DirFiles.dat) was written to facilitate keeping track of the
contents of user group disks.  It reads the DIRFILES.DAT file often used by
BBS's and other public domain sources to document disk contents.  The help
screen is reproduced below:

-------------------------------------------------------------------------------
                              PRNTDF Version 1.0
PRNTDF accepts single-character parameters which may in any order; they may be
lumped together or separated by spaces.   No attempt is made to trap illogical
or contradictory choices; an invalid choice terminates the program.

PARAMETERS:  A,B,C, or D - Drive where DIRFILES.DAT is located
                           (default = current drive)
             F - Formfeed (^L) before printing (default = no formfeed)
             N - No print (default = print)
             S - Screen display (default = no screen display)
             T - Text file output (default = no DIRFILES.PRN output)
             ? - Display this screen (default = no help)

EXAMPLES:    PRNTDF        (print DIRFILES.DAT from the current drive with no
                           formfeed to printer and no screen display -- this
                           is the default)

             PRNTDF S N    (display DIRFILES.DAT on screen with no print --
                           same as DIRFILES.COM with no edit function)

             PRNTDF CFS    (print DIRFILES.DAT from drive C after a formfeed
                           and echo the file to the screen)
-------------------------------------------------------------------------------


An invalid parameter causes the program to halt and display the help screen.
In this case, however, the first line is replaced with:

* * * *  PRNTDF v. 1.0 ERROR:  Invalid parameter(s): X, X ...


If DIRFILES.DAT is not found on the indicated drive, the program halts and
displays the help screen with the line below replacing the first line:

* * * *  PRNTDF v. 1.0 ERROR:  File not on drive X


If a drive which CP/M does not know about (determined by BDOS function 24) is
specified, the following line replaces the first line when the help screen
is displayed:

* * * *  PRNTDF v. 1.0 ERROR:  Drive X not found


If all goes well, the following message is displayed:

PRNTDF Version 1.0  (Copyright 1986 by Steve T. Jones)


In addition, the following messages are displayed as appropriate:

... Sending FormFeed (^L) to printer
... Writing DIRFILES.PRN
... Sending output to printer
... No screen display