SETDRU.DOC                                         Page 1


Copyright 1983  Michael M Rubenstein

Permission is granted to distribute this software and documentation 
provided no fee is charged and the copyright notice is retained.



Credit where credit is due.

SETDRU was written in C and Z80 assembly language.  It was compiled with 
the Software Toolworks C80 compiler and Microsoft M80 assembler.

CP/M  and  CP/M  Plus are trademarks  of  Digital  Research.   WordStar, 
MailMerge, and SpellStar are trademarks of Micropro International 
Corporation.  Microsoft, Multiplan are trademarks of Microsoft 
Corporation.  The Word Plus is a trademark of Oasis Systems.  Perfect 
Writer is a trademark of Perfect Software.  Z80 is a registered 
trademark of Zilog, Inc.



What is it?

Ok, you got a hard disk for your CP/M system.  It's great having all 
that disk space, but then there are the problems.  The directories get 
pretty big;  even with a sorted listing (as from SD) it's pretty hard to 
keep track of what you've got.  So, you start putting things in 
different user areas.  CP/M sure doesn't make that easy though.  
Fortunately, there are a number of programs (SWEEP for example) which 
make it easy to move things around.

Now that things are in different user areas, you can keep track of them, 
but there's another problem -- you end up with lot's of copies of some 
of those programs because CP/M doesn't let you access a program from 
more than one user area.  So you search around and find some program 
which will let you access a program from any user area (and from any 
disk, so you don't always have to specify the disk).  ZCPR by Richard 
Conn works nicely.  That helps with a lot of your programs, but not with 
all.

What's the problem?  Well, a lot of the programs you want to use need 
overlays.  Many -- too many -- don't allow you to specify where those 
overlays will be.  So you need copies, of the overlays at least, on each 
user number.  Others need data files or swap files.  A system can get 
pretty cluttered just with WordStar overlays.

SETDRU allows you to use most (unfortunately, not all) programs with 
some of the files used by the program redirected to standard drive and 
user areas.  When combined with something like ZCPR it allows a single 
copy of a program to be accessible from any drive and user area.













SETDRU.DOC                                         Page 2


What's it need?

SETDRU requires CP/M 2.2 Z80 processor.  It will run with a minimum of 
memory.  SETDRU will probably not be very useful unless the system 
contains a hard disk.

I have reports that SETDRU also works under CP/M Plus.

An 8080 version of SETDRU is being prepared by another person and should 
be available soon.



How does it work?

SETDRU installs a "filter" in high memory which monitors file accesses 
and modifies them, if necessary, to use standard drive and user areas.
This filter is a temporary thing; it will disappear as soon as the 
program terminates.

When you apply SETDRU to a program, you tell it which files need to be 
redirected to another drive and user number.

SETDRU may be installed as a modification to the program (integrated) or 
as a separate program which loads and executes the desired program.

Advantages of integrating SETDRU with the program:

    1.  There's one less file to keep track of.

    2.  In many cases, because of the allocation unit of CP/M, no extra 
        disk space is required.

Advantages of separating SETDRU from the program:

    1.  This technique may be used with programs, such as WordStar, 
        which verify the program on disk.  (WordStar does this when you 
        try to use MailMerge or run a program.)

    2.  Since the program is unchanged, installation procedures are not 
        affected.  Also, some programs may modify themselves.  This is 
        only possible with separate installation.

    3.  If you haven't installed a system to make programs accessible to 
        any user area, you only have a small program (about 1k) to make 
        multiple copies of in different user areas.



When won't it work?

There are several things a program might do which will make it 
impossible to use SETDRU with it.  SETDRU cannot handle programs which:

    1.  Require the CCP to remain resident (e.g. EX or SYNONYM).








SETDRU.DOC                                         Page 3



    2.  Use the BDOS entry address (at location 6) to determine 
        addresses in the BDOS.

    3.  Modify the device field in the FCB after the file is opened.  
        (This should never happen, but, of course, it does.  This is the 
        problem with applying SETDRU to MultiPlan.)

There are, undoubtedly, other situations which will make SETDRU 
unusable.  SETDRU makes some assumptions as to what is intended.  These 
assumptions are usually valid, but may not always give the desired 
result.



Installing SETDRU.

When SETDRU is run, a summary of the instructions is displayed and you 
will be asked a series of questions.  At any point in the procedure, you 
may terminate without installation by typing control C (^C).  Upper or 
lower case may be used.

The first question is

    Do you want SETDRU integrated with the program (y or n)?

Respond "y" or "n" (and press return).

SETDRU will then ask for the name of the program to which it is to be 
applied.  The file type (usually .COM, but it may be different for 
special situations) must be specified.

If SETDRU is to be integrated with the program, a copy must be 
accessible.  The drive must be specified if it is not on the default 
drive.  Make sure you have another copy (several others!!!) as backup in 
case you have to reinstall SETDRU or you find it won't work.

If SETDRU is not to be integrated, the program need not be available.  
The drive specified is the drive from which the program is to be loaded 
when invoked.  In this case, you will be asked for the user number from 
which the program is to be loaded.

SETDRU then asks

    What is the name of the program to be created?

Enter the name you wish to use to invoke the program.  Again, the file 
type (usually .COM) must be specified.  The drive on which the output is 
to go may also be specified.  Note that this name may be the same as the 
name of the program to which SETDRU is applied.  This is fairly normal 
when integrating and may occasionally be useful when not integrating.

You will then be asked for a list of up to 8 files which are to be 
redirected.  If you don't need to use all of them, just press return to 
terminate.








SETDRU.DOC                                         Page 4



If the drive is specified, it is the drive where the program will look 
for the file at run time.  The user number is the user number where the 
program will look.  If not specified, the current (AT INSTALLATION TIME) 
drive and/or user number is used.

Now comes the hard part -- deciding on the file redirection.  The order 
in which the files are specified is important.

File names may be ambiguous (using "?" or "*") or unambiguous.  When a 
the program attempts to open, search for, create, rename, or delete a 
file, the list of files will be scanned.

For an open or search, the file will match the first ambiguous or 
unambiguous name on the list.  If the name on the list is ambiguous, an 
attempt will be made to open the file on the drive specified by the 
program.  If this fails, the open will be attempted on the drive and 
user specified in the list.  If the name on the list is unambiguous, the 
file will always be redirected.

For the other operations, only unambiguous names in the list may match.  
If there is a match, the file will be redirected.

In any case, if there is no match, the file will not be affected.



Examples.

The rules for redirection look more complicated than they really are.  
For most practical purposes, you may just assume that an input file 
matching an ambiguous name will be redirected only if it cannot be 
otherwise found, and that an input or output file which matches an 
unambiguous name will always be redirected.

There are a few things to watch out for.  Remember that most programs do 
not create files with the name you finally see.  It's common to use the 
same name with a file type of .$$$, but other schemes are sometimes 
used.  You will have to specify the name actually used for creation of 
the file.

Also, it's possible to really confuse a program if the order of the 
files in the list is not correct.  For example, if you have the names

    foo.*
    foo.bar

in the list, the program may write foo.bar to a redirected drive and 
user number, but then read a copy on the current drive (or the drive 
specified by the program) and the current user.  It's almost always best 
to put unambiguous file names first in the list.

Example 1:  CAT  (public domain catalog program).

This is a simple case.  The program uses a file called MAST.CAT, 








SETDRU.DOC                                         Page 5


normally on the current drive and user.  There is no reason not to use 
an integrated installation.  If you wish to keep MAST.CAT on drive A: 
user 0, the file list consists of

        A:MAST.CAT     user 0

Example 2:  Perfect Writer

This is only a little more complicated.  If you use an integrated 
installation, you will have to use a plain copy of the program if you 
wish to modify Perfect Writer, so a separate installation of SETDRU 
should be considered.  Let's assume we decided to use an integrated 
installation and put up with a little more work to modify the program.

Perfect Writer uses a file PW.SWP as a virtual memory work area.  It may 
use a file PW.HLP for help.  Again assuming both files are on drive A: 
user 0, the list

        A:PW.SWP       user 0
        A:PW.HLP       user 0

will work.

Example 3:  WordStar

When a program is run is or SpellStar is invoked, WordStar must load 
another program and run it.  Before doing this, WordStar checks to make 
sure that a valid version of WordStar is available.  It will not 
recognize a copy which has been integrated with SETDRU, so a separate 
installation is called for.

In order to keep WordStar accessible, one could include in the file list 
the WS.COM, but one probably has other .COM files that one might wish to 
run, so *.COM should be included.  WS.COM need be included only if it is 
not on the same drive as the other .COM files.

WordStar also uses overlays.  Just which overlays, depend on the options 
used with WordStar, so it's probably best not to specify the unambiguous 
names.

Let's assume that WS.COM and the overlays are on drive B: user 15, but 
that other .COM files that one might run are on drive A: user 0.  The 
list

        B:WS.COM       user 15
        B:*.OVR        user 15
        A:*.COM        user 0

would be appropriate.

Note that this would not work properly if *.COM were before WS.COM.

The program generated by SETDRU could have the name WS.COM if it were 
put elsewhere than drive B: user 15, but that could get confusing.  It 
should have a different name, or one could reinstall WordStar with a 








SETDRU.DOC                                         Page 6


different name.

Example 4:  The Word Plus

This final example is rather complex.  The Word Plus is a spelling 
checker which is implemented as a collection of programs with a master 
program controlling them.  The programs use various files with file 
types .TXT and .CMP.  The master program, TW.COM, may modify itself 
under certain options.  Furthermore, logical updates to the main 
dictionary are actually put in a file UPDICT.CMP.  When this file is 
updated, a new version is created as UPDICT.$$$ and then renamed.

One could make this even more complex, as special dictionaries can be 
updated by the program also.  We'll assume that any special dictionaries 
will be accessible though.

If all these files are on drive b: user 4, an appropriate file list 
would be

        TW.COM         user 4
        UPDICT.CMP     user 4
        UPDICT.$$$     user 4
        *.CMP          user 4
        *.COM          user 4
    



Removing installation of SETDRU.

Sometimes it will be necessary to remove SETDRU from a program.  This is 
only a problem if SETDRU has been integrated with the program, as if it 
is separate, all that's required is to delete the separate program 
generated by setdru.

To do this, the program UNSETDRU is provided.  It is invoked with the 
command

        unsetdru <program-name>

where <program-name> is the name of the program from which SETDRU is to 
be removed.  The file type (usually .COM) must be specified.  Make sure 
you have a backup before doing this.




For the hacker.

The source code of SETDRU and UNSETDRU have been released.  The 
installation program source code won't be that useful without quite a 
bit of work since it uses a private run time system.  It should be 
possible to modify it for your flavor of C, or to rewrite it in whatever 
language you prefer -- it's not a very complicated program.









SETDRU.DOC                                         Page 7


The filters themselves SDRU1 and SDRU2 (which are used when not 
integrated or integrated respectively) are much more interesting.  These 
are coded for Microsoft's M80 assembler using Z80 mnemonics.

The principles involved are quite simple, though the implementation is a 
bit tricky in places.

The filter intercepts all BDOS calls.  For certain file calls (open, 
make, etc.) the table of file names is searched for a match.  In some 
cases (make, delete, rename) only unambiguous names in the list may be 
matched.

If no match is found, control is simply passed to the BDOS to process 
the request.  If a match is found, the request is modified to the 
desired drive and user and tried (for open and search, the request is 
first tried unmodified and only modified if not found).  Assuming the 
modified request is satisfied, the drive in the fcb is then changed to 
17 plus the address (relative to the start of the table) at which the 
match occurred.  This is an otherwise illegal drive specification which 
will be detected on other operations.

On any other file operation, the drive is checked and if illegal is 
modified to the desired drive and the user number is changed to the 
desired value.  Of course, these must be changed back before returning 
to the program.

There are some details to take care of to install the filter.  If 
integrated (SDRU2), the required program must first be loaded.  
Otherwise (SDRU1), the program must be moved down to the start of the 
TPA (0100H).

In either case, the filter must be moved up to just below the BDOS.  
Moving it is easy enough, but there are a number of locations which must 
be relocated.  This is done in a very simple manner.  When modifying 
either of the filters, care must be taken to preserve the relocation.

Because relatively few people will have any need to modify the 
installation program and because it is written using a nonstandard run 
time library, a relocatable version (SETDRU.REL) is provided containing 
all needed routines except the filters themselves.  There are a few 
things which must not be changed if this installation program is to be 
used.

The start of each filter must contain

         Bytes         Usage
        -------        ---------------------------------------------------
          0-  2        A jump to the executable code.
          3-  4        The length of the filter.
          5-  6        The length of the program to be loaded will be 
                       put here by the installation program.  This is 
                       only used by SDRU2.  It is not set or used for 
                       SDRU1.
          7- 19        The drive, user number, and name of the program 
                       to which SETDRU is being applied.  This is only 








SETDRU.DOC                                         Page 8


                       significant for SDRU1, though it is set for SDRU2 
                       also.
         20-123        The table of file names to be redirected.  Each 
                       entry contains the drive (A=1, B=2, ...), the 
                       user number, and the file name (as it appears in 
                       an FCB).  Asterisks are expanded to question 
                       marks.
        123-135        Identification for the filter.  This is only 
                       significant for SDRU2, where it must be 
                       "***SETDRU2***" for unsetdru to work.

Note that the only parts of SETDRU which is dependent on the Z80 are the 
filters themselves (SDRU1 and SDRU2).  The installation program and run 
time system will run on an 8080.

After modifying either of the filters, a new version may be linked with 
the command

        l80 setdru/n,setdru,sdru1,sdru2/e

I'm not sure what modifications anyone would want to make for general 
use, but it might be necessary to change some things for specific 
programs.  The following variations have been found useful in the 
predecessors to SETDRU.  These are not so much recommendations as 
suggestions for things to look at.

SETDRU will not work with Multiplan.  The problem is that Multiplan 
contains code to

        1. Open the overlay file on the current drive and user number.

        2. Get the current drive.

        3. Change the FCB (while it's open!!) for the current drive.

Horrible isn't it?   Well, it doesn't do much good to complain about 
turkeys writing programs; we're stuck with them.  If the filter is 
modified so that the first call to BDOS function 25 (get current drive) 
lies and actually returns the drive the overlay file is on (and the help 
file; they must be on the same drive), Multiplan will work fine with 
SETDRU (I think.  This has not actually been tested, but it works in 
another such filter.)

The filter might also be modified to correct deficiencies in the program 
or operating system.  For example, on a CP/M lookalike which supposedly 
supported incremental backups through an archive attribute, I found that 
the system would allow the archive attribute to be set by the rename 
BDOS call.  Unfortunately, WordStar renames the temporary (.$$$) file 
with the same attributes as the original file.  This resulted in 
modifications made by WordStar not being detected for backups.  It was a 
simple matter to always clear the archive bit on a rename.  (Again, this 
was not actually done with SETDRU, but with another, similar filter -- 
still, it should work here too.)










SETDRU.DOC                                         Page 9




<End of Document>