Q W I K K E Y



                         A Keyboard Redefinition Program
                                V2.1  24-MAR-1985


                   Copyright (c) 1984, 1985 by Anton R. Fleig
              QwikKey may be used for non-commercial purposes only.
              No commercial use of QwikKey may be made without the
                      author's express written permission.


        1.0  INTRODUCTION

        QwikKey  allows  the user to assign a character strings to  keys.  
        When  a key having a string defined in this way  is  struck,  the 
        defined  string,  rather  than the character normally  associated 
        with the key, is delivered to the program running at the time.

        Key  definitions may be loaded from files  containing  previously 
        saved definitions,  or they may be defined on-the-fly, even while 
        a program is running.   Both normal keys (i.e.  keys generating a 
        single  character)  and  keys  generating  escape  sequences  are 
        supported.

        The  maximum length of the defined string is 31 minus the  length 
        of  the  character  or string normally generated by  the  key  in 
        question.  Thirty-one different keys may be defined.


        2.0  OPERATION

        2.1  The First Time

        QwikKey  V2.0  should  be  invoked for the first  time  with  the 
        command "QK".   QwikKey will prompt for an "attention/termination 
        character" and an "escape sequence lead-in character".

        The attention/termination character is used to gain the attention 
        of  QwikKey  in order to enter a new key  definition.   The  same 
        character is used to terminate the definition string.  Thus, this 
        character  should be one that is seldom if ever used,  both  from 
        the keyboard, and in key definition strings.

        The  escape  sequence lead-in character is  the  first  character 
        generated  by  keys which generate escape sequences  rather  than 







        single  characters.   This is almost always the ESCAPE  character 
        (ASCII 27 decimal).

        After  the attention and lead-in characters are entered,  QwikKey 
        loads  itself  below the CCP  (Console  Command  Processor),  and 
        returns  control  to CP/M.   The message "QwikKey  loaded."  will 
        appear  at  each warm boot to remind you that QwikKey  is  indeed 
        active.

        At  this point,  striking the attention character key will  cause 
        QwikKey to respond with the following prompt:

             Key:

        Now  strike the key you wish to define.   The character  normally 
        generated  by  the key will be displayed,  followed by an  equals 
        sign.   Suppose for example,  you wished to define the  control-K 
        key.  The following would appear after striking CTRL-K:

             Key: ^K =

        Now  enter  the  definition string,  followed  by  the  attention 
        character  again.   Suppose  we  wished  to  define  ^K  as  "PIP 
        A:=B:*.*[V]".   The  following would be displayed just before  we 
        hit the attention character to terminate the definition:

             Key: ^K = PIP A:=B:*.*[V]

        Upon  entry  of  the termination character,  the  key  definition 
        dialogue  is  erased.   Note that characters overwritten  by  the 
        definition dialogue are not rewritten, but replaced on the screen 
        with spaces.

        At this point, the key has been defined, and striking the defined 
        key  will result in the definition string being delivered to  the 
        current program (perhaps the CCP).


        2.2  Saving Definitions

        The  following  command  will save your current  definitions  for 
        later  recall in the file KEYDEF.DAT.   It can only be issued  at 
        the CCP prompt level (e.g. A>).

             A>QK SAVE KEYDEF.DAT

        If the filename is omitted in the above example,  the definitions 
        will be saved in the file QWIKKEY.DEF.   SAVE may be  abbreviated 
        to the single character "S".

        Note  that  the  attention/termination character and  the  escape 
        sequence lead-in character are also saved in the definition file.


        2.3  Loading Previously Saved Definitions








        The  following command will load previously saved  commands  from 
        KEYDEF.DAT  into QwikKey's definition table in memory,  replacing 
        any current definitions.  It can only be issued at the CCP prompt 
        level (e.g. A>).

             A>QK LOAD KEYDEF.DAT

        If the filename is omitted in the above example,  the definitions 
        will be read from the file QWIKKEY.DEF.   LOAD may be abbreviated 
        to the single character "L".

        Note  that  the attention/termination character  and  the  escape 
        sequence  lead-in  character  are also read from  the  definition 
        file.


	2.4  Removing QwikKey
	
	QwikKey can be removed from memory with the following command.
	
	    A>QK REMOVE
	
	The word  "remove"  in  the above command can be abbreviated with 
	the single character "R".
	
	
	
	3.0  ADVANCED TOPICS

        The following topics are intended for those familiar with DDT and 
        the attendant risks in its use.


        3.1  Creating Definitions Containing Non-keyboard Characters

        Definitions may be created containing characters not generated by 
        any key on the computer's keyboard through direct modification of 
        the key definition file(s).  This might be useful to add a DELETE 
        key to a computer having only a BACKSPACE key, for example.

        In  order to do this,  the structure of the key  definition  file 
        must  be  understood.   The  key definition file consists  of  32 
        logical records of 32 bytes each.   The first record's first  two 
        bytes  are  the attention character and  the  lead-in  character, 
        respectively.   The  third  byte contains a warm boot  flag  (see 
        section  3.2).  The  remainder of the first record  is  currently 
        unused  and  uninitialized.   The  remaining 31  records  contain 
        definition strings in the following format:

             [Key string] 0 [Definition string] 0

        The key string is the keyboard generated character(s).   Both the 
        key  string  and the definition string  are  null-terminated,  as 
        shown above.








        The  following is an example of the sequence of commands used  to 
        define  CTRL-D  to be DELETE,  assuming the keyboard  being  used 
        cannot generate the DELETE character.

             A>DDT QWIKKEY.DEF           Default definition file
             DDT VERS 2.2
             NEXT  PC
             0500 0100
             -S100                       First record
             0100 2B 0B                  Make ^K attn char
             0101 1B .                   Quit now (note lead-in char)
             -S120                       First definition
             0120 56 08                  Key string is BS char
             0121 1A 00                  Null terminate
             0122 09 7F                  Delete char is definition
             0123 AC 00                  Null terminate
             -G0                         Mods done
             
             A>SAVE 5 QWIKKEY.DEF        Save on disk

         

        3.2  Disabling the Warm Boot Message

        The  third byte in the key definition  file,  if  non-zero,  (the 
        default)  causes the "QwikKey loaded." message to be displayed on 
        each  warm  boot.   Setting this byte to zero will  disable  this 
        feature.


        4.0  MISCELLANEOUS

	QwikKey  occupies the  memory space  just below  CP/M's Console 
	Command Processor (CCP).  In order to accomplish  this, several 
	pointers within the system are modified as QwikKey is installed 
	(notably the WBOOT, CONST,  and  CONIN vectors in the BIOS jump 
	table, and the BDOS vector at location 5).  It is possible that 
	QwikKey  could  interact  detrimentally  with  other  programs, 
	especially any that attempt similar modifications.  Should this 
	circumstance occur, you may  want  to  remove QwikKey while the 
	other program is executing.  The REMOVE command may be used for 
	this.