KERMIT-80 was adapted for the Osborne 1 by Charles Bacon at NIH.

KERMIT-80 was developed originally at Columbia University but 
there are now many implementations of the program up and running 
on many micros as well as main-frame installations.

KERMIT is strictly a non-commercial program developed in the 
spirit of getting computers talking to one another.  It is 
copyrighted by Columbia, but all information about the program is 
available to anyone who asks.

If you want a "manual" for Kermit, CUCCA at Columbia will send 
one for a nominal fee (was $2.50). (Ask for KERMIT USERS GUIDE)
  Write: Kermit Distribution
         Coulumbia University Center for Computing Activities   
         7th Floor, Watson Laboratory
         612 West 115th Street
         New York, New York  10025

Here are some comments on this implementation:

Change speed (BAUD) of the serial line freely between 300 and 1200
with the SET BAUD command. Note that SETUP may later report incorrect
speed.

Type C<esc><CR> to CONNECT to the serial line.  Then dial the remote
computer.

Escape character for CONNECT is CTRL-\.

Osborne 1 [version] was quite a hack, since like too many micros, the
Osborne is sold as a mystery machine and took a lot of detective work
[unquote].

The cable used with the Osborne 1 modem connector has male connectors
at both ends, but is asymmetric.  The black connector should plug into
the Osborne and the gray connector into the modem.  This cable is
fabricated from four-conductor stranded wire, and it may be up to
several hundred feet long.  Here it is:

(Black shell)                       (Gray shell)
Signal Name	Osborne    Modem    Signal Name
at Osborne      Pin no.    Pin no.  at modem

Send data         2          3      Receive data
Receive data      3          2      Send data
Dataset Ready     6         20      Terminal Ready
Signal Ground     7          7      Signal Ground

If there were a fifth wire, it could run between Osborne's pin 20 and
the modem's pin 6.  This would make the cable symmetric.

Note that the "protective ground" is not wired.  Both the Osborne and
the modem should have three-prong power cables.