**>>  RESQ v1.3  <<**

If you've ever lost text due to a WordStar "disk full" glitch, or 
forgotten to save that text file you just downloaded, or frozen your 
console while handling an edited text, or given the wrong answer to
"Abandon current version?", you can use RESQ.

                          This program:
     
     *  dynamically finds the limits of computer memory (the TPA)
     *  hunts between those limits for a text phrase you supply
     *  backs up from the phrase until it hits control characters
     *  now goes forward again, showing you the text
     *  simultaneously saves the text in RES.Q on your logged drive
     *  stops and closes the rescued file when you hit any key, or
     *  when it finds the end-of-file character (^Z)

RESQ searches its own version of RAM with all eighth bits reset. Thus 
it finds text made by WordStar as easily as ASCII text. Similarly, it 
ignores the common WordStar control characters when backing up. The 
backing feature makes it unecessary for you to remember the phrase (up 
to 55 characters) which begins your semi-lost file. Just give RESQ a 
phrase anywhere in the text, and it will usually be able to get back 
to the head of the text before beginning to save. If not, try another 
phrase which may come earlier in the file. You might have to edit the 
beginning and end of the saved text to restore it completely, but 
then...

RESQ works for any program which buffers text above the point where 
RESQ itself leaves off, at about 28FFh. For example, RESQ finds text 
left in RAM by WordStar, Mex, and the Turbo Pascal editor equally 
well. The search is unaffected if you must reset (cold boot) in order
to revive your console before using it to find your text.  RESQ is 
also occasionally useful to find program headers, etc. for manipulation
by DDT, SID, DSD,...because it tells the user the address (in decimal)
where the phrase was found.  Some programs which handle text do not put
it intact in a buffer, and in these cases, RESQ will sign off, reporting
the range of addresses searched unsucessfully.  Another occasional cause
of wierd results is that some programs (eg, VDO and VDE) buffer their
text in an encoded form which differs from the onscreen version.  In
that case, the best that RESQ can do is find and save the encoded text.

Search phrases must be entered exactly as they occur, capitalization
matters.  On the other hand, a single word is likely to be unique in 
RAM, and is usually all that is needed to guide the search successfully.

Though it uses a different algorithm, RESQ was inspired by Chris and
Steve Rudek's MAGE, which is a Public Domain "saver" directed only at
the address of the WordStar text buffer.  RESQ was written for CP/M 2.2
and uses Z80 operations.  Because it searches from its own top to an
address which is determined from the structure of your computer's RAM
at the moment RESQ is invoked, it will probably work without adjustment
on most CP/M systems.  This is the feature which distinguishes v1.2 from
v1.3.

Good luck; but you'll need less luck with RESQ.


September, 1985                              Mike Yarus
                                             2231 16th Street
                                             Boulder, CO 80302

                                             Compuserve 73145,513