This program times your Osborne 1 disk drives.
The form of the command is

        TD<cr>  or  TD A<cr>   or  TD B<cr>

There must be a diskette in the target drive for
this program to work properly.  TD<cr> without
a specified disk drive will default to the "boot"
drive.

The displayed D range is for double density.
Optimum is from 200 to 203 ms/rev.  The farther
from this range that your drive varies, the greater
the chances of BDOS errors.  Single density drives
are more tolerant of the variation in speed, and
I've seen one work at 215 ms/rev.

To stop the program, press and hold any key.  To
test the opposite drive, press and hold the key
that corresponds to that drive.  If no mark appears
to indicate the timing, no index mark is being
detected and the program will wait until one is
detected or you press the RESET button.
                               -M.J.Guerra