8080A Microprocessor Instruction Set Emulator
   by Jeff Sheese, RETS Tech Center, Centerville, Ohio 45459

			     8-18-82

    The 8080A Instruction Set Emulator is a teaching tool used to 
demonstrate  the operation of the assembly language commands  and 
how  they affect the memory and microprocessor register contents.  
The  emulator was designed to operate the computer in	a  machine 
language  'direct' mode.   In BASIC,  the 'direct' mode is when a 
person  types in a command such as PRINT and watches the  results 
of   the  command.    The  emulator  will  speed   learning   and 
comprehension in a positive and instructive atmosphere.

    When the emulator is run, a sign-on message is printed on the 
screen, and immediately following is the prompt:

Initial status:
PC    S Z A P C  A  B	C  D  E  H  L  M  SP	STACK
2000  0 0 0 0 0  00 00 00 00 00 00 00 00 0000	0000

Instruction?_

    The  first line is a description of the type of registers	in 
the microprocessor.  Under each description is the actual content 
of the register.   The letters S,  Z,	A, P, and C are the status 
flags.   They change as the microprocessor status changes.  Their 
functions and descriptions follow:

    Sign  flag  - This flag shows whether the result of the  last 
operation was positive or negative.   The sign flag will be a one 
if negative,  or a zero if positive.	It will be the same as the 
most significant bit in the accumulator.

    Zero  flag - This flag shows whether the result of  the  last 
operation was zero.  If the result is zero, the flag will be one.  
If it was not zero, the flag will be zero.

    Auxiliary	carry  flag - If the result of the last  operation 
caused  a  carry from bit three to bit four,  this will  be  one.  
This flag is only used for the DAA instruction.

    Parity flag - This flag shows whether the result of the  last 
operation  resulted  in  an  even or odd number of  ones  in  the 
resulting byte.  This flag will be one if there is an even number 
one of bits, or odd if there is an odd number of one bits.

    Carry  flag - This flag shows whether the result of the  last 
operation  caused a carry or a borrow from the  last  significant 
bit  of  the result.	It will be one if a carry or a borrow  did 
occur, or it will be zero if it did not occur.

    The  rest of the line will show the different  registers.	 A 
description of the registers follow:

    PC  - This  will  show the current  address  of  the  program 
counter.   Do not let this go below 2000H.   If it does,  you may 
accidentally  alter memory that is essential for the emulator	or 
the operating system of your computer.

    A	- This will show the contents of the accumulator after the 
last instruction typed.

    B	- This will show the contents of the B register after  the 
last instruction typed.

    C	- This will show the contents of the C register after  the 
last instruction typed.

    D	- This will show the contents of the D register after  the 
last instruction typed.

    E	- This will show the contents of the E register after  the 
last instruction typed.

    H	- This will show the contents of the H register after  the 
last instruction typed.

    L	- This will show the contents of the L register after  the 
last instruction typed.

    M - This will show the contents of the memory address pointed 
to by the H-L register pair.

    SP  - This will show the address that is the current  top	of 
the stack.

    STACK  - This will show the last two bytes that were actually 
entered on the stack.	This is data, not a memory address.


    The  next	thing  to  do is to  actually  type  in  an  8080A 
mnemonic.   If you have a copy of the 8080A instruction set,  you 
type  in  the	mnemonic  the same as if  you  were  executing	an 
assembly  language program.   This emulator does not support  the 
use  of labels.   All numbers that are input and displayed are in 
hexidecimal  format.	After  typing in  the  instruction,  press 
return, and the emulator will display the new status.

    WARNING:
    DO  NOT  ALTER ANY MEMORY LOCATIONS BELOW	2000  HEX.   THESE 
MEMORY  LOCATIONS ARE ESSENTIAL FOR THE EMULATOR PROGRAM AND  THE 
OPERATING  SYSTEM OF YOUR COMPUTER.   THE MNEMONICS  AND  COMMAND 
THAT ARE TYPED IN ARE ACTUALLY EXECUTED.