*	safram.doc			Roy Lipscomb
*	version 1.0			Aug 1, 1982
*
*	Secures CCP and relocated modules against destruction until
*	system reset.  Operates as is with any standard CP/M-80.
*
*	Copyright 1982 by Roy Lipscomb, Logic Associates, Chicago
*	Copying permitted only for non-commercial/non-profit uses.
*
*	Original distributor:  HP/RCPM, (312) 955-4493
*
*
********************************************************************
*
* FUNCTION
*
*	SAFRAM creates a safe zone or partition below BDOS in which
*	the CCP and trap modules can reside without fear of being
*	overwritten by transient programs.  The protection lasts until
*	the system is reset.
*
*	SAFRAM makes it possible to load any module below the CCP that
*	previously had to be loaded above CP/M to be secure against
*	warm boots.  Thus, one-size CP/M can now be used with utilities
*	like IOCAP or self-installing drivers for hard disks.
*
*	SAFRAM also makes it possible to create BDOS and/or BIOS
*	extensions without actually installing them in the BDOS and/or
*	BIOS.  This allows them to be RAM-resident only when they are
*	needed.  It also makes possible extensions that are too long
*	to include in the allotted BIOS space on disk.
*
*	Installed, the SAFRAM module occupies less that 128 bytes of
*	RAM.  Each additional execution of SAFRAM will add another
*	3 bytes of overhead.  The CCP (2K) will also be resident
*	whenever SAFRAM has been installed.
*
********************************************************************
*
* BACKGROUND
*
*	Various utility modules or "traps" install themselves
*	just below the CCP before they begin operation.  This
*	allows other programs to load and execute normally,
*	without overlaying and disrupting operation of the traps.
*
*	Essential to this technique is changing location boot+6
*	to point to the start of the trap.  This is necessary because
*	boot+6 tells the next program what the upper end of the
*	available work space is.
*
*	This technique has been hobbled by the fact that warmboot
*	alters the boot+6 address back to its original coldboot
*	value.  This strips away the module's protection.
*
*	SAFRAM operates by making the address at boot+6 "permanent."
*
********************************************************************
*
* THEORY OF OPERATION
*
*	In its simplest terms, SAFRAM operates by patching two traps
*	into the BIOS jump table.  The "WARMBOOT" trap sets a flag
*	indicating that a warmboot has been requested, and then
*	jumps to the normal warmboot routine.  The "CONSOLE OUT"
*	trap checks the warmboot flag.  If the flag is set, this trap
*	resets the flag, and restores boot+6 to the way it was just
*	before the last warmboot.  Whether the flag was set or not,
*	this trap finishes by jumping to the normal CONOUT routine.
*
*	Operation of these traps is disrupted only by pressing reset.
*
*	At installation, the SAFRAM trap module relocates itself to
*	just below the CCP (or the currently protected address), and
*	creates the "safe ram" partition around itself.
*
*	SAFRAM will not install if the CCP is not resident and intact.
*	This is to avert any address contention between the CCP and
*	resident traps.  It is recommended that SAFRAM be executed
*	prior to installing any other traps, thus insuring that
*	that the CCP is protected and secured.
*
*	Once SAFRAM is executed, any number of self-relocating
*	utilities may be installed normally.  Simply follow up each
*	installation with an fresh execution of SAFRAM
*	(without pressing the reset button, of course).  SAFRAM
*	will reuse the resident copy of the SAFRAM trap module, rather
*	than create a new copy.
*
*	SAFRAM has two modes of execution.  Executed without param-
*	eters, it will secure the current address in location boot+6
*	(or secure the CCP if boot+6 points higher than the CCP start).
*	Executed with a hex address as its parameter, it will secure
*	that explicit address instead.  Examples:
*
*		Implicit mode:			A>SAFRAM

*		Explicit mode:			A>SAFRAM A000
*
*
********************************************************************
*
* ASSEMBLING
*
*	This source uses the LINK pseudo-operation featured in
*	Ward Christensen's LASM.COM (available on RCPM's) and
*	its predecessor LINKASM.COM (available from CPM Users
*	Group as 36.11 and 36.12).  This feature is used here to
*	link SAFRAM.ASM to itself, and thus introduce two
*	(partial) copies to the assembler.  The two copies are used
*	by the resultant SAFRAM.COM to produce a relocatable module.
*
*	If neither of the above assemblers is available, this
*	source can be assembled in a more roundabout fashion.
*
*	First, delete these three statements from the end of
*	SAFRAM.ASM:
*
*		if not copy1
*		link safram
*		endif
*
*	Next, execute the following commands:
*
*		PIP  SAFRAM2.ASM=SAFRAM.ASM,SAFRAM.ASM
*		ASM  SAFRAM2      (using any standard assembler)
*		LOAD SAFRAM2
*
*	You should now use SAFRAM2 instead of SAFRAM.
*
********************************************************************
*
* CUSTOMIZING
*
*	Customizing of SAFRAM.ASM is accomplished through several
*	variables:
*
*	VARIABLE		VALUE
*	--------		-----
*
*	BOOT			0 for standard CP/M
*
*	NOTIFY			"yes" for notification of what is
*				the currently secured address.
*				(Displayed at each warmboot.)
*
*	HOTBOOT			0 if not active.  Otherwise gives
*				displacement from start of bios to
*				the first instruction after the end
*				of the CCP/BDOS/BIOS-loading code.
*
*				Used to bypass unnecessary reloading
*				of the CCP and BDOS, which are saved
*				by SAFRAM from being overlaid (with 99%
*				assurance:  somewhere there may be
*				some unlikely program that ignores
*				location boot+6).
*
*	(See document SAFRAM.H for more information on HOTBOOT.)
*
********************************************************************
*
* APPLICATION NOTES
*
*   []  Self-relocating utility modules that will be protected by
*	SAFRAM should insure that they are not overlaying the CCP.
*
*   []  When securing a module that does not protect itself by changing
*	location boot+6, you should use the explicit-address mode
*	of SAFRAM.  (See THEORY OF OPERATION above.)
*
*   []  There is no option to individually "de-secure" a module.  The
*	only way to nullify security is to press the reset button.
*	The de-securing option was deemed infeasible, since there is
*	no simple way to keep track of what patches may have been
*	intalled by any given trap module, so that they could be
*	reversed if the module were de-secured.
*
*   []  To inspect the CCP using DDT (which normally overlays the CCP),
*	execute SAFRAM before invoking DDT.  The CCP will be intact
*	after DDT has been loaded.
*
*   []  It is sometimes desirable to secure DDT (for instance, for
*	use with BACK2DDT, available on RCPM's).  Use this procedure:
*
*		SAFRAM			(to secure the CCP)
*		DDT SAFRAM.COM
*		-G			(to secure DDT itself)
*
*		(DDT may now be used in the normal fashion.)
*
*
*								(end)

*		DDT SAFRAM.COM
*		-G			(to