W. vanRiper 	17 June 1985 

*** exprof ***

This is a rudimentary profiler until a better one comes along. It was written
in response to my frustration regarding the Software Toolworks c compiler,
which is supplied with a profiler for systems with a RTC in memory, and the
recent Dr. Dobbs article on a program monitor for CP/M 2.2.  Neither can
be easily adapted for use on the Exec.

Calling exprof from either c or assembly language toggles a counter. A second
call shuts it off, storing the time between calls internally. Supplying
an optional parameter displays accumulated time to the console, along with 
a number that you pass to the function. Like this:

from c:
------

main()
{
    prof();		/* toggles counter on */
    slowrout();		/* call the routine you want to time */
    prof(0);		/* toggles counter off */
    prof(3,1);		/* let's call this routine #3 and toggle display */
}

slowrout()
{
    int ii;
    for(ii=1;ii < 1000;ii++)
        {
	(lots of time consuming things);
	(more time consuming things);
        }
}			



from assembly language:
----------------------

	extrn	prof
;
	ld	hl,0		;zero signifies toggle
	push	hl
	call	prof
	pop	hl		;tidy stack
	    .
	    .	
 (perform various time-consuming things)
	    .
	    .
	ld	hl,0		;all done with what we want timed
	push	hl		
	call	prof		;so toggle timer off
	pop	hl	
;
	ld	hl,3		;now display how long it took for routine #3
	push	hl
	ld	hl,1		;1 toggles display and zeros out counter
	push	hl
	call	prof
	pop	hl
	pop	hl
;
	ret	


result:

routine: 3
total time: 62

			*************************

alternately, you could put the timer toggle in the subroutine:


main()
{
    slowrout();		/* call is toggled in slowrout() */
    prof(3,1);		/* display when slowrout() is done wasting CPU time */
}

slowrout()
{
    int ii;
    prof(0);
    for(ii=1;ii < 1000;ii++)
        {
	(do various time consuming things);
        (more time-consuming things);
        }
    prof(0);
}

When first called, prof looks at the 0-255 counter (RTC overflow at port
1ah).  A second call causes it to look again, and to store the interval 
between first and second calls.  This can be displayed as above, or prof
can be called two more times, in which case the stored time from the initial
two calls is incremented by the time between the second two, and so on.
Any even number of calls without toggling the display causes the internal
counter to be incremented.

As long as there is an even number of ON-OFF toggles everything is ok and
when you send prof the 1 the cumulative time will be displayed.  It's up to
you to keep track of things.  255 clock ticks on the Exec are about 4.27 sec,
so one tick is about .017 sec.  If the routine takes less time than this it 
will display as zero.  If you wait for more than 4.27 sec. between calls to
prof you will miss 4.27 secs from the maximum time that can be stored in
a 16-bit word which is about ffffh * .017 secs/tick = 1114 secs = 18 min.
approximately.

The advantage to prof is that it is simple so there is little processing
overhead.  The main problem is that successive calls to prof must be
more than .017 secs and less than 4.27 seconds apart.  For my own use this
is not a limitation - less than .017 seconds - who cares! - more than 4.27
seconds - use a stopwatch! 
 For my own use this
is not a limitation - less