TEACH3.ASM  is a version of TEACH2.ASM modified 
to relocate the BEEP routine above 4000h while leav-
ing  the  rest of the program in low memory  like  a 
normal CP/M program.   This results in a  COM.  file 
that is only 1k in size rather than the 17k required 
by  the original version.   TEACH3 is set up for the 
double density machines but could easily be modified 
for single density versions by changing the  "shadow 
mode" routines.

     The new version relocates the code for the BEEP 
routine  to the protected area above 4000h when  the 
program  first starts.   The method used is not  the 
most  elegant  but it works.   The beginning and  of 
BEEP  are labeled and the length is computed by  the 
assembler.  When the program is invoked a small sec-
tion  of code takes this information  and  relocates 
BEEP by the Z80 LDIR instruction.  The LDIR instruc-
tion  is obtained by the use of 8080 DB's so ASM  is 
usable.

     Since  There  is only one call to  BEEP  it  is 
replaced  by a fixed CALL 4000h.   A label might  be 
more  elegant  but  there is no real  need  for  the 
routine to be moving around.  The labels within BEEP 
have offsets in the source code that are computed by 
the assembler.  This alows BEEP to be modified easi-
ly  if so desired.   By only relocating the one rou-
tine  affected by the I/O process  the  modification 
was kept very simple.

     I  also added some punctuation to the  program.  
I would like to add the common procedure signals but 
I  don't know of a standard single character  repre-
sentation.  The RSGB handbook gives some equivilenc-
es   but I'm not sure if they  are  standard.   This 
could be a simple modification for someone.



Richard Hall WB4OEM
5 December, 1984
ur