HOW TO USE KERMIT FOR TRANSFERRING FILES BETWEEN MICROCOMPUTERS:

                     CP/M AND MSDOS SYSTEMS


                     Norman Weatherby, Ph.D.


             Center for Population and Family Health
                       Columbia University
                      60 Haven Avenue,  B-3
                       New York, NY  10032


                        October 30, 1984


                             PREFACE


     The use of microcomputers is rapidly increasing throughout
the world.  For example, in the last three years, the Center for
Population and Family Health (the Center) has moved from having
no microcomputers to the support of installations in Bolivia,
Haiti, Nigeria, Tanzania, Nepal, the Sudan, and our central
offices.  We see continued growth in the use of microcomputers
for data entry, editing and analysis; the writing and editing of
reports; project management and administration; and accounting.

     Although microcomputers speed the processing of information,
there are problems with the transfer of information among
systems.  The first problem is distance--diskettes must be
carried from one installation to another, or the information must
be sent across telephone lines that are sometimes too noisy and
full of static to be used even for voice communications.  The
second problem is one of compatability of diskettes across
systems.  For example, diskettes from Apple II series, Apple
Macintosh, Hewlett-Packard, TurboDos, CP/M, and IBM PC-type
systems are not interchangable.  Even within product lines, such
as the IBM PC series, problems may occur if different versions of
the disk operating system are used to produce the diskettes.
Thus, information may not be successfully transferred even if
diskettes are carried from one system to another.

     One solution to these problems is to use programs such as
KERMIT that allow information to be electronically transmitted
between systems, either across telephone lines or through a
direct connection between the computers.  Such programs must be
able to transfer information without error even across poor-
quality telephone lines.  The program running on one system must
have a specific protocol, or method of packaging the information,
that is used by the other system.  Thus, a consistent protocol,
used in programs for different computers, should allow the error-
free transfer of information.

     This document explains to the novice user how to get KERMIT
to transfer files between certain types of microcomputers.  It is
useful to those who are in the difficult situation of needing to
send information between incompatible microcomputer systems,
either directly or across telephone lines.  For example, by
following the procedures in this guide, Center staff in Haiti
will be able to transfer information from a Corona system to an
Osborne Executive.  This ability to transfer information quickly
and without error is an essential element of the continued
success of our research and service efforts.


                              INDEX


TOPIC                                                       PAGE

Introduction ...............................................   1

Now, KERMIT ................................................   2

Getting ready to use KERMIT ................................   3

Connecting the computers ...................................   4

Loading KERMIT into memory .................................   5

Setting KERMIT's options ...................................   6

Setting the baud rate ......................................   7

Communicating between computers ............................   8

Sending and receiving files ................................   9

Checking what was sent .....................................   9

Figuring out why (if) KERMIT does not work .................  10

Summary ....................................................  11

Appendix 1  Current KERMIT versions ........................  13

Appendix 2  Known KERMIT versions ..........................  15


                          INTRODUCTION

     KERMIT (like the frog, a registered trademark of Henson
Associates, Inc., used by permission) is ideal for transferring
ASCII and binary files between computers of all sizes.  It is a
protocol for transferring sequential files between computers of
all sizes over ordinary asynchronous telecommunication lines
using packets, checksums, and retransmission to promote data
integrity.  KERMIT is non-proprietary, thoroughly documented,
well tested, and in wide use.  The protocol and the original
implementations were developed at Columbia University and have
been shared with many other institutions, some of which have made
significant contributions of their own.  KERMIT programs have
been written for a wide variety of microcomputers, minicomputers,
and mainframes.

     Which ones?  At the end of this document is an extensive
listing that was downloaded (using KERMIT) from a DEC mainframe
at Columbia University.  In addition, you will find the address
to write for futher documentation, and some information for those
who would like to participate in the growth and acceptance of
KERMIT as one of the major file-transfer protocols.

     This guide was written so that people who have very little
computer experience could use KERMIT to transfer files between
CP/M micros or between CP/M and MSDOS (IBM PC-type) systems.  It
simply tells you how to work with KERMIT, without going into its
features.  However, it is not a substitute for the published
documentation.  And, as the real documentation states:

     No warranty of the software nor of the accuracy of the
     documentation surrounding it is expressed or implied,
     and neither the authors nor Columbia University
     acknowledge any liability resulting from program or
     documentation errors.

KERMIT is copyrighted, and it is not "public domain".  Simply, it
is a free program that is not to be sold as a product.  As the
distributors state, you are free to redistribute KERMIT on your
own terms, and are encouraged to do so, with the following
stipulations: KERMIT should not be sold for profit; credit should
be given where it is due; and new material should be sent back to
Columbia University at the address given in the summary so that
they can maintain a definitive and comprehensive set of KERMIT
implementations and documentation for further distribution.

     Where do you get KERMIT?  As stated below, Columbia
University distributes versions of the program only on nine track
magnetic tape.  You can get the program from friends or bulletin
board systems.  Look around for the latest version for your
micro, and be aware that the program is constantly improving.


                                1


                           NOW, KERMIT

     Without going into the details of KERMIT, this guide shows
you how to use the program to transfer files between micro-
computers that have KERMIT. The sections include

     1. Getting ready to use KERMIT
     2. Connecting the computers, either directly or through
        modems
     3. Loading KERMIT into memory
     4. Setting KERMIT's options
     5. Setting the baud rate
     6. Communicating between computers
     7. Sending and receiving files
     8. Checking what was sent
     9. Figuring out why (If) KERMIT does not work
    10. Summary


GETTING READY TO USE KERMIT

     You will need the following items in order to use KERMIT for
file transfers.  The only real problem is given last--determining
what kind of cable(s) you will need for the systems.

1. Two microcomputers.  It is best if each one has two or more
   disk drives.  Each one should have a serial port that can be
   used with a modem.

     IBM PC-type systems should have a DTE ("T" for terminal)
     port on an asynchronous communications adaptor (the serial
     port) that is called COM1:.  Perhaps there is a serial port,
     but it is used to send information to a serial printer.  In
     this case, the port may be DCE ("C" for communications)
     port.  Using a DCE port will not cause problems if you have
     the correct cable.  Note that the IBM dot matrix printer,
     which is made by Epson, is a parallel printer and not a
     serial printer.  Never connect a modem or other serial
     device to the parallel port used for the parallel printer,
     even though it appears that the cable will plug into the
     connection.

     CP/M systems typically come with one or more serial ports.
     One should be for a modem (DTE) and another for a printer
     (DCE).  In the CONFIGUR or SETUP program that came with the
     system, the modem port is usually labeled  RDR:/PUN:  or
     AUXIN:/AUXOUT:.  The printer port is labeled  LST: or PRT:.
     The words "modem" or "printer" may be stamped on the
     computer's case, but it is best not to pay attention to
     this, since you use the CONFIGUR or SETUP program to set the
     port you are going to use as a modem port.  For example, the


                                2


     Osborne Executive's "modem" port is not standard.  In order
     to use KERMIT, you have to use the Executive's SETUP program
     to label the "printer" port as AUXIN:/AUXOUT:.  Although
     this printer port is DCE, it can then be used with a modem
     if you have the right cable.

2. Two full duplex modems if you are going to transfer files
   across telephone lines.  You should be able to set at least
   one of the modems to answer mode.  File transfers work well
   but slowly at 300 baud (around 30 characters per second), so
   it is best to have two 1200 baud modems.

3. Two diskettes with KERMIT, one for each computer.  These
   diskettes should contain the operating system of your computer
   so that you can boot the system off of them.  You may also
   want to have system utilities, such as the CONFIGUR or SETUP
   program, on the diskettes.

4. The diskette with the file you want to send from one computer,
   and a blank, formatted diskette for the computer that will
   receive the file.

5. The right cable(s).  You should be able to plug in the ends of
   the cable(s) to the equipment that you are using.  Pins 1
   through 8 and 20 are connected.  Do not have other pins
   connected unless you are using a modem that was sold under the
   same brand name as the manufacturer of your computer, since
   some manufacturers of computers put electricity on other pins
   to power their own modems.  This electicity can damage your
   modem.  In addition, do not "jumper" or short-circuit any pins
   in the cable.

   The main question is whether or not pins 2 and 3 have to be
   switched.  "Switched" means that the signals from pin 2 on one
   end will go to pin 3 on the other end.  Likewise, signals from
   pin 3 on one end will go to pin 2 on the other end.


     IF YOU ARE DIRECTLY CONNECTING THE COMPUTERS:

     a. Do not switch pins 2 and 3 if you are connecting a modem
        (DTE) port on one system to a printer (DCE) port on the
        other system.

     b. Switch pins 2 and 3 if you are connecting a modem (DTE)
        port on one system to a modem (DTE) port on the other
        system, or if you are connecting a printer (DCE) port on
        one system to a printer (DCE) port on the other system.





                                3


     IF YOU ARE USING MODEMS TO COMMUNICATE THROUGH THE TELEPHONE
     LINES:

     For each system,

     a. Do not switch pins 2 and 3 if you are connecting a modem
        (DTE) port to the modem.

     b. Switch pins 2 and 3 if you are connecting a printer (DCE)
        port to the modem.


By making sure that you have your modems, diskettes, and the
right cable(s) together before attempting to use KERMIT, you will
avoid problems later on.


CONNECTING THE COMPUTERS

     IF YOU ARE GOING TO USE MODEMS, use the correct cable to
hook up a

                        full duplex modem

to each computer's serial communications port.  If you are
working with acoustically coupled modems, set one modem to answer
mode and the other modem to originate mode.


     IF YOU ARE GOING TO DIRECTLY CONNECT THE COMPUTERS,

     a. Directly connect the serial modem ports of the two
        machines.

                               OR

     b. Directly connect the serial modem port of one computer to
        the serial (not parallel) printer port of the other
        computer.

One benefit of using a direct connection between the computers is
that you can use high baud rates, such as 4800 baud, to transfer
the files.  Since you are not using modems and telephones, ignore
the parts of this guide that concern use of the modems and
dialing of the telephone.








                                4


LOADING KERMIT INTO MEMORY

     Loading KERMIT into the memory of an Apple II or Atari
computer is more difficult than loading it into CP/M or MSDOS
(PCDOS) systems.  Thus, readers should refer to other
documentation and help files for assistance with these systems.

     IF YOU HAVE A HARD DISK: Micros with hard disks, such as the
IBM PC-XT, often refer to all or part of the hard disk as disk C.
If you have a hard disk, copy your KERMIT program and associated
utility, help, and documentation files from the KERMIT floppy to
the hard disk (if someone else has not copied them over already).
Then work off the hard disk.  If you do not see the prompt for
the hard disk on your screen, type the command

                             c:<cr>

Then, to load KERMIT into memory, type the name of your kermit
program, which is usually KERMIT.  For example, at your operating
system's prompt, type

                           kermit<cr>

Then skip to the section below about setting KERMIT's options.

     IF YOU HAVE TWO FLOPPY DRIVES: Put the KERMIT diskette in
drive A of each computer.  Note that on a CP/M machine such as
the Kaypro, H89, or Osborne 1, it is wise to have the operating
system on the KERMIT disk (through the use of the SYSGEN utility)
and to type the command

               cntl C (without a carriage return)

where  cntl  is the control key and  C  can be upper or lower
case, to make the computer realize that a new disk has been put
in drive A.  This "warm boot" command is not necessary on micros
that use CP/M 3.0, MSDOS, or PCDOS operating systems.

     Put a blank, formatted disk in drive B of the system which
is to receive the file.  On the sending system, put the disk with
the file that you want to transfer in drive B.  Go to drive B,
and then get into KERMIT on each machine by typing  a: and the
name of the program, which is usually KERMIT.  For example, type

                          a:kermit<cr>

Newer versions of KERMIT allow you to change the "logged disk
drive," but it is wise to follow the above advice so that you are
sure of the disk that you are sending from or receiving to.




                                5


SETTING KERMIT'S OPTIONS

     To see the options that are available in your version of
KERMIT, type at the prompt the command

                           status<cr>

Note that the toggle command   set ibm  (set on or off) is NOT
FOR IBM PC MICROS--it is a command for IBM mainframes.

     SETTING THE PARITY: A computer "byte" is composed of  eight
bits, where each bit is a zero or one.  All (english) printable
letters, numbers, punctuation marks, and spaces between words can
be represented by seven of the eight bits.  The eighth bit is
reserved for checking to make sure that the other seven bits are
correct.  However, some microcomputer software packages (such as
WordStar) use the eighth bit for special characters that allow
features such as right justification.  In any event, if both
computers allow the following command, issue it to allow the
transmission of all eight bits:

                       set parity none<cr>


     SETTING THE BAUD RATE: The baud rate controls the speed of
the file transfer.  It can be set from within KERMIT on some CP/M
machines, such as the Osborne 1 and the Intertec Superbrain, and
on MSDOS (PCDOS) computers.  One really nice feature of KERMIT is
that you do not have to cope with that poorly-documented mode
command on the IBM PC-type micros.

     If you can set the baud rate from within KERMIT, make the
baud rates of both computers equal by typing at the prompt the
command

                          set baud ? <cr>

and select the correct baud rate from a menu that is given on the
screen.  Then go to the section of this guide that discusses
communicating between computers.

     If you get messages that the  set baud  command is not
implemented,  you will have to get out of KERMIT and set it from
your operating system, as discussed below.

Note that a faster way to set the baud rate is to type

                        set baud xxxx<cr>

where  xxxx  is the baud rate you want.



                                6


SETTING THE BAUD RATE

     If you cannot set the baud rate from within KERMIT, such as
on Heath/Zenith 89 systems, then you can get back to your
operating system by typing, at the prompt,

                            exit<cr>

Then use the computer's software to set the baud rate of the
serial port to which the cable is attached.  This is 300 or 1200
baud when modems are used and 4800 baud when a direct connection
is made.  The baud rate of a CP/M machine is set through the
SETUP or CONFIGUR utilities supplied with the system.

     While you are setting the baud rate, you can also check to
make sure that the serial port is set up as the RDR:/PUN: or
AUXIN:/AUXOUT: device.


COMMUNICATING BETWEEN COMPUTERS

     After KERMIT is loaded into the memory of each computer, and
its options are set, type at the prompt the command

                           connect<cr>

on each computer.  This will put you into the connect mode, which
allows one computer operator to send messages to the other
operator through the modems or the direct connection.  Note that
KERMIT replies with an "escape" message that tells you how to get
back to the command state of the program.  WRITE DOWN THIS
MESSAGE, AS YOU WILL NEED IT LATER.

     In fact, it is a good idea to test the command now.  The way
you get back to the KERMIT prompt varies by the type of system.
Note that you may have to issue the command but add a  C  (upper
or lower case) to it to get back to the KERMIT prompt.  For
example, on many CP/M machines that have the backslash character
\ , the "escape" command is control \  , but you type

                ctrl\c  (without typing a return)

where  ctrl  is the control key.  After some experimentation, you
will see the KERMIT prompt, and you can again type the command
connect<cr> .








                                7


     IF YOU ARE USING MODEMS: From the originate modem, dial the
answering modem.  If you have an auto-dial modem, you can issue
the dial command to it.  For example, with a touch tone
telephones and a Hayes SmartModem, the only command that is
necessary for the originate modem is

                         ATDTxxxxxxx<cr>

where xxxxxxx is the telephone number to dial.  The answering
SmartModem should be issued the command

                           ATS0=1<cr>

to make sure that the modem answers on the first ring.


     IF YOU ARE USING MODEMS OR A DIRECT CONNECTION: When the
connection is made, each of you each will be able to send and
receive messages that serve to test the connection.

     If you want to see what you are typing, get back to the
     KERMIT prompt by typing the "escape" command that you
     wrote down and tested above.  Then issue the command

                         set loc on<cr>

     to have a local echo, but you must remember to

                         set loc off<cr>

     before attempting to transfer a file.

If the connection is not made, so that it is not possible to
send AND receive messages, then you should check

     the baud rates of the computers
     the modems, and the wiring to the modems
     or the wiring between the directly-connected
     computers.

Make sure that the computer is sending or receiving data
to the correct port on the computer.  It is also helpful, as a
last resort, to check whether or not the telephone died because
you forgot to pay the bill (don't laugh...it once happened to
us!)








                                8


SENDING AND RECEIVING FILES

     When each computer operator is satisfied that a connection
has been made, then both operators return to the KERMIT prompt,
as explained above.

     The operator that wants to receive a file types

                           receive<cr>

The file name will be sent from the other system.

     The operator that wants to send a file types the command

                  send [drive:]filename.ext<cr>

For example, to send the file on disk B that is named
myfile.txt , the sending operator would type

                      send b:myfile.txt<cr>

It is usually not necessary to type in the drive specification,
since you should be using disk B as the "logged disk drive", but
it is always safe to do so.  If the receiving operator hits the
return after the sending operator hits the return, it may be
necessary for the receiving operator to hit another return before
the file will be sent.

     KERMIT will wait for a few seconds, and then the operators
will see on their screens that packets of information are being
sent and received.  KERMIT first sends the file name, and it is a
good sign to the receiving operator when the file name appears on
his or her screen.  The number of packets will increment on both
machines until the transfer is complete, and then each computer
will return to the KERMIT prompt.  At that time, the receiving
operator can check the file or another file can be sent.


CHECKING WHAT WAS SENT

     Once a connection has been established with KERMIT, it is
not broken if one or both of the operators return to the
operating system of their computers to check something such as
the length or name of a file.  Thus, when a transfer is complete,
the receiving operator can get out of KERMIT by typing

                            exit<cr>

at the KERMIT prompt.  The file that was received can be
examined, usually by issuing the command



                                9


                  type [drive:]filename.ext<cr>

The file will scroll by on the screen, and you will see that it
has been transferred without error!

     The receiving operator can then return to KERMIT by
reloading it into memory (discussed above).  If you need to,
reset the baud rate and the parity, and you will then be able to
transfer another file or get into connect mode and send messages.


FIGURING OUT WHY (IF) KERMIT DOES NOT WORK

     KERMIT has never, in our two years of experience with the
program, made a mistake in sending and receiving files between
CP/M computers or between CP/M computers and mainframes.  It
accurately transfers files even when the telephone line is
unusable for voice transmissions because of static and noise.

     Operators do, however, tend to make mistakes.  One such
problem is impatience.  Please let KERMIT wait for a few seconds
before you touch a carriage return on the receiving computer to
"make it work."  If KERMIT seems to be dead after about thirty
seconds of waiting, then something is wrong.  If you were able to
send messages back and forth in connect mode, or if KERMIT fails
after the first four or five packets, then probably the problem
is that one of the operators set the local echo switch on but
forgot to set it off.  It is also possible that the file that you
wanted to send does not exist, or the sending operator misspelled
its name in the send command.

     Occasionally, KERMIT will fail for reasons beyond its
control.  The transfer will fail if one of the computers involved
goes down.  For example, mainframe computers or their communi-
cation ports often go down (that's why we are now using micros
for most of our work, right?).  A feature such as call waiting or
intercom messages on a telephone line will stop the transmission
if they happen during a transfer.  These failures are advantages
in that they show that KERMIT is smart enough to quit when there
is a major problem.

     We have also encountered a problem with the way BASICA and
dBASE II on IBM PC-type computers mark the end of a file and save
it.  The solution is to load the file into a text editor or word
processor and then resave it before sending it.  For example,
load a file into WordStar and then save it.  An unreliable
alternative is to copy the file using the /A parameter.  The
problem is not fully understood; it centers around the PCDOS and
MSDOS software's use of buffered output when writing disk files.




                               10


     Apple II versions of KERMIT will work with DOS 3.3.
However, Apple IIs are slow, there are differences between the
II, the II+ and the IIe, and there is no standard way that people
set up their Apple's for communications.  If you plan to use
Apple KERMIT, please check with other Apple KERMIT users before
ordering your communications card and modem.  Currently, the best
cards may be the Apple Communications card, the Hayes Micromodem
II, or the Super Serial Card.  Actually, the best way may be to
install a Z80 card in the Apple II and run the Apple CP/M version
of KERMIT.


SUMMARY

     KERMIT is a very powerful program, with extensive error
checking, and thus it is ideal for transferring files between
computers.  The full documentation will show you many commands
and options for the program.  You may want to order the
documentation, but the simple procedures in this guide may be
adequate for your needs.

Extensive documentation is available for this program from

          KERMIT Distribution
          Columbia University Center for Computing Activities
          7th Floor, Watson Laboratory
          612 West 115th Street
          New York, NY  10025

There are three publications: the User's Guide, the Protocol
Manual, and the Source Listing for your system.  Each costs
$5.00, and you should make out your check to Columbia University
Center for Computing Activities.  Make sure and tell them what
microcomputer and operating system you are using.  Those who are
interested in mainframe implementations (which currently cost
$100 for the complete distribution) should write for ordering
information.  Note that the KERMIT distributors can provide the
programs only on 9-track magnetic tape in a varity of formats.
They do not provide the program on floppies.

     When necessary, there are specific help files that are
distributed with KERMIT to help with its use.  For example, there
is a help file with the Kaypro II version because of the non-
standard way it handles tab stops on its screen.

     There are also articles and announcements about KERMIT.  For
example, see the June-July, 1984 issues of BYTE.

     Please do not call the Kermit Distribution Center for
assistance with KERMIT for your micro.  After all, it is a free
program, and national support, sales, service, debugging,


                               11


revisions, everything else is being handled by only two or three
part-time people.  You can write, however, for the publications.

     Finally, KERMIT is changing and improving constantly --
versions are added for new systems, old versions are improved,
and documentation is rewritten.  You are encouraged to make your
own contributions to "KERMIT culture" and to make them available
not only to your friends, but also to send them back to Columbia
at the address given above, on 9-track magnetic tape or IBM PC
single-sided, eight sector floppy disk.  For example, we need
KERMIT for the TurboDos operating system.

     The most current versions of KERMIT are listed in Appendix
1. A brand-new MSDOS version that acts as a server for remote
communications has been released.  Appendix 2 lists the systems
for which KERMIT is available.  The codes shown with each group
show the status of the versions.

     Good luck with KERMIT, and watch for new releases and
updates!


                               12

(see VERSIONS.DOC and CURRENT.DOC for information about Kermit
versions)