DRIVES.DOC                                                 July 7,1986

                     Increase Your Disk Capacity
                           by Romanus Wille

     Many letters and articles have been dealing with the problem, how 
to increase the disk capacity. Here are two new methods to increase 
the disk capacity, each one will give you a plus of 5k.

     The first method uses a normal Osborne DD disk. If you look at 
the disk using DU.COM you will see that there is no information except 
E5H between track 1 sector 24 and track 3 sector 1. This means that 
track 2 is completly empty ( 5k ). This room was left by Osborne 
Computer Corp. for future BIOS versions. I think you'll never find any 
future BIOS versions that use track 2 on a DD disk. This first method 
uses the empty track 2 for more space. 
     How can you access this track? Normally CP/M is not able to 
access the tracks between track 0 and the directory. On an Osborne 1 
disk you can find the directory on track 3. The only thing you have to 
do is to move the directory from track 3 to track 2. The best way to 
move the directory is to tell CP/M that the directory is to be built 
on track 2 and because CP/M asks the BIOS where to build the 
directory, you have to change the BIOS. Use DU.COM to change the BIOS 
on the disk. You'll find the disk parameter block for Osborne DD 
drives on track 1, sector 8:

DU<CR>           ( <CR> = carriage return )

T1;S8;D<CR>

T=1, S=8, PS=7
00 00000000 00000000  00000000 00000000  *................*
10 00000000 00000000  00000000 00000C28  *...............(*
20 00030700 B8003F00  C0001000 03000514  *....8.?.@.......*
30 00040F01 2D003F00  80001000 03000112  *....-.?.........*
40 00030700 52001F00  80000800 03000820  *....R.......... *
50 00030700 9B003F00  C0001000 01000824  *......?.@......$*
60 00030700 AA003F00  C0001000 02000000  *....*.?.@.......*
70 00000000 00000000  00000000 00003A08  *..............:.*

The information between location 1E and 2D is the disk parameter block 
of the Osborne DD drive. What does the code mean?

0C ----> 00001100 = double density, 1024 bytes / sector
28 ----> total number of 128-byte sectors per track
00       0028H = 40 decimal
03 ----> block shift
07 ----> block mask
00 ----> extent mask
B8 ----> disk capacity - 1 ( max. allocation block # )
00       00B8H = 184 decimal
3F ----> number of directory entries - 1
00       003FH = 63 decimal
10 ----> bit map for allocation blocks used for directory
00       1100000000000000B = 2 allocation blocks
03 ----> number of tracks before directory
00

What you have to do is:

     1. change the disk capacity from 184 to 189 or 00B8H to 00BDH
     2. change the number of tracks before the directory from 3 to 2.

If you use DU please type in:

T1;S8;D<CR>
CH24,BD;CH2C,2;W;D<CR>
X<CR>

     After rebooting your system you'll have now 190k of disk 
capacity. But there is only one problem. Your aren't able to access 
the data on the original Osborne DD disk. So before using the new 
system, you have to copy all programs and data to a single density 
disk (or to an other format provided by UNIFORM or MEDIA MASTER and 
one SD disk for reboot) and after reboot from the SD disk you have to 
copy all programs and data back. This will be a lot of work, if you 
have hundreds of disks (don't forget the backup's but don't change 
your original disks, these are the only way back to the old system) 
but the result is great and very inexpensive.

     The second method is a more strange one. You know that the 
Osborne drives are single sided drives with 40 tracks per drive. To 
avoid complaints the manufacturers of the drives produces drives that 
normally can easily address 41 tracks. How can you use track 41? You 
have to do two things:

     1. alter your system
     2. use a program that is able to format 41 tracks.

     To alter your system means to alter the BIOS. Use DU.COM to 
change the BIOS on the disk. Again you'll find the disk parameter 
block for Osborne DD drives on track 1, sector 8:

DU<CR>           ( <CR> = carriage return )

T1;S8;D<CR>

T=1, S=8, PS=7
00 00000000 00000000  00000000 00000000  *................*
10 00000000 00000000  00000000 00000C28  *...............(*
20 00030700 B8003F00  C0001000 03000514  *....8.?.@.......*
30 00040F01 2D003F00  80001000 03000112  *....-.?.........*
40 00030700 52001F00  80000800 03000820  *....R.......... *
50 00030700 9B003F00  C0001000 01000824  *......?.@......$*
60 00030700 AA003F00  C0001000 02000000  *....*.?.@.......*
70 00000000 00000000  00000000 00003A08  *..............:.*

The information between location 1E and 2D is the disk parameter block 
of the Osborne DD drive. As described in the first method you have to 
change the disk capacity, however it is not necessary to change the 
number of tracks before the directory.

If you use DU please type in:

T1;S8;D<CR>
CH24,BD;W;D<CR>
X<CR>

     There are two ways to get a program that formats 41 tracks. The 
first way is to write your own as I did. I named the program F41T.COM 
for Format 41 Tracks and I hope you'll find it in the library. I 
prefer F41T.COM because it allows you to format only one track. 
Therefore it is possible to format the new track while the rest of the 
disk remains unchanged. The second way is to patch the original 
COPY.COM which was delivered by OCC on the system disk.
     If you prefer to patch the COPY.COM, make a copy of DDT.COM and 
COPY.COM to a new formatted disk. Please type in:

DDT COPY.COM<CR>

for version 3.1                  |    for version 3.2               
                                 |                                  
response of DDT	  you type in    |    response of DDT   you type in 
NEXT  PC                         |    NEXT  PC                      
1200  0100                       |    1200  0100                    
-                 S381<CR>       |    -                 S383<CR>    
0381 2A           2B<CR>         |    0383 2A           2B<CR>      
0382 CA           .<CR>          |    0384 CA           .<CR>       
_                 S392<CR>       |    _                 S394<CR>    
0392 28           29<CR>         |    0394 28           29<CR>      
0393 C2           .<CR>          |    0395 C2           .<CR>       
-                 S3FD<CR>       |    -                 S3FF<CR>    
03FD 28           29<CR>         |    03FF 28           29<CR>      
03FE C8           .<CR>          |    0400 C8           .<CR>       
-                 S44A<CR>       |    -                 S44C<CR>    
044A 28           29<CR>         |    044C 28           29<CR>      
044B C8           .<CR>          |    044D C8           .<CR>       
-                 S524<CR>       |    -                 S526<CR>    
0524 27           28<CR>         |    0526 27           28<CR>      
0525 32           .<CR>          |    0527 32           .<CR>       
-                 S534<CR>       |    -                 S536<CR>    
0534 26           27<CR>         |    0536 26           27<CR>      
0535 32           .<CR>          |    0537 32           .<CR>       
-                 S545<CR>       |    -                 S547<CR>    
0545 25           26<CR>         |    0547 25           26<CR>      
0546 32           .<CR>          |    0548 32           .<CR>       
-                 S7AF<CR>       |    -                 S7B1<CR>    
07AF 20           50<CR>         |    07B1 20           50<CR>      
07B0 20           41<CR>         |    07B2 20           41<CR>      
07B1 20           54<CR>         |    07B3 20           54<CR>      
07B2 20           43<CR>         |    07B4 20           43<CR>      
07B3 20           48<CR>         |    07B5 20           48<CR>      
07B4 20           <CR>           |    07B6 20           <CR>        
07B5 20           34<CR>         |    07B7 20           34<CR>      
07B6 20           31<CR>         |    07B8 20           31<CR>      
07B7 20           <CR>           |    07B9 20           <CR>        
07B8 52           54<CR>         |    07BA 52           54<CR>      
07B9 65           52<CR>         |    07BB 65           52<CR>      
07BA 76           41<CR>         |    07BC 76           41<CR>      
07BB 20           43<CR>         |    07BD 20           43<CR>      
07BC 33           4B<CR>         |    07BE 33           4B<CR>      
07BD 2E           53<CR>         |    07BF 2E           53<CR>      
07BE 31           20<CR>         |    07C0 31           20<CR>      
07BF 20           .<CR>          |    07C1 20           .<CR>       
-                 ^C<CR>         |    -                 ^C<CR>      

Now save the patch:

A>SAVE 20 COPY41T.COM<CR>

Finally, you are able to combine both methods and get the greatest 
result. As described before, you have to change the BIOS.

If you use DU please type in:

T1;S8;D<CR>
CH24,C2;CH2C,2;W;D<CR>
X<CR>

Ok, this is my first note for increasing drive capacities. Some 
special hardware solutions may follow. If you have any problems with 
these patches, don't worry about it, drop me a line.


                            Romanus Wille
                          E.-Mueller-Weg 15
                           D-2081 Prisdorf
                             West Germany