RESTORE.DOC - Documentation for RESTORE.COM
				31 January 19871
				Steve Dirickson


Description:
-----------
RESTORE is a utility program that improves disk performance by regrouping
the allocation groups assigned to each file on the disk so that each file
is allocated to sequential sectors on the disk i.e., 'restoring' the disk
to the condition it was in when it was new.

Discussion:
----------
CP/M-compatible operating systems store files on disk in what are called
"allocation groups."  The size of an allocation group is determined by
the system's BIOS, and is typically 1k or 2k bytes for floppy disks, and
2k, 4k, or 8k for hard disks.  The allocation group is the smallest unit
of storage on the disk; if you write a one-byte file to the disk, it will
take up just as much space (in the sense of making that space unavailable
for storing other files) as would a file the size of one entire alloca-
tion group.

When a disk is formatted, all allocation groups are free, and the first
file written to the disk occupies the allocation groups immediately after
the directory, in sequence.  The next file written to the disk occupies
the groups after the first and so on.  When a file is deleted, its allo-
cation groups are freed up, and may be reused by the system.

As files are written and erased, later files start to become 'fragmented'
i.e., they are written with some allocation groups in one location and
other groups in other locations.  Thus, when these 'fragmented' files are
read or written, the system must position the read/write head over one
track for part of the file, then move the head to another track for more
of the file.  This starts to degrade disk performance, because more and
more time is spent moving the head around to find the various parts of
the file, causing access times for the files to get longer and longer.
This problem affects both floppy and hard disks.  The effect this has on
the system response is dependent on how the system buffers the disk data
in memory.  A system that uses a 'track buffer' system, where an entire
track is saved in memory each time the disk is read, will be VERY much
slower when accessing severely fragmented files than when the files are
stored in sequential allocation groups and thus several related groups
are kept in memory together.  Similarly, a system that uses multiple-
record disk I/O will be seriously degraded by disk fragmentation.  Con-
versely, an unbuffered BIOS, and especially an unblocked BIOS, will be
less affected, because latency (the time the controller has to wait for
the desired record to rotate under the head) is more significant in com-
parison to track stepping times.

The only way to recover from this situation has been to copy all files
on the disk to backup disks, reformat the disk (or simply erase all the
files), and then recopy the files from the backup disk(s) to the working
disk.  This takes a significant amount of time to do, and it is even more
inconvenient if files are assigned to several user areas on the disk,
since each user area on the backup disk must be individually entered and
the files in that area copied to the corresponding area on the work disk.

RESTORE is designed to make this process easier by eliminating the copy
to and from the backup disks.  RESTORE works only on the disk being re-
stored, and thus may be used even in a single-disk system.


			    ***WARNING***

Since RESTORE does in-place restoration of the disk, it has INCREDIBLE
potential for wrecking havoc with your disk if something goes wrong while
it is working, like a loss of power or a controller fault.  Therefore,
you should ALWAYS back up the disk to be RESTOREd shortly before running
the program.  This shouldn't be much of a problem, since you do a full
back up of your hard disk at least every weekend, right?  RIGHT?  NO?!!
Well, if you don't, you should.  It only takes one occurrence of having
to rebuild a disk's directory one group at a time to make you a believer.
Just after a full backup is the optimum time to run RESTORE.


Use:
---
NOTE:  You MUST sort the directory of the disk to be RESTOREd before
running RESTORE, by running SAP, SAPP, CLEANDIR or some similar program.
If RESTORE finds that the directory is not sorted, it will tell you so
and quit. (SAP.COM, version 5.0 is included in this .LBR).  Also note
that some older versions of CLEANDIR, SAP, SAPP, etc., did not properly
sort the directory because they did not include the last directory entry
on the disk in the sort.  RESTORE WILL find this entry, and will tell
you that your directory is not sorted.	You can use DUU, DU3, PATCH or
your own favorite disk utility to examine the directory of the disk to
see what is wrong.

Once you have the disk's directory sorted, simply start the program by
typing 'RESTORE'.  The program will sign on, and ask you to change disks
if you desire.	This allows single-disk users to place the disk contain-
ing the program in the drive, start the program, and then swap in the
disk to be restored.  This means you don't have to copy the program to
each disk you want to restore.

Note that RESTORE  --ALWAYS--  works on the user's default disk i.e.,
the one you were on when you invoked the program.  So, if you want to
restore the disk in drive B but RESTORE is on the disk in drive A, you
MUST log onto disk B and then call the program from drive A:

	    A>B:<ret>
	    B>A:RESTORE <ret>

RESTORE reads in the directory of the default disk, analyzes the direc-
tory, and prints some information; how many directory entries are on the
disk, how many groups are allocated, how many groups have to be swapped,
and how many times the directory will be rewritten.  This last is sig-
nificant since 1) directory writes usually take much longer than other
writes, because most BIOSs immediately write their buffer to the disk
after a change in the directory, rather than waiting until the user wants
to write somewhere else, and 2) the directory takes up several allocation
groups, and the entire directory is rewritten after each directory entry
has been fixed.  Note that the number of directory entries reported by
RESTORE will probably not match the number of files on the disk, since
each extent of a file takes up its own directory entry.

After RESTORE tells you what it is going to have to do to the disk, it
asks you to type 'Y' to restore the disk, or anything else to abort.  You
may enter an upper or lower case Y, or even type CTL-Y.  Anything else
will cause RESTORE to abort without doing anything to the disk.

After you type 'y', RESTORE will start to fix your disk.  It prints the
name of the directory entry is is working on, so you can keep track of
how it is doing.  You may type a CTL-C at any time, and RESTORE will a-
bort after it finishes the current directory entry, and tell you how many
directory entries are left over.  Left to itself, RESTORE will finish the
disk, then tell you it is finished and terminate.

If you are using a system that does not reload the directories from disk
on each warm boot, like ZRDOS version 1.6 and later, you will need to do
whatever your system needs (run DISKRST in the case of ZRDOS) to restore
the system's directory to match the one on disk.  Remember, RESTORE works
thorough the BIOS, so the DOS has no idea what is going on.


System Requirements:
-------------------
Operating System - A CP/M-compatible operating system that supports con-
sole input and output and the following direct BIOS function calls:

	  Select Disk
	  Set Track
	  Set Sector
	  Set DMA Address
	  Disk Read
	  Disk Write
	  Sector Translation

These are the only direct BIOS calls used by RESTORE.  Console I/O is
done via the BDOS, so you may use the CTL-P to echo the output to your
printer.  If you do so, you may need to install the patch discussed be-
low.

Processor - Versions are provided for both 8080/8085-compatible proces-
sors (RESTOREI.COM) and for Z80-compatible processors (RESTOREZ.COM).
The Z80 version is about 5% smaller and runs about 1% faster than the
8080 version.

Memory - Depends on your disk system.  The largest disk directory RESTORE
can handle is 1024 entries (DRM = 1023 for you operating system hacker
types).  This size disk typically uses 4k byte allocation groups.  With
this type of disk, RESTORE requires a 44k TPA.	This is the largest TPA
requirement.  Other disk sizes can be restored in less TPA.  A SSSD
floppy limited to 64 directory entries using 1k allocation groups can be
RESTOREd in 8k of TPA.

Note that RESTORE is NOT a ZCPR3 utility.  I have tried to make it as
nearly universal as possible.  It does not use cursor-positioning se-
quences for the terminal, or require any installation.	The only thing
your terminal has to be able to do is receive and display standard ASCII
characters, including being able to do a carriage return without a line-
feed.  This is used in the display of the files being processed.  The
same line is rewritten as each new file is started.  If your terminal
can't do a carriage return without a line feed (or makes a mess doing
so, like a TTY), or if you want to echo the output of the program to
your printer without wearing a hole in the paper, install the following
patch:

	Patches:
	-------
	To make the file display do a line feed as well as a
	carriage return, use your debugger or disk utility to
	look at the word at address 103h (just after the jump
	at the start of the program).  This word is the address
	of the location in the file display string where you
	can insert a line feed character (0ah).  Put a LF there
	and write the modified file back to disk.

	The other patch option is the flag that controls the
	disk-change wait.  As released, the program will print
	a message telling you to change disks if necessary, and
	press any key when ready.  Then it waits for you to
	press any key.	Later, after the statistics for the disk
	are printed, it asks you to press 'Y' to continue, or
	any other key to abort.  If you don't want these waits,
	or you want to do unattended 'batch processing' of mul-
	tiple drives, you will need to patch this byte to zero.
	It is located just after the word described above, at
	address 105h.  It is non-zero to have the program wait
	for input in these two situations, or zero to start
	processing immediately.  The input for these two user
	waits is done using the BDOS 'Read Console Buffer'
	function, so ZEX or XSUB may be used to provide the
	input; note, however, that doing so will cost you about
	3k of TPA, and may cause a memory shortage problem.
	Try it on your largest disk.  If it works, you can have
	it both ways.


Limitations:
-----------
As discussed above, the maximum size disk RESTORE can handle is one with
a limit of 1024 directory entries using 4K byte allocation groups (ac-
tually, it will also handle this size disk with 8K allocation groups but
only if you have a 51.5k TPA i.e., your BDOS starts at some address after
CE00h.	Since I am a believer in the 48k TPA convention, this is not the
advertised maximum disk size).	This is the typical configuration for
most popular CP/M hard disks (10-30 Mb).  If you have a drive with a DRM
of 2047, RESTORE will not run.	I'm not really sure why people make disks
like this, since, with CP/M's limit of 8 Mb per logical disk, this means
that there is room for one directory entry for each allocation group on
the disk!.  That's a lot of lost directory space.  Since it would take
64k simply to read in the directory of such a disk, RESTORE will tell you
that there is not enough memory and quit.  I have chosen not to use the
incremental-directory-read technique that was added to CLEANDIR and SAP
for such disks, since, to remain within the 48k TPA boundary, this would
only increase the maximum number of directory entries from 1024 to 1152.

One of the problems associated with a program of this type is the hand-
ling of bad sectors on the disk.  Since there is no standard way of
marking bad sectors, I have completely ignored the issue in writing the
program.  I recommend the following system for those with bad sectors
on their hard disk:

     1) You have probably used BDxx, FBAD, or whatever you use to
	mark the bad sectors on the disk.  Use DUU, DU3, PATCH, or
	your own disk utility to examine the disk's directory.
	Note the allocation groups that are assigned to the '.BAD'
	(or however your utility marks them) files.  Make a list
	of the allocation groups containing the bad sectors.

     2) After you finish backing up your disk (that IS when you use
	RESTORE, isn't it?  See the WARNING above if not), run RE-
	STORE, then use your disk utility to look at the disk's di-
	rectory and see what files are now assigned to the allocation
	groups on your list of bad groups.  Make a list of these
	files.

     3) Erase the files on the list.

     4) Rerun FBAD, etc., to re-mark the bad wgroups.

     5) Copy over the files on the list from your backup disk.

I realize that this is somewhat cumbersome, and I apologize for that.
But, since there is no sandardized method for handling bad sectors, this
this is the best I have been able to come up with.

Note:  When the discussion above talks about 'using your disk utility'
to examine the disk's directory, you may use the DMAP program included
with RESTORE instead.  See the DMAP.DOC file for information on this u-
tility.  Simply type 'DMAP' and look for the filenames or allocation
groups you want to scroll by.


Operation:
---------
RESTORE uses a brute-force method to relocate allocation groups.  It
reads in the directory (which MUST be sorted), and decides from the di-
directory allocation data in the Disk Parameter Block for the disk how
many groups are allocated to the directory.  The next sequential alloca-
tion group should be assigned to the first file in the directory.  RE-
STORE looks to see if that is the case.  If not, it scans the directory
to find what file has that group allocated to it.  If the desired group
is not allocated, RESTORE copies the group referenced in the directory
into the desired group, then changes the directory entry to show the new
group.	If the group is allocated to another file, RESTORE reads both
groups into memory, then writes them to the alternate locations, effect-
ively swapping the groups in place.  Both directory entries are modified,
the next sequential allocation group is selected, and the process re-
peats.	The updated directory is written to the disk after each directory
entry is completed, not after each allocation group swap.  Thus, the
number of directory rewrites will typically be about one-half to one-
fourth (on a hard disk; one-fourth to one-eighth on a floppy disk) of
the number of group swaps required.

When I say that the method is 'brute force', I mean that no intelligence
is used in the sort process.  Under worst-case conditions, the first al-
location group on a disk might be free, with all other groups assigned
in the desired sequence to the files in the directory.	In this case the
disk is really not fragmented and nothing needs to be done.  If you run
RESTORE on a disk in this situation, it will tell you that EVERY GROUP
on the disk must be moved, and will do so if you let it.  No analysis of
the fragmentation of the disk is done, and no optimization is used to
figure out how to restore the disk using the least number of group swaps.
While possible, the code to do this would make the program long enough
that it might not be able to process a 1024-entry directory.  On a more
basic level, it would take me longer to write the optimization than I
feel is reasonable.  RESTORE works, and works well.  The machine does
not in the least mind moving the same allocation group three or four
times.

On the subject of speed:  RESTORE is, in addition to being more conven-
ient than copying all the files back from a backup disk, considerably
faster than that method.  While times vary depending on the degree of
fragmentation and the hardware, I have found RESTORE to be about 20%
faster than a NON-VERIFYING copy of files from backup floppies back to
my hard disk.  RESTORE does read-after-write CRC verification of all
disk writes.  Plus, you don't have to sit around and feed your machine
floppies for hours.  RESTORE will process a filled 20 Meg hard disk in
about 5 hours on my hardware; doing the same thing, with verification,
from floppies takes over 9 hours and about 28 disk swaps!  With RESTORE,
simply use a multiple-command line or SUBMIT file (DON'T use ZEX or XSUB
if you have a big hard disk) and let RESTORE crunch away over night, or
while you are out shopping for a computer for your wife (or husband).
Note that if you want to use this 'batch processing' of multiple drives,
you must patch the disk-change flag to zero as described above to disable
the disk-change wait.


DISCLAIMER:
----------
This is a very useful utility, and I have tested it extensively.  How-
ever, as noted above, it is also very capable of lunching your disks
completely if the system has a problem.  Use it in good health and hap-
piness, but MAKE BACKUPS BEFORE YOU USE IT!!.  Papa Wallenda ran his
system without a backup.  He's not around any more.  'Nuff said.

				Steve Dirickson
				21145 Raintree Place NW
				Poulsbo  WA  98370-9726
				Voice: 206-697-1270/9311
				BBS: Seattle's 'downspout': 206-325-1325
				     ZNode Central: 415-489-9005