.. Print this document with Wordstar for full underlining,
.. superscripts, etc..
..
.PN1
                INSTALLING ZCPR3 ON AN OSBORNE 1 
                --------------------------------
            Adapted from previous ZCPR3 Installations
              by the author, Barry Siegfried, K2MF, 
                    with Walt Wheeler, Y.O.U.

                      Updated and Annotated
                 by Daryl D. Gehlbach, YOUr CUG
                           19 Apr 1990

INTRODUCTION
------------
Despite published assertions to the contrary, a fully implemented  
ZCPR3 System can be installed on a Osborne 1.   Fully implemented 
is used here to mean inclusion of the following features:

 1. the CCP replacement
 2. the System Environment
 3. the System Flow Control Package
 4. the System I/O Redirection Package \1
 5. the System Named Directory Package
 6. the System Resident Command Package
 7. the External Message Buffer
 8. the External File Control Block
 9. the Multiple Command Buffer
10. the Shell Stack
11. the External Stack
12. the External Path
13. the BIOS cold boot initialization patch

The files required to do the installation are:

System .COM files
-----------------
1. MOVCPM.COM - Digital Research CP/M System Relocation Utility
2. SYSGEN.COM - Digital Research System Generator
3. DDT.COM    - Digital Research Dynamic Debugging Tool
4. MAC.COM    - Digital Research Macro Assembler
5. MLOAD.COM  - Public domain replacement for Digital Research LOAD.COM
6. your program text editor - for example, WORDSTAR.COM or V.COM

System Source files
-------------------
1. ZCPR3.ASM  - the working code for the CCP replacement
2. Z3BASE.LIB - Base address definition library for the ZCPR3 CCP 
                replacement and external packages
3. Z3HDR.LIB  - Option selection library for the ZCPR3 CCP replacement
4. SYSENV.ASM & SYSENV.LIB - ZCPR3 Environment Descriptors
5. SYSFCP.ASM & SYSFCP.LIB - ZCPR3 Flow Control Package
6. SYSIOP.ASM & SYSIOP.LIB - ZCPR3 I/O Redirection Package
7. SYSNDR.ASM & SYSNDR.LIB - ZCPR3 Named Directory Package
8. SYSRCP.ASM & SYSRCP.LIB - ZCPR3 Resident Command Package


ŠSpecial File
------------
1. Z3OS-OVL.ASM - SYSGEN patch overlay 


ZCPR3 Application programs
--------------------------
1. Z3INS.COM - ZCPR3 System Environment .COM file installer
2. LDR.COM   - ZCPR3 External Package loader
3. ALIAS.COM - ZCPR3 command .COM file creator


THEORY OF OPERATION
-------------------
The Osborne 1 Double Density 59K (Single Density 60K) CP/M System
occupies the following addresses in memory:

CCP    : CB00 - D2FF ( 2K ) (CCP  BASE = CF00 in Single Density System)
BDOS   : D300 - E0FF (3.5K) (BDOS BASE = D700 in Single Density System)
BIOS   : E100 ~ E980 (>2K ) (BIOS BASE = E500 in Single Density System)
SCRATCH: EA80 - EFFF      NB:  System scratch, regardless of BIOS Size; 
                               and is NOT available to the user
VIDEO  : F000 - FFFF      NB:  NOT available to the user
 
The amount of space required to fully implement the ZCPR3 system is 
about 4K.  The way to provide that space for the ZCPR3 System is to
use MOVCPM.COM to relocate the CP/M System down in memory and allocate
space above the BIOS.

The relocated Osborne 1 55K (DD) CP/M System occupies the following 
addresses in memory:

CCP    : BB00 - C2FF ( 2K )
BDOS   : C300 - D0FF (3.5K)
BIOS   : D100 ~ D980 (>2K)  
Z-PKGS : D980 - EA80 (4.25K) (This is SPACE to use for Z-packages)
SCRATCH: EA80 - EFFF   NB:  System scratch, regardless of BIOS Size; 
                            and is NOT available for other uses
VIDEO  : F000 - FFFF   NB:  NOT available for other uses



INSTALLATION
------------
Prepare the following disks:

Drive A: - DDT.COM, MAC.COM, MLOAD.COM, MOVCPM.COM, SYSGEN.COM, and
           your text editor
Drive B: (Disk 1) - ZCPR3.ASM,  Z3BASE.LIB, Z3HDR.LIB
Drive B: (Disk 2) - SYSENV.ASM, SYSENV.LIB, Z3INS.COM, LDR.COM,
                    ALIAS.COM, Z3OS-OVL.ASM
Drive B: (Disk 3) - SYSFCP.ASM, SYSFCP.LIB, SYSNDR.ASM
                    SYSNDR.LIB, SYSRCP.ASM, SYSRCP.LIB

.paŠPart 1) Assemble the CCP

1. Place disk 1 into drive B.

2. Edit Z3BASE.LIB and put in the base addresses for your system com-
   ponents as desired.  It is suggested that you use the values in the
   following table, although they may be changed as desired.  CAUTION:
   If you do change these values, be VERY careful about which blocks
   of memory you specify.  After you finish editing Z3BASE.LIB, trans-
   fer a copy of this file to Disk 3, as it is additionally needed to
   prepare the external packages of ZCPR3.

      HEX      DECIMAL  Function                  Source Code 
   Addresses    Bytes  Description               LABEL: and values     
 ____________________________________________________________________
   0040 - 0046    7 b  External Search Path      EXPATH   EQU  40H
                       3 External Search Paths   EXPATHS  EQU  3 
          004B    1 b  Wheel Byte                WHEEL    EQU  4BH
   BB00 - C2FF    2 K  CCP                       CCP      EQU  0BB00H
   E900 - E950   80 b  External Message Buffer   Z3MSG    EQU  0E900H
   E95C - E97F   36 b  Ext. File Control Block   EXTFCB   EQU  0E95CH
   E980 - E9FF  128 b  Named Directory Package   Z3NDIR   EQU  0E980H
            \2         14 Named Directories      Z3NDIRS  EQU  14
   E700 - E7FF  256 b  Multiple Command Buffer   Z3CL     EQU  0E700H
                       251 Characters Maximum    Z3CLS    EQU  251
   E800 - E8BF  192 b  Shell Stack               SHSTK    EQU  0E800H
                       6 Shell Stacks            SHSTKS   EQU  6
                       1 Shell Stack = 32 bytes  SHSIZE   EQU  32
   E8D0 - E8FF   48 b  External Stack            EXTSTK   EQU  0E8D0H
   E600 - E6FF  256 b  Environment Descriptor    Z3ENV    EQU  0E600H
                        2 128-byte blocks        Z3ENVS   EQU  2
   E400 - E5FF  512 b  Flow Control Package      FCP      EQU  0E400H
                        4 128-byte blocks        FCPS     EQU  4
   DC00 - E3FF    2 K  Resident Command Package  RCP      EQU  0DC00H
                       16 128-byte blocks        RCPS     EQU  16
    (n/a  \3)     2 K  I/O Redirection Package   IOP      EQU  00000H
                       16 128-byte blocks        IOPS     EQU  0 

3. Edit Z3HDR.LIB and select the options you want for your CCP, by set-
   ting the relevant equates (GOON, SAVEON, etc) "TRUE" or "FALSE."  It
   is suggested that you turn on only the following CCP Resident Com-
   mands:  GO, SAVE, REN, GET and JUMP (which appear in the foregoing 
   order just before the end of Z3HDR.LIB).  GET, GO, JUMP and SAVE are
   available only in the CCP.  Even though REN is available in the
   External Resident Command Package, we elect to turn it on in the
   CCP because it does not appreciably add to the amount of generated
   code in the CCP while it saves very valuable space in the External
   Resident Command Package by not turning it on there.

4. Log into Drive B: and assemble ZCPR3.ASM using MAC:

   B0>A:MAC ZCPR3 $PZ-S

   Using the $PZ-S option of MAC will give you the fastest assembly
   without generating a large .PRN file.  If the generated code inŠ   your CCP is larger than 2K, an error message will print out at the
   end of assembly.  When assembly is complete you will find ZCPR3.HEX
   on Disk 1.

5. Generate the binary code from the .HEX file using MLOAD:

   B0>A:MLOAD ZCPR3

   When the load is complete you will find ZCPR3.COM on Disk 1.

5. REName ZCPR3.BIN=ZCPR3.COM  - and -  transfer a copy of ZCPR3.BIN
   to Disk 2.


Part 2) Create Special SYSGEN program.

1. Place disk 2 into drive B.

2. Relocate the CP/M System, create your SYSGEN program and read
   ZCPR3.BIN into it using DDT:

   B0>A:MOVCPM 55 *

   CONSTRUCTING 55k CP/M vers 2.2
   READY FOR "SYSGEN" OR
   "SAVE 39 CPM55.COM"

   B0>A:SYSGEN
   OPERATING SYSTEM GENERATION PROGRAM 
   OSBORNE COMPUTER SYSTEM ONE
   Rev 2.1  (c) 1982  OCC
   SOURCE DRIVE (A OR B)<CR> (even tho that option is NOT displayed)
   DESTINATION (A, B or RETURN TO EXIT)<CR>
   B0>SAVE 39 CPM55.COM

   B0>A:DDT CPM55.COM
   DDT VERS 2.2
   NEXT  PC
   2800 0100
   -F0980,117F,0       (initialize the CPR image area to 00)
   -IZCPR3.BIN         (identify the binary CPR image)
   -R0880              (read the binary CPR image into CPM55.COM
                        at 0980 [0880 + 100H offset] )
   -G0

   B0>SAVE 39 ZCPR3.COM (save the new ZCPR3 SYSGEN program to disk)


3. Assemble the SYSGEN patch file. In the original article these
   patches were made manually with DDT. This file intends to
   simplify the patching process by using MLOAD to overlay the
   changes. 

   These patches are needed to in order to allow the Osborne I to
   initializå properlù alì oæ thå bufferó needeä bù ZCPR3® Onå Š   word of caution is needed. These patches are based on BIOS
   addresses in the original, unmodified Osborne BIOS. IF YOUR
   BIOS HAS BEEN MODIFIED, THESE PATCHES WILL NOT WORK. Creatå 
   the HEX file as follows:

   B0>A:MAC Z3OS-OVL $PZ-S

4. Overlay the HEX file onto the SYSGEN program.

   B0>A:MLOAD Z3SYS.COM=ZCPR3.COM,Z3OS-OVL

5. Z3SYS can now be used to SYSGEN disks to bring up ZCPR30 on
   the Osborne I.


Part 3) Create Environment Descriptor

1. Place disk 2 into drive B.

2. Edit SYSENV.LIB and put in your terminal control codes.  It is
   suggested that you use the values in the following table for the
   Osborne 1:

   Cursor UP    - 0Bh           CL String - 1Ah
   Cursor DOWN  - 0Ah           CM String - 1Bh,'=%+ %+ '
   Cursor RIGHT - 0Ch           CE String - 1Bh,54h
   Cursor LEFT  - 08h           SI String - 1Bh,29h
                                SO String - 1Bh,28h

3. Log into Drive B: and assemble SYSENV.ASM using MAC:

   B0>A:MAC SYSENV $PZ-S

   Using the $PZ-S option of MAC will give you the fastest assembly
   without generating a large .PRN file.  When assembly is complete
   you will find SYSENV.HEX on Disk 2.

4. Generate the binary code from the .HEX file using MLOAD:

   B0>A:MLOAD SYSENV

   When the load is complete you will find SYSENV.COM on Disk 2.

5. REName SYS.ENV=SYSENV.COM

6. Install your Environment Descriptors into LDR.COM and ALIAS.COM
   using Z3INS:

   B0>Z3INS SYS.ENV LDR.COM  - and -  B>Z3INS SYS.ENV ALIAS.COM

   This procedure will be used from here on to install ZCPR3-specific
   utility programs.  Once installed, they may be run freely on your
   ZCPR3 System without re-installation.

ŠPart 4) Create Other Packages

1. Place disk 3 into drive B.

2. Edit SYSFCP.LIB, SYSNDR.LIB and SYSRCP.LIB and select the options
   you desire for your external Flow Control, I/O Redirection, Named 
   Directory and Resident Command Packages, respectively.
   It is suggested that you turn off the REN External Resident Command
   in SYSRCP.LIB.  You might additionally need to turn off other op-
   tions and commands in order to get SYSRCP.ASM to assemble to within
   2K of code.  It is STRONGLY suggested that you DO NOT revise the
   External Resident Command equates in Z3BASE.LIB in order to accom-
   modate an External Resident Command Package that is greater than 2K.

3. Log into Drive B: and assemble SYSFCP.ASM, SYSNDR.ASM and
   SYSRCP.ASM using MAC:

   B0>A:MAC SYSFCP $PZ-S  - and -  B0>A:MAC SYSNDR $PZ-S  - and -  
   B0>A:MAC SYSRCP $PZ-S

   Using the $PZ-S option of MAC will give you the fastest assemblies
   without generating large .PRN files.  If the generated code in
   either SYSFCP or SYSRCP is larger than the space allotted to it,
   an error message will print out at the end of assembly.  When all
   three assemblies are complete you will find SYSFCP.HEX, SYSNDR.HEX
   and SYSRCP.HEX on Disk 3.

4. Generate the binary code from the .HEX files using MLOAD:

   B0>A:MLOAD SYSFCP  - and -  B0>A:MLOAD SYSNDR  - and -
   B0>A:MLOAD SYSRCP

   When all three loads are complete you will find SYSFCP.COM,
   SYSNDR.COM and SYSRCP.COM on Disk 3.

5. REName SYS.FCP=SYSFCP.COM  - and -  REName SYS.NDR=SYSNDR.COM
   - and -  REName SYS.RCP=SYSRCP.COM


STARTING ZCPR3
--------------

Z30SYS.COÍ ió no÷ readù tï tï generatå ne÷ systeí disks® Afteò �
yoõ havå booteä á ZCPR³ system¬ yoõ maù theî loaä anù oò alì oæ �
thå externaì packageó usinç LDR:

A0>LDR SYS.ENV,SYS.FCP,SYS.IOP,SYS.NDR,SYS.RCP ... etc.

Thå firsô packagå tï bå loadeä musô alwayó bå SYS.ENV®  Thå otheò �
packageó wilì loaä intï theiò designateä protecteä areaó seô �
asidå bù thå ZCPR³ systeí anä defineä iî SYS.ENV¬ anä wilì noô bå �
overwritteî bù applicatioî programs.


ŠZCPR33 INTEGRATION
------------------

Á bootablå ZCPR3³ systeí caî bå createä bù followinç thå abovå �
steps® Althougè noô writteî foò DRI'ó Macrï Assembleò thå procesó �
is similar. Just keep in mind three things:

     1. Substitute the appropriate source files for ZCPR33.

     2. Make sure to generate a HEX file that can be LOADed
        using MLOAD.

          ZAS ==>  B>A:ZAS ZCPR33 H

          M80 ==>  B>A:M80 =ZCPR33/Z/M
                   B>L80 /P:xxxx,ZCPR33,/X,ZCPR33/N/E

               xxxx = CCP address, needed

     3. Under ZCPR33 the utilities need not be installed as the
        CCP does that automatically each time the program is
        executed.



CONCLUSION
----------
ZCPR3 is a flexible and much improved Console Command Processor over 
the stock Digital Research CCP which contains a variety of new funct-
ions and commands, particularly if the external packages are loaded.  
In addition, there are many ZCPR3-specific programs which can now run 
on your OSBORNE 1 system that offer very interesting video capabili-
ties.  

Wå recommenä thaô yoõ geô á copù oæ "ZCPR³ - Thå Manual¢ foò �
$19.95®  Thió manuaì containó alì thå technicaì informatioî abouô �
ZCPR³ theory¬ design¬ installatioî anä usage®  Abovå all¬ enjoù �
usinç ZCPR3.


ACKNOWLEDGEMENTS
----------------
Thanks to Richard Conn who wrote and copyrighted ZCPR3, and Mike Cohen 
who created the BIOS initialization patch for the Apple ZCPR2 System, 
upon which the Kaypro 1, Kaypro 4, and Osborne patches are based.

.paŠNOTES

\1  IOPs are not implemented in the instructions below, for lack
    of applications by this user.   Those who wish to add IOPs should
    allow an additional 1.5 - 2K above the BIOS, beyond that detailed
    here, and should edit Z3BASE.LIB accordingly.

\2  This value was increased from the more common "7" to facilitate
    use of many user areas on a hard disk.

\3  As noted above, the writers had no applications for IOPs at
    the time this document was written.  Assign an appropriate base
    address to replace the "00000H" at "IOP EQU"  and a non-zero
    value (conventionally, 16 decimal) at "IOPS EQU."

\4  Take these on faith.  A full explanation of the apparently 
    convoluted logic would require the addition of the equivalent
    of a short novel.  This is another way of saying "derivation
    is left as an exercise for the reader."


End of OZ-ZCPR3.DOC

.paŠ