VDCLIB 1.3      by Leonard Howie

              CP/M Graphics For C128 VDC and 1750 Ram Expansion

17 July 1987

INTRODUCTION

VDCLIB13.REL is a collection of graphics routines for the Commodore 128
Video Display Controller (8563) 80 column chip.  The routines are written
in the C language implementation by Software Toolworks, however, the 
special features of this implementation were generally not used.  Included
are routines to write/read the chip registers, bitmap the entire 80 column
screen, plot points or bytes, and draw/erase lines between two points.

     These routines, as well as those that put text on the bitmap, work fine
with my 1750 ramdisk.  Since you must wipe out your text capability in order
to use the full bitmap, it is necessary to save the initial screen to the
1750 and return it after plotting.  Re-booting is not necessary.  Without
the ramdisk, the point plotting routines work okay, but the character plot-
ing does not work.  Re-booting CP/M is also required.

     All routines are documented in VDCLIB13.C and further examples of how
to call the routines are given in DEMO8563.C, which is heavily commented.
To see the full library at work, run the program DEMO8563.COM.  It produces
a simple x-y plot with title, labeled axes, and other text in arbitrary 
locations on the screen.

BACKGROUND

     I originally wrote these routines in Turbo Pascal (which is much
smoother to use than C/80) but the screen saving and returning was far too
slow to be of any practical use.  Because C/80 allows easy interfacing to
assembly language (ugh!) and a gradual buildup using RMAC and LINK, I 
switched to C/80.  Not being a programmer, I used only plain vanilla C and
assembly code.  The main routines were adapted from Z80 source code provided
with the 128 CP/M, chip instructions in the 128 Programmer's Reference Guide,
and various magazine articles.

PROGRAMMING NOTES

     Assuming you have constructed a single library out of the various C/80
relocatables, you must:

        c -m2 yourfile
        rmac yourfile
        link yourfile[nl,nr], vdclib13[s], yourlib[s]

GRAPHICS ROUTINES 


/*  bitmap()    :  Puts VDC in 80 col bitmap mode              */

/*  colorm()    :  Sets proper monochrome values in reg 26     */

/*  wrtvdc(i,j) :  i = reg nr, j=value to be written to reg    */

/*  k=rdvdc(i)  :  i = reg nr, k= register value               */

/*  zeroram()   :  Points to first byte of VDC memory          */

/*  clrmap()    :  Clears the bitmap                           */

/*  textmode()  :  Return register 25 to text                  */

/*  vdcram(i)   :  i=1 saves ram to disk, i=0 returns ram      */
/*                 i=3 saves, i=2 returns under filename given */
/*                 in scrnam[]                                 */

/*  saveram()   :  Save entire VDC ram to disk file VDCRAM.DAT */

/*  ramback()   :  Return VDCRAM.DAT data to VDC ram           */

/*  plot(x,y,n) :  plots a dot on 639x199 map if n=1.  Erase if n=0 */

/*  hires80     :  Sets, clears, and colors the bitmap         */

/*  chrpat(chr) :  Returns address of 8 byte char pattern       */

/*  rotpat(chr) :  Returns address of 8 byte character pattern */
/*                 character is rotated 90 deg counter clockwise  */

/*  plotby(byte,x,y) : Plot a byte - upper left hand corner     */
/*      (bit 7) located at x=0-631, y=0-199                     */

/*  plotch(chraddr,x,y) : Plot a character - upper left hand corner */
/*  (bit 7, byte 0) located at x,y : address of byte at chraddr */
/*  x <= 631, y>=7                                              */  

/*  twotal(chraddr,x,y) : Plot a  character using 16 bits */
/*  in the horizontal direction - upper left corner as above      */
/*  compensates for squat look due to screen aspect ratio         */

/*  hstrg1(strg addr,x,y) : write a horizontal string of 8 bit  wide */
/*    characters with upper left corner of first char at x,y    */

/*  hstrg2(strg addr,x,y) : write a horizontal string of 16 bit wide */
/*    chars with upper left corner of first char at x,y         */

/*  vstrg1(strg addr,x,y) : write a vertical string  of 8 bit wide */
/*    ROTATED chars starting at x,y for upper left corner, char #1. */
/*    string is drawn from bottom of screen to top of screen    */

/*  vstrg2(strg addr,x,y) : same as above but chars are 16 bit wide */
/*    in the screen's horizontal direction                      */

/*  vstrg3(strg addr,x,y):  write a vertical string with ordinary */
/*    unrotated chars with x,y being the upper left corner of the */
/*    first char.  String is drawn DOWN from TOP OF SCREEN.       */

/*  doline(x1,y1,x2,y2,color): draw/erase line between 2 points */

/*  doscrn(k,l) : Does the work for savescrn() & getscrn()      */

/*  savescrn(k)  : saves 16k screen- k is address of filename   */
/*      filename must be UPPERCASE.SCR                          */

/*  getscrn(k)   : returns 16k screen - k is filename address   */
/*      filename must be UPPERCASE.SCR                          */


 --------------------------------------------------------------------------

 UPPERCASE.SCR                          */


 ----------------------------------------------------------------