file: UMP.DOC

The origional UMPIRE.DOC is inserted here for completeness.
- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - 
                         UMPIRE.DOCUMENTATION
                         Memory Test Program

   UMPIRE is a comprehensive Memory Test Program. It implements two test
algorithms developed at the University of Illinois. The algorithms were
published in June 1978 'IEEE  TRANSACTIONS ON COMPUTERS'.
   The  University of Illinois test algorithms are the 'BOOMERANG' and the
'HALF SLOW' test routines.
   Also included are two test routines I devised.

   The test will automatically size the TPA and test all of Memory up the start
of BDOS.  There are only three control codes.

                   Control Codes:
  Test start:

    ^S will start or stop this Test Program.

The ^S function is particularlly useful in the 'SCRAMBLE' and 'SPIRAL' routine
to Stop to Test causing refresh verification on Dynamic Memories.  Another ^S
will cause the test to start up again.  Both the 'SCRAMBLE' and 'SPIRAL' test
routines use random data so this is a fair test of a memory array for pattern
sensitivity.

    ^K will cause the test to restart.

    ^C will cause a jump to address zero (i.e. warm boot).
   

Send any comments or suggestions to:
     Mel Cruts
     DIGITAL DELI COMPUTER STORE
     80 WEST EL CAMINO REAL
     MOUNTAIN VIEW, CA. 94040
- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - 
                UMPire for the Osborne Executive

The UMPIRE.COM memory diagnostic will not operate properly on the Osborne
Executive I computer.  The reason is that the first thing UMPIRE does is
disable interrupts.  Interrupts must be enabled on the Executive for proper
disk and keyboard operation.

UMP.COM is UMPIRE.COM with the following minor changes:

    1.	The interrupt disable was deleted.

    2.	A pass counter was added (prints pass # in hex).

    3.	The print routine was modified to print the test title prior to running
        the test.  This clarifies what error printouts go with what memory test.
	
A commented source listing is included to aid in diagnosing printed test results
(UMP.ASM).  This version should work fine on the Osborne 1 also but I haven't
tested it on that machine.

This diagnostic proved very useful in diagnosing a memory problem with a couple
of Osborne Executives in this area.  The problem was very elusive and occured
only on a couple of applications programs (WordStar mostly) but none of the
available memory diagnostics would reveal the problem.  

UMPIRE was the only diagnostic that would indicate a memory problem.  The
failures were random in addressing and data and only occured in common memory
(above 0FF00H).  As it turned out, the problem was fixed by adding a wire to
beef up grounding on the memory board (Roy Beers is a wiz with memory problems).
Also note that UMPIRE or UMP only checks user memory in bank 1 and is not a
global memory test for the Executive.

My thanks to Mel Curts, the author of the diagnostic, and to FOG for making it
available to members.
                                                            George Walker
                                                            Columbia, Md.
                                                            April 1984
                                        Columbia, Md.