____________________________________________________________________

        SUPERZAP  DISC SECTOR EDITOR   SUPERZAP.COM  (SPZ)
        ____________________________________________________________________


        SUPERZAP is a full screen interactive disk update utility, providing
        many of the features found in DU.COM, one of the earlier PD sector
        editors.  The program is menu driven, and little additional documen-
        tation is required. The following notes consist of a functional
        overview,  plus notes on features not documented in the menus.

        The version of SUPERZAP on this disc has been specilly configured
        for the MicroBee keyboard and needs no setting up.

        The program is menu-driven.  These notes are for further information
        and guidance.  The notes at the end of this document are supplied
        by S J Younger and refer to his modifications for CP/M Plus.

        SYSTEM REQUIREMENTS

        SUPERZAP (SPZ) requires a Z80 - it may be possible to update  the
        source for 8080 but extensive use is made of Z80 opcodes, and this
        would be a lrge exercise.  Subroutines would be required to
        simulate  LDR, LDDR,  and  CPIR,  to  say nothing of varieties of
        shift,  rotate and load instructions.

        One or more disks may be used - SPZ determines if a selected disk
        is defined in the BIOS before attempting to access it.

        The  terminal  used must support cursor addressing, clear screen,
        and erase to end of line. At least an 80 by  24  display  is
        required.

        FACILITIES

        SUPERZAP enables disk sector editing in HEX or ASCII, using  File
        Relative  or  Track/Sector addressing.  In File Relative mode a
        sorted  directory  listing is used to select the  file. In both
        modes  forward  and backward browse is provided,  in  addition to
        random record selection.  The displayed sector may be  copied to a
        scratchpad  buffer,   or  exchanged  with  the  scratchpad. The
        directory  list may be full (*.*) or selective,  eg  *.ASM and the
        selection may be changed at any time.

        A file TYPE facility gives a paged, formatted display of any file.
        Control characters are displayed as "." except  for  TAB  and
        Carriage return/Line feed which are processed  normally.  COM files
        are not formatted.

        The  SPZ command format may enter any operational mode directly:-

              SPZ                   enters SPZ with a *.* directory list.
              SPZ d:                as above with d:*.* diectory list.
              SPZ [d:]afn           as above with d:afn directory list.
              SPZ [d:]ufn           enters SPZ in file relative mode,
                                    using the specified file.
              SPZ [d:]DSK:          enters SPZ in Track Sector addressing
                                    mode on the specified drive.

        DIRECTORY LIST MODE.

        In directory list mode the cursor is positioned on the first
        filename displayed.  The cursor can be moved LEFT, RIGHT, UP or
        DOWN using Control keys.  A file is selected by typing a command
        character against the required file name - "E" for file relative
        editing, or "T" for the TYPE function.

        Up to 32 file names are listed. If there are more files, the
        directory list may be paged forward and back.

        Other drives may be selected or the current disk changed.

        NOTE  - if the disk in the current drive is changed, the "change
        disk" function  should be used to select the same drive again.
        This provides a new directory list, and avoids CP/M making the
        disk Read Only.

        Track/Sector addressing is selected from the directory list
        display.

        The directory list selection may be changed - the  default  is
        *.* unless set by the SPZ command.

        FILE RELATIVE MODE.

        In this mode the selected file is displayed in HEX and ASCII format
        with  record number and file offset displayed. For .COM files the
        address when loaded at 0100H is displayed.

        The record displayed may be selected by browsing forward and back,
        locating the first or last record, or by setting a record number
        (in HEX).  When setting a record number, Hex digit are entered in
        "calculator style" - new digits are entered on the right while the
        number moves left.  Backspace deletes the last digit entered, and
        Escape restores the original number. These features are common to
        all number entries in SPZ. The selected record is read when RETURN
        is pressed. If it is not found, the previous record number will be
        restored.

        The displayed record may be changed by typing "C". The cursor
        is positioned on the first hex digit, and is moved using the
        same control keys as are used in the directory list mode. Any
        valid hex digit may be typed to alter the record. Ctrl A  key
        moves the cursor to it corresponding location in the ASCII
        display, allowing character strings to be easily changed. Another
        Ctrl A returns the cursor to the HEX display area.

        Two control codes are available to stop editing  the record - one
        saves the changes and rewrites the  record  to  disk, the other
        restores the record to its original contents.

        Return to directory list mode is made by typing "L".

        TYPE FILE

        Files are TYPEd with up to 72 characters per line, 18 lines per
        page.  Except for .COM files, Carriage  return/Line  feed  codes are
        honoured, and Tabs are expanded. All  other  control  characters are
        displayed as  "."  to prevent unwanted terminal control functions.

        Forward and backward paging operations are provided, including
        return to top of file.  Following paging, the highest page displayed
        can be restored.

        DIRECTORY LIST SELECTION.

        The ambiguous file name used for the directory list may be edited by
        typing "M" in the directory list  mode dislay. The existing  file
        NAME and TYPE may be overwritten or edited using INSERT and
        DELETE control keys.  Only those characters defined as legal in
        the CPM documentation are permitted.

        If  "*"  is  typed at any point in the  NAME or TYPE, the
        remainder  of the field will be filled with "?". If a SPACE is
        typed the remainder of the field will be blanked out. Period also
        has  this  effect if used in the  NAME  field  -  an  ambiguous
        filename may thus be entered in the normal fashion.

        The TAB key switches between editing the NAME and TYPE.

        The ESCAPE key restores the original selection, RETURN produces
        a new direcory list.

        NOTE  - insert and delete affect only the field being
        edited, - characters do not wrap between name and type.


        TRACK/SECTOR ADDRESSING

        This mode is entered by typing "S" in directory list mode. The
        facilities provided here are similar to File Relative mode, but
        sectors  are  selected  by setting (or browsing back and forward)
        track and sector numbers.  The allocation  block number is also
        displayed and may be set.  When a block number is set, the first
        sector of that block is displayed. The record displayed may be
        altered  in the same manner as  File Relative mode.  The
        scratchpad  facility is also available in this mode.  Note that
        sectors saved in one mode are available for exchange in the other
        mode.

        INSTALLATION

        SPZ uses the following terminal facilities -

                  Cursor Addressing
                  Clar Screen
                  Erase to end of line.

        The  screen control strings start at 180h and each is eight bytes
        long including the length prefix:

              180-187   Clear screen and home cursor
              188-18F   Clear to end of line
              190-197   Set inverse video
              198-19F   Set normal video
              1A0-1A7   Cursor-positioning prefix
              1A8-1AF   String sent to screen BETWEEN cursor coordinates
              1B0-1B7   String sent to screen at end of cursor-positioning

        The  next  few  bytes relate to cursor positioning. Rows are
        numbered  0 to 23 from top down, columns are numbered  0-79
        from left to right.

              1B8                   1  if  row    coordinate  sent    before
                                    column  coordinate(usual case) or  0  if
                                    row before  column.   WARNING:   Do  not
                                    set this location to any value except  0
                                    or 1!

              1B9                   "Offset" to add to row (usually 20h)

              1BA                   "Offset" to add to column (usually 20h)

              1BB                   Non-zero  if  coordinates  are  sent  as
                                    single-byte  binary values  (usual case)
                                    or  zero  if  coordinates  are  sent  as
                                    multi-byte decimal  numbers  (e.g.  ANSI
                                    terminals).

        Finally, if you are using a Hazeltine terminal  which  doesn't  like
        the tilde character:

              1BC                   Set to 7Dh for Hazeltine terminals,  7Eh
                                    for others.

        If you are using Z8E to configure the object file then the symbol
        names for the above locations can be loaded from the .PRN file:

              z8e zap.com zap.prn

        You can the use the following names with the E command:

              clsstr    Clear screen and home cursor
              cllstr    Clear to end of current line
              vinv      Set inverse video
              vnorm     Set normal video
              cppref    Cursor positioning prefix
              cpmid     Cursor positioning infix
              cpend     Cursor positioning suffix
              row1st    Row-before-column flag (remember, set to 0 or 1
                        ONLY)
              rowoff    Offset to add to row
              coloff    Offset to add to column
              cpbin     Binary/ASCII coordinate flag
              maxasc    Higest displayable character

        When you select track/sector mode,  the deault track number used to
        be 0 but I changed it so that  the default  is  now  the  directory
        track.   It  is  not  very often you want to look at   the   system
        tracks with a disk eitor.   More frequently you want  to    recover
        files by fiddling the directory.  Besides, on a  "split" hard  disk
        where the splitting is done by cylinder rather than  by  platter or
        surface, there may not even be a track 0 on the selected disk.

        In  sector  displays,  characters with the high bit set   are   now
        displayed in inverse video rather than as dots.    This  simplifies
        reading directory sectors where files have attribute bits set.

        I put an .XLIST directive at the start and a .LIST directive at the
        end of the source file  to generate  a  .PRN file suitable  for use
        with the Z8E  debug  tool (SIG/M vol 239).

         If anyone wants to contact John, his address is:-

                       John Hastwell-Batten,
                       SYSOP,
                       Tesseract RCPM+,
                       P.O. Box 242,
                       Dural, NSW 2158,
                       AUSTRALIA

        Now to the real goodies in  3.4  -  more  object  code  patches  for
        control commands.



              1BD                   The "flag" character used  in  directory
                                    list
              1BE                   The number of command  codes  following.
                                    Do NOT change.
              1BF                   Cursor Left control code
              1C0                   Cursor Right
              1C1                   Cursor Up
              1C2                   Cursor Down
              1C3                   Cursor Tab
              1C4                   ESCape
              1C5                   Insert mode in file name edit
              1C6                   Character delete in file name edit
              1C7                   Quit - applies to sector and string edit
              1C8                   End Edit.

       Once these codes are patched in - using SPZ of  course,  the  panels
       are displayed with the new values.

                                 Thats it Folks -
                                           Willie Davidson.


                 Installation for CP/M PLUS - S.J. Younger

              This version (now 3.7) had been modified to  run   under  CP/M
        Plus before I became aware of the Hastwell-Batten version,  and  was
        written on an Amstrad PCW.  Having had the  opportunity  to  examine
        version 3.4, I have attempted to retain th best features from  both
        sources.  Thus Michael Hendry's CP/M Plus implementation  beats  the
        JHB system in that the latter has un-necessary calls to BDOS 50.   I
        have taken in all the object code patchable features and the inverse
        video feature except that it has been eliminated from 'Type' mode by
        the simple expedient of clobbering bit 7 first.  This makes WordStar
        document mode files  fully  legible  without  being  spattered  with
        inverse video characters.

              It should be mentioned that all the routines in  this  program
        controlling keyboard input can be aborted by pressing "ESC" ("EXIT")
        and that partial deletions of the input are achieved by pressing the
        'Cursor Left' arrow.

              A 'Select to Page No.' routine has been introduced into    the
        Type routine.  The input is  decimal.    Since   the    relationship
        between  page of text and sector numbers is not   predictable    the
        only  way  to  avoid  ending  up  totally  knotted  is  to      read
        sequentially  down or up the file.  The routine can  be  stopped  at
        any time by pressing the STOP button (Control-C).  Large  files  can
        be scanned more quickly if they  are first transferred onto  the  M:
        drive.  When working under CP/M Plus the program acquires  knowledge
        of the screen size and if  it  finds  that  it's  a  90x32  it  then
        proceeds to use all of it in 'Type' Mode.

              Due to it's strict attention to format LocoScript  takes  some
        time to display it's documents.  This can make the use of LocoScript
        for selecting and clearing out unwanted files  a  tedious  business.
        SUPERZAP can  quickly  make an intelligible  display  of  LocoScript
        files.  To be a useful  file cleaner in this context it  needed  the
        opportunity to  select  user number and also erase  files  from  the
        Directory  mode.    The  user number follows the convention of   the
        CCP,  namely  I/O  is  decimal and user zero is not displayed.   The
        user number  is  not  re-set other than explicitly when the drive is
        changed.

              The Erase File feature deletes the file at the curso position
        using CP/M's  erasure routines,   which  prefix the directory entry
        (entries) with E5h.  If  a  file  is  erasd  in  error  it  can  be
        resurrected by re-setting the directory entry  (or entries  if  the
        file is greater than 16k) by  switching  to  the  'Track  /  Sector
        Addressing Mode' and changing the directory entry back to 0n  where
        n is User No.

        TAKE GREAT CARE NOT TO DWELL ON THE 'K' FOR ERASE BUTTON SINCE  THIS
        MAY DELETE MORE THAT ONE FILE!

              In this version of Superzap the 'Find  a  String'  routine in
        Edit Mode has been re-introduced with input either in ASCII  or HEX
        format.  The search is precise to case - e.g. a search for the word
        'Function' will be unsuccessful  with  the  input  'function'.   If
        control  characters  are  included in  an  ASCII  string  they  are
        displayed.  Thus a press ofthe 'TAB' key  will  be  represented  on
        screen as '^I'.  The maximum length of string that can  be  entered
        for the search is 32 characters.  Searches will run more quickly if
        the file is first put onto the 'M:' drive.


        S.J. Younger     February 1988

es will run more quickly if
        the file is first put onto t