DOCUMENTATION FOR DPP v1.0 - Disk physical parameters
                       by Julian Loke, November 1985

     One  of  the  nice things about disk  systems  built  around 
floppy-disk controller (FDC) integrated circuits like the  WD1793 
series  (Western Digital) is that only a few changes in  software 
are  needed  in  order  to read from and write  to  a  number  of 
different  CP/M  disk  formats.   This feature has  already  been 
implemented  on  the commercial disk systems  available  for  the 
Microbee.

     There  are a number of "Drive Redefinition" programs  around 
(mostly  in the public domain) which list a number  of  different 
disk  formats  for  which  a  particular drive  can  be  set  up.  
However,  if you do not have access to some of these programs, or 
if  you  need  to  use  a disk  format  which  is  not  currently 
supported,  then  you (or a friend) will need to figure  out  the 
disk parameters yourself.

     One  of  the  first (and easiest) tasks is to work  out  the 
disk physical parameters.  These are the rules which the hardware 
uses  to  specify the way data is stored on a disk,  for  example 
whether single density or double density recording is used.

     DPP  is a program written for the MicroBee 56k disk  system.  
It performs a few simple and non-destructive read tests on a disk 
in  order to determine a few physical parameters associated  with 
the way that the disk has been formatted.

     To "measure" the physical parameters of a disk,  use the DPP 
command.   There are no parameters (at present).  All the numbers 
displayed are in hexadecimal format.

     Here is a sample run, performed on a "standard" Microbee disk:

A>dpp

Log (disk physical parameters) for MicroBee 56k disk system by J.Loke Nov 1985
No distribution for profit without author's express permission

Mount "foreign" disk in drive B, then press RETURN ?

Data recording density          = Double
Physical sector length (bytes)  = 0200
Physical sectors per track      = 01..0A
Number of sectors per track     = 0A
Track size (128 byte records)   = 0028
Readable tracks on side 0       = 00..27
Readable tracks on side 1       = 28..4F
Number of sides per disk        = 02
Number of readable tracks       = 50
Total disk capacity (kilobytes) = 0190

Returning to system
A>_

     As you can see,  only a limited amount of information can be 
"measured"  by  DPP,  but this may prove very useful as  a  first 
step.Š
     Unfortunately,  there is not enough room here to explain how 
to  completely  specify a disk format so that you  can  access  a 
"foreign" disk on your system.  That remains the task for someone 
with better skills at explaining things.

     I  hope  that  DPP is useful to someone.   If you  have  any 
comments, criticisms, or enquiries, please leave a message for me 
on this bulletin board, RE: DPP.

                              Good Luck
                              Julian Loke