DDFPAT (MULTIPLE FORMAT SUPPORT FOR DDFORMAT) DOCUMENTATION
by Julian Loke, 1986 July 06
No distribution for profit without author's express permission.


                          INTRODUCTION

     With  the  capability of using powerful  utilities  such  as
SETDRIVE, SETDISK, SDR, DRIVESET, etc., etc., on my MicroBee 56k,
it seemed sad that it was not possible to format disks compatible
with other machines,  such as the ubiquitous and widely supported
KAYPRO II.  This  situation  does  not  exist for  a  some  other
machines in the market.

     The  DDFORMAT.COM utility provided with my  system  produces
disk  formats with 10 sectors per track,  40 tracks per  side,  2
sides per disk.   It is a relatively simple matter to patch it to
produced  formats  compatible with machines using 10  sector  per
track  formats.   Fortunately the KAYPRO II (SSDD) and the  AMPRO
(DSDD) are systems fitting this description.

     So,  to produce disks compatible with a Kaypro II system,  I
can now type:
                     A>ddformat kaypro2


                         USAGE AND NOTES

     The  syntax for the patch appears below:

                     DDFORMAT [ M | K | A ]

1)   No parameters:   A  menu  showing the options  available  is
          displayed.    Pushing   the  appropriate  key  (M   for
          Microbee,  K for KayproII, and A for Ampro) will set up
          the  program  for the required system.   Typing  Ctrl-C
          aborts the program.

2)   Parameter  M,  K,  A:   The  patch program will  select  the
          correct data for the corresponding system, and DDFORMAT
          will run in a manner akin to the unpatched version.

3)   Parameters other than M, K, A:  The program behaves as if no
          parameter had been entered, and the menu is displayed.


                   FURTHER NOTES AND DISCLAIMER

     Disk formats produced using this method ARE NOT THE SAME  as
those  produced  on the proper  target  machines.   However,  the
formats are COMPATIBLE with the appropriate target machine, which
can read and write data/text on the disk.  Of course they are not
"system" disks, and so cannot be used for booting.  Despite this,
there is no problem with using them as TRANSFER disks.

     There  is  only one new error message produced by the  patch
program.   A  "Bad  Version"  error results if  your  version  of
DDFORMAT.COM  is not one of the two supported.   If this  is  the
case,  then  a new patch program will have to be written.


                      INSTALLING THE PATCH

     The  two  versions of DDFORMAT.COM supported  use  the  same
installation sequence.   Before you start, make sure that you are
NOT altering your system disk.   Work with backup copies.  You'll
need the following files:

               DDFORMAT.COM        Your original copy, of course!
               DDFPAT.HEX          The patch program itself
               DDT.COM             A standard CP/M utility

     Use  the following sequence of commands to produce the  file
NDDF.COM,  which you will rename later.  Note that the letters in
lower case are to be typed by the user:

               A>ddt ddformat.com
               DDT VERS 2.2
               NEXT  PC
               0500 0100
               -iddfpat.hex
               -r
               NEXT  PC
               0688 0000
               -g0

               A>save 6 nddf.com
               A>_

     Now,  test  the  formatting program using a blank disk  (NOT
the disk with your precious public domain software on  it!),  and
the  NDDF command.   Once you are satisfied with the new program,
rename it to DDFORMAT.COM using the following commands:

               A>era ddformat.com
               A>ren ddformat.com=nddf.com
               A>_


                 ACKNOWLEDGEMENTS AND ENQUIRIES

     Thanks  to  Mirko  Fluher for his help  and  advice  in  the
development and testing of this software.

     If you have any enquiries,  requests for source, etc, please
feel free to get in touch with for me either via the magazine, or
via the MBUG bulletin board (7*24h (03)-882-1571).


END OF DOCUMENTATION