DUU.DOC
by Ward Christensen (revised 10/23/81)
Includes notes by Ron Fowler for DU-V75.

HOW TO USE DU ver 7.5 DISK UTILITY
	(Extended and called DUU on CP/MUG v.71)

DUU, Disk Utility-Universal, is an enhanced version of
previous DU programs, on CP/MUG volumes 40 and 46.

The primary change over the earlier CP/MUG versions is the
additions by Ron Fowler, to make DU work with virtually any 1.4
or 2.2 system, single or double density.


	INDEX
0.0	Changes from DU-V75
1.0	INSTALLATION:
2.0	USE:
  2.1	COMMANDS, BY FUNCTION (quick reference)
  2.2	ALPHABETIC COMMAND SUMMARY
3.0	NOTES
4.0	INTERPRETATING DIRECTORY DATA
  4.1	SINGLE DENSITY
  4.2	DOUBLE DENSITY


0.0	CHANGES FROM DU-V75
===

	The primary change is that all routines	which original-
ly accepted a decimal number, such as /, +, -, and Z, which
were changed to HEX in DU-V75, are now changed BACK to decimal.
	The "F" command now works completely under 1.4 and 2.2,
and finds all users, and even erased files.  Ambiguous file
names are now allowed.  After using "F" with a specifid name,
F with no operands will find the next "occurrence" (i.e.
extent, or earlier erased copy, etc) of a file.
	This is	a matter of taste - I don't believe in
"babying" CP/M users with "press any key to continue" when more
than 16 lines has scrolled by.  I removed these, so use ^S to
suspend scrolling of the "?" (help) output.
	The "U"	command	has been deleted, since	its only
purpose was to change users for the sake of the old "F"
command.  The new "F" command obsoleted the "U" command.
	Made sure + and	- check	the "NOTPOS" flag; that	was a
"loophole" that could "mislead" you.
	Added ability to put Hex into default decimal fields.
Needed this to transfer files, where their hex length is known,
i.e. a file 29h sectors long in contiguous extents may be read
into memory via: <<;+;/29h
	Added "E" (erase screen) command.  Store the character
sequence, 0ffH terminated, at 104h.  Useful as in "e;+;d;z20;/"
to dump, sit, loop.  The screen clear "e" causes the display to
"sit".
	Set "@" when using "F" command, so for example to erase
a file: "ffoo.zot;ch@,e5";w 	Also change "not found" of "F"
command so it aborts, thus preventing, in the above ex., the
actual change-and-write.


1.0	INSTALLATION:
===
	The 7.0	and later versions of DU are designed to be
installed with a minimum of trouble.  In fact, in almost all
cases, no changes to the source file should be necessary to get
DU up and running. This is because DU uses the disk paramter
block of CP/M to determine the characteristics of the disk
environment.  (see the disclaimer for certain non-standard
versions of CP/M 1.4).
	The only parameter that	should need to be changed will
be the clock speed flag at 103H.  Leave this byte zero if you
have a 2 mhz clock.  Patch it non-zero for 4 mhz.  This is only
needed for the "Z" (sleep) command.  An alternative is just to
use larger numbers when running 4mHZ or 5MHz.


2.0	USE:
===
An initial command string may optionally be placed as an
operand of the original DU command, i.e.:

     A>DU G0;D;G2;=OK<D><A><1A>;D

For example, if you want to only MAP the disk, then exit:

	A>DU M;X

Once DU is running, it expects single-letter commands much
like SID or DDT.  For ease of use, multiple commands may be
placed on one line, separated by ";".  In addition, a given
command or string of commands may be repeated, either indef-
initely (until ^C is pressed), or a given number of times.

To avoid an accidental ^C from dropping out of DU, only an
explicit "X" command will exit DU.


2.1	COMMANDS, BY FUNCTION
===

Help:
	?	request help

Positioning:

	Gnn	by allocation group
	Snn	by sector
	Tnn	by track
	+nn	going ahead nn sectors
	-nn	going back nn sectors

I/O:
	R	Reads sector
	W	Writes sector
	<	Puts current sector "away" into a buffer
	>	Recalls previously saved sector

Displaying:
	G	Shows current group, track, sector
	M	Maps the disk - where are the files
	Mxx	Map starting at group xx
	D	Dump the sector (hex + ascii)
	A	Dump sector in ASCII
	H	Dump sector in hex
	Vnn	Views (like CP/M TYPE) nn sectors
	#	Shows disk parameters, also # of sectors
		stacked and used via "<<" and ">>"

Changing:
	CHnn,val Change data in hex
	CAnn,val Change data in ascii ( with <xx> escape to hex)
	N	insert new disk
	Unn	Change user to nn

Searching:
	Fname	Find a file in the directory
	F	Find next occurrence (extent) of same name
	=aaaa	Scan for aaaa (in ASCII) from current
		sector on

Misc:
	Znn	Sleep (nn tenths of a second) such as to allow
		viewing data before it scrolls off
	Lx	Log in disk x
	P	Turn on/off printer output toggle
	Q	Before any command does it "quietly"
	X	Exit to CP/M
	/nn	Repeat previous command nn times
		(indefinitely if nn omitted)


2.2	ALPHABETIC COMMAND SUMMARY
===

	#	Prints the disk parameters

	+	advance 1 sector (if below track 2,
		this advances to next numerical, if
		2 or >, advances based on CP/M's normal
		sector scrambling algorithm, i.e. so +
		will get the next logical sector of the file

	-	backs up 1 logical sector

		Note + and - may take an amount:
		for example, +15 steps in 15 sectors.

	/	Repeats entire command.  Defaults
	/nn	to "forever".  nn may be 2 to 65535

	<	Saves current sector in a save buffer
		also resets buffer pointer used by << and >>

	<<	Saves current sector, bumps memory pointer.
		Thus subsequent "<<" saves "next" buffer in
		memory.  Use "<" to reset, or ">>" to
		sequentially retrieve the buffers, such as to
		move several sectors from one place on disk
		to another, or to another disk, or just to
		memory (stored at 2000H where DDT or SID
		can subsequently access them)

	=string	Ascii search, starting at current
		sector. <xx> hex may be imbedded,
		or used alone:  To find "IN 0FEH":
		=<db><fe>
		Ignores bit 7 unless <xx> is used.

		Since ";" is a command delimiter, you
		have to use <3b> to search for a ";".
		
		Also, since "<" is a hex-escape char,
		use << to meane a single "<".

		N-O-T-E the special symbol "@" contains
		the displacement at which the match occurred.
		It may thus be subsequently used in a C
		command, as in:

			=LIX;CA@,LXI;W

		would search for the string LIX, change
		it to an LXI, and write it back.

	>	Gets saved buffer.  < and > may be used
		to move a sector to another place.

	>>	Restore "oldest" unrestored sector saved
		by "<<" command.  This command may be
		"buried" in the middle of an infinite
		repeat "/", because it will stop operating
		when there are no more sectors in the buffer.

	?	Gives command summary

	A	Dump sector, ASCII only

	CHaddr,val,val,val... change hex in sector
	CAaddr,char string... change ASCII in sector
		NOTE that <xx> may be hex imbedded
		in the Ascii:  ca0,OK<d><a><1a>

		----> Use W to write changes to disk.
		Note that the C command echoes
		the overlaid data for verification.

	CHaddr-addr,byte
 or	CAaddr-addr,byte	repeats a change

	D	Dump sector, hex + ASCII

	Fname	print directory for file "name",
		then positions to it's directory
		sector.

	F	Find next occurrence of name in dir.

	Gnn	Position to group nn and read.

	G	Shows current position

	H	Dump sector, hex only

	L	Re-logs in the current disk. You may pull
		out a disk, put in a new, and "L" just
		to log it in. (See "LOGGING IN DISK" in NOTES
		below)

	Lx	Logs in disk 'x', such as: LB

	M	Dumps a map of the group allocations
		for files.
	Mn	Shows which file is allocated to
		group "n".

	N	Resets CP/M via the BDOS.  This may
		make it possible under some implementations
		of CP/M to change the disk format (e.g., density,
		sides, etc)

	P	Toggle printer switch on/off

	Q	Quiet: Preceeding any command, suppresses console
		output

	R	Reads the sector currently positioned to
		into memory.  Note R (Read) is implicit in
		the G, +, and - commands, but N-O-T in the
		S and T commands (I did it because I was
		tired of disk reading after T command before
		I had a chance to issue the S command)


	Snn	Position to sector nn, and read

	Tnn	Seek to track nn (no read)

	Ux	Logs user 'x' for next F command.  Gives
		'?' error if not CP/M version 2.x.
		(Note "F" no longer needs this - finds
		 ALL files - erased, any user, etc)

	V	Views the current sector.
		(assumes ASCII data)
	Vnn	Views nn sectors

	W	Write back the current sector (N-O-T-E may
		not be used after an F command, as CP/M was
		used to find the file in the directory

	X	Exit back to CP/M (Must press return).  Ctl-c
		was too easy to hit over modem lines, so I
		decided on 2-byte (X, CR) to exit.


	Z	Sleep - causes the program to pause, such
		as to look at a dump.  Z is 1 sec.  Znn
		is nn tenths of a second on a 2 MHz 8080.



3.0	====== NOTES ======
===
* MULTIPLE COMMANDS: May be separated by ";"

Example: the following commands will erase the
	b disk directory to all E5's:

	lb		log in b drive
	g0		position to dir.
	ch0-7f,e5	fill with e5
	<		save the sector
	>;w;+;/16	restore, write, next,
			repeat 16

----This could be shortened to:

	lb;g0;ch0-7f,e5;<
	>;w;+;/16

* DUMP COMMANDS: All dump commands (D, A, H) may be optionally
followed by a starting and ending address:
	D0,7F	is the same as just D
	D3,5
	A20,3F

* LOGGING IN DISK: In the original DU, I logged in the disk the
way DU now does.  Then, I found that when you had a blown
directory, you DIDN'T want to log the new disk in.  Thus I
changed DU to just change which disk was selected.  Then along
came double density, with its attendant "select density"
functions, and Ron apparently put this back in.  So, it now
sometimes works for double density, but makes DU very
"intolerant" of disks with un-readable directories.  A
solution is to log in a disk which is OK, and is of the same
density as the blown disk, then put in the blown disk WITHOUT
logging it in.
	However, you are now opening yourself up to possible
problems because of the buffering of physical sectors in the
BIOS.  The best technique, (but not guaranteed), would be to
seek to the unused inner tracks of the first disk, do the
read, THEN change disks.  That way if it writes anything, you
won't have destroyed anything.  ...assuming the disk is not
completely full.  Another technique, assuming the second disk
does not contain a CP/M system, would be to seek to track 1,
then do the read there, then change disks to the blown one.

	Regarding the << and >> commands:
*	Up to 255 sectors (only because its a 1 byte counter)
	may be saved by <<.
*	ANY TIME "<" is executed, the buffers are "thrown away".
*	One ">>" to fetch a saved buffer and make it available
	for writing, may be issued for each previous "<<".
*	The "M" (directory map) command uses an area of memory
	for a buffer.  To minimize problems, the Map buffer is
	placed a the END of the CURRENTLY HIGHEST USED "<<"
	buffer.  On small systems, where a "lot" of buffers have
	been saved via "<<", the "M" command might report that
	it ran out of memory.  Executing "<" (or ">>" sufficient
	times for it to tell you there are no more sectors
	in the buffer) will then make room available at a lower
	address, for "M" to use for the directory.

	The following command could be used to move your directory
	out to the end of your disk. (to keep a "back up" copy).

	1) Map the disk to find an open space at the end:
		Me0		map starting at e0.
	2) Suppose E0 is wide open.  Capture the directory:
		g0
		<<;+;/26



4.0	INTERPRETATING DIRECTORY DATA
===

4.1	SINGLE DENSITY
===

The following explains the format of a CP/M directory entry
as shown by DU, using either the "F" (find file) command,
or just doing "D" (dump) of the directory sectors, which
are located in groups 0 and 1 on a single density disk.
		----------------
Sample result of "FSID.COM" command:

40  00534944 20202020  20434F4D 0000003A  *.SID     COM...:*
50  33343536 3738393A  00000000 00000000  *3456789:........*

First line -

40  00534944 20202020  20434F4D 0000003A  *.SID     COM...:*
||  |||                      |  ||    ||    |         |
||  ||^----hex file name-----^  ||    ||    ^file name^
||  ||                          ||    ||     in ASCII
||  ||                   extent-^^    ||
||  ||                                ||
||  ||           file size in sectors-^^
||  ||
||  ^^-00 = file active  Other values (e.g 03) = User #
||     E5 = file erased
^^-displacement of line in directory sector

Second line -

50  33343536 3738393A  00000000 00000000  *3456789:........*
    |				       |   |
    |				       |   ^- allocation groups
    ^-----allocation group numbers-----^	just happened
						to be printable


4.2	DOUBLE DENSITY
===

The following is a sample of FSID.COM running on double
density system:

:FSID.COM
00  00534944 20202020  20434F4D 0000003A  *.SID     COM...:*
10  38003900 3A003B00  00000000 00000000  *8.9.:.;.........*
G=0000:00, T=2, S=1, PS=0

The primary difference is that the groups now occupy
2 bytes, i.e. "38 00" "39 00" ...  This follows the INTEL
and CP/M convention of putting 16 bit values high-byte-first.
Thus it means group 0038, 0039, etc.

Note that in double density, each group stood for 2K, not 1K,
so there were half as many groups for the same file.

Be VERY careful when patching a directory under double density.
I once made the mistake of putting, for example:

	ch10,38,39,3a,3b...

When I went to read this file, it tried to access group 3938,
with resultant angry exclamations from the disk stepper as it
attempted to go south to Peoria for the data.

					10/23/81 Ward C.